| Input Contribution |
| --- |
| Meeting ID* | TDE#43 |
| Title:* | TS-0013 Geo-query interop test case |
| Source:* | In Song Lee, KETI, insong@keti.re.kr SeungMyeong Jeong, KETI, sm.jeong@keti.re.kr NakMyoung Sung, KETI, nmsung@keti.re.kr |
| Date:* | 2019-12-05 |
| Input related to* | TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) |  |
| Decision requested or recommendation:* |  |
| Template Version: November 2018 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution is containing new interop test case for geo-query. Based on the below contributions in SDS, geo-query function has been defiend.

- SDS-2019-0485R03-TS-0001_geo-query_feature

- SDS-2019-0625-TS-0004_geo-query_filter_representation_update

Find a detailed test information from the table.

********** Start of new text 1 **********

#### 8.1.6.7	Discovery with geoQuery filter criteria

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_103 |
| Objective: | AE discovers container based on the geoQuery filter criteria |
| Configuration: | M2M_CFG_01 |
| References: | oneM2M TS-0001 [1], clause 10.2.6 oneM2M TS-0004 [2], clause 7.3.3.17 |
| Pre-test conditions: | <AE1> and <AE2> resources are created in Registrar CSE. A <Container> resource is created under the <AE2> resource in Registrar CSE. The <Container> resource has location attribute set to type as 2(LineString) and coordinates as [[100.0, 0.0], [101.0, 1,0]]. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE1 is requested to send a Discovery request in order to discover resources located in Registrar CSE using geoQuery filter criteria |
| 2 | Mca | PRO Check Primitive | Sent request contains op = 2 (Retrieve) to = {CSEBaseName} fr = AE1-ID rqi = (token-string) fu=1 gq = {gmty=3, geom=[[99.0,0.0],[99.0,1.0],[101.0,0.0],[101.0,1.0]], gsf=1} pc = empty |
| 3 | Mca | PRO Check Primitive | Registrar CSE sends response containing: rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = Serialized representation of data object containing <container> which fulfill the geoQuery discovery hosted by the Registrar CSE |
| 4 |  | IOP Check | AE1 indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

********** End of new text 1 **********