| CHANGE REQUEST |
| --- |
| Meeting:* | TDE #45 12 May |
| Source:* | ETSI |
| Date:* | 2020-05-07 |
| Contact:* | Miguel Angel Reina Ortega, ETSI, MiguelAngel.ReinaOrtega@etsi.org |
| Reason for Change/s:* | Update Test components variables R3 |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0019-V-3.0.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Update of test component variables (change 1), a typo found in chapter 5.1 (change 2) and addition of new pixits in chapter 7.3 (change 3).

----------------------- Start of change 1 -----------------------

## 5.5	Test components

### 5.5.1	Tester

The Tester test component includes a set of ports, timers and variables that are common to the other defined components which are described in table 5.5.1-1.

Table 5.5.1-1: Tester component elements

| Name | Instance type | Element type | Description |
| --- | --- | --- | --- |
| acPort | port | AdapterControlPort | Port that communicates with the adapter for sending configuration parameters |
| infoPort | port | InfoPort | Port between test components for exchanging information |
| utPort | port | UpperTesterPort | Port that communicates with the UT Application for triggering actions on the IUT |
| tc_ac | timer | N/A | Timer for the reception of a message |
| tc_wait | timer | N/A | Timer for the reaction of the IUT to an upper tester primitive |
| tc_done | Timer | N/A | Timer for waiting completion of a component behaviour |
| vc_config | variable | Configurations | Configuration being used for the given test case |
| vc_testSystemRole | variable | TestSystemRole | Role of the test component |
| vc_resourcesList | variable | MyResourcesList | List of all resources created by the test system on the IUT |
| vc_resourcesIndexToBeDeleted | variable | IntegerList | List of indexes of resources created by the test system on the IUT that need to be deleted |
| vc_acpIndex | variable | integer | Index of accessControlPolicy resource used by the test system by default (when required) |
| vc_request | variable | MsgIn | Latest request primitive received/sent |
| vc_response | variable | MsgIn | Latest response primitive received/sent |
| vc_aeSimu | variable | default | Reference to the default behaviour for an AeSimu component |
| vc_cseSimu | variable | default | Reference to the default behaviour for an CseSimu component |
| vc_primitiveContentRetrievedResource | variable | PrimitiveContent | Latest content of a RETRIEVE operation |
| vc_myInterfaces | variable | Interfaces | Parameters for the ports of the given component: Port (mcaPort, mcaPortIn, mccPort, mccPortIn) Host (SUT IP address :port) Protocol binding Serialization |

Note that vc_aeSimu and vc_cseSimu are not common to the other defined test components, but those variables are required in Tester for the correct activation/deactivation of default behaviours.

### 5.5.2	AeSimu

The AeSimu test component extends the Tester component by adding elements specific to an AE entity. Table 5.5.2-1 summarizes those elements.

Table 5.5.2-1: AeSimu component elements

| Name | Instance type | Element type | Description |
| --- | --- | --- | --- |
| mcaPort | port | OneM2MPort | Port that implements the mca interface when test system is the client (sending requests) |
| mcaPortIn | port | OneM2MPort | Port that implements the mca interface when test system is the server (receiving requests) |
| vc_ae2 | test component | AeSimu | Reference to the AE2 component when required |
| vc_cse1 | test component | CseSimu | Reference to the CSE1 component when CF02 is used |
| vc_ae1 | test component | AeSimu | Reference to the AE1 component when required |
| vc_das | test component | AeSimu | Reference to the DAS component when required |
| vc_aeSimuDesc | variable | AeSimuComponentDesc | Component configuration extracted from required (AE1 or AE2) tester pixit |
| vc_dasSimuDesc | variable | AeSimuComponentDesc | Component configuration extracted from DAS tester pixit |
| vc_auxiliaryAe2Up | variable | boolean | Flag to indicate that AE2 component has been started |
| vc_aeIndex | variable | integer | Index of the AE resource in vc_resourcesList created by AeSimu component |

### 5.5.3	CseSimu

The CseSimu test component extends the Tester component by adding elements specific to an CSE entity. Table 5.5.3-1 summarizes those elements.

Table 5.5.3-1: CseSimu component elements

| Name | Instance type | Element type | Description |
| --- | --- | --- | --- |
| mcaPort | port | OneM2MPort | Port that implements the mca interface when test system is the client (sending requests) |
| mcaPortIn | port | OneM2MPort | Port that implements the mca interface when test system is the server (receiving requests) |
| mccPort | port | OneM2MPort | Port that implements the mcc interface when test system is the client (sending requests) |
| mccPortIn | port | OneM2MPort | Port that implements the mcc interface when test system is the server (receiving requests) |
| vc_ae1 | test component | AeeSimu | Reference to the AE1 component when CF02 (CseSimu as master) is used |
| vc_cse2 | test component | CseSimu | Reference to the CSE1 component when required |
| vc_cseSimuDesc | variable | CseSimuComponentDesc | Component configuration extracted from required (CSE1 or CSE2) tester pixit |
| vc_localResourcesList | variable | MyResourcesList | List of all resources created by the IUT on the test system |
| vc_localRemoteCseIndex | variable | integer | Index of the remoteCSE resource in vc_localResourcesList representing the IUT (CSE) |
| vc_remoteCseIndex | variable | integer | Index of the remoteCSE resource in vc_resourcesList representing the CseSimu component |
| vc_cSEBaseIndex | variable | integer | Index of the CSEBase resource in vc_localResourcesList of the CseSimu component |
| vc_cseType | variable | CseTypeID | CSE type of the test system (default is MN) |
| vc_auxiliaryCse2Up | variable | boolean | Flag to indicate that CSE2 component has been started |

## ----------------------- End of change 1 -----------------------

----------------------- Start of change 2 -----------------------

## 5.1	Abstract protocol tester

An abstract protocol tester (APT) is a process that provides behaviours for testing an IUT by emulating a peer IUT at the same layer, and enabling to address a single test objective.

APTs used by the oneM2M test suite are described in figure 5.1-1. The test system will simulate valid and invalid protocol behaviour, and will analyse the reaction of the IUT.

Figure 5.1-1: Abstract protocol testers - oneM2M

As figure 5.1-1 illustrates, the corresponding ATS needs to use lower layers to establish a proper connection to the system under test (SUT) over a physical link (Lower layers link). Four different lower layers have been specified corresponding to the binding protocols considered in oneM2M: HTTP, CoAP, WebSocket and MQTT.

----------------------- End of change 2 -----------------------

----------------------- Start of change 3 -----------------------

## 7.3	IXIT

The following parameters are used by the oneM2M ATS for the correct execution of the test cases.

Table 7.3-1: oneM2M ATS IXITs

| GROUP | IXIT NAME | DESCRIPTION | DEFAULT VALUE |
| --- | --- | --- | --- |
| IutParameters | PX_IN_CSE | MN-CSE | True |
|  | PX_MN_CSE | IN-CSE | False |
|  | PX_ASN_CSE | ASN-CSE | False |
|  | PX_SUT_ADDRESS | SUT address | "127.0.0.1:8080" |
|  | PX_UT_IMPLEMENTED | Upper Tester implemented | False |
|  | PX_CSE_NAME | IUT CSE Name | "cseName" |
|  | PX_CSE_ID | IUT CSE-ID with SP-relative-CSE-ID format (relative) according to oneM2M TS-0001 [1], table 7.2-1 | "/cseId" |
|  | PX_CSE_RESOURCE_ID | IUT CSE resource ID with Unstructured-CSE-relative-Resource-ID (relative) format according to oneM2M TS-0001 [1], table 7.2-1 | "cseResourceId" |
|  | PX_SP_ID | IUT M2M-SP-ID with M2M-SP-ID format (absolute) according to oneM2M TS-0001 [1], table 7.2-1 Unstructured-CSE-relative -Resource-ID | "//om2m.org" |
|  | PX_SUPER_AE_ID | AE-ID with privileges to CREATE at the IUT CSEBase with AE-ID-Stem format (relative) according to oneM2M TS-0001 [1], table 7.2-1 | "admin:admin" |
|  | PX_SUPER_CSE_ID | CSE-ID with privileges to CREATE at the IUT CSEBase with SP-relative-CSE-ID format (relative) according to oneM2M TS-0001 [1], table 7.2-1 | "/admin:admin" |
|  | PX_ALLOWED_C_AE_IDS |  | {"C-AllowedAeId"} |
|  | PX_NOT_ALLOWED_C_AE_IDS |  | {"C-NotAllowedAeId"} |
|  | PX_ALLOWED_S_AE_IDS |  | {"S-AllowedAeId"} |
|  | PX_NOT_ALLOWED_S_AE_IDS |  | {"S-NotAllowedAeId"} |
|  | PX_NOT_ALLOWED_APP_ID |  | "NotAllowedAppId" |
|  | PX_ADDRESSING_METHOD | Addressing method | e_hierarchical |
|  | PX_PRIMITIVE_SCOPE | Primitive scope | e_cseRelative |
|  | PX_WS_PROTOCOL | WebSocket protocol | "oneM2M.R2.0.xml" |
|  | PX_REQUEST_URI | WebSocket context | "/" |
|  | PX_HOSTING_CSE_ID | Hosting CSE-ID for MQTT | "CSE-ID" |
|  | PX_CREDENTIAL_ID | Credential-ID for MQTT | "admin:admin" |
|  | PX_XML_NAMESPACE | XML Namespace | "m2m=""http://www.onem2m.org/xml/protocols""" |
|  | PX_ACOR | AccessControlOriginators | {"all"} |
|  | PX_TCONFIG_IUT | Time to configure IUT after a requested action | 10.0 |
| TesterParameters | PX_TS_AE1 | AE1 component settings | aeIdStem = "" appId = "NMyApp1Id" mcaPort and mcaPortIn settings which include per port the following info: Binding: - bindingProtocol - bindingDesc: - tsAddress - localPort - sutAddress - remotePort Serialization |
|  | PX_TS_AE2 | AE2 component settings | aeIdStem = "" appId = "NMyApp2Id" mcaPort and mcaPortIn settings which include per port the following info: Binding: - bindingProtocol - bindingDesc: - tsAddress - localPort - sutAddress - remotePort Serialization |
|  | PX_TS_CSE1 | CSE1 component settings | cseName = "CSE1_NAME" cseId = "/CSE1_ID" cseResourceId = "CSE1_RESOURCE_ID" spId = "//onem2m.org" supportedResourceType = {int1, int2, int3, int16} mcaPort, mcaPortIn, mccPort and mccPortIn settings which include per port the following info: Binding: - bindingProtocol - bindingDesc: - tsAddress - localPort - sutAddress - remotePort Serialization |
|  | PX_TS_CSE2 | CSE2 component settings | cseName = "CSE2_NAME" cseId = "/CSE2_ID" cseResourceId = "CSE2_RESOURCE_ID" spId = "//onem2m.org" supportedResourceType = {int1, int2, int3, int16} mcaPort, mcaPortIn, mccPort and mccPortIn settings which include per port the following info: Binding: - bindingProtocol - bindingDesc: - tsAddress - localPort - sutAddress - remotePort Serialization |
|  | PX_TS_DAS | DAS1 component settings | aeIdStem = "" appId = "" mcaPort and mcaPortIn settings which include per port the following info: Binding: - bindingProtocol - bindingDesc: - tsAddress - localPort - sutAddress - remotePort Serialization |
|  | PX_TS_UT | UpperTester settings | url = "http://127.0.0.1:43000/" |
| ExecutionParameters | PX_RESOURCES_TO_BE_DELETED | (For debugging purposes) | {"MyAe", "MyAccessControlPolicyResource", "SubscriptionVerificationAcp", "MyAcp", "MyRemoteCSEResource"} |
|  | PX_RUN_POSTAMBLE | (For debugging purposes) | true |
|  | PX_CERTIFICATE_PATH | charstring | “” |
|  | PX_CERTIFICATE_NAME | charstring | “” |
|  | PX_PAIRWISEKEY_METHOD | PairwiseKeyMethod | e_establish |
|  | PX_KEY_PROVISION | Provisioned | e_preProvisioning |

----------------------- End of change 3 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?