| CHANGE REQUEST |
| --- |
| Meeting:* | TDE #45.2 30 June |
| Source:* | ETSI |
| Date:* | 2020-06-30 |
| Contact:* | Miguel Angel Reina Ortega, ETSI, MiguelAngel.ReinaOrtega@etsi.org |
| Reason for Change/s:* | New TPs for service charging and accounting release 4 |
| CR against: Release* | Rel-4 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018-V-4.0.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

New TPs for service accounting release 4.

----------------------- Start of change 1 -----------------------

#### 7.2.2.17	Service Charging and Accounting(CSA)

##### 7.2.2.17.1	Event Based Charging (EBC)

TP/oneM2M/CSE/SCA/EBC/001

| TP Id | TP/oneM2M/CSE/SCA/EBC/001 |
| --- | --- |
| Test objective | Check that the IUT successfully generates the statistics collection record and send to target AE once the IUT receives an event collection trigger from AE when the eventType event is TIMERBASED in the stat collection configuration |
| Reference | TS-0001 [1], clause 10.2.11, clause 9.6.24, TS004 [2], clause 7.4.24 |
| Config Id | CF01 |
| Parent Release | Release 1 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered an AE and the IUT having a statsConfig resource containing a child eventConfig resource containing eventType attribute set to TIMERBASED and the AE having privileges to perform Create operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send statictic collection record } | IUT ( AE |
|  | then { the IUT sends a valid Notification Request containing Content (?) containing Statistic collection representation } | AE ( IUT |

TP/oneM2M/CSE/SCA/EBC/002

| TP Id | TP/oneM2M/CSE/SCA/EBC/002 |
| --- | --- |
| Test objective | Check that the IUT successfully generates the statistics collection record and send to target AE once the IUT receives an event collection trigger from AE when the eventType attribute is TIMERBASED in the stat collection configuration |
| Reference | TS-0001 [1], clause 10.2.11, clause 9.6.24, TS004 [2], clause 7.4.24 |
| Config Id | CF01 |
| Parent Release | Release 1 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered an AE and the IUT having a statsConfig resource containing a child eventConfig resource containing eventType attribute set to TIMERBASED and the AE having privileges to perform Update operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send statictic collection record } | IUT ( AE |
|  | then { the IUT sends a valid Notification Request containing Content (?) containing statistic collection representation } | AE ( IUT |

TP/oneM2M/CSE/SCA/EBC/003

| TP Id | TP/oneM2M/CSE/SCA/EBC/003 |
| --- | --- |
| Test objective | Check that the IUT successfully generates the statistics collection record and send to target AE once the IUT receives an event collection trigger from AE when the eventType attribute is STORAGEBASED in the stat collection configuration |
| Reference | TS-0001 [1], clause 10.2.11, clause 9.6.24, TS004 [2], clause 7.4.24 |
| Config Id | CF01 |
| Parent Release | Release 1 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered an AE and the IUT having a statsConfig resource containing a child eventConfig resource containing eventType attribute set to STORAGEBASED and the AE having privileges to perform Create operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send statistic collection record } | IUT ( AE |
|  | then { the IUT sends a valid Notification Request containing Content (?) containing statistic collection resource representation } | AE ( IUT |

TP/oneM2M/CSE/SCA/EBC/004

| TP Id | TP/oneM2M/CSE/SCA/EBC/004 |
| --- | --- |
| Test objective | Check that the IUT successfully generates the statistics collection record and send to target AE once the IUT receives an event collection trigger from AE when the eventType attribute is DataOperation in the stat collection configuration |
| Reference | TS-0001 [1], clause 10.2.11, clause 9.6.24, TS004 [2], clause 7.4.24 |
| Config Id | CF01 |
| Parent Release | Release 1 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered an AE and the IUT having a statsConfig resource containing a child eventConfig resource containing eventType attribute set to DataOperation and the AE having privileges to perform Create operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send statistic collection record } | IUT ( AE |
|  | then { the IUT sends a valid Notification Request containing Content (?) containing statistic collection resource representation } | AE ( IUT |

## ---------------------- End of change 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

Service Charging content value is not specified

Service Charging content value is not specified

Service Charging content value is not specified

Service Charging content value is not specified