| CHANGE REQUEST |
| --- |
| Meeting:* | TDE #46 |
| Source:* | TF-oneM2M |
| Date:* | 2020-07-13 |
| Contact:* | Miguel Angel Reina Ortega, ETSI, MiguelAngel.ReinaOrtega@etsi.org |
| Reason for Change/s:* | New TPs for discovery based operations release 4 |
| CR against: Release* | Rel-4 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018-V-4.1.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

New TPs for discovery-based operations release 4.

R01 Some corrections implemented while presenting the contribution

----------------------- Start of change 1 -----------------------

##### 7.2.2.6.2	BASIC OPERATION

##### TP/oneM2M/CSE/DIS/012

| TP Id | TP/oneM2M/CSE/DIS/012 |
| --- | --- |
| Test objective | Check that the IUT successfully performs a Discovery-based OPERATION |
| Reference | TS-0001 [1], clause 8.1.3 and clause 10.2.6.4, TS-0004 [2], clause 7.3.3.14 |
| Parent Release | Release 1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource TARGET_RESOURCE_ADDRESS containing a child resource at CONTAINER_RESOURCE_ADDRESS_1 and a child resource at CONTAINER_RESOURCE_ADDRESS_2 and the AE having privileges to perform DISCOVERY and OPERATION on children resources } |
| Expected behaviour | Test events | Expected behaviour |
|  | when { the IUT receives a valid Discovery-based OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Filter Criteria containing filterUsage set to 4 (Discovery-based Operation) } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000(OK) and Content containing aggregatedResponse containing Response for CONTAINER_RESOURCE_ADDRESS_1, Response for CONTAINER_RESOURCE_ADDRESS_2 } | IUT ( AE |

| TP Id | OPERATION |
| --- | --- |
| TP/oneM2M/CSE/DIS/012_CRE | CREATE |
| TP/oneM2M/CSE/DIS/012_UPD | UPDATE |
| TP/oneM2M/CSE/DIS/012_DEL | DELETE |

TP/oneM2M/CSE/DIS/013

| TP Id | TP/oneM2M/CSE/DIS/013 |
| --- | --- |
| Test objective | Check that the IUT successfully performs a Discovery-based OPERATION when the filter criteria is provided in the request |
| Reference | TS-0001 [1], clause 8.1.3 and clause 10.2.6.4, TS-0004 [2], clause 7.3.3.14 |
| Parent Release | Release 1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource TARGET_RESOURCE_ADDRESS containing a child resource at CONTAINER_RESOURCE_ADDRESS_1 and a child resource at CONTAINER_RESOURCE_ADDRESS_2 and the AE having privileges to perform DISCOVERY and OPERATION on children resources and FILTER_CRITERIA_CONDITIONS matching child resource at CONTAINER_RESOURCE_ADDRESS_1 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid Discovery-based OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Filter Criteria set to FILTER_CRITERIA_CONDITIONS containing filterUsage set to 4 (Discovery-based Operation) } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000(OK) and Content containing aggregatedResponse containing Response for CONTAINER_RESOURCE_ADDRESS_1 } | IUT ( AE |

| TP Id | OPERATION |
| --- | --- |
| TP/oneM2M/CSE/DIS/013_CRE | CREATE |
| TP/oneM2M/CSE/DIS/013_UPD | UPDATE |
| TP/oneM2M/CSE/DIS/013_DEL | DELETE |

TP/oneM2M/CSE/DIS/014

| TP Id | TP/oneM2M/CSE/DIS/014 |
| --- | --- |
| Test objective | Check that the IUT returns the empty content when no result matching with filter criteria is discovered in a Discovery-based OPERATION |
| Reference | TS-0001 [1], clause 8.1.3 and clause 10.2.6.4, TS-0004 [2], clause 7.3.3.14 |
| Parent Release | Release 1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource TARGET_RESOURCE_ADDRESS containing a child resource and the AE having privileges to perform DISCOVERY and OPERATION on child resource and FILTER_CRITERIA_CONDITIONS not matching child resource } |
| Expected behaviour | Test events | Expected behaviour |
|  | when { the IUT receives a valid Discovery-based OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Filter Criteria set to FILTER_CRITERIA_CONDITIONS containing filterUsage set to 4 (Discovery-based Operation) } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Content containing aggregatedResponse containing empty list } | IUT ( AE |

| TP Id | OPERATION |
| --- | --- |
| TP/oneM2M/CSE/DIS/014_CRE | CREATE |
| TP/oneM2M/CSE/DIS/014_UPD | UPDATE |
| TP/oneM2M/CSE/DIS/014_DEL | DELETE |

TP/oneM2M/CSE/DIS/015

| TP Id | TP/oneM2M/CSE/DIS/015 |
| --- | --- |
| Test objective | Check that the IUT successfully performs a Discovery-based OPERATION using Non-hierarchical addressing form when the Result Content and Desired Identifier Result Type is provided in the request |
| Reference | TS-0001 [1], clause 8.1.3 and clause 10.2.6.4, TS-0004 [2], clause 7.3.3.14 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a container resource TARGET_RESOURCE_ADDRESS containing a child resource and the AE having privileges to perform DISCOVERY and OPERATION on child resource } |
| Expected behaviour | Test events | Expected behaviour |
|  | when { the IUT receives a valid Discovery-based OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Result Content set to 11 (discovery result resource references) and Desired Identifier Result Type set to 2 (unstructured) and Filter Criteria containing filterUsage set to 4 (Discovery-based Operation) } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000(OK) and Content containing URIList containing unstructured addresses of discovered resources } | IUT ( AE |

| TP Id | OPERATION |
| --- | --- |
| TP/oneM2M/CSE/DIS/015_CRE | CREATE |
| TP/oneM2M/CSE/DIS/015_UPD | UPDATE |
| TP/oneM2M/CSE/DIS/015_DEL | DELETE |

TP/oneM2M/CSE/DIS/016

| TP Id | TP/oneM2M/CSE/DIS/016 |
| --- | --- |
| Test objective | Check that the IUT accepts a Discovery-based OPERATION request to the resource TARGET_RESOURCE_ADDRESS when AE has no privilege to perform the discovery operation |
| Reference | TS-0001 [1], clause 8.1.3 and clause 10.2.6.4, TS-0004 [2], clause 7.3.3.14 |
| Parent Release | Release 1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE containing child resources and the AE having no privileges to perform DISCOVERY and OPERATION on children resources } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid Discovery-based OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Filter Criteria containing filterUsage set to 4 (Discovery-based Operation) } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Content containing aggregatedResponse containing empty list } | IUT ( AE |

| TP Id | OPERATION |
| --- | --- |
| TP/oneM2M/CSE/DIS/016_CRE | CREATE |
| TP/oneM2M/CSE/DIS/016_UPD | UPDATE |
| TP/oneM2M/CSE/DIS/016_DEL | DELETE |

TP/oneM2M/CSE/DIS/017

| TP Id | TP/oneM2M/CSE/DIS/017 |
| --- | --- |
| Test objective | Check that the IUT accepts a Discovery-based OPERATION request to the resource TARGET_RESOURCE_ADDRESS when AE has privilege to perform the discovery operation but AE has no privilege to perform the OPERATION request |
| Reference | TS-0001 [1], clause 8.1.3 and clause 10.2.6.4, TS-0004 [2], clause 7.3.3.14 |
| Parent Release | Release 1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource TARGET_RESOURCE_ADDRESS containing a child resource at CONTAINER_RESOURCE_ADDRESS_1 and a child resource at CONTAINER_RESOURCE_ADDRESS_2 and the AE having privileges to perform DISCOVERY on children resources and the AE having no privileges to perform OPERATION on children resources } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid Discovery-based OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Filter Criteria containing filterUsage set to 4 (Discovery-based Operation) } | IUT ( AE |
|  | then { the IUT does not perform OPERATION and the IUT sends a valid Response containing Response Status Code set to 2000 (OK) aggregatedResponse containing Response for CONTAINER_RESOURCE_ADDRESS_1 containing Response Status Code set to 4103(ACCESS_DENIED) Response for CONTAINER_RESOURCE_ADDRESS_2 containing Response Status Code set to 4103(ACCESS_DENIED) } | IUT ( AE |

| TP Id | OPERATION |
| --- | --- |
| TP/oneM2M/CSE/DIS/017_CRE | CREATE |
| TP/oneM2M/CSE/DIS/017_UPD | UPDATE |
| TP/oneM2M/CSE/DIS/017_DEL | DELETE |

TP/oneM2M/CSE/DIS/018

| TP Id | TP/oneM2M/CSE/DIS/018 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the AE sends Discovery-based OPERATION requests to the resource TARGET_RESOURCE_ADDRESS which does not exist in the Hosting CSE |
| Reference | TS-0001 [1], clause 8.1.3 and clause 10.2.6.4, TS-0004 [2], clause 7.3.3.14 |
| Config Id | CF01 |
| Parent Release | Release 1 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having not yet created a resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Expected behaviour |
|  | when { the IUT receives a valid Discovery-based OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Filter Criteria containing filterUsage set to 4(Discovery-based Operation) } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4004 (NOT_FOUND) } | IUT ( AE |

| TP Id | OPERATION |
| --- | --- |
| TP/oneM2M/CSE/DIS/018_CRE | CREATE |
| TP/oneM2M/CSE/DIS/018_UPD | UPDATE |
| TP/oneM2M/CSE/DIS/018_DEL | DELETE |

TP/oneM2M/CSE/DIS/019

| TP Id | TP/oneM2M/CSE/DIS/019 |
| --- | --- |
| Test objective | Check that the IUT responds to the originator with an error when the originator sends a Discovery-based OPERATION request including an invalid format of filter criteria to discover the resource TARGET_RESOURCE_ADDRESS |
| Reference | TS-0001 [1], clause 8.1.3 and clause 10.2.6.4, TS-0004 [2], clause 7.3.3.14 |
| Parent Release | Release 1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the originator AE and the IUT having a container resource TARGET_RESOURCE_ADDRESS containing a child resource and the AE having privileges to perform DISCOVERY and OPERATION on child resource } |
| Expected behaviour | Test events | Expected behaviour |
|  | when { the IUT receives a valid Discovery-based OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Filter Criteria set to FILTER_CRITERIA_CONDITIONS not being valid format } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT ( AE |

| TP Id | OPERATION |
| --- | --- |
| TP/oneM2M/CSE/DIS/019_CRE | CREATE |
| TP/oneM2M/CSE/DIS/019_UPD | UPDATE |
| TP/oneM2M/CSE/DIS/019_DEL | DELETE |

TP/oneM2M/CSE/DIS/020

| TP Id | TP/oneM2M/CSE/DIS/020 |
| --- | --- |
| Test objective | Check that the IUT responds to the originator with a success response when the originator sends a Discovery-based OPERATION including two conflicted filter criteria of different type FILTER_CRITERIA_CONDITION_1 and FILTER_CRITERIA_CONDITION_2 (E.G. createBefore < createdAfter) |
| Reference | TS-0001 [1], clause 8.1.3 and clause 10.2.6.4, TS-0004 [2], clause 7.3.3.14 and clause 7.3.3.17 |
| Parent Release | Release 1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the originator AE and the IUT having a container resource TARGET_RESOURCE_ADDRESS containing a child resource and the AE having privileges to perform DISCOVERY and OPERATION on child resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid Discovery-based OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Filter Criteria containing filterUsage set to 4 (Discovery-based Operation) and having conflict conditions } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Content containing aggregatedResponse containing empty list } | IUT ( AE |

| TP Id | FILTER_CRITERIA _CONDITION_1 | FILTER_CRITERIA _CONDITION_2 | OPERATION |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DIS/020_CRB/CRA/CRE | createdBefore | createdAfter | CREATE |
| TP/oneM2M/CSE/DIS/020_MS/US/CRE | unmodifiedSince | modifiedSince | CREATE |
| TP/oneM2M/CSE/DIS/020_STS/STB/CRE | stateTagSmaller | stateTagBigger | CREATE |
| TP/oneM2M/CSE/DIS/020_EXB/EXA/CRE | expireBefore | expireAfter | CREATE |
| TP/oneM2M/CSE/DIS/020_CRB/CRA/UPD | createdBefore | createdAfter | UPDATE |
| TP/oneM2M/CSE/DIS/020_MS/US/UPD | unmodifiedSince | modifiedSince | UPDATE |
| TP/oneM2M/CSE/DIS/020_STS/STB/UPD | stateTagSmaller | stateTagBigger | UPDATE |
| TP/oneM2M/CSE/DIS/020_EXB/EXA/UPD | expireBefore | expireAfter | UPDATE |
| TP/oneM2M/CSE/DIS/020_CRB/CRA/DEL | createdBefore | createdAfter | DELETE |
| TP/oneM2M/CSE/DIS/020_MS/US/DEL | unmodifiedSince | modifiedSince | DELETE |
| TP/oneM2M/CSE/DIS/020_STS/STB/DEL | stateTagSmaller | stateTagBigger | DELETE |
| TP/oneM2M/CSE/DIS/020_EXB/EXA/DEL | expireBefore | expireAfter | DELETE |

TP/oneM2M/CSE/DIS/021

| TP Id | TP/oneM2M/CSE/DIS/021 |
| --- | --- |
| Test objective | Check that the IUT returns the empty content when resources match the filter criteria but they do not include Discovery-based OPERATION permission. |
| Reference | TS-0001 [1], clause 9.6.2.3 and clause 10.2.6.4, TS-0004 [2], clause 7.3.3.14 |
| Parent Release | Release 1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource TARGET_RESOURCE_ADDRESS containing a child resource and the AE not having privileges to perform DISCOVERY on child resource and the AE having privileges to perform OPERATION on child resource and FILTER_CRITERIA_CONDITIONS matching the child resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid Discovery-based OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Filter Criteria set to FILTER_CRITERIA_CONDITIONS containing filterUsage set to 4 (Discovery-based Operation) } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Content containing aggregatedResponse containing empty list } | IUT ( AE |

| TP Id | OPERATION |
| --- | --- |
| TP/oneM2M/CSE/DIS/021_CRE | CREATE |
| TP/oneM2M/CSE/DIS/021_UPD | UPDATE |
| TP/oneM2M/CSE/DIS/021_DEL | DELETE |

TP/oneM2M/CSE/DIS/022

| TP Id | TP/oneM2M/CSE/DIS/022 |
| --- | --- |
| Test objective | Check that the IUT successfully performs a Discovery-based OPERATION using hierarchical addressing form when the Result Content and Desired Identifier Result Type is provided in the request |
| Reference | TS-0001 [1], clause 8.1.3 and clause 10.2.6.4, TS-0004 [2], clause 7.3.3.14 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a container resource TARGET_RESOURCE_ADDRESS containing a child resource and the AE having privileges to perform DISCOVERY and OPERATION on child resource } |
| Expected behaviour | Test events | Expected behaviour |
|  | when { the IUT receives a valid Discovery-based OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Result Content set to 11 (discovery result resource references) and Desired Identifier Result Type set to 1 (structured) and Filter Criteria containing filterUsage set to 4 (Discovery-based Operation) } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000(OK) and Content containing URIList containing structured addresses of discovered resources } | IUT ( AE |

| TP Id | OPERATION |
| --- | --- |
| TP/oneM2M/CSE/DIS/022_CRE | CREATE |
| TP/oneM2M/CSE/DIS/022_UPD | UPDATE |
| TP/oneM2M/CSE/DIS/022_DEL | DELETE |

TP/oneM2M/CSE/DIS/023

| TP Id | TP/oneM2M/CSE/DIS/023 |
| --- | --- |
| Test objective | Check that the IUT successfully performs a Discovery-based OPERATION using hierarchical addressing form when the Desired Identifier Result Type is not provided in the request |
| Reference | TS-0001 [1], clause 8.1.3 and clause 10.2.6, TS-0004 [2], clause 7.2.3.13 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a container resource TARGET_RESOURCE_ADDRESS containing a child resource and the AE having privileges to perform DISCOVERY and OPERATION on child resource } |
| Expected behaviour | Test events | Expected behaviour |
|  | when { the IUT receives a valid Discovery-based OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Result Content set to 11 (discovery result resource references) and no Desired Identifier Result Type parameter and Filter Criteria containing filterUsage set to 4 (Discovery-based Operation) } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000(OK) and Content containing URIList containing structured addresses of discovered resources } | IUT ( AE |

| TP Id | OPERATION |
| --- | --- |
| TP/oneM2M/CSE/DIS/023_CRE | CREATE |
| TP/oneM2M/CSE/DIS/023_UPD | UPDATE |
| TP/oneM2M/CSE/DIS/023_DEL | DELETE |

TP/oneM2M/CSE/DIS/024

| TP Id | TP/oneM2M/CSE/DIS/024 |
| --- | --- |
| Test objective | Check that the IUT responds to the originator with an error when resources match the filter criteria in a Discovery-based OPERATION request but including an invalid Content |
| Reference | TS-0001 [1], clause 8.1.3 and clause 10.2.6.4, TS-0004 [2], clause 7.3.3.14 |
| Parent Release | Release 1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a container resource TARGET_RESOURCE_ADDRESS containing a child resource and the AE having privileges to perform DISCOVERY and OPERATION on child resource and FILTER_CRITERIA_CONDITIONS matching the child resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid Discovery-based OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content not being valid and Filter Criteria set to FILTER_CRITERIA_CONDITIONS containing filterUsage set to 4 (Discovery-based Operation) } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) aggregatedResponse containing Response for child resource containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT ( AE |

| TP Id | OPERATION |
| --- | --- |
| TP/oneM2M/CSE/DIS/024_CRE | CREATE |
| TP/oneM2M/CSE/DIS/024_UPD | UPDATE |

TP/oneM2M/CSE/DIS/025

| TP Id | TP/oneM2M/CSE/DIS/025 |
| --- | --- |
| Test objective | Check that the IUT successfully performs a Discovery-based OPERATION when resources match the filter criteria containing geoQuery condition provided in the request |
| Reference | TS-0001 [1], clause 8.1.3 and clause 10.2.6.4, TS-0004 [2], clause 7.3.3.14 |
| Parent Release | Release 1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource TARGET_RESOURCE_ADDRESS containing a child resource at CONTAINER_RESOURCE_ADDRESS_1 containing location attribute not set to LOCATION and a child resource at CONTAINER_RESOURCE_ADDRESS_2 containing location attribute set to LOCATION and the AE having privileges to perform DISCOVERY and OPERATION on child resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid Discovery-based OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Filter Criteria containing geoQuery set to LOCATION and filterUsage set to 4 (Discovery-based Operation) } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000(OK) and Content containing aggregatedResponse containing Response for CONTAINER_RESOURCE_ADDRESS_2 } | IUT ( AE |

| TP Id | OPERATION |
| --- | --- |
| TP/oneM2M/CSE/DIS/025_CRE | CREATE |
| TP/oneM2M/CSE/DIS/025_UPD | UPDATE |
| TP/oneM2M/CSE/DIS/025_DEL | DELETE |

TP/oneM2M/CSE/DIS/026

| TP Id | TP/oneM2M/CSE/DIS/026 |
| --- | --- |
| Test objective | Check that the IUT returns the empty content when no result matching with filter criteria containing geoQuery condition provided in a Discovery-based OPERATION |
| Reference | TS-0001 [1], clause 8.1.3 and clause 10.2.6.4, TS-0004 [2], clause 7.3.3.14 |
| Parent Release | Release 1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource TARGET_RESOURCE_ADDRESS containing a child resource containing location attribute set to LOCATION and the AE having privileges to perform DISCOVERY and OPERATION on child resource and FILTER_CRITERIA_CONDITIONS not matching child resource location attribute } |
| Expected behaviour | Test events | Expected behaviour |
|  | when { the IUT receives a valid Discovery-based OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Filter Criteria set to FILTER_CRITERIA_CONDITIONS containing geoQuery not matching LOCATION and filterUsage set to 4 (Discovery-based Operation) } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Content containing aggregatedResponse containing empty list } | IUT ( AE |

| TP Id | OPERATION |
| --- | --- |
| TP/oneM2M/CSE/DIS/026_CRE | CREATE |
| TP/oneM2M/CSE/DIS/026_UPD | UPDATE |
| TP/oneM2M/CSE/DIS/026_DEL | DELETE |

TP/oneM2M/CSE/DIS/027

| TP Id | TP/oneM2M/CSE/DIS/027 |
| --- | --- |
| Test objective | Check that the IUT responds to the originator with an error when the originator sends a Discovery-based OPERATION request including an invalid format of filter criteria containing geoQuery condition to discover the resource TARGET_RESOURCE_ADDRESS |
| Reference | TS-0001 [1], clause 8.1.3 and clause 10.2.6.4, TS-0004 [2], clause 7.3.3.14 |
| Parent Release | Release 1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the originator AE and the IUT having a container resource TARGET_RESOURCE_ADDRESS containing a child resource containing location attribute set to LOCATION and the AE having privileges to perform DISCOVERY and OPERATION on child resource } |
| Expected behaviour | Test events | Expected behaviour |
|  | when { the IUT receives a valid Discovery-based OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Filter Criteria containing geoQuery not being valid format filterUsage set to 4 (Discovery-based Operation) } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT ( AE |

| TP Id | OPERATION |
| --- | --- |
| TP/oneM2M/CSE/DIS/027_CRE | CREATE |
| TP/oneM2M/CSE/DIS/027_UPD | UPDATE |
| TP/oneM2M/CSE/DIS/027_DEL | DELETE |

TP/oneM2M/CSE/DIS/028

| TP Id | TP/oneM2M/CSE/DIS/028 |
| --- | --- |
| Test objective | Check that the IUT returns the empty content when the originator sends a Discovery-based OPERATION request including filter criteria containing geQuery condition but resources do not have location attribute |
| Reference | TS-0001 [1], clause 8.1.3 and clause 10.2.6.4, TS-0004 [2], clause 7.3.3.14 |
| Parent Release | Release 1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource TARGET_RESOURCE_ADDRESS containing a child resource containing no location attribute and the AE having privileges to perform DISCOVERY and OPERATION on child resource } |
| Expected behaviour | Test events | Expected behaviour |
|  | when { the IUT receives a valid Discovery-based OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Filter Criteria containing geoQuery set to LOCATION and filterUsage set to 4 (Discovery-based Operation) } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Content containing aggregatedResponse containing empty list } | IUT ( AE |

| TP Id | OPERATION |
| --- | --- |
| TP/oneM2M/CSE/DIS/028_CRE | CREATE |
| TP/oneM2M/CSE/DIS/028_UPD | UPDATE |
| TP/oneM2M/CSE/DIS/028_DEL | DELETE |

## ---------------------- End of change 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

discoveryBasedOperation value is not specified in TS-0004, section 6.3.4.2.31.

Specified by SDS-2020-0213R01

discoveryBasedOperation value is not specified in TS-0004, section 6.3.4.2.31.

Specified by SDS-2020-0213R01

discoveryBasedOperation value is not specified in TS-0004, section 6.3.4.2.31.

Specified by SDS-2020-0213

discovery-result-references value is not specified in TS-0004, section 6.3.4.2.7

Specified by SDS-2020-0213R01

discoveryBasedOperation value is not specified in TS-0004, section 6.3.4.2.31. Should value 1 be used?

Specified by SDS-2020-0213R01

discoveryBasedOperation value is not specified in TS-0004, section 6.3.4.2.31.

Specified by SDS-2020-0213R01

discoveryBasedOperation value is not specified in TS-0004, section 6.3.4.2.31.

Specified by SDS-2020-0213R01

discoveryBasedOperation value is not specified in TS-0004, section 6.3.4.2.31.

Specified by SDS-2020-0213R01

discoveryBasedOperation value is not specified in TS-0004, section 6.3.4.2.31.

Specified by SDS-2020-0213R01

discoveryBasedOperation value is not specified in TS-0004, section 6.3.4.2.31.

Specified by SDS-2020-0213R01

discovery-result-references value is not specified in TS-0004, section 6.3.4.2.7

Specified by SDS-2020-0213R01

discoveryBasedOperation value is not specified in TS-0004, section 6.3.4.2.31. Should value 1 be used?

Specified by SDS-2020-0213R01

discovery-result-references value is not specified in TS-0004, section 6.3.4.2.7

Specified by SDS-2020-0213R01

discoveryBasedOperation value is not specified in TS-0004, section 6.3.4.2.31. Should value 1 be used?

Specified by SDS-2020-0213R01

discoveryBasedOperation value is not specified in TS-0004, section 6.3.4.2.31. Should value 1 be used?

Specified by SDS-2020-0213R01

discoveryBasedOperation value is not specified in TS-0004, section 6.3.4.2.31. Should value 1 be used?

Specified by SDS-2020-0213R01

discoveryBasedOperation value is not specified in TS-0004, section 6.3.4.2.31. Should value 1 be used?

Specified by SDS-2020-0213R01

discoveryBasedOperation value is not specified in TS-0004, section 6.3.4.2.31. Should value 1 be used?

Specified by SDS-2020-0213R01

discoveryBasedOperation value is not specified in TS-0004, section 6.3.4.2.31. Should value 1 be used?

Specified by SDS-2020-0213R01