| CHANGE REQUEST |
| --- |
| Meeting:* | TDE #48 |
| Source:* | TF-oneM2M |
| Date:* | 2020-12-10 |
| Contact:* | Miguel Angel Reina Ortega, ETSI, MiguelAngel.ReinaOrtega@etsi.org |
| Reason for Change/s:* | New TPs for 3GPP interworking release 4 |
| CR against: Release* | Rel-4 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018-V-4.1.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

New TPs for 3GPP interworking release 4.

R02 – Correction to the TPs and addition of 2 TPs according to the discussion during the presentation of R01

----------------------- Start of change 1 -----------------------

TP/oneM2M/CSE/3GPP/TRIG/006

| TP Id | TP/oneM2M/CSE/3GPP/TRIG/006 |
| --- | --- |
| Test objective | Check that the IUT sends an explicit Device Trigger Replace Request when it receives a valid Device Trigger Replace Request from an AE |
| Reference | TS-0001 [1], clause 8.3.3.2.2, 9.6.49, TS-0026 [5], clause 7.5.2 |
| Parent Release | Release 4 |
| Config Id | CF05 |
| PICS Selection | PICS_CSE, PICS_3GPP |
| Initial conditions | with { the IUT being in the "initial state" and the IUT allowing to register an AE2 and the AE2 being hosted on a 3GPP UE and the IUT allowing to register an AE1 and AE1 having created a TRIGGER_REQUEST and the IUT having a <triggerRequest> resource at TARGET_RESOURCE_ADDRESS and the IUT having sent a POST 3GPP Device Trigger Request containing triggerReference and the IUT having not received a Response for Device Trigger Request } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE request from AE1 containing To set to TARGET_RESOURCE_ADDRESS and From set to AE1_ID } | IUT ( AE1 |
|  | then { the IUT assigns a new triggerReference for the new trigger message and the IUT sends a HTTP PUT 3GPP Request to the SCEF targeting the correct transactionID containing 3GPP Device Trigger Request message containing a valid 3GPP Device Replace Request with updated triggerReference } | IUT ( SCEF |

TP/oneM2M/CSE/3GPP/TRIG/007

| TP Id | TP/oneM2M/CSE/3GPP/TRIG/007 |
| --- | --- |
| Test objective | Check that the IUT sends an explicit Device Trigger Recall Request when it receives a valid Device Trigger Recall Request from an AE |
| Reference | TS-0001 [1], clause 8.3.3.2, 9.6.49, TS-0026 [5], clause 7.5.2 |
| Parent Release | Release 4 |
| Config Id | CF05 |
| PICS Selection | PICS_CSE, PICS_3GPP |
| Initial conditions | with { the IUT being in the "initial state" and the IUT allowing to register an AE2 and the AE2 being hosted on a 3GPP UE and the IUT allowing to register an AE1 and AE1 having created a TRIGGER_REQUEST and the IUT having a <triggerRequest> resource at TARGET_RESOURCE_ADDRESS and the IUT having sent a POST 3GPP Device Trigger Request and the IUT having not received a Response for Device Trigger Request } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid DELETE request from AE1 containing To set to TARGET_RESOURCE_ADDRESS and From set to AE1_ID } | IUT ( AE1 |
|  | then { the IUT sends a HTTP DELETE 3GPP Request to the SCEF targeting the correct transactionID with NULL payload } | IUT ( SCEF |

TP/oneM2M/CSE/3GPP/TRIG/008

| TP Id | TP/oneM2M/CSE/3GPP/TRIG/008 |
| --- | --- |
| Test objective | Check that the IUT sends an implicit (initiated by IN-CSE) Device Trigger Replace Request when it determines there is a need for a Replace based on internal policies |
| Reference | TS-0001 [1], clause 8.3.3.2.2, 9.6.49, TS-0026 [5], clause 7.5.2 |
| Parent Release | Release 4 |
| Config Id | CF05 |
| PICS Selection | PICS_CSE, PICS_3GPP |
| Initial conditions | with { the IUT being in the "initial state" and IUT having created a TRIGGER_REQUEST for TARGET_RESOURCE and TARGET_RESOURCE (AE/MN-CSE/ADN-AE) being hosted on a 3GPP UE and the IUT having a <triggerRequest> resource and the IUT having sent a POST 3GPP Device Trigger Request for TARGET_RESOURCE containing triggerReference and the IUT having not received a Response for Device Trigger Request } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT generates a UPDATE <triggerRequest> message after determining a need for a Trigger Request Replace based on internal policies } | IUT |
|  | then { the IUT assigns a new triggerReference for the new trigger message and the IUT sends a HTTP PUT 3GPP Request to the SCEF targeting the correct transactionID containing 3GPP Device Trigger Request message containing a valid 3GPP Device Replace Request with updated triggerReference } | IUT ( SCEF |

TP/oneM2M/CSE/3GPP/TRIG/009

| TP Id | TP/oneM2M/CSE/3GPP/TRIG/009 |
| --- | --- |
| Test objective | Check that the IUT sends an implicit (initiated by IN-CSE) Device Trigger Recall Request when it determines there is a need for a Recall based on internal policies |
| Reference | TS-0001 [1], clause 8.3.3.2, 9.6.49, TS-0026 [5], clause 7.5.2 |
| Parent Release | Release 4 |
| Config Id | CF05 |
| PICS Selection | PICS_CSE, PICS_3GPP |
| Initial conditions | with { the IUT being in the "initial state" and IUT having created a TRIGGER_REQUEST for TARGET_RESOURCE and TARGET_RESOURCE (AE/MN-CSE/ADN-AE) being hosted on a 3GPP UE and the IUT having a <triggerRequest> resource and the IUT having sent a POST 3GPP Device Trigger Request for TARGET_RESOURCE containing triggerReference and the IUT having not received a Response for Device Trigger Request } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT generates a DELETE <triggerRequest> message after determining a need for a Trigger Request Recall based on internal policies } | IUT |
|  | then { the IUT sends a HTTP DELETE 3GPP Request to the SCEF targeting the correct transactionID with NULL payload } | IUT ( SCEF |

TP/oneM2M/CSE/3GPP/TRIG/010

| TP Id | TP/oneM2M/CSE/3GPP/TRIG/010 |
| --- | --- |
| Test objective | Check that the IUT sets the triggerStatus attribute of the <triggerRequest> to ERROR_NSE_NOT_FOUND when the SCEF does not respond to the Device Trigger Recall/Replace Request prior to the timeout period |
| Reference | TS-0026 [5], clause 7.5.2, step 3 |
| Parent Release | Release 4 |
| Config Id | CFG05 |
| PICS Selection | PICS_CSE, PICS_3GPP |
| Initial conditions | with { the IUT being in the "initial state" and IUT having created a TRIGGER_REQUEST for TARGET_RESOURCE and TARGET_RESOURCE (AE/MN-CSE/ADN-AE) being hosted on a 3GPP UE and the IUT having a <triggerRequest> resource and the IUT having sent a 3GPP Device Trigger Replace/Recall Request } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT does not receive a response from SCEF for the 3GPP Device Trigger Replace/Recall Request } | IUT |
|  | then { the IUT updates <triggerRequest> resource containing triggerStatus attribute set to ERROR_NSE_NOT_FOUND } | IUT |

TP/oneM2M/CSE/3GPP/TRIG/011

| TP Id | TP/oneM2M/CSE/3GPP/TRIG/011 |
| --- | --- |
| Test objective | Check that the IUT sets the triggerStatus attribute of the <triggerRequest> to the proper value and generates an appropriate response to AE when the SCEF responds to the Device Trigger Replace Request |
| Reference | TS-0026 [5], clause 7.5.2, 8.3.1, TS-0004 [2] clause 6.6.3, 7.4.57.2.3 |
| Parent Release | Release 4 |
| Config Id | CFG05 |
| PICS Selection | PICS_CSE, PICS_3GPP |
| Initial conditions | with { the IUT being in the "initial state" and the IUT allowing to register an AE2 and the AE2 being hosted on a 3GPP UE and the IUT allowing to register an AE1 and AE1 having initiated a TRIGGER_REQUEST and the IUT having a <triggerRequest> resource and the IUT having sent a PUT 3GPP Device Trigger Replace Request } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid Device Triggering response from SCEF containing SCEF_RESULT_RESPONSE_CODE } | IUT ( SCEF |
|  | then { the IUT sets triggerStatus attribute of a <triggerRequest> resource to TRIGGER_RESULT and the IUT sends a valid response to AE1 containing Response Status Code set to TRIGGER_RESPONSE_CODE } | IUT ( AE1 |

| TP Id | SCEF_RESULT_RESPONSE_CODE | TRIGGER_RESULT | TRIGGER_RESPONSE_CODE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/3GPP/TRIG/011_1 | 200 OK (deliveryResult set to REPLACED) | TRIGGER-REPLACED | 2004 (UPDATED) |
| TP/oneM2M/CSE/3GPP/TRIG/011_2 | 400 Bad Request | TRIGGER-FAILED | 5219 (UNABLE_TO_REPLACE_REQUEST) |
| TP/oneM2M/CSE/3GPP/TRIG/011_3 | 401 Unauthorized | TRIGGER-FAILED | 5219 (UNABLE_TO_REPLACE_REQUEST) |
| TP/oneM2M/CSE/3GPP/TRIG/011_4 | 403 Forbidden | TRIGGER-FAILED | 5219 (UNABLE_TO_REPLACE_REQUEST) |
| TP/oneM2M/CSE/3GPP/TRIG/011_5 | 404 Not Found | TRIGGER-FAILED | 5219 (UNABLE_TO_REPLACE_REQUEST) |
| TP/oneM2M/CSE/3GPP/TRIG/011_6 | 411 Length Required | TRIGGER-FAILED | 5219 (UNABLE_TO_REPLACE_REQUEST) |
| TP/oneM2M/CSE/3GPP/TRIG/011_7 | 413 Payload Too Large | TRIGGER-FAILED | 5219 (UNABLE_TO_REPLACE_REQUEST) |
| TP/oneM2M/CSE/3GPP/TRIG/011_8 | 415 Unsupported Media Type | TRIGGER-FAILED | 5219 (UNABLE_TO_REPLACE_REQUEST) |
| TP/oneM2M/CSE/3GPP/TRIG/011_9 | 429 Too Many Requests | TRIGGER-FAILED | 5219 (UNABLE_TO_REPLACE_REQUEST) |
| TP/oneM2M/CSE/3GPP/TRIG/011_10 | 500 Internal Server Error | TRIGGER-FAILED | 5219 (UNABLE_TO_REPLACE_REQUEST) |
| TP/oneM2M/CSE/3GPP/TRIG/011_11 | 503 Service Unavailable | TRIGGER-FAILED | 5219 (UNABLE_TO_REPLACE_REQUEST) |

TP/oneM2M/CSE/3GPP/TRIG/012

| TP Id | TP/oneM2M/CSE/3GPP/TRIG/012 |
| --- | --- |
| Test objective | Check that the IUT deletes the <triggerRequest> resource and generates an appropriate response to AE when it receives a successful trigger recall response from SCEF |
| Reference | TS-0026 [5], clause 7.5.2, TS-0004 [2] clause 6.6.3, 7.4.57.2.4 |
| Parent Release | Release 4 |
| Config Id | CFG05 |
| PICS Selection | PICS_CSE, PICS_3GPP |
| Initial conditions | with { the IUT being in the "initial state" and the IUT allowing to register an AE2 and the AE2 being hosted on a 3GPP UE and the IUT allowing to register an AE1 and AE1 having created a TRIGGER_REQUEST and the IUT having a <triggerRequest> resource and the IUT having sent a POST 3GPP Device Trigger Request and the IUT having not received a Response for Device Trigger Request and the AE1 having sent a DELETE <triggerRequest> request to the IUT and the IUT having sent a DELETE 3GPP Device Trigger Recall Request } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid Device Triggering response from SCEF containing Response Status Code set to 204 (NO CONTENT) } | IUT ( SCEF |
|  | then { the IUT deletes the <triggerRequest> resource and the IUT sends a valid response to AE1 containing Response Status Code set to 2002 (DELETED) } | IUT ( AE1 |

TP/oneM2M/CSE/3GPP/TRIG/013

| TP Id | TP/oneM2M/CSE/3GPP/TRIG/013 |
| --- | --- |
| Test objective | Check that the IUT does not delete the <triggerRequest> resource and generates an appropriate response to AE when it receives an unsuccessful trigger recall response from SCEF |
| Reference | TS-0026 [5], clause 7.5.2, 8.3.1, TS-0004 [2] clause 6.6.3, 7.4.57.2.4 |
| Parent Release | Release 4 |
| Config Id | CFG05 |
| PICS Selection | PICS_CSE, PICS_3GPP |
| Initial conditions | with { the IUT being in the "initial state" and the IUT allowing to register an AE2 and the AE2 being hosted on a 3GPP UE and the IUT allowing to register an AE1 and AE1 having created a TRIGGER_REQUEST and the IUT having a <triggerRequest> resource and the IUT having sent a POST 3GPP Device Trigger Request and the IUT having not received a Response for Device Trigger Request and the AE1 having sent a DELETE <triggerRequest> request to the IUT and the IUT having sent a DELETE 3GPP Device Trigger Recall Request } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid Device Triggering response from SCEF containing Response Status Code set to SCEF_ERROR_CODE } | IUT ( SCEF |
|  | then { the IUT sends a valid response to AE1 containing Response Status Code set to TRIGGER_RESPONSE_CODE } | IUT ( AE1 |

| TP Id | SCEF_ERROR_CODE | TRIGGER_RESPONSE_CODE |
| --- | --- | --- |
| TP/oneM2M/CSE/3GPP/TRIG/013_1 | 400 Bad Request | 5220 (UNABLE_TO_RECALL_REQUEST) |
| TP/oneM2M/CSE/3GPP/TRIG/013_2 | 401 Unauthorized | 5220 (UNABLE_TO_RECALL_REQUEST) |
| TP/oneM2M/CSE/3GPP/TRIG/013_3 | 403 Forbidden | 5220 (UNABLE_TO_RECALL_REQUEST) |
| TP/oneM2M/CSE/3GPP/TRIG/013_4 | 404 Not Found | 5220 (UNABLE_TO_RECALL_REQUEST) |
| TP/oneM2M/CSE/3GPP/TRIG/013_5 | 411 Length Required | 5220 (UNABLE_TO_RECALL_REQUEST) |
| TP/oneM2M/CSE/3GPP/TRIG/013_6 | 413 Payload Too Large | 5220 (UNABLE_TO_RECALL_REQUEST) |
| TP/oneM2M/CSE/3GPP/TRIG/013_7 | 415 Unsupported Media Type | 5220 (UNABLE_TO_RECALL_REQUEST) |
| TP/oneM2M/CSE/3GPP/TRIG/013_8 | 429 Too Many Requests | 5220 (UNABLE_TO_RECALL_REQUEST) |
| TP/oneM2M/CSE/3GPP/TRIG/013_9 | 500 Internal Server Error | 5220 (UNABLE_TO_RECALL_REQUEST) |
| TP/oneM2M/CSE/3GPP/TRIG/013_10 | 503 Service Unavailable | 5220 (UNABLE_TO_RECALL_REQUEST) |

TP/oneM2M/CSE/3GPP/TRIG/014

| TP Id | TP/oneM2M/CSE/3GPP/TRIG/014 |
| --- | --- |
| Test objective | Check that the IUT does not accept the request for Trigger Replace and Recall operation if the original Device Trigger request has already been processed and responds with an error |
| Reference | TS-001 [1], clause 9.6.49, TS-0026 [5], clause 7.5.2, 8.3.1, TS-0004 [2], clause 6.6.3.6, 7.4.57.2 |
| Parent Release | Release 4 |
| Config Id | CFG05 |
| PICS Selection | PICS_CSE, PICS_3GPP |
| Initial conditions | with { the IUT being in the "initial state" and the IUT allowing to register an AE2 and the AE2 being hosted on a 3GPP UE and the IUT allowing to register an AE1 and AE1 having created a TRIGGER_REQUEST and the IUT having a <triggerRequest> resource at TARGET_RESOURCE_ADDRESS containing triggerStatus not set to PROCESSING and the IUT having sent a POST 3GPP Device Trigger Request and the IUT having received a Response for Device Trigger Request and the IUT having processed the Device Trigger Request } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION request from AE1 containing To set to TARGET_RESOURCE_ADDRESS and From set to AE1_ID } | IUT ( AE1 |
|  | then { the IUT sends a valid response to AE1 containing Response Status Code set to ERROR_RESPONSE_CODE } | IUT ( AE1 |

| TP Id | OPERATION | ERROR_RESPONSE_CODE |
| --- | --- | --- |
| TP/oneM2M/CSE/3GPP/TRIG/014_1 | UPDATE | 5219 (UNABLE_TO_REPLACE_REQUEST) |
| TP/oneM2M/CSE/3GPP/TRIG/014_2 | DELETE | 5220 (UNABLE_TO_RECALL_REQUEST) |

## ---------------------- End of change 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

Need a subscription

Need more clarity on this comment regarding 'subscription'. According to TS docs and existing TPs for 3GPP interworking, the <triggerRequest> resources have been created in a similar fashion by AEs.

Trigger Recall or Replace request should be entertained by the IN-CSE only if the triggerStatus attribute of <triggerRequest> resource is set to PROCESSING according to TS-0004 clause 7.4.57.2