| CHANGE REQUEST |
| --- |
| Meeting:* | TDE #49.2 |
| Source:* | TF-oneM2M |
| Date:* | 2021-03-18 |
| Contact:* | Siddharth Trikha, C-DOT, strikha@cdot.in |
| Reason for Change/s:* | Corrections in TPs for Semantics based operations release 4 |
| CR against: Release* | Rel-4 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018-V-4.2.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution introduces following corrections for Semantics CSF in the existing TS-0018 Test Purposes:

- Correction of status code from 5207 (NOT_ACCEPTABLE) to 4000 (BAD_REQUEST)

- Removal of resourceType in UPDATE request as it is NP for UPADTE Request

----------------------- Start of change 1 -----------------------

##### 7.2.2.15.2	UPDATE Operation

TP/oneM2M/CSE/SEM/UPD/001

| TP Id | TP/oneM2M/CSE/SEM/UPD/001 |
| --- | --- |
| Test objective | Check that the IUT rejects the update request of a <semanticDescriptor> resource indicating a " BAD_REQUEST " error when the request contains both semanticOpExec and descriptor attributes |
| Reference | TS-0004 [2], clause 7.4.34.2.3 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <semanticDescriptor> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform UPDATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing <semanticDescriptor> resource representation containing descriptor attribute set to a valid value semanticOpExec attribute set to a valid value } | IUT ( AE |
|  | then { the IUT does not update the <semanticDescriptor> resource and the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT ( AE |

TP/oneM2M/CSE/SEM/UPD/002

| TP Id | TP/oneM2M/CSE/SEM/UPD/002 |
| --- | --- |
| Test objective | Check that the IUT rejects the update request of a <semanticDescriptor> resource indicating a " BAD_REQUEST " error when the request contains a semanticOpExec attribute which does not contain a valid SPARQL query request |
| Reference | TS-0004 [2], clause 7.4.34.2.3 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <semanticDescriptor> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform UPDATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing <semanticDescriptor> resource representation containing no descriptor attribute and semanticOpExec attribute set to a non-valid SPARQL query request } | IUT ( AE |
|  | then { the IUT does not update the <semanticDescriptor> resource and the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT ( AE |

TP/oneM2M/CSE/SEM/UPD/003

| TP Id | TP/oneM2M/CSE/SEM/UPD/003 |
| --- | --- |
| Test objective | Check that the IUT rejects the update request of a <semanticDescriptor> resource when the request contains a descriptor attribute which does not conform to the RDF/XML syntax as defined in RDF 1.1 XML Syntax |
| Reference | TS-0004 [2], clause 7.4.34.2.3 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <semanticDescriptor> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform UPDATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing <semanticDescriptor> resource representation containing no semanticOpExec attribute and descriptor attribute set to a value that does not conform to the RDF/XML syntax } | IUT ( AE |
|  | then { the IUT does not update the <semanticDescriptor> resource and the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT ( AE |

TP/oneM2M/CSE/SEM/UPD/004

| TP Id | TP/oneM2M/CSE/SEM/UPD/004 |
| --- | --- |
| Test objective | Check that the IUT retrieves the referenced ontology from the ontology hosting CSE when performing a semantic validation as a result of an update of a stand-alone <semanticDescriptor> resource |
| Reference | TS-0034 [6], clauses 6.1.4 and 7.10.3, and TS-0004 [2], clause 7.4.34.2.3 |
| Parent Release | Release 3 |
| Config Id | CF02 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <semanticDescriptor> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform UPDATE operation at TARGET_RESOURCE_ADDRESS and the IUT having a local policy that allows semantic validation procedures and the ontology hosting CSE having an <ontology> resource at REFERENCED_ONTOLOGY_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing <semanticDescriptor> resource representation containing validationEnable attribute set to “True” and descriptor attribute and ontologyRef attribute set to REFERENCED_ONTOLOGY_ADDRESS } | IUT ( AE |
|  | then { the IUT sends a valid RETRIEVE Request containing To set to REFERENCED_ONTOLOGY_ADDRESS and Content containing <ontology> resource representation } | IUT ( CSE |

TP/oneM2M/CSE/SEM/UPD/008

| TP Id | TP/oneM2M/CSE/SEM/UPD/008 |
| --- | --- |
| Test objective | Check that the IUT rejects the update request of a <semanticMashupJobProfile> resource, indicating a " BAD_REQUEST " error, when its inputDescriptor attribute value does not conform to the RDF/XML syntax as defined in RDF 1.1 XML Syntax |
| Reference | TS-0034 [6], clause 6.3.4, and TS-0004 [2], clause 7.4.49.2.3 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <semanticMashupJobProfile> resource at TARGET_RESOURCE_ADDRESS containing accessControlPolicyIDs attribute set to allow the AE privileges to perform UPDATE operation } |
| Expected behaviour | Test events | Direction |
|  | When { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing <semanticMashupJobProfile> resource representation containing inputDescriptor attribute set to a value that does not conform to the RDF/XML syntax } | IUT ( AE |
|  | then { the IUT does not create the <semanticMashupJobProfile> resource andg the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT ( AE |

TP/oneM2M/CSE/SEM/UPD/009

| TP Id | TP/oneM2M/CSE/SEM/UPD/009 |
| --- | --- |
| Test objective | Check that the IUT rejects the update request of a <semanticMashupJobProfile> resource, indicating a " BAD_REQUEST " error, when its outputDescriptor attribute value does not conform to the RDF/XML syntax as defined in RDF 1.1 XML Syntax |
| Reference | TS-0034 [6], clause 6.3.4, and TS-0004 [2], clause 7.4.49.2.3 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a < semanticMashupJobProfile > resource at TARGET_RESOURCE_ADDRESS containing accessControlPolicyIDs attribute set to allow the AE privileges to perform UPDATE operation } |
| Expected behaviour | Test events | Direction |
|  | When { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing <semanticMashupJobProfile> resource representation containing outputDescriptor attribute set to a value that does not conform to the RDF/XML syntax } | IUT ( AE |
|  | then { the IUT does not create the <semanticMashupJobProfile> resource and the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT ( AE |

TP/oneM2M/CSE/SEM/UPD/010

| TP Id | TP/oneM2M/CSE/SEM/UPD/010 |
| --- | --- |
| Test objective | Check that the IUT rejects the update request of a <semanticMashupJobProfile> resource, indicating a " BAD_REQUEST " error, when its functionDescriptor attribute value does not conform to the RDF/XML syntax as defined in RDF 1.1 XML Syntax |
| Reference | TS-0034 [6], clause 6.3.4, and TS-0004 [2], clause 7.4.49.2.3 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <semanticMashupJobProfile> resource at TARGET_RESOURCE_ADDRESS containing accessControlPolicyIDs attribute set to allow the AE privileges to perform UPDATE operation } |
| Expected behaviour | Test events | Direction |
|  | When { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing <semanticMashupJobProfile> resource representation containing functionDescriptor attribute set to a value that does not conform to the RDF/XML syntax } | IUT ( AE |
|  | then { the IUT does not create the <semanticMashupJobProfile> resource and the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT ( AE |

TP/oneM2M/CSE/SEM/UPD/011

| TP Id | TP/oneM2M/CSE/SEM/UPD/011 |
| --- | --- |
| Test objective | Check that the IUT rejects the creation request of a <semanticMashupJobProfile> resource, indicating a " BAD_REQUEST " error, when its memberFilter attribute value does not conform to a valid SPARQL query request |
| Reference | TS-0034 [6], clause 6.3.4, and TS-0004 [2], clause 7.4.49.2.3 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a < semanticMashupJobProfile > resource at TARGET_RESOURCE_ADDRESS containing accessControlPolicyIDs attribute set to allow the AE privileges to perform UPDATE operation } |
| Expected behaviour | Test events | Direction |
|  | When { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing <semanticMashupJobProfile> resource representation containing memberFilter attribute set to a value that does not conform to a valid SPARQL query request } | IUT ( AE |
|  | then { the IUT does not create the <semanticMashupJobProfile> resource and the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT ( AE |

TP/oneM2M/CSE/SEM/UPD/012

| TP Id | TP/oneM2M/CSE/SEM/UPD/012 |
| --- | --- |
| Test objective | Check that the IUT creates a new sematicMashupResult when the parameter smjpInputParameter is updated |
| Reference | TS-0034 [6], clause 6.3.4, and TS-0004 [2], clause 7.4.49.2.3 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <semanticMashupInstance> resource at TARGET_RESOURCE_ADDRESS containing accessControlPolicyIDs attribute set to allow the AE privileges to perform UPDATE operation } |
| Expected behaviour | Test events | Direction |
|  | When { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing smjpInputParameter attribute set to a valid value } | IUT ( AE |
|  | then { the IUT creates a new <sematicMashupResult> resource and the IUT sends a valid Response containing Response Status Code set to 2004 (UPDATED) } | IUT ( AE |

TP/oneM2M/CSE/SEM/UPD/013

| TP Id | TP/oneM2M/CSE/SEM/UPD/013 |
| --- | --- |
| Test objective | Check that the IUT changes the mashupMember attribute of sematicMashupInstance when the parameter memberStoreType is updated |
| Reference | TS-0034 [6], clause 6.4.4, and TS-0004 [2], clause 7.4.50.2.3, TS-0001 [1], clause 9.6.54 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <semanticMashupInstance> resource at TARGET_RESOURCE_ADDRESS containing accessControlPolicyIDs attribute set to allow the AE privileges to perform UPDATE operation } |
| Expected behaviour | Test events | Direction |
|  | When { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing memberStoreType attribute set to a new valid value } | IUT ( AE |
|  | then { the IUT updates mashupMember attribute of resource and the IUT sends a valid Response containing Response Status Code set to 2004 (UPDATED) } | IUT ( AE |

##### 7.2.2.15.3	RETRIEVE Operation

TP/oneM2M/CSE/SEM/RET/001

| TP Id | TP/oneM2M/CSE/SEM/RET/001 |
| --- | --- |
| Test objective | Check that the IUT generates a Response Status Code indicating a “BAD_REQUEST” error to a retrieve request of a <semanticFanOutPoint> resource when the request contains a semanticsFilter condition set to a non-valid SPARQL query request |
| Reference | TS-0004 [2], clause 7.4.35.2.2 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <group> resource at TARGET_RESOURCE_ADDRESS containing semanticSupportIndicator attribute set to "True" and accessControlPolicyIDs attribute set to allow the AE privileges to perform RETRIEVE operation and <semanticFanOutPoint> virtual resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request from AE containing To set to TARGET_RESOURCE_ADDRESS/sfop and From set to AE-ID and Semantic Query Indicator set to "True" and Filter Criteria containing semanticsFilter condition set to a non-valid SPARQL query request } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT ( AE |

TP/oneM2M/CSE/SEM/RET/003

| TP Id | TP/oneM2M/CSE/SEM/RET/003 |
| --- | --- |
| Test objective | Check that the IUT generates a Response Status Code indicating a “BAD_REQUEST” error to a retrieve request of a <semanticFanOutPoint> resource when the request addresses a group resource with semanticSupportIndicator attribute set to “False” |
| Reference | TS-0004 [2], clause 7.4.35.2.2, and TS-0001 [1], clause 10.2.7.12 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <group> resource at TARGET_RESOURCE_ADDRESS containing semanticSupportIndicator attribute set to "False" and accessControlPolicyIDs attribute set to allow the AE privileges to perform RETRIEVE operation and <semanticFanOutPoint> virtual resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request from AE containing To set to TARGET_RESOURCE_ADDRESS/sfop and From set to AE-ID and Filter Criteria containing semanticsFilter condition set to a valid SPARQL query request } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT ( AE |

## ---------------------- End of change 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?