| CHANGE REQUEST |
| --- |
| Meeting ID:* | TDE 49.2 |
| Source:* | oneM2M-TF Neeta Meshram, C-DOT, neeta@cdot.in |
| Date:* | 2021-04-06 |
| Reason for Change/s:* | Transaction Management test purposes |
| CR against: Release* | Rel-4 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018 v4.2.0 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2019 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution introduces test case for Transaction Management resources as per TS-0004 and TS-0001 documents.

R02- Tables with no changes are represented by ….  These tables are intact in original TS-0018 document.

----------------------- Start of change 1 -----------------------

#### 7.2.2.3 Data Management and Repository Function (DMR)

##### 7.2.2.3.1	RETRIEVE Operation

TP/oneM2M/CSE/DMR/RET/001

…

| TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/001_CNT | Release 1 | TS-0001 [1], clause 10.2.4.2 | 3 (container) |
| TP/oneM2M/CSE/DMR/RET/001_ACP | Release 1 | TS-0001 [1], clause 10.2.21.2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/RET/001_SUB | Release 1 | TS-0001 [1], clause 10.2.11.3 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/RET/001_CIN | Release 1 | TS-0001 [1], clause 10.2.4.2 | 4 (contentInstance) |
| TP/oneM2M/CSE/DMR/RET/001_GRP | Release 1 | TS-0001 [1], clause 10.2.7.3 | 9 (group) |
| TP/oneM2M/CSE/DMR/RET/001_SCH | Release 3 | TS-0001 [1], clause 10.2.40.2 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/RET/001_PCH | Release 2 | TS-0001 [1], clause 10.2.13.3 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/RET/001_TS | Release 3 | TS-0001 [1], clause 10.2.30.2 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/RET/001_TRAM | Release 4 | TS-0001 [1], clause 10.2.18.3 | 50(transactionMgmt) |
| TP/oneM2M/CSE/DMR/RET/001_TRAC | Release 4 | TS-0001 [1], clause 10.2.18.7 | 51(transaction) |

...

TP/oneM2M/CSE/DMR/RET/003

…

| TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/003_CNT | Release 1 | TS-0001 [1], clause 10.2.4.2 | 3 (container) |
| TP/oneM2M/CSE/DMR/RET/003_ACP | Release 1 | TS-0001 [1], clause 10.2.21.2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/RET/003_SUB | Release 1 | TS-0001 [1], clause 10.2.11.3 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/RET/003_GRP | Release 1 | TS-0001 [1], clause 10.2.7.3 | 9 (group) |
| TP/oneM2M/CSE/DMR/RET/003_SCH | Release 3 | TS-0001 [1], clause 10.2.40.2 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/RET/003_TS | Release 3 | TS-0001 [1], clause 10.2.30.2 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/RET/003_TRAM | Release 4 | TS-0001 [1], clause 10.2.18.3 | 50(transactionMgmt) |
| TP/oneM2M/CSE/DMR/RET/003_TRAC | Release 4 | TS-0001 [1], clause 10.2.18.7 | 51(transaction) |

TP/oneM2M/CSE/DMR/RET/004

…

| TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/004_CNT | Release 1 | TS-0001 [1], clause 10.2.4.2 | 3 (container) |
| TP/oneM2M/CSE/DMR/RET/004_ACP | Release 1 | TS-0001 [1], clause 10.2.21.2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/RET/004_SUB | Release 1 | TS-0001 [1], clause 10.2.11.3 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/RET/004_GRP | Release 1 | TS-0001 [1], clause 10.2.7.3 | 9 (group) |
| TP/oneM2M/CSE/DMR/RET/004_SCH | Release 3 | TS-0001 [1], clause 10.2.40.2 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/RET/004_PCH | Release 2 | TS-0001 [1], clause 10.2.13.3 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/RET/004_TS | Release 3 | TS-0001 [1], clause 10.2.30.2 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/RET/004_TRAM | Release 4 | TS-0001 [1], clause 10.2.18.3 | 50(transactionMgmt) |
| TP/oneM2M/CSE/DMR/RET/004_TRAC | Release 4 | TS-0001 [1], clause 10.2.18.7 | 51(transaction) |

TP/oneM2M/CSE/DMR/RET/005

…

| TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/005_CNT | Release 1 | TS-0001 [1], clause 10.2.4.2 | 3 (container) |
| TP/oneM2M/CSE/DMR/RET/005_ACP | Release 1 | TS-0001 [1], clause 10.2.21.2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/RET/005_SUB | Release 1 | TS-0001 [1], clause 10.2.11.3 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/RET/005_GRP | Release 1 | TS-0001 [1], clause 10.2.7.3 | 9 (group) |
| TP/oneM2M/CSE/DMR/RET/005_SCH | Release 3 | TS-0001 [1], clause 10.2.40.2 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/RET/005_PCH | Release 2 | TS-0001 [1], clause 10.2.13.3 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/RET/005_TS | Release 3 | TS-0001 [1], clause 10.2.30.2 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/RET/005_TRAM | Release 4 | TS-0001 [1], clause 10.2.18.3 | 50(transactionMgmt) |
| TP/oneM2M/CSE/DMR/RET/005_TRAC | Release 4 | TS-0001 [1], clause 10.2.18.7 | 51(transaction) |

TP/oneM2M/CSE/DMR/RET/006

…

| TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/006_CNT | Release 1 | TS-0001 [1], clause 10.2.4.2 | 3 (container) |
| TP/oneM2M/CSE/DMR/RET/006_ACP | Release 1 | TS-0001 [1], clause 10.2.21.2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/RET/006_SUB | Release 1 | TS-0001 [1], clause 10.2.11.3 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/RET/006_GRP | Release 1 | TS-0001 [1], clause 10.2.7.3 | 9 (group) |
| TP/oneM2M/CSE/DMR/RET/006_SCH | Release 3 | TS-0001 [1], clause 10.2.40.2 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/RET/006_PCH | Release 2 | TS-0001 [1], clause 10.2.13.3 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/RET/006_TS | Release 3 | TS-0001 [1], clause 10.2.30.2 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/RET/006_TRAM | Release 4 | TS-0001 [1], clause 10.2.18.3 | 50(transactionMgmt) |
| TP/oneM2M/CSE/DMR/RET/006_TRAC | Release 4 | TS-0001 [1], clause 10.2.18.7 | 51(transaction) |

TP/oneM2M/CSE/DMR/RET/007

| …TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE | ATTRIBUTE |
| --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/007_CNT/LBL | Release 1 | TS-0001 [1], clause 10.2.4.2 | 3 (container) | labels |
| TP/oneM2M/CSE/DMR/RET/007_ACP/LBL | Release 1 | TS-0001 [1], clause 10.2.21.2 | 1 (accessControlPolicy) | labels |
| TP/oneM2M/CSE/DMR/RET/007_SUB/LBL | Release 1 | TS-0001 [1], clause 10.2.11.3 | 23 (subscription) | labels |
| TP/oneM2M/CSE/DMR/RET/007_GRP/LBL | Release 1 | TS-0001 [1], clause 10.2.7.3 | 9 (group) | labels |
| TP/oneM2M/CSE/DMR/RET/007_SCH/LBL | Release 3 | TS-0001 [1], clause 10.2.40.2 | 18 (schedule) | labels |
| TP/oneM2M/CSE/DMR/RET/007_PCH/LBL | Release 2 | TS-0001 [1], clause 10.2.13.3 | 15 (pollingChannel) | labels |
| TP/oneM2M/CSE/DMR/RET/007_TS/LBL | Release 3 | TS-0001 [1], clause 10.2.30.2 | 29 (timeSeries) | labels |
| TP/oneM2M/CSE/DMR/RET/007_TRAM/LBL | Release 4 | TS-0001 [1], clause 10.2.18.3 | 50(transactionMgmt) | labels |
| TP/oneM2M/CSE/DMR/RET/007_TRAC/LBL | Release 4 | TS-0001 [1], clause 10.2.18.7 | 51(transaction) | labels |

Editor Note: A common ATTRIBUTE has been chosen for all types of resource. A note could replace ATTRIBUTE column.

TP/oneM2M/CSE/DMR/RET/008

| …TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE | ATTRIBUTE_1 | ATTRIBUTE_2 |
| --- | --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/008_CNT/LBL/AT | Release 1 | TS-0001 [1], clause 10.2.4.2 | 3 (container) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/008_SUB/LBL/AT | Release 1 | TS-0001 [1], clause 10.2.11.3 | 23 (subscription) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/008_ACP/LBL/AT | Release 1 | TS-0001 [1], clause 10.2.21.2 | 1 (accessControlPolicy) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/008_GRP/LBL/AT | Release 1 | TS-0001 [1], clause 10.2.7.3 | 9 (group) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/008_SCH/LBL/AT | Release 3 | TS-0001 [1], clause 10.2.40.2 | 18 (schedule) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/008_TS/LBL/AT | Release 3 | TS-0001 [1], clause 10.2.30.2 | 29 (timeSeries) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/001_TRAM/LBL/TEXT | Release 4 | TS-0001 [1], clause 10.2.18.3 | 50(transactionMgmt) | labels | transactionExecuteTime |
| TP/oneM2M/CSE/DMR/RET/001_TRAC/LBL/TEXT | Release 4 | TS-0001 [1], clause 10.2.18.7 | 51(transaction) | labels | transactionExecuteTime |

Editor Note: The references to the TS-0001 for the operations (CREATE, RETRIEVE) procedures of the resource type <schedule> have not been found. To check whether these procedures are missing or they have been added in newer versions (TS-0001 v1.12.0 as basis)

…

TP/oneM2M/CSE/DMR/RET/010

…

TP/oneM2M/CSE/DMR/RET/013

…

| TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/013_ACP | Release 1 | TS-0001 [1], clause 10.2.21.2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/RET/013_AE | Release 1 | TS-0001 [1], clause 10.2.1.2 | 2 (AE) |
| TP/oneM2M/CSE/DMR/RET/013_CNT | Release 1 | TS-0001 [1], clause 10.2.4.2 | 3 (container) |
| TP/oneM2M/CSE/DMR/RET/013_CSR | Release 1 | TS-0001 [1], clause 10.2.2.2 | 16 (remoteCSE) |
| TP/oneM2M/CSE/DMR/RET/013_SUB | Release 1 | TS-0001 [1], clause 10.2.11.3 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/RET/013_GRP | Release 1 | TS-0001 [1], clause 10.2.7.3 | 9 (group) |
| TP/oneM2M/CSE/DMR/RET/013_DLV | Release 4 | TS-0001 [1], clause 10.2.5.3 | 6 (delivery) |
| TP/oneM2M/CSE/DMR/RET/013_LCP | Release 3 | TS-0001 [1], clause 10.2.10.1.2 | 10 (locationPolicy) |
| TP/oneM2M/CSE/DMR/RET/013_MGC | Release 4 | TS-0001 [1], clause 10.2.8.3 | 12 (mgmtCmd) |
| TP/oneM2M/CSE/DMR/RET/013_NOD | Release 4 | TS-0001 [1], clause 10.2.14.2 | 14 (node) |
| TP/oneM2M/CSE/DMR/RET/013_REQ | Release 2 | TS-0001 [1], clause 10.2.20.2 | 17 (request) |
| TP/oneM2M/CSE/DMR/RET/013_SCH | Release 3 | TS-0001 [1], clause 10.2.40.2 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/RET/013_STCL | Release 4 | TS-0001 [1], clause 10.2.15.11 | 21 (statsCollect) |
| TP/oneM2M/CSE/DMR/RET/013_STCG | Release 4 | TS-0001 [1], clause 10.2.15.3 | 22 (statsConfig) |
| TP/oneM2M/CSE/DMR/RET/013_TS | Release 3 | TS-0001 [1], clause 10.2.30.2 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/RET/013_TRAM | Release 4 | TS-0001 [1], clause 10.2.18.3 | 50(transactionMgmt) |
| TP/oneM2M/CSE/DMR/RET/013_TRAC | Release 4 | TS-0001 [1], clause 10.2.18.7 | 51(transaction) |

TP/oneM2M/CSE/DMR/RET/014

…

| TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/014_ACP | Release 1 | TS-0001 [1], clause 10.2.21.2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/RET/014_AE | Release 1 | TS-0001 [1], clause 10.2.1.2 | 2 (AE) |
| TP/oneM2M/CSE/DMR/RET/014_CNT | Release 1 | TS-0001 [1], clause 10.2.4.2 | 3 (container) |
| TP/oneM2M/CSE/DMR/RET/014_CSR | Release 1 | TS-0001 [1], clause 10.2.2.2 | 16 (remoteCSE) |
| TP/oneM2M/CSE/DMR/RET/014_SUB | Release 1 | TS-0001 [1], clause 10.2.11.3 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/RET/014_GRP | Release 1 | TS-0001 [1], clause 10.2.7.3 | 9 (group) |
| TP/oneM2M/CSE/DMR/RET/014_DLV | Release 4 | TS-0001 [1], clause 10.2.5.3 | 6 (delivery) |
| TP/oneM2M/CSE/DMR/RET/014_LCP | Release 3 | TS-0001 [1], clause 10.2.10.1.2 | 10 (locationPolicy) |
| TP/oneM2M/CSE/DMR/RET/014_MGC | Release 4 | TS-0001 [1], clause 10.2.8.3 | 12 (mgmtCmd) |
| TP/oneM2M/CSE/DMR/RET/014_NOD | Release 4 | TS-0001 [1], clause 10.2.14.2 | 14 (node) |
| TP/oneM2M/CSE/DMR/RET/014_REQ | Release 2 | TS-0001 [1], clause 10.2.20.2 | 17 (request) |
| TP/oneM2M/CSE/DMR/RET/014_SCH | Release 3 | TS-0001 [1], clause 10.2.40.2 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/RET/014_STCL | Release 4 | TS-0001 [1], clause 10.2.15.11 | 21 (statsCollect) |
| TP/oneM2M/CSE/DMR/RET/014_STCG | Release 4 | TS-0001 [1], clause 10.2.15.3 | 22 (statsConfig) |
| TP/oneM2M/CSE/DMR/RET/014_TS | Release 3 | TS-0001 [1], clause 10.2.30.2 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/RET/014_TRAM | Release 4 | TS-0001 [1], clause 10.2.18.3 | 50(transactionMgmt) |
| TP/oneM2M/CSE/DMR/RET/014_TRAC | Release 4 | TS-0001 [1], clause 10.2.18.7 | 51(transaction) |

TP/oneM2M/CSE/DMR/RET/015

| …TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/015_ACP | Release 1 | TS-0001 [1], clause 10.2.21.2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/RET/015_AE | Release 1 | TS-0001 [1], clause 10.2.1.2 | 2 (AE) |
| TP/oneM2M/CSE/DMR/RET/015_CNT | Release 1 | TS-0001 [1], clause 10.2.4.2 | 3 (container) |
| TP/oneM2M/CSE/DMR/RET/015_CSR | Release 1 | TS-0001 [1], clause 10.2.2.2 | 16 (remoteCSE) |
| TP/oneM2M/CSE/DMR/RET/015_SUB | Release 1 | TS-0001 [1], clause 10.2.11.3 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/RET/015_GRP | Release 1 | TS-0001 [1], clause 10.2.7.3 | 9 (group) |
| TP/oneM2M/CSE/DMR/RET/015_DLV | Release 4 | TS-0001 [1], clause 10.2.5.3 | 6 (delivery) |
| TP/oneM2M/CSE/DMR/RET/015_LCP | Release 3 | TS-0001 [1], clause 10.2.10.1.2 | 10 (locationPolicy) |
| TP/oneM2M/CSE/DMR/RET/015_MGC | Release 4 | TS-0001 [1], clause 10.2.8.3 | 12 (mgmtCmd) |
| TP/oneM2M/CSE/DMR/RET/015_NOD | Release 4 | TS-0001 [1], clause 10.2.14.2 | 14 (node) |
| TP/oneM2M/CSE/DMR/RET/015_REQ | Release 2 | TS-0001 [1], clause 10.2.20.2 | 17 (request) |
| TP/oneM2M/CSE/DMR/RET/015_SCH | Release 3 | TS-0001 [1], clause 10.2.40.2 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/RET/015_STCL | Release 4 | TS-0001 [1], clause 10.2.15.11 | 21 (statsCollect) |
| TP/oneM2M/CSE/DMR/RET/015_STCG | Release 4 | TS-0001 [1], clause 10.2.15.3 | 22 (statsConfig) |
| TP/oneM2M/CSE/DMR/RET/015_TS | Release 3 | TS-0001 [1], clause 10.2.30.2 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/RET/015_TRAM | Release 4 | TS-0001 [1], clause 10.2.18.3 | 50(transactionMgmt) |
| TP/oneM2M/CSE/DMR/RET/015_TRAC | Release 4 | TS-0001 [1], clause 10.2.18.7 | 51(transaction) |

Editor’s Note: Update the reference of schedule resource to TS-0001 9.6.9

TP/oneM2M/CSE/DMR/RET/016

…

| TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/016_ACP | Release 1 | TS-0001 [1], clause 10.2.21.2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/RET/016_AE | Release 1 | TS-0001 [1], clause 10.2.1.2 | 2 (AE) |
| TP/oneM2M/CSE/DMR/RET/016_CNT | Release 1 | TS-0001 [1], clause 10.2.4.2 | 3 (container) |
| TP/oneM2M/CSE/DMR/RET/016_CSR | Release 1 | TS-0001 [1], clause 10.2.2.2 | 16 (remoteCSE) |
| TP/oneM2M/CSE/DMR/RET/016_SUB | Release 1 | TS-0001 [1], clause 10.2.11.3 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/RET/016_GRP | Release 1 | TS-0001 [1], clause 10.2.7.3 | 9 (group) |
| TP/oneM2M/CSE/DMR/RET/016_DLV | Release 4 | TS-0001 [1], clause 10.2.5.3 | 6 (delivery) |
| TP/oneM2M/CSE/DMR/RET/016_LCP | Release 3 | TS-0001 [1], clause 10.2.10.1.2 | 10 (locationPolicy) |
| TP/oneM2M/CSE/DMR/RET/016_MGC | Release 4 | TS-0001 [1], clause 10.2.8.3 | 12 (mgmtCmd) |
| TP/oneM2M/CSE/DMR/RET/016_NOD | Release 4 | TS-0001 [1], clause 10.2.14.2 | 14 (node) |
| TP/oneM2M/CSE/DMR/RET/016_REQ | Release 2 | TS-0001 [1], clause 10.2.20.2 | 17 (request) |
| TP/oneM2M/CSE/DMR/RET/016_SCH | Release 3 | TS-0001 [1], clause 10.2.40.2 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/RET/016_STCL | Release 4 | TS-0001 [1], clause 10.2.15.11 | 21 (statsCollect) |
| TP/oneM2M/CSE/DMR/RET/016_STCG | Release 4 | TS-0001 [1], clause 10.2.15.3 | 22 (statsConfig) |
| TP/oneM2M/CSE/DMR/RET/016_TS | Release 3 | TS-0001 [1], clause 10.2.30.2 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/RET/016_TRAM | Release 4 | TS-0001 [1], clause 10.2.18.3 | 50(transactionMgmt) |
| TP/oneM2M/CSE/DMR/RET/016_TRAC | Release 4 | TS-0001 [1], clause 10.2.18.7 | 51(transaction) |

TP/oneM2M/CSE/DMR/RET/017

…

| TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/017_ACP | Release 1 | TS-0001 [1], clause 10.2.21.2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/RET/017_AE | Release 1 | TS-0001 [1], clause 10.2.1.2 | 2 (AE) |
| TP/oneM2M/CSE/DMR/RET/017_CNT | Release 1 | TS-0001 [1], clause 10.2.4.2 | 3 (container) |
| TP/oneM2M/CSE/DMR/RET/017_CSR | Release 1 | TS-0001 [1], clause 10.2.2.2 | 16 (remoteCSE) |
| TP/oneM2M/CSE/DMR/RET/017_SUB | Release 1 | TS-0001 [1], clause 10.2.11.3 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/RET/017_GRP | Release 1 | TS-0001 [1], clause 10.2.7.3 | 9 (group) |
| TP/oneM2M/CSE/DMR/RET/017_DLV | Release 4 | TS-0001 [1], clause 10.2.5.3 | 6 (delivery) |
| TP/oneM2M/CSE/DMR/RET/017_LCP | Release 3 | TS-0001 [1], clause 10.2.10.1.2 | 10 (locationPolicy) |
| TP/oneM2M/CSE/DMR/RET/017_MGC | Release 4 | TS-0001 [1], clause 10.2.8.3 | 12 (mgmtCmd) |
| TP/oneM2M/CSE/DMR/RET/017_NOD | Release 4 | TS-0001 [1], clause 10.2.14.2 | 14 (node) |
| TP/oneM2M/CSE/DMR/RET/017_REQ | Release 2 | TS-0001 [1], clause 10.2.20.2 | 17 (request) |
| TP/oneM2M/CSE/DMR/RET/017_SCH | Release 3 | TS-0001 [1], clause 10.2.40.2 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/RET/017_STCL | Release 4 | TS-0001 [1], clause 10.2.15.11 | 21 (statsCollect) |
| TP/oneM2M/CSE/DMR/RET/017_STCG | Release 4 | TS-0001 [1], clause 10.2.15.3 | 22 (statsConfig) |
| TP/oneM2M/CSE/DMR/RET/017_TS | Release 3 | TS-0001 [1], clause 10.2.30.2 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/RET/017_TRAM | Release 4 | TS-0001 [1], clause 10.2.18.3 | 50(transactionMgmt) |
| TP/oneM2M/CSE/DMR/RET/017_TRAC | Release 4 | TS-0001 [1], clause 10.2.18.7 | 51(transaction) |

TP/oneM2M/CSE/DMR/RET/018

…

| TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE | ATTRIBUTE |
| --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/018_ACP/LBL | Release 1 | TS-0001 [1], clause 10.2.21.2 | 1 (accessControlPolicy) | labels |
| TP/oneM2M/CSE/DMR/RET/018_AE/LBL | Release 1 | TS-0001 [1], clause 10.2.1.2 | 2 (AE) | labels |
| TP/oneM2M/CSE/DMR/RET/018_CNT/LBL | Release 1 | TS-0001 [1], clause 10.2.4.2 | 3 (container) | labels |
| TP/oneM2M/CSE/DMR/RET/018_CSR/LBL | Release 1 | TS-0001 [1], clause 10.2.2.2 | 16 (remoteCSE) | labels |
| TP/oneM2M/CSE/DMR/RET/018_SUB/LBL | Release 1 | TS-0001 [1], clause 10.2.11.3 | 23 (subscription) | labels |
| TP/oneM2M/CSE/DMR/RET/018_GRP/LBL | Release 1 | TS-0001 [1], clause 10.2.7.3 | 9 (group) | labels |
| TP/oneM2M/CSE/DMR/RET/018_DLV/LBL | Release 4 | TS-0001 [1], clause 10.2.5.3 | 6 (delivery) | labels |
| TP/oneM2M/CSE/DMR/RET/018_LCP/LBL | Release 3 | TS-0001 [1], clause 10.2.10.1.2 | 10 (locationPolicy) | labels |
| TP/oneM2M/CSE/DMR/RET/018_MGC/LBL | Release 4 | TS-0001 [1], clause 10.2.8.3 | 12 (mgmtCmd) | labels |
| TP/oneM2M/CSE/DMR/RET/018_NOD/LBL | Release 4 | TS-0001 [1], clause 10.2.14.2 | 14 (node) | labels |
| TP/oneM2M/CSE/DMR/RET/018_REQ/LBL | Release 2 | TS-0001 [1], clause 10.2.20.2 | 17 (request) | labels |
| TP/oneM2M/CSE/DMR/RET/018_SCH/LBL | Release 3 | TS-0001 [1], clause 10.2.40.2 | 18 (schedule) | labels |
| TP/oneM2M/CSE/DMR/RET/018_STCL/LBL | Release 4 | TS-0001 [1], clause 10.2.15.11 | 21 (statsCollect) | labels |
| TP/oneM2M/CSE/DMR/RET/018_STCG/LBL | Release 4 | TS-0001 [1], clause 10.2.15.3 | 22 (statsConfig) | labels |
| TP/oneM2M/CSE/DMR/RET/018_TS | Release 3 | TS-0001 [1], clause 10.2.30.2 | 29 (timeSeries) | labels |
| TP/oneM2M/CSE/DMR/RET/018_TRAM | Release 4 | TS-0001 [1], clause 10.2.18.3 | 50(transactionMgmt) | labels |
| TP/oneM2M/CSE/DMR/RET/018_TRAC | Release 4 | TS-0001 [1], clause 10.2.18.7 | 51(transaction) | labels |

TP/oneM2M/CSE/DMR/RET/019

…

| TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE | ATTRIBUTE_1 | ATTRIBUTE_2 |
| --- | --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/019_ACP/LBL/AT | Release 1 | TS-0001 [1], clause 10.2.21.2 | 1 (accessControlPolicy) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/019_AE/LBL/AT | Release 1 | TS-0001 [1], clause 10.2.1.2 | 2 (AE) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/019_CNT/LBL/AT | Release 1 | TS-0001 [1], clause 10.2.4.2 | 3 (container) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/019_CSR/LBL/AT | Release 1 | TS-0001 [1], clause 10.2.2.2 | 16 (remoteCSE) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/019_SUB/LBL/AT | Release 1 | TS-0001 [1], clause 10.2.11.3 | 23 (subscription) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/019_GRP/LBL/AT | Release 1 | TS-0001 [1], clause 10.2.7.3 | 9 (group) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/019_DLV/LBL/AT | Release 4 | TS-0001 [1], clause 10.2.5.3 | 6 (delivery) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/019_LCP/LBL/AT | Release 3 | TS-0001 [1], clause 10.2.10.1.2 | 10 (locationPolicy) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/019_MGC/LBL/AT | Release 4 | TS-0001 [1], clause 10.2.8.3 | 12 (mgmtCmd) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/019_NOD/LBL/AT | Release 4 | TS-0001 [1], clause 10.2.14.2 | 14 (node) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/019_REQ/LBL/AT | Release 3 | TS-0001 [1], clause 10.2.20.2 | 17 (request) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/019_SCH/LBL/AT | Release 3 | TS-0001 [1], clause 10.2.40.2 | 18 (schedule) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/019_STCL/LBL/AT | Release 4 | TS-0001 [1], clause 10.2.15.11 | 21 (statsCollect) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/019_STCG/LBL/AT | Release 4 | TS-0001 [1], clause 10.2.15.3 | 22 (statsConfig) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/019_TS/LBL/AT | Release 3 | TS-0001 [1], clause 10.2.30.2 | 29 (timeSeries) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/019_TRAM/LBL/TEXT | Release 4 | TS-0001 [1], clause 10.2.18.3 | 50(transactionMgm) | labels | transactionExecuteTime |
| TP/oneM2M/CSE/DMR/RET/019_TRAC/LBL/TEXT | Release 4 | TS-0001 [1], clause 10.2.18.7 | 51(transaction) | labels | transactionExecuteTime |

…

TP/oneM2M/CSE/DMR/RET/021

…

| TP Id | PARENT_RELEASE | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/021_CNT | Release 2 | 3 (container) |
| TP/oneM2M/CSE/DMR/RET/021_GRP | Release 2 | 9 (group) |
| TP/oneM2M/CSE/DMR/RET/021_ACP | Release 2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/RET/021_SCH | Release 3 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/RET/021_PCH | Release 3 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/RET/021_SUB | Release 3 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/RET/021_TS | Release 3 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/RET/021_TRAM | Release 4 | 50 (TransactionMgmt) |
| TP/oneM2M/CSE/DMR/RET/021_TRAC | Release 4 | 51 (Transaction) |

TP/oneM2M/CSE/DMR/RET/022

…

| TP Id | PARENT_RELEASE | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/022_CNT | Release 3 | 3 (container) |
| TP/oneM2M/CSE/DMR/RET/022_GRP | Release 3 | 9 (group) |
| TP/oneM2M/CSE/DMR/RET/022_ACP | Release 3 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/RET/022_SCH | Release 3 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/RET/022_PCH | Release 3 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/RET/022_SUB | Release 3 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/RET/022_TS | Release 3 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/RET/022_TRAM | Release 4 | 50 (TransactionMgmt) |
| TP/oneM2M/CSE/DMR/RET/022_TRAC | Release 4 | 51 (Transaction) |

TP/oneM2M/CSE/DMR/RET/023

…

| TP Id | PARENT_RELEASE | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/023_CNT | Release 3 | 3 (container) |
| TP/oneM2M/CSE/DMR/RET/023_GRP | Release 3 | 9 (group) |
| TP/oneM2M/CSE/DMR/RET/023_ACP | Release 3 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/RET/023_SCH | Release 3 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/RET/023_PCH | Release 3 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/RET/023_SUB | Release 3 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/RET/023_TS | Release 3 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/RET/023_TRAM | Release 4 | 50 (TransactionMgmt) |
| TP/oneM2M/CSE/DMR/RET/023_TRAC | Release 4 | 51 (Transaction) |

TP/oneM2M/CSE/DMR/RET/024

…

| TP Id | PARENT_RELEASE | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/024_CNT | Release 3 | 3 (container) |
| TP/oneM2M/CSE/DMR/RET/024_GRP | Release 3 | 9 (group) |
| TP/oneM2M/CSE/DMR/RET/024_ACP | Release 3 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/RET/024_SCH | Release 3 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/RET/024_SUB | Release 3 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/RET/024_TS | Release 3 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/RET/024_PCH | Release 3 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/RET/024_TRAM | Release 4 | 50 (TransactionMgmt) |
| TP/oneM2M/CSE/DMR/RET/024_TRAC | Release 4 | 51 (Transaction) |

TP/oneM2M/CSE/DMR/RET/025

…

| TP Id | PARENT_RELEASE | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/025_CNT | Release 3 | 3 (container) |
| TP/oneM2M/CSE/DMR/RET/025_GRP | Release 3 | 9 (group) |
| TP/oneM2M/CSE/DMR/RET/025_ACP | Release 3 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/RET/025_SCH | Release 3 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/RET/025_SUB | Release 3 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/RET/025_TS | Release 3 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/RET/025_PCH | Release 3 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/RET/025_TRAM | Release 4 | 50 (TransactionMgmt) |
| TP/oneM2M/CSE/DMR/RET/025_TRAC | Release 4 | 51 (Transaction) |

…

##### 7.2.2.3.2	UPDATE Operation

TP/oneM2M/CSE/DMR/UPD/001

| …TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE | ATTRIBUTE_NAME |
| --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/001_CNT/LBL | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.4.3 | 3 (container) | labels |
| TP/oneM2M/CSE/DMR/UPD/001_ACP/LBL | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.21.3 | 1 (accessControlPolicy) | labels |
| TP/oneM2M/CSE/DMR/UPD/001_SUB/LBL | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.11.4 | 23 (subscription) | labels |
| TP/oneM2M/CSE/DMR/UPD/001_GRP/LBL | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.7.4 | 9 (group) | labels |
| TP/oneM2M/CSE/DMR/UPD/001_SCH/LBL | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.40.2 | 18 (schedule) | labels |
| TP/oneM2M/CSE/DMR/UPD/001_PCH/LBL | Release 2 | TS-0001 [Error: Reference source not found], clause 10.2.13.4 | 15 (pollingChannel) | labels |
| TP/oneM2M/CSE/DMR/UPD/001_TS/LBL | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.13.4 | 29 (timeSeries) | labels |
| TP/oneM2M/CSE/DMR/UPD/001_TRAM/LBL | Release 4 | TS-0001 [1], clause 10.2.18.4 | 50 (transactionMgmt) | labels |
| TP/oneM2M/CSE/DMR/UPD/001_TRAC/LBL | Release 4 | TS-0001 [1], clause 10.2.18.8 | 51 (transaction) | labels |

TP/oneM2M/CSE/DMR/UPD/002

…

| TP Id | PARENT_RELEASE | PICS Selection | Reference | RESOURCE_TYPE | ATTRIBUTE_NAME |
| --- | --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/002_CNT/LBL | Release 1 | PICS_CNT_LBL | TS-0001 [Error: Reference source not found], clause 10.2.4.3 | 3 (container) | labels |
| TP/oneM2M/CSE/DMR/UPD/002_ACP/LBL | Release 1 | PICS_ACP_LBL | TS-0001 [Error: Reference source not found], clause 10.2.21.3 | 1 (accessControlPolicy) | labels |
| TP/oneM2M/CSE/DMR/UPD/002_SUB/LBL | Release 1 | PICS_SUB_LBL | TS-0001 [Error: Reference source not found], clause 10.2.11.4 | 23 (subscription) | labels |
| TP/oneM2M/CSE/DMR/UPD/002_GRP/LBL | Release 1 | PICS_GRP_LBL | TS-0001 [Error: Reference source not found], clause 10.2.7.4 | 9 (group) | labels |
| TP/oneM2M/CSE/DMR/UPD/002_SCH/LBL | Release 3 |  | TS-0001 [Error: Reference source not found], clause 10.2.40.2 | 18 (schedule) | labels |
| TP/oneM2M/CSE/DMR/UPD/002_PCH/LBL | Release 2 |  | TS-0001 [Error: Reference source not found], clause 10.2.13.4 | 15 (pollingChannel) | Labels |
| TP/oneM2M/CSE/DMR/UPD/002_TS/LBL | Release 3 |  | TS-0001 [Error: Reference source not found], clause 10.2.30.3 | 29 (timeSeries) | Labels |
| TP/oneM2M/CSE/DMR/UPD/002_TRAM/LBL | Release 4 |  | TS-0001 [1], clause 10.2.18.4 | 50 (transactionMgmt) | labels |
| TP/oneM2M/CSE/DMR/UPD/002_TRAC/LBL | Release 4 |  | TS-0001 [1], clause 10.2.18.8 | 51 (transaction) | labels |

TP/oneM2M/CSE/DMR/UPD/003

…

| TP Id | PARENT_RELEASE | PICS Selection | Reference | RESOURCE_TYPE | ATTRIBUTE_NAME |
| --- | --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/003_CNT/LBL | Release 1 | PICS_CNT_LBL | TS-0001 [Error: Reference source not found], clause 10.2.4.3 | 3 (container) | Labels |
| TP/oneM2M/CSE/DMR/UPD/003_ACP/LBL | Release 1 | PICS_ACP_LBL | TS-0001 [Error: Reference source not found], clause 10.2.21.3 | 1 (accessControlPolicy) | labels |
| TP/oneM2M/CSE/DMR/UPD/003_SUB/LBL | Release 1 | PICS_SUB_LBL | TS-0001 [Error: Reference source not found], clause 10.2.11.4 | 23 (subscription) | labels |
| TP/oneM2M/CSE/DMR/UPD/003_GRP/LBL | Release 1 | PICS_GRP_LBL | TS-0001 [Error: Reference source not found], clause 10.2.7.4 | 9 (group) | labels |
| TP/oneM2M/CSE/DMR/UPD/003_SCH/LBL | Release 3 |  | TS-0001 [Error: Reference source not found], clause 10.2.40.2 | 18 (schedule) | labels |
| TP/oneM2M/CSE/DMR/UPD/003_PCH/LBL | Release 2 |  | TS-0001 [Error: Reference source not found], clause 10.2.13.4 | 15 (pollingChannel) | labels |
| TP/oneM2M/CSE/DMR/UPD/003_TS/LBL | Release 3 |  | TS-0001 [Error: Reference source not found], clause 10.2.30.3 | 29 (timeSeries) | labels |
| TP/oneM2M/CSE/DMR/UPD/003_TRAM/LBL | Release 4 |  | TS-0001 [1], clause 10.2.18.4 | 50 (transactionMgmt) | lables |
| TP/oneM2M/CSE/DMR/UPD/003_TRAC/LBL | Release 4 |  | TS-0001 [1], clause 10.2.18.8 | 51 (transaction) | lables |

TP/oneM2M/CSE/DMR/UPD/004

…

| TP Id | PARENT_RELEASE | PICS Selection | Reference | RESOURCE_TYPE | ATTRIBUTE_NAME_1 | ATTRIBUTE_NAME_2 | ATTRIBUTE_NAME_3 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/004_CNT/ET/MNI/LBL | Release 1 | PICS_CNT_MNI and PICS_CNT_LBL | TS-0001 [Error: Reference source not found], clause 10.2.4.3 | 3 (container) | expirationTime | maxNrOfInstances | labels |
| TP/oneM2M/CSE/DMR/UPD/004_ACP/PVS/PV/LBL | Release 1 | PICS_ACP_LBL | TS-0001 [Error: Reference source not found], clause 10.2.21.3 | 1 (accessControlPolicy) | selfPrivileges | privileges | labels |
| TP/oneM2M/CSE/DMR/UPD/004_ACP/PV/AT/LBL | Release 3 | PICS_ACP_AT and PICS_ACP_LBL | TS-0001 [Error: Reference source not found], clause 10.2.21.3 | 1 (accessControlPolicy) | privileges | announceTo | labels |
| TP/oneM2M/CSE/DMR/UPD/004_SUB/ET/LBL/EXC | Release 1 | PICS_SUB_LBL and PICS_SUB_EXC | TS-0001 [Error: Reference source not found], clause 10.2.11.4 | 23 (subscription) | expirationTime | labels | expirationCounter |
| TP/oneM2M/CSE/DMR/UPD/004_GRP/ET/GN/LBL | Release 1 | PICS_GRP_GN and PICS_GRP_LBL | TS-0001 [Error: Reference source not found], clause 10.2.7.4 | 9 (group) | expirationTime | groupName | labels |
| TP/oneM2M/CSE/DMR/UPD/004_SCH/SE/AT/LBL | Release 3 |  | TS-0001 [Error: Reference source not found], clause 10.2.40.2 | 18 (schedule) | scheduleElement | announceTo | labels |
| TP/oneM2M/CSE/DMR/UPD/004_TS/ET/MNI/LBL | Release 3 |  | TS-0001 [Error: Reference source not found], clause 10.2.13.4 | 15 (pollingChannel) | expirationTime | maxNrOfInstances | labels |

…

TP/oneM2M/CSE/DMR/UPD/006

| …TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE | ATTRIBUTE_NAME |
| --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/006_CNT/LBL | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.4.3 | 3 (container) | labels |
| TP/oneM2M/CSE/DMR/UPD/006_ACP/LBL | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.21.3 | 1 (accessControlPolicy) | labels |
| TP/oneM2M/CSE/DMR/UPD/006_SUB/LBL | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.11.4 | 23 (subscription) | labels |
| TP/oneM2M/CSE/DMR/UPD/006_GRP/LBL | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.7.4 | 9 (group) | labels |
| TP/oneM2M/CSE/DMR/UPD/006_SCH/LBL | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.40.2 | 18 (schedule) | labels |
| TP/oneM2M/CSE/DMR/UPD/005_TS/LBL | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.30.3 | 29 (timeSeries) | labels |
| TP/oneM2M/CSE/DMR/UPD/006_TRAM/LBL | Release 4 | TS-0001 [1], clause 10.2.18.4 | 50 (transactionMgmt) | labels |
| TP/oneM2M/CSE/DMR/UPD/006_TRAC/LBL | Release 4 | TS-0001 [1], clause 10.2.18.8 | 51 (transaction) | labels |

TP/oneM2M/CSE/DMR/UPD/007

…

| TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE | ATTRIBUTE_NAME |
| --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/007_CNT/CT | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.4.3 | 3 (container) | creationTime |
| TP/oneM2M/CSE/DMR/UPD/007_ACP/CT | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.21.3 | 1 (accessControlPolicy) | creationTime |
| TP/oneM2M/CSE/DMR/UPD/007_SUB/CT | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.11.4 | 23 (subscription) | creationTime |
| TP/oneM2M/CSE/DMR/UPD/007_GRP/CT | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.7.4 | 9 (group) | creationTime |
| TP/oneM2M/CSE/DMR/UPD/007_SCH/CT | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.40.2 | 18 (schedule) | creationTime |
| TP/oneM2M/CSE/DMR/UPD/007_PCH/CT | Release 2 | TS-0001 [Error: Reference source not found], clause 10.2.13.4 | 15 (pollingChannel) | creationTime |
| TP/oneM2M/CSE/DMR/UPD/007_TS/CT | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.30.3 | 29 (timeSeries) | creationTime |
| TP/oneM2M/CSE/DMR/UPD/007_TRAM/CT | Release 4 | TS-0001 [1], clause 10.2.18.4 | 50 (transactionMgmt) | creationTime |
| TP/oneM2M/CSE/DMR/UPD/007_TRAC/CT | Release 4 | TS-0001 [1], clause 10.2.18.8 | 51 (transaction) | creationTime |

4

…

TP/oneM2M/CSE/DMR/UPD/009

…

| TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE | ATTRIBUTE_NAME |
| --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/009_CNT/EXC | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.4.3 | 3 (container) | expirationCounter |
| TP/oneM2M/CSE/DMR/UPD/009_ACP/EXC | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.21.3 | 1 (accessControlPolicy) | expirationCounter |
| TP/oneM2M/CSE/DMR/UPD/009_SUB/MNI | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.11.4 | 23 (subscription) | maxNrOfInstances |
| TP/oneM2M/CSE/DMR/UPD/009_GRP/EXC | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.7.4 | 9 (group) | expirationCounter |
| TP/oneM2M/CSE/DMR/UPD/009_SCH/EXC | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.40.2 | 18 (schedule) | expirationCounter |
| TP/oneM2M/CSE/DMR/UPD/009_PCH/EXC | Release 2 | TS-0001 [Error: Reference source not found], clause 10.2.13.4 | 15 (pollingChannel) | expirationCounter |
| TP/oneM2M/CSE/DMR/UPD/009_TS/EXC | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.30.3 | 29 (timeSeries) | expirationCounter |
| TP/oneM2M/CSE/DMR/UPD/009_TRAM/EXT | Release 4 | TS-0001 [Error: Reference source not found], clause 10.2.18.4 | 50 (transactionMgmt) | expirationTime |
| TP/oneM2M/CSE/DMR/UPD/009_TRAC/EXT | Release 4 | TS-0001 [Error: Reference source not found], clause 10.2.18.8 | 51 (transaction) | expirationTime |

…

TP/oneM2M/CSE/DMR/UPD/020

…

| TP Id | PARENT_RELEASE | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/020_CNT | Release 2 | 3 (container) |
| TP/oneM2M/CSE/DMR/UPD/020_GRP | Release 2 | 9 (group) |
| TP/oneM2M/CSE/DMR/UPD/020_ACP | Release 2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/UPD/020_SCH | Release 3 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/UPD/020_PCH | Release 3 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/UPD/020_SUB | Release 3 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/UPD/020_TS | Release 3 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/UPD/020_TRAM | Release 4 | 50 (TransactionMgmt) |
| TP/oneM2M/CSE/DMR/UPD/020_TRAC | Release 4 | 51 (Transaction) |

TP/oneM2M/CSE/DMR/UPD/021

| …TP Id | PARENT_RELEASE | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/021_CNT | Release 2 | 3 (container) |
| TP/oneM2M/CSE/DMR/UPD/021_GRP | Release 2 | 9 (group) |
| TP/oneM2M/CSE/DMR/UPD/021_ACP | Release 2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/UPD/021_SCH | Release 3 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/UPD/021_PCH | Release 3 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/UPD/021_SUB | Release 3 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/UPD/021_TS | Release 3 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/UPD/021_TRAM | Release 4 | 50 (transactionMgmt) |
| TP/oneM2M/CSE/DMR/UPD/021_TRAC | Release 4 | 51 (transaction) |

TP/oneM2M/CSE/DMR/UPD/022

…

| TP Id | PARENT_RELEASE | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/UPD/022_CNT | Release 2 | 3 (container) |
| TP/oneM2M/CSE/DMR/UPD/022_GRP | Release 2 | 9 (group) |
| TP/oneM2M/CSE/DMR/UPD/022_ACP | Release 2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/UPD/022_SCH | Release 3 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/UPD/022_PCH | Release 3 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/UPD/022_SUB | Release 3 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/UPD/022_TS | Release 3 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/UPD/022_TRAM | Release 4 | 50 (transactionMgmt) |
| TP/oneM2M/CSE/DMR/UPD/022_TRAC | Release 4 | 51 (transaction) |

##### 7.2.2.3.3	CREATE Operation

TP/oneM2M/CSE/DMR/CRE/001

…

| TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE | PARENT_RESOURCE_TYPE |
| --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/CRE/001_CNT/CB | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.4.1 | 3 (container) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_CNT/AE | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.4.1 | 3 (container) | 2 (AE) |
| TP/oneM2M/CSE/DMR/CRE/001_CNT/CNT | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.4.1 | 3 (container) | 3 (container) |
| TP/oneM2M/CSE/DMR/CRE/001_ACP/CB | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.21.1 | 1 (accessControlPolicy) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_ACP/AE | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.21.1 | 1 (accessControlPolicy) | 2 (AE) |
| TP/oneM2M/CSE/DMR/CRE/001_SUB/CB | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.11.2 | 23 (subscription) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_SUB/AE | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.11.2 | 23 (subscription) | 2 (AE) |
| TP/oneM2M/CSE/DMR/CRE/001_SUB/CNT | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.11.2 | 23 (subscription) | 3 (container) |
| TP/oneM2M/CSE/DMR/CRE/001_SUB/ACP | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.11.2 | 23 (subscription) | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/CRE/001_SUB/CSR | Release 1 | TS-0001 [Error: Reference source not found], clause 9.6.4-1 | 23 (subscription) | 16 (remoteCSE) |
| TP/oneM2M/CSE/DMR/CRE/001_CIN/CNT | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.4.1 | 4 (contentInstance) | 3 (container) |
| TP/oneM2M/CSE/DMR/CRE/001_GRP/CB | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.7.2 | 9 (group) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_GRP/AE | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.7.2 | 9 (group) | 2 (AE) |
| TP/oneM2M/CSE/DMR/CRE/001_SUB/GRP | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.11.2 | 23 (subscription) | 9 (group) |
| TP/oneM2M/CSE/DMR/CRE/001_SCH/CB | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.40.2 | 18 (schedule) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_SCH/SUB | Release 2 | TS-0001 [Error: Reference source not found], clause 10.2.40.2 | 18 (schedule) | 23 (subscription) |
| TP/oneM2M/CSE/DMR/CRE/001_PCH/AE | Release 2 | TS-0001 [Error: Reference source not found], clause 10.2.13.2 | 15 (pollingChannel) | 2 (AE) |
| TP/oneM2M/CSE/DMR/CRE/001_SUB/SCH | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.11.2 | 23 (subscription) | 18 (schedule) |
| TP/oneM2M/CSE/DMR/CRE/001_NOD/CB | Release 4 | TS-0001 [Error: Reference source not found], clause 9.6.3-1 | 14 (node) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_MGC/CB | Release 4 | TS-0001 [Error: Reference source not found], clause 9.6.3-1 | 12 (mgmtCmd) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_LCP/CB | Release 3 | TS-0001 [Error: Reference source not found], clause 9.6.3-1 | 10 (locationPolicy) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_STCG/CB | Release 4 | TS-0001 [Error: Reference source not found], clause 9.6.3-1 | 22 (statsConfig) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_STCL/CB | Release 4 | TS-0001 [Error: Reference source not found], clause 9.6.3-1 | 21 (statsCollect) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_ASAR/CB | Release 3 | TS-0001 [Error: Reference source not found], clause 9.6.3-1 | 19(serviceSubscribedAppRule) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_SUB/AEA | Release 3 | TS-0001 [Error: Reference source not found], clause 9.6.5-1 | 23 (subscription) | 10002 (AEannc) |
| TP/oneM2M/CSE/DMR/CRE/001_CNT/AEA | Release 3 | TS-0001 [Error: Reference source not found], clause 9.6.5-1 | 3 (container) | 10002 (AEannc) |
| TP/oneM2M/CSE/DMR/CRE/001_GRP/AEA | Release 3 | TS-0001 [Error: Reference source not found], clause 9.6.5-1 | 9 (group) | 10002 (AEannc) |
| TP/oneM2M/CSE/DMR/CRE/001_ACP/AEA | Release 3 | TS-0001 [Error: Reference source not found], clause 9.6.5-1 | 1 (accessControlPolicy) | 10002 (AEannc) |
| TP/oneM2M/CSE/DMR/CRE/001_EVCF/STCG | Release 4 | TS-0001 [Error: Reference source not found], clause 9.6.23-1 | 7 (eventConfig) | 22 (statsConfig) |
| TP/oneM2M/CSE/DMR/CRE/001_SUB/STCG | Release 4 | TS-0001 [Error: Reference source not found], clause 9.6.23-1 | 23 (subscription) | 22 (statsConfig) |
| TP/oneM2M/CSE/DMR/CRE/001_TS/CB | Release 3 | TS-0001 [Error: Reference source not found], clause 9.6.36-1 | 29 (timeSeries) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_TS/AE | Release 3 | TS-0001 [Error: Reference source not found], clause 9.6.36-1 | 29 (timeSeries) | 2 (AE) |
| TP/oneM2M/CSE/DMR/CRE/001_TS/CSR | Release 3 | TS-0001 [Error: Reference source not found], clause 9.6.36-1 | 29 (timeSeries) | 16 (remoteCSE) |
| TP/oneM2M/CSE/DMR/CRE/001_TS/AEA | Release 3 | TS-0001 [Error: Reference source not found],clause 9.6.36-1 | 29 (timeSeries) | 10002 (AEAnnc) |
| TP/oneM2M/CSE/DMR/CRE/001_TSI/TS | Release 3 | TS-0001 [Error: Reference source not found], clause 9.6.37-1 | 30 (timeSeriesInstance) | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAM/CB | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 50 (transactionMgmt) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAM/AE | Release 4 | TS-0001 [], Table 9.6.1.1-1 | 50 (transactionMgmt) | 2 (AE) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAM/CSR | Release 4 | TS-0001 [], Table 9.6.1.1-1 | 50 (transactionMgmt) | 16 (RemoteCSE) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/ACP | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 1 (AccessControlPolicy) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/AE | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 2 (AE) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/CNT | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 3 (Container) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/CIN | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 4 (ContentInstance) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/CB | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 5 (CSEBase) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/GRP | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 9 (Group) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/LCP | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 10 (LocationPolicy) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/MSSP | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 11 (M2MServiceSubscriptionProfile) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/MGC | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 12 (MgmtCmd) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/MGO | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 13 (MgmtObj) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/MGO | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 13 (MgmtObj) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/NOD | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 14 (Node) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/CSR | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 16 (RemoteCSE) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/SCH | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 18 (Schedule) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/ASAR | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 19 (ServiceSubscribedAppRule) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/SVSN | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 20 (ServiceSubscribedNode) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/STCL | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 21 (StatsCollect) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/STCG | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 22 (StatsConfig) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/SUB | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 23 (Subscription) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/SMD | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 24 (SemanticDescriptor) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/NTPR | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 25 (NotificationTargetMgmtPolicyRef) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/NTP | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 26 (NotificationTargetPolicy) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/PDR | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 27 (PolicyDeletionRules) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/TS | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 29 (TimeSeries) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/TSI | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 30 (TimeSeriesInstance) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/ROL | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 31 (Role) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/TK | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 32 (Token) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/TS | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 29 (TimeSeries) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/ACPANNC | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 10001 (AccessContraolPolicyAnnc) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/AEANNC | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 10002 (AEAnnc) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/CNTANNC | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 10003 (ContainerAnnc) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/CINANNC | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 10001 (ContentInstanceAnnc) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/GRPANNC | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 10009 (GroupAnnc) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/LCPANNC | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 10010 (LocationPolicyAnnc) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/MGOANNC | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 10013 (MgmtObjAnnc) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/NODANNC | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 10014 (NodeAnnc) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/CSRANNC | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 10016 (RemoteCSEAnnc) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/SCHANNC | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 10018 (ScheduleAnnc) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/SMDANNC | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 10024 (AccessContraolPolicyAnnc) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/TSANNC | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 10029 (TimeSeriesAnnc) |
| TP/oneM2M/CSE/DMR/CRE/001_TRAC/TSIANNC | Release 4 | TS-0001 [1], Table 9.6.1.1-1 | 51 (transaction) | 10030 (TimeSeriesInstanceAnnc) |

TP/oneM2M/CSE/DMR/CRE/002

…

| TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/CRE/002_CNT | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.4.1 | 3 (container) |
| TP/oneM2M/CSE/DMR/CRE/002_ACP | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.21.1 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/CRE/002_SUB | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.11.2 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/CRE/002_GRP | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.7.2 | 9 (group) |
| TP/oneM2M/CSE/DMR/CRE/002_SCH | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.40.2 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/CRE/002_PCH | Release 2 | TS-0001 [Error: Reference source not found], clause 10.2.13.2 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/CRE/002_TS | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.30.1 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/CRE/002_FLXC | Release 2 | TS-0001 [Error: Reference source not found], clause 10.2.29.1 | 28 (flexContainer) |
| TP/oneM2M/CSE/DMR/CRE/002_TRAM | Release 4 | TS-0001 [1f], clause 10.1.2, Step-2 | 50 (transactionMgmt) |
| TP/oneM2M/CSE/DMR/CRE/002_TRAC | Release 4 | TS-0001 [1], clause 10.1.2, Step-2 | 51 (transaction) |

TP/oneM2M/CSE/DMR/CRE/003

| … TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/CRE/003_CNT | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.4.1 | 3 (container) |
| TP/oneM2M/CSE/DMR/CRE/003_ACP | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.21.1 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/CRE/003_SUB | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.11.2 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/CRE/003_GRP | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.7.2 | 9 (group) |
| TP/oneM2M/CSE/DMR/CRE/003_SCH | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.40.2 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/CRE/003_PCH | Release 2 | TS-0001 [Error: Reference source not found], clause 10.2.13.2 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/CRE/003_TS | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.30.1 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/CRE/003_TRAM | Release 4 | TS-0001 [1], clause 10.1.2, Step-2 | 50 (transactionMgmt) |
| TP/oneM2M/CSE/DMR/CRE/003_TRAC | Release 4 | TS-0001 [1], clause 10.2.30.1 | 51 (transaction) |

TP/oneM2M/CSE/DMR/CRE/004

…

| TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/CRE/004_CNT | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.4.1 | 3 (container) |
| TP/oneM2M/CSE/DMR/CRE/004_ACP | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.21.1 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/CRE/004_SUB | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.11.2 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/CRE/004_GRP | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.7.2 | 9 (group) |
| TP/oneM2M/CSE/DMR/CRE/004_SCH | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.40.2 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/CRE/004_PCH | Release 2 | TS-0001 [Error: Reference source not found], clause 10.2.13.2 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/CRE/004_TS | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.30.1 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/CRE/004_TRAM | Release 4 | TS-0001 [1], clause 10.1.2, Step-2 | 50 (transactionMgmt) |
| TP/oneM2M/CSE/DMR/CRE/004_TRAC | Release 4 | TS-0001 [1], clause 10.2.30.1 | 51 (transaction) |

…

TP/oneM2M/CSE/DMR/CRE/012

…

| TP Id | PARENT_RELEASE | PICS Selection | Reference | RESOURCE_TYPE | OPTIONAL_ATTRIBUTE |
| --- | --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/CRE/012_CNT/ACPI | Release 1 | PICS_CNT_ACPI | TS-0001 [Error: Reference source not found], clause 9.6.1.3.2-1 | 3 (container) | accessControlPolicyIDs |
| TP/oneM2M/CSE/DMR/CRE/012_CNT/ET | Release 1 | PICS_CNT_ET | TS-0001 [Error: Reference source not found], clause 9.6.1.3.1-1 | 3 (container) | expirationTime |
| TP/oneM2M/CSE/DMR/CRE/012_CNT/LBL | Release 1 | PICS_CNT_LBL | TS-0001 [Error: Reference source not found], clause 9.6.1.3.2-1 | 3 (container) | labels |
| TP/oneM2M/CSE/DMR/CRE/012_CNT/MNI | Release 1 | PICS_CNT_MNI | TS-0001 [Error: Reference source not found], clause 9.6.6-2 | 3 (container) | maxNrOfInstances |
| TP/oneM2M/CSE/DMR/CRE/012_CNT/MBS | Release 1 | PICS_CNT_MBS | TS-0001 [Error: Reference source not found], clause 9.6.6-2 | 3 (container) | maxByteSize |
| TP/oneM2M/CSE/DMR/CRE/012_CNT/MIA | Release 1 | PICS_CNT_MIA | TS-0001 [Error: Reference source not found], clause 9.6.6-2 | 3 (container) | maxInstanceAge |
| TP/oneM2M/CSE/DMR/CRE/012_CNT/OR | Release 1 | PICS_CNT_OR | TS-0001 [Error: Reference source not found], clause 9.6.6-2 | 3 (container) | ontologyRef |
| TP/oneM2M/CSE/DMR/CRE/012_CNT/CR | Release 1 | PICS_CNT_CR | TS-0001 [Error: Reference source not found], clause 9.6.6-2 | 3 (container) | creator |
| TP/oneM2M/CSE/DMR/CRE/012_CIN/ET | Release 1 | PICS_CIN_ET | TS-0001 [Error: Reference source not found], clause 9.6.1.3.1-1 | 4 (contentInstance) | expirationTime |
| TP/oneM2M/CSE/DMR/CRE/012_CIN/LBL | Release 1 | PICS_CIN_LBL | TS-0001 [Error: Reference source not found], clause 9.6.1.3.2-1 | 4 (contentInstance) | labels |
| TP/oneM2M/CSE/DMR/CRE/012_CIN/CR | Release 1 | PICS_CIN_CR | TS-0001 [Error: Reference source not found], clause 9.6.7-2 | 4 (contentInstance) | creator |
| TP/oneM2M/CSE/DMR/CRE/012_CIN/CNF | Release 1 | PICS_CIN_CNF | TS-0001 [Error: Reference source not found], clause 9.6.7-2 | 4 (contentInstance) | contentInfo |
| TP/oneM2M/CSE/DMR/CRE/012_CIN/OR | Release 1 | PICS_CIN_OR | TS-0001 [Error: Reference source not found], clause 9.6.7-2 | 4 (contentInstance) | ontologyRef |
| TP/oneM2M/CSE/DMR/CRE/012_ACP/ET | Release 1 | N/A | TS-0001 [Error: Reference source not found], clause 9.6.1.3.1-1 | 1 (accesControlPolicy) | expirationTime |
| TP/oneM2M/CSE/DMR/CRE/012_ACP/LBL | Release 1 | PICS_ACP_LBL | TS-0001 [Error: Reference source not found], clause 9.6.1.3.2-1 | 1 (accesControlPolicy) | labels |
| TP/oneM2M/CSE/DMR/CRE/012_SUB/ACPI | Release 1 | PICS_SUB_ACPI | TS-0001 [Error: Reference source not found], clause 9.6.1.3.2-1 | 23 (subscription) | accessControlPolicyIDs |
| TP/oneM2M/CSE/DMR/CRE/012_SUB/ET | Release 1 | N/A | TS-0001 [Error: Reference source not found], clause 9.6.1.3.1-1 | 23 (subscription) | expirationTime |
| TP/oneM2M/CSE/DMR/CRE/012_SUB/LBL | Release 1 | PICS_SUB_LBL | TS-0001 [Error: Reference source not found], clause 9.6.1.3.2-1 | 23 (subscription) | labels |
| TP/oneM2M/CSE/DMR/CRE/012_SUB/ENC | Release 1 | PICS_SUB_ENC | TS-0001 [Error: Reference source not found], clause 9.6.8-2 | 23 (subscription) | eventNotificationCriteria |
| TP/oneM2M/CSE/DMR/CRE/012_SUB/EXC | Release 1 | PICS_SUB_EXC | TS-0001 [Error: Reference source not found], clause 9.6.8-2 | 23 (subscription) | expirationCounter |
| TP/oneM2M/CSE/DMR/CRE/012_SUB/GPI | Release 1 | PICS_SUB_GPI | TS-0001 [Error: Reference source not found], clause 9.6.8-2 | 23 (subscription) | groupID |
| TP/oneM2M/CSE/DMR/CRE/012_SUB/NFU | Release 1 | PICS_SUB_NFU | TS-0001 [Error: Reference source not found], clause 9.6.8-2 | 23 (subscription) | notificationForwardingURI |
| TP/oneM2M/CSE/DMR/CRE/012_SUB/BN | Release 1 | PICS_SUB_BN | TS-0001 [Error: Reference source not found], clause 9.6.8-2 | 23 (subscription) | batchNotify |
| TP/oneM2M/CSE/DMR/CRE/012_SUB/RL | Release 1 | PICS_SUB_RL | TS-0001 [Error: Reference source not found], clause 9.6.8-2 | 23 (subscription) | rateLimit |
| TP/oneM2M/CSE/DMR/CRE/012_SUB/PSN | Release 1 | PICS_SUB_PSN | TS-0001 [Error: Reference source not found], clause 9.6.8-2 | 23 (subscription) | preSubscriptionNotify |
| TP/oneM2M/CSE/DMR/CRE/012_SUB/PN | Release 1 | PICS_SUB_PN | TS-0001 [Error: Reference source not found], clause 9.6.8-2 | 23 (subscription) | pendingNotification |
| TP/oneM2M/CSE/DMR/CRE/012_SUB/NSP | Release 1 | PICS_SUB_NSP | TS-0001 [Error: Reference source not found], clause 9.6.8-2 | 23 (subscription) | notificationStoragePriority |
| TP/oneM2M/CSE/DMR/CRE/012_SUB/LN | Release 1 | PICS_SUB_LN | TS-0001 [Error: Reference source not found], clause 9.6.8-2 | 23 (subscription) | latestNotify |
| TP/oneM2M/CSE/DMR/CRE/012_SUB/NCT | Release 1 | PICS_SUB_NCT | TS-0001 [Error: Reference source not found], clause 9.6.8-2 | 23 (subscription) | notificationContentType |
| TP/oneM2M/CSE/DMR/CRE/012_SUB/NEC | Release 1 | PICS_SUB_NEC | TS-0001 [Error: Reference source not found], clause 9.6.8-2 | 23 (subscription) | notificationEventCat |
| TP/oneM2M/CSE/DMR/CRE/012_SUB/CR | Release 1 | PICS_SUB_CR | TS-0001 [Error: Reference source not found], clause 9.6.8-2 | 23 (subscription) | creator |
| TP/oneM2M/CSE/DMR/CRE/012_SUB/SU | Release 1 | PICS_SUB_SU | TS-0001 [Error: Reference source not found], clause 9.6.8-2 | 23 (subscription) | subscriberURI |
| TP/oneM2M/CSE/DMR/CRE/012_STCG/CR | Release 4 |  | TS-0001 [Error: Reference source not found], clause 9.6.23-2 | 22 (statsConfig) | creator |
| TP/oneM2M/CSE/DMR/CRE/012_TS/ACPI | Release 3 |  | TS-0001 [Error: Reference source not found], clause 9.6.36-2 | 29 (timeSeries) | accessControlPolicyIDs |
| TP/oneM2M/CSE/DMR/CRE/012_TS/ET | Release 3 |  | TS-0001 [Error: Reference source not found], clause 9.6.36-2 | 29 (timeSeries) | expirationTime |
| TP/oneM2M/CSE/DMR/CRE/012_TS/LBL | Release 3 |  | TS-0001 [Error: Reference source not found], clause 9.6.36-2 | 29 (timeSeries) | labels |
| TP/oneM2M/CSE/DMR/CRE/012_TS/CR | Release 3 |  | TS-0001 [Error: Reference source not found], clause 9.6.36-2 | 29 (timeSeries) | creator |
| TP/oneM2M/CSE/DMR/CRE/012_TS/MNI | Release 3 |  | TS-0001 [Error: Reference source not found], clause 9.6.36-2 | 29 (timeSeries) | maxNrOfInstances |
| TP/oneM2M/CSE/DMR/CRE/012_TS/MBS | Release 3 |  | TS-0001 [Error: Reference source not found], clause 9.6.36-2 | 29 (timeSeries) | maxByteSize |
| TP/oneM2M/CSE/DMR/CRE/012_TS/MIA | Release 3 |  | TS-0001 [Error: Reference source not found], clause 9.6.36-2 | 29 (timeSeries) | maxInstanceAge |
| TP/oneM2M/CSE/DMR/CRE/012_TS/PEI | Release 3 |  | TS-0001 [Error: Reference source not found], clause 9.6.36-2 | 29 (timeSeries) | periodicInterval |
| TP/oneM2M/CSE/DMR/CRE/012_TS/MDD | Release 3 |  | TS-0001 [Error: Reference source not found], clause 9.6.36-2 | 29 (timeSeries) | missingDataDetect |
| TP/oneM2M/CSE/DMR/CRE/012_TS/MDN | Release 3 |  | TS-0001 [Error: Reference source not found], clause 9.6.36-2 | 29 (timeSeries) | missingDataMaxNr |
| TP/oneM2M/CSE/DMR/CRE/012_TS/MDT | Release 3 |  | TS-0001 [Error: Reference source not found], clause 9.6.36-2 | 29 (timeSeries) | missingDataDetectTimer |
| TP/oneM2M/CSE/DMR/CRE/012_TS/OR | Release 3 |  | TS-0001 [Error: Reference source not found], clause 9.6.36-2 | 29 (timeSeries) | ontologyRef |
| TP/oneM2M/CSE/DMR/CRE/012_TSI/ET | Release 3 |  | TS-0001 [Error: Reference source not found], clause 9.6.37-2 | 30 (timeSeriesInstance) | expirationTime |
| TP/oneM2M/CSE/DMR/CRE/012_TSI/LBL | Release 3 |  | TS-0001 [Error: Reference source not found], clause 9.6.37-2 | 30 (timeSeriesInstance) | labels |
| TP/oneM2M/CSE/DMR/CRE/012_TSI/SNR | Release 3 |  | TS-0001 [Error: Reference source not found], clause 9.6.37-2 | 30 (timeSeriesInstance) | sequenceNr |
| TP/oneM2M/CSE/DMR/CRE/012_TRAM/TLTM | Release 4 |  | TS-0004 [2], Table 7.4.60.1-363 | 50 (transactionMgmt) | transactionLockTime |
| TP/oneM2M/CSE/DMR/CRE/012_TRAM/TEXT | Release 4 |  | TS-0004 [2], Table 7.4.60.1-363 | 50 (transactionMgmt) | transactionExecuteTime |
| TP/oneM2M/CSE/DMR/CRE/012_TRAM/TCT | Release 4 |  | TS-0004 [2], Table 7.4.60.1-363 | 50 (transactionMgmt) | transactionCommitTime |
| TP/oneM2M/CSE/DMR/CRE/012_TRAM/TEPT | Release 4 |  | TS-0004 [2], Table 7.4.60.1-363 | 50 (transactionMgmt) | transactionExpirationTime |
| TP/oneM2M/CSE/DMR/CRE/012_TRAM/TMD | Release 4 |  | TS-0004 [2], Table 7.4.60.1-363 | 50 (transactionMgmt) | transactionMode |
| TP/oneM2M/CSE/DMR/CRE/012_TRAM/TLTP | Release 4 |  | TS-0004 [2], Table 7.4.60.1-363 | 50 (transactionMgmt) | transactionLockType |
| TP/oneM2M/CSE/DMR/CRE/012_TRAM/TMR | Release 4 |  | TS-0004 [2], Table 7.4.60.1-363 | 50 (transactionMgmt) | transactionMaxRetries |
| TP/oneM2M/CSE/DMR/CRE/012_TRAM/TMH | Release 4 |  | TS-0004 [2], Table 7.4.60.1-363 | 50 (transactionMgmt) | transactionManagementHandling |
| TP/oneM2M/CSE/DMR/CRE/012_TRAC/TLTM | Release 4 |  | TS-0004 [2], Table 7.4.61.1-367 | 51 (transaction) | transactionLockTime |
| TP/oneM2M/CSE/DMR/CRE/012_TRAC/TEXT | Release 4 |  | TS-0004 [2], Table 7.4.61.1-367 | 51 (transaction) | transactionExecuteTime |
| TP/oneM2M/CSE/DMR/CRE/012_TRAC/TCT | Release 4 |  | TS-0004 [2], Table 7.4.61.1-367 | 51 (transaction) | transactionCommitTime |
| TP/oneM2M/CSE/DMR/CRE/012_TRAM/TLTP | Release 4 |  | TS-0004 [2], Table 7.4.61.1-367 | 51 (transaction) | transactionLockType |

…

TP/oneM2M/CSE/DMR/CRE/015

…

| TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/CRE/015_CNT | Release 2 | TS-0001 [Error: Reference source not found], clause 10.2.4.1 | 3 (container) |
| TP/oneM2M/CSE/DMR/CRE/015_GRP | Release 2 | TS-0001 [Error: Reference source not found], clause 10.2.7.2 | 9 (group) |
| TP/oneM2M/CSE/DMR/CRE/015_ACP | Release 2 | TS-0001 [Error: Reference source not found], clause 10.2.21.1 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/CRE/015_SUB | Release 2 | TS-0001 [Error: Reference source not found], clause 10.2.11.2 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/CRE/015_PCH | Release 2 | TS-0001 [Error: Reference source not found], clause 10.2.13.2 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/CRE/015_SCH | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.40.2 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/CRE/015_TS | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.30.1 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/CRE/015_TRAM | Release 4 | TS-0001 [1], clause 10.2.18.2 | 50 (transactionMgmt) |
| TP/oneM2M/CSE/DMR/CRE/015_TRAC | Release 4 | TS-0001 [1], clause 10.2.18.6 | 51 (transaction) |

TP/oneM2M/CSE/DMR/CRE/016

…

| TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/CRE/016_CNT | Release 2 | TS-0001 [Error: Reference source not found], clause 10.2.4.1 | 3 (container) |
| TP/oneM2M/CSE/DMR/CRE/016_GRP | Release 2 | TS-0001 [Error: Reference source not found], clause 10.2.7.2 | 9 (group) |
| TP/oneM2M/CSE/DMR/CRE/016_ACP | Release 2 | TS-0001 [Error: Reference source not found], clause 10.2.21.1 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/CRE/016_SUB | Release 2 | TS-0001 [Error: Reference source not found], clause 10.2.11.2 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/CRE/016_PCH | Release 2 | TS-0001 [Error: Reference source not found], clause 10.2.13.2 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/CRE/016_SCH | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.40.2 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/CRE/016_TS | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.30.1 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/CRE/016_TRAM | Release 4 | TS-0001 [1], clause 10.2.18.2 | 50 (transactionMgmt) |
| TP/oneM2M/CSE/DMR/CRE/016_TRAC | Release 4 | TS-0001 [1], clause 10.2.18.6 | 51 (transaction) |

TP/oneM2M/CSE/DMR/CRE/017

…

| TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/CRE/017_CNT | Release 2 | TS-0001 [Error: Reference source not found], clause 10.2.4.1 | 3 (container) |
| TP/oneM2M/CSE/DMR/CRE/017_GRP | Release 2 | TS-0001 [Error: Reference source not found], clause 10.2.7.2 | 9 (group) |
| TP/oneM2M/CSE/DMR/CRE/017_ACP | Release 2 | TS-0001 [Error: Reference source not found], clause 10.2.21.1 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/CRE/017_SUB | Release 2 | TS-0001 [Error: Reference source not found], clause 10.2.11.2 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/CRE/017_PCH | Release 2 | TS-0001 [Error: Reference source not found], clause 10.2.13.2 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/CRE/017_SCH | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.40.2 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/CRE/017_TS | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.30.1 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/CRE/017_TRAM | Release 4 | TS-0001 [1], clause 10.2.18.2 | 50 (transactionMgmt) |
| TP/oneM2M/CSE/DMR/CRE/017_TRAC | Release 4 | TS-0001 [1], clause 10.2.18.6 | 51 (transaction) |

…

TP/oneM2M/CSE/DMR/CRE/019

…

| TP Id | PARENT_RELEASE | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/CRE/019_CNT | Release 2 | 3 (container) |
| TP/oneM2M/CSE/DMR/CRE/019_GRP | Release 2 | 9 (group) |
| TP/oneM2M/CSE/DMR/CRE/019_ACP | Release 2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/CRE/019_PCH | Release 2 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/CRE/019_SUB | Release 2 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/CRE/019_SCH | Release 3 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/CRE/019_TS | Release 3 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/CRE/019_TRAM | Release 4 | 50 (transactionMgmt) |
| TP/oneM2M/CSE/DMR/CRE/019_TRAC | Release 4 | 51 (transaction) |

TP/oneM2M/CSE/DMR/CRE/020

…

| TP Id | PARENT_RELEASE | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/CRE/020_CNT | Release 2 | 3 (container) |
| TP/oneM2M/CSE/DMR/CRE/020_GRP | Release 2 | 9 (group) |
| TP/oneM2M/CSE/DMR/CRE/020_ACP | Release 2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/CRE/020_PCH | Release 2 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/CRE/020_SUB | Release 2 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/CRE/020_SCH | Release 3 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/CRE/020_TS | Release 3 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/CRE/020_TRAM | Release 4 | 50 (transactionMgmt) |
| TP/oneM2M/CSE/DMR/CRE/020_TRAC | Release 4 | 51 (transaction) |

…

##### 7.2.2.3.4	DELETE Operation

TP/oneM2M/CSE/DMR/DEL/001

…

| TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/DEL/001_CNT | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.4.4 | 3 (container) |
| TP/oneM2M/CSE/DMR/DEL/001_ACP | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.21.4 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/DEL/001_SUB | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.11.5 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/DEL/001_CIN | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.4.1 | 4 (contentInstance) |
| TP/oneM2M/CSE/DMR/DEL/001_GRP | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.7.5 | 9 (group) |
| TP/oneM2M/CSE/DMR/DEL/001_SCH | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.40.2 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/DEL/001_PCH | Release 2 | TS-0001 [Error: Reference source not found], clause 10.2.13.5 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/DEL/001_STCG | Release 4 | TS-0001 [Error: Reference source not found], clause 10.2.15.5 | 22 (statsConfig) |
| TP/oneM2M/CSE/DMR/DEL/001_TS | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.30.4 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/DEL/001_TSI | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.31.4 | 30 (timeSeriesInstance) |
| TP/oneM2M/CSE/DMR/DEL/001_TRAM | Release 4 | TS-0001 [1], clause 10.2.18.5 | 50 (transactionMgmt) |
| TP/oneM2M/CSE/DMR/DEL/001_TRAC | Release 4 | TS-0001 [1], clause 10.2.18.9 | 51 (transaction) |

TP/oneM2M/CSE/DMR/DEL/002

…

| TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/DEL/002_CNT | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.4.4 | 3 (container) |
| TP/oneM2M/CSE/DMR/DEL/002_ACP | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.21.4 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/DEL/002_SUB | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.11.5 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/DEL/002_GRP | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.7.5 | 9 (group) |
| TP/oneM2M/CSE/DMR/DEL/002_SCH | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.40.2 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/DEL/002_TS | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.30.4 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/DEL/002_TRAM | Release 4 | TS-0001 [1], clause 10.2.18.5 | 50 (transactionMgmt) |
| TP/oneM2M/CSE/DMR/DEL/002_TRAC | Release 4 | TS-0001 [1], clause 10.2.18.9 | 51 (transaction) |

…

TP/oneM2M/CSE/DMR/DEL/004

…

| TP Id | PARENT_RELEASE | Reference | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/DEL/004_CNT | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.4.4 | 3 (container) |
| TP/oneM2M/CSE/DMR/DEL/004_ACP | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.21.4 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/DEL/004_SUB | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.11.5 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/DEL/004_GRP | Release 1 | TS-0001 [Error: Reference source not found], clause 10.2.7.5 | 9 (group) |
| TP/oneM2M/CSE/DMR/DEL/004_SCH | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.40.2 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/DEL/004_STCG | Release 4 | TS-0001 [Error: Reference source not found], clause 10.2.15.5 | 22 (statsConfig) |
| TP/oneM2M/CSE/DMR/DEL/004_TS | Release 3 | TS-0001 [Error: Reference source not found], clause 10.2.30.4 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/DEL/004_TRAM | Release 4 | TS-0001 [1], clause 10.2.18.5 | 50 (transactionMgmt) |
| TP/oneM2M/CSE/DMR/DEL/004_TRAC | Release 4 | TS-0001 [1], clause 10.2.30.4 | 51 (transaction) |

…

TP/oneM2M/CSE/DMR/DEL/012

…

| TP Id | PARENT_RELEASE | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/DEL/012_CNT | Release 2 | 3 (container) |
| TP/oneM2M/CSE/DMR/DEL/012_GRP | Release 2 | 9 (group) |
| TP/oneM2M/CSE/DMR/DEL/012_ACP | Release 2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/DEL/012_SCH | Release 3 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/DEL/012_PCH | Release 3 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/DEL/012_SUB | Release 3 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/DEL/012_TS | Release 3 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/DEL/012_TRAM | Release 4 | 50 (transactionMgmt) |
| TP/oneM2M/CSE/DMR/DEL/012_TRAC | Release 4 | 51 (transaction) |

TP/oneM2M/CSE/DMR/DEL/013

…

| TP Id | PARENT_RELEASE | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/DEL/013_CNT | Release 2 | 3 (container) |
| TP/oneM2M/CSE/DMR/DEL/013_GRP | Release 2 | 9 (group) |
| TP/oneM2M/CSE/DMR/DEL/013_ACP | Release 2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/DEL/013_SCH | Release 3 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/DEL/013_PCH | Release 3 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/DEL/013_SUB | Release 3 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/DEL/013_TS | Release 3 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/DEL/013_TRAM | Release 4 | 50 (transactionMgmt) |
| TP/oneM2M/CSE/DMR/DEL/013_TRAC | Release 4 | 51 (transaction) |

TP/oneM2M/CSE/DMR/DEL/014

…

| TP Id | PARENT_RELEASE | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/DEL/014_CNT | Release 3 | 3 (container) |
| TP/oneM2M/CSE/DMR/DEL/014_GRP | Release 3 | 9 (group) |
| TP/oneM2M/CSE/DMR/DEL/014_ACP | Release 3 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/DEL/014_SCH | Release 3 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/DEL/014_SUB | Release 3 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/DEL/014_TS | Release 3 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/DEL/014_TRAM | Release 4 | 50 (transactionMgmt) |
| TP/oneM2M/CSE/DMR/DEL/014_TRAC | Release 4 | 51 (transaction) |

TP/oneM2M/CSE/DMR/DEL/015

…

| TP Id | PARENT_RELEASE | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/DEL/015_CNT | Release 3 | 3 (container) |
| TP/oneM2M/CSE/DMR/DEL/015_GRP | Release 3 | 9 (group) |
| TP/oneM2M/CSE/DMR/DEL/015_ACP | Release 3 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/DEL/015_SCH | Release 3 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/DEL/015_SUB | Release 3 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/DEL/015_TS | Release 3 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/DEL/015_TRAM | Release 4 | 50 (transactionMgmt) |
| TP/oneM2M/CSE/DMR/DEL/015_TRAC | Release 4 | 51 (transaction) |

TP/oneM2M/CSE/DMR/DEL/016

…

| TP Id | PARENT_RELEASE | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/DEL/016_CNT | Release 3 | 3 (container) |
| TP/oneM2M/CSE/DMR/DEL/016_GRP | Release 3 | 9 (group) |
| TP/oneM2M/CSE/DMR/DEL/016_ACP | Release 3 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/DEL/016_SCH | Release 3 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/DEL/016_SUB | Release 3 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/DEL/016_TS | Release 3 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/DEL/016_TRAM | Release 4 | 50 (transactionMgmt) |
| TP/oneM2M/CSE/DMR/DEL/016_TRAC | Release 4 | 51 (transaction) |

TP/oneM2M/CSE/DMR/DEL/017

…

| TP Id | PARENT_RELEASE | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/DEL/017_CNT | Release 3 | 3 (container) |
| TP/oneM2M/CSE/DMR/DEL/017_GRP | Release 3 | 9 (group) |
| TP/oneM2M/CSE/DMR/DEL/017_ACP | Release 3 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/DEL/017_SCH | Release 3 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/DEL/017_SUB | Release 3 | 23 (subscription) |
| TP/oneM2M/CSE/DMR/DEL/017_TS | Release 3 | 29 (timeSeries) |
| TP/oneM2M/CSE/DMR/DEL/017_TRAM | Release 4 | 50 (transactionMgmt) |
| TP/oneM2M/CSE/DMR/DEL/017_TRAC | Release 4 | 51 (transaction) |

- ----------------------- End of change 1 -----------------------