| CHANGE REQUEST |
| --- |
| Meeting ID:* | TDE49.2 |
| Source:* | Laurent Velez , ETSI, laurent.velez@etsi.org |
| Date:* | 2021-04-07 |
| Reason for Change/s:* | Change of the format of the API guide with AE as exemple |
| CR against: Release* | Rel 3 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0051 V3.0.0 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | na |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2019 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

The CR proposes to change new format of the API guide V3.0.0,  describing the APIs in a more simpler way comparing the guide of the release 2.

The contribution is applied to AE resource as an example. If the format is agreed, it will then be reflected in the whole document for all existing APIs and the future ones.

### -----------------------Start of change 1-------------------------------------------

### 6.2.4	Resource Type AE

#### 6.2.4.0	Introduction

The <AE> resource represents information about an Application Entity that is registered to a CSE. The originator of an <AE> create request is and only can be an AE. A CSE is not allowed to initiate an <AE> create request.

The <AE> resource which resides in different kind of nodes such as Application Dedicated Node, Middle Node, Infrastructure Node, etc. An Application Dedicated Node could reside in a constrained M2M device, while a Middle Node could reside in an M2M gateway and an Infrastructure Node could reside in an M2M Service Infrastructure. For example, in smart home scenario, light bulbs are modelled as Application Dedicated Node which communicate with home gateway which is modelled as a Middle Node and in resource registration phase, light bulbs can be registered as an <AE> resource.

OpenAPI repository for <AE> Resource:

https://labs.etsi.org/rep/iot/onem2m-api/blob/master/OpenAPI/API-AE.json

#### 6.2.4.1	AE CREATE

- Initial state on CSE:

- Call flow:

- Example:

- HTTP Request:

POST /csename HTTP/1.1

Host: 192.168.1.30:8080

X-M2M-Origin: CAdmin

Content-Type: application/json;ty=2

X-M2M-RI: 1234

X-M2M-RVI:3

{

"m2m:ae" : {

"rn": "temperature",

"api": "N01.com.company.temperature ",

"lbl": ["key1", "key2"],

"rr": true,

"srv": ["3"],

"poa": ["http://192.168.1.30:8080"]

}

}

- HTTP Response:

201 Created

content-length: 313

content-type: application/json

date: Tue, 30 Mar 2021 15:39:34 GMT

x-m2m-ri: 1234

x-m2m-rsc: 2001

x-m2m-rvi: 3

{

"m2m:ae": {

"rn": "temperature",

"api": "N01.com.company.temperature ",

"lbl": [

"key1",

"key2"

],

"rr": true,

"srv": [

"3"

],

"poa": [

"http://192.168.1.30:8080"

],

"ri": "CAdmin",

"ct": "20210330T153934,791690",

"lt": "20210330T153934,791690",

"et": "20220330T153934,791714",

"pi": "id-in",

"ty": 2,

"aei": "CAdmin"

}

}

#### 6.2.4.2	AE Retrieve

- Initial state on CSE:

- Call flow:

- Example:

- HTTP Request:

GET /csename/temperature HTTP/1.1

Accept: application/json

Host: 192.168.0.10:8282

X-M2M-Origin: CAdmin

X-M2M-RI:1234

X-M2M-RVI: 3

- HTTP Response:

200 OK

Content-Length:323

Content-Type:application/json

X-M2M-RI:1234

X-M2M-RVI: 3

X-M2M-RSC:2000

{

"m2m:ae": {

"rn": "temperature",

"api": "N01.com.company.temperature ",

"lbl": [

"key1",

"key2"

],

"rr": true,

"srv": [

"3"

],

"poa": [

"http://192.168.1.30:8080"

],

"ri": "CSUQPRVK06v",

"ct": "20210407T093125,074401",

"lt": "20210407T093125,074401",

"et": "20220407T093125,074426",

"pi": "id-in",

"ty": 2,

"aei": "CSUQPRVK06v"

}

#### 6.2.4.3	AE Update

- Initial state on CSE:

- Call flow:

- Example:

- HTTP Request:

PUT /csename/temperature HTTP/1.1

Host: 192.168.1.30:8080

X-M2M-Origin: CAdmin

Content-Type:application/json

Accept: application/json

X-M2M-RI: 1234

X-M2M-RVI: 3

{

"m2m:ae" : {

"lbl": ["temperature bedroom"],

"poa": ["http://192.168.1.50:9090"]

}

}

- HTTP Response:

200 OK

Content-Length:330

Content-Type:application/json

X-M2M-RI:1234

X-M2M-RVI: 3

X-M2M-RSC:2004

{

"m2m:ae": {

"rn": "temperature",

"api": "N01.com.company.temperature ",

"lbl": [

"temperature bedroom"

],

"rr": true,

"srv": [

"3"

],

"poa": [

"http://192.168.1.50:9090"

],

"ri": "CSUQPRVK06v",

"ct": "20210407T093125,074401",

"lt": "20210407T094636,903417",

"et": "20220407T093125,074426",

"pi": "id-in",

"ty": 2,

"aei": "CSUQPRVK06v"

}

#### 6.2.4.3	AE Delete

- Initial state on CSE:

- Call flow:

- Example:

- HTTP Request:

DELETE /csename/temperature HTTP/1.1

Host: 192.168.1.30:8080

X-M2M-Origin: CAdmin

X-M2M-RI:1234

X-M2M-RVI: 3

- HTTP Response:

200 OK

Content-Length:0

Content-Type:application/json

X-M2M-RI:1234

X-M2M-RVI: 3

X-M2M-RSC:2002

### -----------------------End of change 1---------------------------------------------

# Text boxes

CSE <CSEBase>

notification HTTP body

CSE <CSEBase>

temperature <AE>

CSE <CSEBase>

temperature <AE>

CSE <CSEBase>

temperature <AE>