| CHANGE REQUEST |
| --- |
| Meeting ID:* | TDE #49.4 |
| Source:* | Rahul, C-DOT, krahul@cdot.in Anupama, C-DOT, anupama@cdot.in Poornima, C-DOT, poornima@cdot.in |
| Date:* | 2021-04-22 |
| Reason for Change/s:* | See the introduction |
| CR against: Release* | Release 4 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018 V4.3.0 |
| Clauses * | 7.2.2.18 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2020 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

If this is  a correction, and the change applies to previous releases, a separate “mirror CR” should be posted at the same time as this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made e.g. a change impacting 5 tables should not only include a proposal to change only 3 tables. Include any changes to references, definitions, and abbreviations in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar.

Use change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the proposed new clause is located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to the content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The CR added a section for service subscription management, service subscription user profile functionality is moved under it.

This CR proposes to add new TP’s for <m2mServiceSubscriptionProfile>. As per TS-0001 the resource exist on IN-CSE only, but no specific handling mentioned for this resource in TS-0004 hence only success case TPs are added. More TPs can be added after addition of failure behaviour such as

“OPERATION_NOT_ALLOWED” error should be given if the request is received by MN/ASN-CSE.

### -----------------------Start of change 1-------------------------------------------

#### 7.2.2.18	Service Subscription Management

##### 7.2.2.18.1       Service Subscription User Profile(SSUP)

##### 7.2.2.18.1.1	Basic Operation

TP/oneM2M/CSE/SSUP/001

| TP Id | TP/oneM2M/CSE/SSUP/001 |
| --- | --- |
| Test objective | Check that the IUT successfully performs operations on resource serviceSubscribedUserProfile for authorized M2M Service User |
| Reference | TS-0001 [1], clauses 9.6.68 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having m2mServiceSubscriptionProfile at TARGET_RESOURCE_ADDRESS containing a child resource and the AE having privileges to perform OPERATION on TARGET_RESOURCE_ADDRESS and the IUT having an authorized M2M Service User AE-ID } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to authorized M2M Users AE-ID and } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status set to RESPONSE_STATUS_CODE and Content containing serviceSubscribedUserProfile resource representation (when required) } | IUT ( AE |

| TP Id | OPERATION | RESPONSE_STATUS_CODE |
| --- | --- | --- |
| TP/oneM2M/CSE/SSUP/001_CRE | CREATE | 2001 (CREATED) |
| TP/oneM2M/CSE/SSUP/001_RET | RETRIEVE | 2000 (OK) |
| TP/oneM2M/CSE/SSUP/001_UPD | UPDATE | 2004 (UPDATED) |
| TP/oneM2M/CSE/SSUP/002_DEL | DELETE | 2002 (DELETED) |

TP/oneM2M/CSE/SSUP/002

| TP Id | TP/oneM2M/CSE/SSUP/002 |
| --- | --- |
| Test objective | Check that the IUT rejects the operation on serviceSubscribedUserProfile resource when the attributes violate the limits specified in the parent resource |
| Reference | TS-0001 [1], clauses 9.6.68 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered an AE and the IUT having serviceSubscribedUserProfile at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform OPERATION on TARGET_RESOURCE and the IUT having an authorized M2M Service User AE-ID } |
| Expected behavior | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to authorized M2M Users AE-ID } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4102 (CONTENTS_UNACCEPTABLE) } | IUT ( AE |

| TP Id | OPERATION |
| --- | --- |
| TP/oneM2M/CSE/SSUP/002_CRE | CREATE |
| TP/oneM2M/CSE/SSUP/002_UPD | UPDATE |

TP/oneM2M/CSE/SSUP/003

| TP Id | TP/oneM2M/CSE/SSUP/003 |
| --- | --- |
| Test objective | Check that the IUT successfully restricts the usage of services by a M2M Service User |
| Reference | TS-0001 [1], clauses 9.6.68 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered an AE and the IUT having m2mServiceSubscriptionProfile at TARGET_RESOURCE_ADDRESS containing a child resource the AE having privileges to perform OPERATION on TARGET_RESOURCE_ADDRESS and the IUT having an authorized M2M Service User } |
| Expected behavior | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to an authorized M2M Service User AE-ID } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to RESPONSE_STATUS_CODE and Content containing serviceSubscribedUserProfile resource representation } | IUT ( AE |

| TP Id | OPERATION | RESPONSE_STATUS_CODE |
| --- | --- | --- |
| TP/oneM2M/CSE/SSUP/003_CRE | CREATE | 2001 (CREATED) |
| TP/oneM2M/CSE/SSUP/003_UPD | UPDATE | 2004 (UPDATED) |

TP/oneM2M/CSE/SSUP/004

| TP Id | TP/oneM2M/CSE/SSUP/004 |
| --- | --- |
| Test objective | Check that the IUT rejects the OPERATION when the associated services of a M2M Service User reach limits provided in the serviceSubscribedUserProfile resource |
| Reference | TS-0001 [1], clauses 9.6.68 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered an AE and the IUT having serviceSubscribedUserProfile at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform OPERATION on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to an authorized M2M Service User AE-ID } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4102 (CONTENTS_UNACCEPTABLE) } | IUT ( AE |

| TP Id | OPERATION |
| --- | --- |
| TP/oneM2M/CSE/SSUP/004_CRE | CREATE |
| TP/oneM2M/CSE/SSUP/004_UPD | UPDATE |

TP/oneM2M/CSE/SSUP/005

| TP Id | TP/oneM2M/CSE/SSUP/005 |
| --- | --- |
| Test objective | Check that IUT rejects the request when the values of ATTRIBUTE in request exceed the actual resources associated with the Service user |
| Reference | TS-0001 [1], clauses 9.6.68 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered an AE and the IUT having serviceSubscribedUserProfile at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform UPDATE on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to an authorized M2M Service User AE-ID } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4102 (CONTENTS_UNACCEPTABLE) } | IUT ( AE |

| TP Id | ATTRIBUTE |
| --- | --- |
| TP/oneM2M/CSE/SSUP/005_MNA | maxNumAEs |
| TP/oneM2M/CSE/SSUP/005_MNN | maxNumNodes |
| TP/oneM2M/CSE/SSUP/005_MNC | maxNumContainers |
| TP/oneM2M/CSE/SSUP/005_MNI | maxNumInstancesPerContainer |

TP/oneM2M/CSE/SSUP/006

| TP Id | TP/oneM2M/CSE/SSUP/006 |
| --- | --- |
| Test objective | Check that IUT accepts the request when the values of ATTRIBUTE in request do not exceed the actual resources associated with the Service user |
| Reference | TS-0001 [1], clauses 9.6.68 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS _CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered an AE and the IUT having serviceSubscribedUserProfile at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform UPDATE on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2004 (UPDATED) } | IUT ( AE |

| TP Id | RESOURCE_TYPE |
| --- | --- |
| TP/oneM2M/CSE/SSUP/006_MNA | maxNumAEs |
| TP/oneM2M/CSE/SSUP/006_MNN | maxNumNodes |
| TP/oneM2M/CSE/SSUP/006_MNC | maxNumContainers |
| TP/oneM2M/CSE/SSUP/006_MNI | maxNumInstancesPerContainer |

TP/oneM2M/CSE/SSUP/007

| TP Id | TP/oneM2M/CSE/SSUP/007 |
| --- | --- |
| Test objective | Check that IUT successfully accepts the request with the default access control policies when the accessControlPolicyIDs attribute of a resource serviceSubscribedUserProfile created by this M2M Service User is not configured |
| Reference | TS-0001 [1], clauses 9.6.68 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS _CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having m2mServiceSubscriptionProfile at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform OPERATION on TARGET_RESOURCE_ADDRESS and the IUT having an authorized M2M Service User AE-ID } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to an authorized M2M Service User AE-ID } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to RESPONSE_STATUS_CODE } | IUT ( AE |

| TP Id | OPERATION | RESPONSE_STATUS_CODE |
| --- | --- | --- |
| TP/oneM2M/CSE/SSUP/007_CRE | CREATE | 2001 (CREATED) |
| TP/oneM2M/CSE/SSUP/007_RET | RETRIEVE | 2000 (OK) |
| TP/oneM2M/CSE/SSUP/007_UPD | UPDATE | 2004 (UPDATED) |

TP/oneM2M/CSE/SSUP/008

| TP Id | TP/oneM2M/CSE/SSUP/008 |
| --- | --- |
| Test objective | Check that IUT rejects OPERATION request if service subscription profile associated with the M2M service user/AE is not available |
| Reference | TS-0004 [2], clauses 7.3.2 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_IN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT not having a <serviceSubscribedUserProfile> associated with the M2M service user at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Request from an AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and a valid content } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (UNAUTHORIZED_USER) } | IUT ( AE |

| TP Id | OPERATION |
| --- | --- |
| TP/oneM2M/CSE/SSUP/008_RET | RETRIEVE |
| TP/oneM2M/CSE/SSUP/008_UPD | UPDATE |
| TP/oneM2M/CSE/SSUP/008_DEL | DELETE |

##### 7.2.2.18.2       Service Subscription Profile(SSP)

##### 7.2.2.18.2.1      Basic Operation

TP/oneM2M/CSE/SSP/001

| TP Id | TP/oneM2M/CSE/SSP/001 |
| --- | --- |
| Test objective | Check that the IUT successfully performs operations on resource m2mServiceSubscriptionProfile for authorized AE |
| Reference | TS-0001 [1], clauses 9.6.19 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_IN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform OPERATION on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to authorized AE-ID and } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status set to RESPONSE_STATUS_CODE } | IUT  AE |

| TP Id | OPERATION | RESPONSE_STATUS_CODE |
| --- | --- | --- |
| TP/oneM2M/CSE/SSP/001_CRE | CREATE | 2001 (CREATED) |
| TP/oneM2M/CSE/SSP/001_RET | RETRIEVE | 2000 (OK) |
| TP/oneM2M/CSE/SSP/001_UPD | UPDATE | 2004 (UPDATED) |
| TP/oneM2M/CSE/SSP/002_DEL | DELETE | 2002 (DELETED) |

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

Should it be generic or more specified?

Should It be generic or more specified?

Should it be “IN_CSE_BASE ADDRESS”