| CHANGE REQUEST |
| --- |
| Meeting:* | TDE #49.2 |
| Source:* | TF-oneM2M |
| Date:* | 2021-05-17 |
| Contact:* | Neeta Meshram, C-DOT, neeta@cdot.in |
| Reason for Change/s:* | New TPs for Transaction management CSF release |
| CR against: Release* | Rel-4 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018-V-4.2.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution introduces new TPs for Transaction Management CSF as per TS-0004 and TS-0001 documents.

R01- TP/oneM2M/CSE/TMG/RET/001 has been updated to TP/oneM2M/CSE/TMG/CRE/005.

R02- Updated Table for InvalidTransactionControl values corresponding to transactionState value for <transactionMgmt> and <transaction> resource.

R03- New TP added for Successful update of transactionMgmt and transaction resource.

R04- Corrected some typos.

----------------------- Start of new text 1 -----------------------

#### 7.2.2.x	Transaction Management(TMG)

7.2.2.x.y 	CREATE Operation

TP/oneM2M/CSE/TMG/CRE/001

| TP Id | TP/oneM2M/CSE/TMG/CRE/001 |
| --- | --- |
| Test objective | Check that the IUT sets value of transactionControl to INITIAL during the creation of <transactionMgmt> resource. |
| Reference | TS-0004 [2] clause 7.4.60.2.1 Recv-6.4 (a) |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource PARENT_RESOURCE_ADDRESS allowing the AE to perform CREATE operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to PARENT_RESOURCE_ADDRESS and Resource Type set to 50 (transactionMgmt) and From set to AE-ID and Content containing transactionMgmt resource containing requestPrimitives attribute set to LIST_OF_REQUESTPRIMITIVES } | IUT  AE |
|  | then { the IUT creates the transactionMgmt resource and the IUT sends Response Status Code set to 2001 (CREATED) Content containing transactionMgmt resource containing transactionControl attribute set to INITIAL } | IUT  AE |

TP/oneM2M/CSE/TMG/CRE/002

| TP Id | TP/oneM2M/CSE/TMG/CRE/002 |
| --- | --- |
| Test objective | Check that the IUT rejects creation of <transactionMgmt> resource when From parameters contained in the requestPrimitives attribute of the received <transactionMgmt> resource is not AE1. |
| Reference | TS-0004 [2] clause 7.4.60.2.1 Recv-6.4 (a) |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE1 and the IUT having registered the AE2 and and the IUT having a resource PARENT_RESOURCE_ADDRESS allowing the AE1 to perform CREATE operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to PARENT_RESOURCE_ADDRESS and Resource Type set to 50 (transactionMgmt) and From set to AE1 and Content containing transactionMgmt resource containing requestPrimitives attribute set to LIST_OF_REQUESTPRIMITIVES containing From set to AE2 } | IUT  AE |
|  | then { the IUT does not create the transactionMgmt resource and the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/TMG/CRE/003

| TP Id | TP/oneM2M/CSE/TMG/CRE/003 |
| --- | --- |
| Test objective | Check that the IUT sets value of transactionControl to LOCK during the creation of <transaction> resource. |
| Reference | TS-0004 [2] clause 7.4.61.2.1, Recv-6.4 |
| Parent Release | Release 4 |
| Config Id | CF02 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource PARENT_RESOURCE_ADDRESS and the AE having privileges to perform CREATE operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to PARENT_RESOURCE_ADDRESS and Resource Type set to 51 (transaction) and From set to AE-ID and Content containing transaction resource containing requestPrimitive attribute set to REQUESTPRIMITIVE } | IUT  AE |
|  | then { the IUT creates the transaction resource and the IUT sends Response Status Code set to 2001 (CREATED) Content containing transaction resource containing transactionControl attribute set to LOCK } | IUT  AE |

TP/oneM2M/CSE/TMG/CRE/004

| TP Id | TP/oneM2M/CSE/TMG/CRE/004 |
| --- | --- |
| Test objective | Check that the IUT rejects creation of <transaction> resource when From parameters contained in the requestPrimitive attribute of the received <transaction> resource is not AE1. |
| Reference | TS-0004 [2] clause 7.4.60.2.1 Recv-6.4 (a) |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE1 and the IUT having registered the AE2 and and the IUT having a resource PARENT_RESOURCE_ADDRESS allowing the AE1 to perform CREATE operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to PARENT_RESOURCE_ADDRESS and Resource Type set to 51 (transaction) and From set to AE1 and Content containing transaction resource containing requestPrimitive attribute set to REQUESTPRIMITIVE containing From set to AE2 } | IUT  AE |
|  | then { the IUT does not create the transaction resource and the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/TMG/CRE/005

| TP Id | TP/oneM2M/CSE/TMG/CRE/005 |
| --- | --- |
| Test objective | Check that the IUT creates a <transaction> resource as child for each target resource contained in the requestPrimitives attribute when receiving a valid transactionMgmt create request. |
| Reference | TS-0001 [2] clause 10.2.18.1 |
| Parent Release | Release 4 |
| Config Id | CF02 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource PARENT_RESOURCE_ADDRESS and the IUT having a resource TARGET_RESOURCE_ADDRESS the AE having privileges to perform CREATE operation at PARENT_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to PARENT_RESOURCE_ADDRESS and From set to AE-ID and Content containing TransactionMgmt containing requestPrimitives attribute containing to set to TARGET_RESOURCE_ADDRESS } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) and Content containing Valid transactionMgmt resource representation and IUT creates a transaction resource as child of the target resource address } | IUT  AE |

##### 7.2.2.x.y	UPDATE Operation

TP/oneM2M/CSE/TMG/UPD/001

| TP Id | TP/oneM2M/CSE/TMG/UPD/001 |
| --- | --- |
| Test objective | Check that the IUT rejects the update of transactionControl attribute of transactionMgmt resource when Originator of update request is not the creator of transactionMgmt resource. |
| Reference | TS-0001 [4], clause 7.4.60.2.3, Recv-6.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE2 and the IUT having registered the AE1 and and the IUT having a transactionMgmt resource at TARGET_RESOURCE_ADDRESS containing creator attribute set to AE2 and the AE1 having privileges to perform UPDATE operation on the TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE1 containing To set to TARGET_RESOURCE_ADDRESS and From set to AE1 and Content containing transactionMgmt resource containing transactionControl attribute set to TRANSACTION_CONTROL_VALUE } | IUT  AE1 |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4103 (ORIGINATOR_HAS _NO_PRIVILEGE) } | IUT  AE1 |

TP/oneM2M/CSE/TMG/UPD/002

| TP Id | TP/oneM2M/CSE/TMG/UPD/002 |
| --- | --- |
| Test objective | Check that the IUT rejects update of transactionControl attribute of transactionMgmt resource when transactionMode is "CSE_CONTROLLED". |
| Reference | TS-0004 [4], clause 7.4.60.2.3, Recv-6.3 |
| Parent Release | Release 4 |
| Config Id | CF02 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and and the IUT having a transactionMgmt resource at TARGET_RESOURCE_ADDRESS containing creator attribute set to AE and transactionMode set to "CSE_CONTROLLED" } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE and Content containing transactionMgmt resource containing transactionControl attribute set to TRANSACTION_CONTROL_VALUE } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/TMG/UPD/003

| TP Id | TP/oneM2M/CSE/TMG/UPD/003 |
| --- | --- |
| Test objective | Check that the IUT rejects update of transactionMgmt resource when the transactionControl value in the request primitive does not transition to values specified in Table 10.2.18.1-1 of oneM2M TS-0001 |
| Reference | TS-0001 [4], Table 10.2.18.1-1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE1 and the IUT having a transactionMgmt resource at TARGET_RESOURCE_ADDRESS containing creator attribute set to AE1 and transactionMode set to "CREATOR_CONTROLLED" and transactionState set to TRANSACTION_STATE_VALUE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE1 containing To set to TARGET_RESOURCE_ADDRESS and From set to AE1 and Content containing transactionMgmt resource containing transactionControl attribute set to INVALID_CORRESPONDING_TRANSACTION_CONTROL_VALUE } | IUT  AE1 |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4123 (ILLEGAL_TRANSACTION_STATE_TRANSITION_ATTEMPTED) } | IUT  AE1 |

Table: 7.2.2.x.y-1: Invalid <transactionMgmt> transactionControl values

| TP Id | TRANSACTION_STATE_VALUE | INVALID_CORRESPONDING_TRANSACTION_CONTROL_VALUE |
| --- | --- | --- |
| TP/oneM2M/CSE/TMG/UPD/003_INI | INITIAL | EXECUTE, ABORT,COMMIT, INITIAL, ERROR |
| TP/oneM2M/CSE/TMG/UPD/003_LOC | LOCKED | COMMIT, INITIAL, LOCK, ERROR |
| TP/oneM2M/CSE/TMG/UPD/003_EXE | EXECUTED | INITIAL,LOCK, EXECUTE, ERROR |
| TP/oneM2M/CSE/TMG/UPD/003_ERR | ERROR | LOCK, EXECUTE, COMMIT, ERROR |
| TP/oneM2M/CSE/TMG/UPD/003_COM | COMMITTED | EXECUTE, ABORT,COMMIT, LOCK, ERROR |
| TP/oneM2M/CSE/TMG/UPD/003_ABT | ABORTED | EXECUTE, ABORT,COMMIT, LOCK, ERROR |

| TP Id | TP/oneM2M/CSE/TMG/UPD/004 |
| --- | --- |
| Test objective | Check that the IUT successfully updates of transactionMgmt resource when transactionMode is “CREATOR_CONTROLLED” and the transactionControl value in the request primitive transitions to values specified in Table 10.2.18.1-1 of oneM2M TS-0001 and Originator of request matches creator attribute of transactionMgmt resource. |
| Reference | TS-0001 [4], Table 10.2.18.1-1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE1 and the IUT having a transactionMgmt resource at TARGET_RESOURCE_ADDRESS containing creator attribute set to AE1 and transactionMode set to "CREATOR_CONTROLLED" and transactionState set to TRANSACTION_STATE_VALUE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE1 containing To set to TARGET_RESOURCE_ADDRESS and From set to AE1 and Content containing transactionMgmt resource containing transactionControl attribute set to VALID_CORRESPONDING_TRANSACTION_CONTROL_VALUE } | IUT  AE1 |
|  | then { the IUT updates the transactionMgmt resource and the IUT sends a valid Response containing Response Status Code set to 2004 (UPDATED) Content containing transactionMgmt resource containing transactionControl attribute set to VALID_CORRESPONDING_TRANSACTION_CONTROL_VALUE } | IUT  AE1 |

Table: 7.2.2.x.y-1: valid <transactionMgmt> transactionControl values

| TP Id | TRANSACTION_STATE_VALUE | VALID_CORRESPONDING_TRANSACTION_CONTROL_VALUE |
| --- | --- | --- |
| TP/oneM2M/CSE/TMG/UPD/004_INI | INITIAL | LOCK |
| TP/oneM2M/CSE/TMG/UPD/004_LOC | LOCKED | EXECUTE, ABORT |
| TP/oneM2M/CSE/TMG/UPD/004_EXE | EXECUTED | COMMIT, ABORT |
| TP/oneM2M/CSE/TMG/UPD/004_ERR | ERROR | ABORT, INITIAL |
| TP/oneM2M/CSE/TMG/UPD/004_COM | COMMITTED | INITIAL |
| TP/oneM2M/CSE/TMG/UPD/004_ABT | ABORTED | INITIAL |

TP/oneM2M/CSE/TMG/UPD/005

| TP Id | TP/oneM2M/CSE/TMG/UPD/005 |
| --- | --- |
| Test objective | Check that the IUT rejects the update of transactionControl attribute of transaction resource when Originator of update request is not the creator of transaction resource. |
| Reference | TS-0001 [4], clause 7.4.61.2.3, Recv-6.3 |
| Parent Release | Release 4 |
| Config Id | CF02 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE2 and the IUT having registered the AE1 and and the IUT having a transaction resource at TARGET_RESOURCE_ADDRESS containing creator attribute set to AE2 and the AE1 having privileges to perform UPDATE operation on the TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE1 containing To set to TARGET_RESOURCE_ADDRESS and From set to AE1 and Content containing transaction resource containing transactionControl attribute set to TRANSACTION_CONTROL_VALUE } | IUT  AE1 |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4103 (ORIGINATOR_HAS _NO_PRIVILEGE) } | IUT  AE1 |

TP/oneM2M/CSE/TMG/UPD/006

| TP Id | TP/oneM2M/CSE/TMG/UPD/006 |
| --- | --- |
| Test objective | Check that the IUT rejects update of transaction resource when the transactionControl value in the request primitive does not transition to values specified in Table 10.2.18.1-2 of oneM2M TS-0001 |
| Reference | TS-0001 [4], Table 10.2.18.1-2 |
| Parent Release | Release 4 |
| Config Id | CF02 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE1 and the IUT having a transaction resource at TARGET_RESOURCE_ADDRESS containing creator attribute set to AE1 and transactionState set to TRANSACTION_STATE_VALUE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE1 containing To set to TARGET_RESOURCE_ADDRESS and From set to AE1 and Content containing transaction resource containing transactionControl attribute set to INVALID_CORRESPONDING_TRANSACTION_CONTROL_VALUE } | IUT  AE1 |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4123 (ILLEGAL_TRANSACTION_STATE_TRANSITION_ATTEMPTED) } | IUT  AE1 |

Table: 7.2.2.x.y-1: Invalid <transaction> transactionControl values

| TP Id | TRANSACTION_STATE_VALUE | INVALID_CORRESPONDING_TRANSACTION_CONTROL_VALUE |
| --- | --- | --- |
| TP/oneM2M/CSE/TMG/UPD/006_LOC | LOCKED | COMMIT, LOCK, ERROR |
| TP/oneM2M/CSE/TMG/UPD/006_EXE | EXECUTED | INITIAL,LOCK, EXECUTE, ERROR |
| TP/oneM2M/CSE/TMG/UPD/006_ERR | ERROR | EXECUTE,COMMIT, ERROR |
| TP/oneM2M/CSE/TMG/UPD/006_COM | COMMITTED | EXECUTE, ABORT,COMMIT, ERROR |
| TP/oneM2M/CSE/TMG/UPD/006_ABT | ABORTED | EXECUTE, ABORT,COMMIT, ERROR |

| TP Id | TP/oneM2M/CSE/TMG/UPD/007 |
| --- | --- |
| Test objective | Check that the IUT successfully updates of transaction resource when the transactionControl value in the request primitive transitions to values specified in Table 10.2.18.1-2 of oneM2M TS-0001 and Originator of request is matches creator attribute of transaction resource. |
| Reference | TS-0001 [4], Table 10.2.18.1-1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE1 and the IUT having a transaction resource at TARGET_RESOURCE_ADDRESS containing creator attribute set to AE1 and transactionState set to TRANSACTION_STATE_VALUE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE1 containing To set to TARGET_RESOURCE_ADDRESS and From set to AE1 and Content containing transaction resource containing transactionControl attribute set to VALID_CORRESPONDING_TRANSACTION_CONTROL_VALUE } | IUT  AE1 |
|  | then { the IUT updates the transaction resource and the IUT sends a valid Response containing Response Status Code set to 2004 (UPDATED) Content containing transaction resource containing transactionControl attribute set to VALID_CORRESPONDING_TRANSACTION_CONTROL_VALUE } | IUT  AE1 |

Table: 7.2.2.x.y-1: valid <transaction> transactionControl values

| TP Id | TRANSACTION_STATE_VALUE | VALID_CORRESPONDING_TRANSACTION_CONTROL_VALUE |
| --- | --- | --- |
| TP/oneM2M/CSE/TMG/UPD/007_LOC | LOCKED | EXECUTE, ABORT |
| TP/oneM2M/CSE/TMG/UPD/007_EXE | EXECUTED | COMMIT, ABORT |
| TP/oneM2M/CSE/TMG/UPD/007_ERR | ERROR | ABORT, LOCK |
| TP/oneM2M/CSE/TMG/UPD/007_COM | COMMITTED | LOCK |
| TP/oneM2M/CSE/TMG/UPD/007_ABT | ABORTED | LOCK |

##### 7.2.2.x.y	DELETE Operation

TP/oneM2M/CSE/TMG/DEL/001

| TP Id | TP/oneM2M/CSE/TMG/DEL/001 |
| --- | --- |
| Test objective | Check that the IUT deletes RESOURCE_TYPE resource when transactionState is either "COMMITTED" or "ABORTED". |
| Reference | TS-0004 [2], clause 7.4.61.2.4, 7.4.60.2.4 |
| Config Id | CF02 |
| Parent Release | Release 4 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE containing transactionState set to "COMMITTED" or "ABORTED" and the AE having privileges to perform DELETE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid DELETE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and no Content } | IUT  AE |
|  | then { the IUT deletes the RESOURCE_TYPE resource and sends a valid Response containing Response Status Code set to 2002 (DELETED) } | IUT  AE |

| TP ID | RESOURCE_TYPE |
| --- | --- |
| TP/oneM2M/CSE/TMG/DEL/001_TRAM_COM | 50 (transactionMgmt) |
| TP/oneM2M/CSE/TMG/DEL/001_TRAM_ABT | 50 (transactionMgmt) |
| TP/oneM2M/CSE/TMG/DEL/001_TRAC_COM | 51 (transaction) |
| TP/oneM2M/CSE/TMG/DEL/001_TRAC_ABT | 51 (transaction) |

---------------------- End of new text 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?