| CHANGE REQUEST |
| --- |
| Meeting:* | TDE #50 |
| Source:* | TF-oneM2M |
| Date:* | 2021-05-21 |
| Contact:* | Siddharth Trikha, C-DOT, strikha@cdot.in |
| Reason for Change/s:* | New TPs for Semantics based operations release 3 |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018-V-3.8.1 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: TDE-2021-0033-New_TestPurposes_Semantics_R4 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution introduces new TPs for Semantics CSF which were missing as per TS-0004 and TS-0034 documents.

----------------------- Start of change 1 -----------------------

TP/oneM2M/CSE/SEM/RET/015

| TP Id | TP/oneM2M/CSE/SEM/RET/015 |
| --- | --- |
| Test objective | Check that the IUT returns successfully the attributes of the <semanticDescriptor> resource except the semanticOpEx attribute. |
| Reference | TS-0004 [2], clause 7.4.34.2.2,, TS-0001 [1], clause 9.6.30 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <semanticDescriptor> resource at TARGET_RESOURCE_ADDRESS containing accessControlPolicyIDs attribute set to allow the AE privileges to perform RETRIEVE operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and no Content } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Content containing attributes of resource representation ensuring that the semanticOpExec attribute is never returned in the response. } | IUT  AE |

TP/oneM2M/CSE/SEM/CRE/017

| TP Id | TP/oneM2M/CSE/SEM/CRE/017 |
| --- | --- |
| Test objective | Check that the IUT generates a Response Status Code indicating a “ONTOLOGY_NOT_AVAILABLE” error when referenced ontology of the local linked <semanticDescriptor> resources cannot be retrieved during a semantic validation process. |
| Reference | TS-0004 [2], clause 7.4.34.2.1 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS and the IUT having a local policy that allows semantic validation procedures } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 24 (semanticDescriptor) and From set to AE-ID and Content containing <semanticDescriptor> resource representation containing validationEnable attribute set to “True” and relatedSemantics attribute is set or descriptor attribute contains triples having annotation property m2m:resourceDescriptorLink and linked <semanticDescriiptor> resources has an ontologyRef attribute set to a non-resolvable URI } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4118 (ONTOLOGY_NOT_AVAILABLE) } | IUT  AE |

TP/oneM2M/CSE/SEM/CRE/018

| TP Id | TP/oneM2M/CSE/SEM/CRE/018 |
| --- | --- |
| Test objective | Check that the IUT generates a Response Status Code indicating a “INVALID_SEMANTICS” error when any aspect of the semantic validation process fails (according to clause 7.10.3.7.10.4 in TS-0034[6] ). |
| Reference | TS-0004 [2], clause 7.4.34.2.1, TS-0034 [6], clause 7.10.3, 7.10.4 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS and the IUT having a local policy that allows semantic validation procedures } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 24 (semanticDescriptor) and From set to AE-ID and Content containing <semanticDescriptor> resource representation containing validationEnable attribute set to “True” and descriptor attribute contains invalid RDF triples or if relatedSemantics attribute is set and any related <semanticDescriptor> contains invalid triples. } | iIUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4120 (INVALID_SEMANTICS) } | IUT  AE |

## ---------------------- End of change 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?