| CHANGE REQUEST |
| --- |
| Meeting ID:* | TDE #50.2 |
| Source:* | Rahul, C-DOT, krahul@cdot.in Anupama, C-DOT, anupama@cdot.in Poornima, C-DOT, poornima@cdot.in |
| Date:* | 2021-07-14 |
| Reason for Change/s:* | See the introduction |
| CR against: Release* | Release 4 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018 V4.4.0 |
| Clauses * | 7.2.2.18, 7.2.2.3.5, 7.2.2.2.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2020 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

If this is  a correction, and the change applies to previous releases, a separate “mirror CR” should be posted at the same time as this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made e.g. a change impacting 5 tables should not only include a proposal to change only 3 tables. Include any changes to references, definitions, and abbreviations in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar.

Use change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the proposed new clause is located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to the content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposes to add TPs for service subscription management functionality.

### -----------------------Start of change 1-------------------------------------------

##### 7.2.2.18.2	Service Subscription Profile(SSP)

TP/oneM2M/CSE/SSM/SSP/001

| TP Id | TP/oneM2M/CSE/SSM/SSP/001 |
| --- | --- |
| Test objective | Check that the IUT successfully performs operations on resource m2mServiceSubscriptionProfile for authorized AE |
| Reference | TS-0001 [1], clauses 9.6.19 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_IN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform OPERATION on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to authorized AE-ID } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status set to RESPONSE_STATUS_CODE } | IUT  AE |

| TP Id | OPERATION | RESPONSE_STATUS_CODE |
| --- | --- | --- |
| TP/oneM2M/CSE/SSM/SSP/001_CRE | CREATE | 2001 (CREATED) |
| TP/oneM2M/CSE/SSM/SSP/001_RET | RETRIEVE | 2000 (OK) |
| TP/oneM2M/CSE/SSM/SSP/001_UPD | UPDATE | 2004 (UPDATED) |
| TP/oneM2M/CSE/SSM/SSP/001_DEL | DELETE | 2002 (DELETED) |

7.2.2.18.2.1	UPDATE

TP/oneM2M/CSE/SSM/SSP/UPD/001

| TP Id | TP/oneM2M/CSE/SSM/SSP/UPD/001 |
| --- | --- |
| Test objective | Check that the IUT updates the value of the attributes activationTime, status, deactivationTime in <m2mserviceSubscriptionProfile> resource when activate attribute is set to TRUE in resource representation of UPDATE request |
| Reference | TS-0001 [1], clauses 9.6.19, TS-0004[2], clauses 7.4.19.2.3 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_IN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform UPDATE on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to authorized AE-ID Content containing m2mServiceSubscriptionProfile resource containing activate attribute set to TRUE } | IUT  AE |
|  | then { the IUT updates the TARGET_RESOURCE_ADDRESS resource and the IUT sends a valid Response containing Response Status Code set to 2004 (UPDATED) and Content containing m2mServiceSubscriptionProfile resource containing activate attribute set to TRUE activationTime attribute set to Current Time deactivationTime attribute set to Null status attribute set to ACTIVE } | IUT  AE |

TP/oneM2M/CSE/SSM/SSP/UPD/002

| TP Id | TP/oneM2M/CSE/SSM/SSP/UPD/002 |
| --- | --- |
| Test objective | Check that the IUT updates the value of the attributes deactivationTime, status when activate attribute is set to FALSE in resource representation of UPDATE request |
| Reference | TS-0001 [1], clauses 9.6.19, TS-0004[2], clauses 7.4.19.2.3 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_IN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform UPDATE on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to authorized AE-ID Content containing m2mServiceSubscriptionProfile resource containing activate attribute set to FALSE } | IUT  AE |
|  | then { the IUT updates the TARGET_RESOURCE_ADDRESS resource and the IUT sends a valid Response containing Response Status Code set to 2004 (UPDATED) and Content containing m2mServiceSubscriptionProfile resource containing activate attribute set to FALSE deactivationTime attribute set to Current Time status attribute set to INACTIVE } | IUT  AE |

TP/oneM2M/CSE/SSM/SSP/UPD/003

| TP Id | TP/oneM2M/CSE/SSM/SSP/UPD/003 |
| --- | --- |
| Test objective | Check that the IUT overrides the value of the attribute ATTRIBUTE_NAME with the current limit when the value provided in the resource representation of the UPDATE request is less than the current limit. |
| Reference | TS-0001 [1], clauses 9.6.19, TS-0004[2], clauses 7.4.19.2.3 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_IN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a <m2mServiceSubscriptionProfile> resource at TARGET_RESOURCE_ADDRESS containing ATTRIBUTE_NAME attribute set to MAX_VALUE and the IUT having the current limit VALUE_1 corresponding to this ATTRIBUTE_NAME and the AE having privileges to perform UPDATE on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to authorized AE-ID Content containing m2mServiceSubscriptionProfile resource containing ATTRIBUTE_NAME attribute set to value less than VALUE_1. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2004 (UPDATED) and Content containing m2mServiceSubscriptionProfile resource containing ATTRIBUTE_NAME attribute set to VALUE_1 } | IUT  AE |

| TP Id | ATTRIBUTE_NAME |
| --- | --- |
| TP/oneM2M/CSE/SSM/SSP/UPD/003_MAE | maxNumAEs |
| TP/oneM2M/CSE/SSM/SSP/UPD/003_MND | maxNumNodes |
| TP/oneM2M/CSE/SSM/SSP/UPD/003_MNB | maxNumBytes |
| TP/oneM2M/CSE/SSM/SSP/UPD/003_MNU | maxNumUsers |
| TP/oneM2M/CSE/SSM/SSP/UPD/003_MRR | maxRequestRate |
| TP/oneM2M/CSE/SSM/SSP/UPD/003_MNC | maxNumContainers |
| TP/oneM2M/CSE/SSM/SSP/UPD/003_MIC | maxNumInstancesPerContainer |
| TP/oneM2M/CSE/SSM/SSP/UPD/003_MNT | maxNumTimeSeries |
| TP/oneM2M/CSE/SSM/SSP/UPD/003_MIT | maxNumInstancesPerTimeSeries |
| TP/oneM2M/CSE/SSM/SSP/UPD/003_MMG | maxMembersPerGroup |
| TP/oneM2M/CSE/SSM/SSP/UPD/003_MNR | maxNotificationRate |
| TP/oneM2M/CSE/SSM/SSP/UPD/003_MNF | maxNumFlexContainers |
| TP/oneM2M/CSE/SSM/SSP/UPD/003_MIF | maxNumInstancesPerFlexContainer |

TP/oneM2M/CSE/SSM/SSP/UPD/004

| TP Id | TP/oneM2M/CSE/SSM/SSP/UPD/004 |
| --- | --- |
| Test objective | Check that the IUT updates successfully the value of the attribute ATTRIBUTE_NAME of the TARGET_RESOURCE_ADDRESS resource, when the value provided in the resource representation of the UPDATE request is more than the current limit. |
| Reference | TS-0001 [1], clauses 9.6.19, TS-0004[2], clauses 7.4.19.2.3 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_IN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a m2mServiceSubscriptionProfile resource at TARGET_RESOURCE_ADDRESS containing ATTRIBUTE_NAME attribute set to MAX_VALUE and the IUT having the current limit with CURRENT_VALUE corresponding to this ATTRIBUTE_NAME and the AE having privileges to perform UPDATE on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to authorized AE-ID Content containing m2mServiceSubscriptionProfile resource containing ATTRIBUTE_NAME attribute set to VALUE_1 more than CURRENT_VALUE } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2004 (UPDATED) and Content containing m2mServiceSubscriptionProfile resource containing ATTRIBUTE_NAME attribute set to VALUE_1 } | IUT  AE |

| TP Id | ATTRIBUTE_NAME |
| --- | --- |
| TP/oneM2M/CSE/SSM/SSP/UPD/004_MAE | maxNumAEs |
| TP/oneM2M/CSE/SSM/SSP/UPD/004_MND | maxNumNodes |
| TP/oneM2M/CSE/SSM/SSP/UPD/004_MNB | maxNumBytes |
| TP/oneM2M/CSE/SSM/SSP/UPD/004_MNU | maxNumUsers |
| TP/oneM2M/CSE/SSM/SSP/UPD/004_MRR | maxRequestRate |
| TP/oneM2M/CSE/SSM/SSP/UPD/004_MNC | maxNumContainers |
| TP/oneM2M/CSE/SSM/SSP/UPD/004_MIC | maxNumInstancesPerContainer |
| TP/oneM2M/CSE/SSM/SSP/UPD/004_MNT | maxNumTimeSeries |
| TP/oneM2M/CSE/SSM/SSP/UPD/004_MIT | maxNumInstancesPerTimeSeries |
| TP/oneM2M/CSE/SSM/SSP/UPD/004_MMG | maxMembersPerGroup |
| TP/oneM2M/CSE/SSM/SSP/UPD/004_MNR | maxNotificationRate |
| TP/oneM2M/CSE/SSM/SSP/UPD/004_MNF | maxNumFlexContainers |
| TP/oneM2M/CSE/SSM/SSP/UPD/004_MIF | maxNumInstancesPerFlexContainer |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

##### 7.2.2.18.3	Service Subscribed App Rule

TP/oneM2M/CSE/SSM/SSAR/001

| TP Id | TP/oneM2M/CSE/SSM/SSAR/001 |
| --- | --- |
| Test objective | Check that the IUT successfully performs operations on resource seriviceSubscribedAppRule for authorized AE |
| Reference | TS-0001 [1], clauses 9.6.29, TS-0004, clauses 7.4.29 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_IN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform OPERATION on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to authorized AE-ID } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status set to RESPONSE_STATUS_CODE } | IUT  AE |

| TP Id | OPERATION | RESPONSE_STATUS_CODE |
| --- | --- | --- |
| TP/oneM2M/CSE/SSM/SSAR/001_CRE | CREATE | 2001 (CREATED) |
| TP/oneM2M/CSE/SSM/SSAR/001_RET | RETRIEVE | 2000 (OK) |
| TP/oneM2M/CSE/SSM/SSAR/001_UPD | UPDATE | 2004 (UPDATED) |
| TP/oneM2M/CSE/SSM/SSAR/001_DEL | DELETE | 2002 (DELETED) |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

##### 7.2.2.18.3	Service Subscribed Node

TP/oneM2M/CSE/SSM/SSN/001

| TP Id | TP/oneM2M/CSE/SSM/SSN/001 |
| --- | --- |
| Test objective | Check that the IUT successfully performs operations on resource seriviceSubscribedNode for authorized AE |
| Reference | TS-0001 [1], clauses 9.6.20, TS-0004, clauses 7.4.20 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_IN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform OPERATION on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to authorized AE-ID } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status set to RESPONSE_STATUS_CODE } | IUT  AE |

| TP Id | OPERATION | RESPONSE_STATUS_CODE |
| --- | --- | --- |
| TP/oneM2M/CSE/SSM/SSN/001_CRE | CREATE | 2001 (CREATED) |
| TP/oneM2M/CSE/SSM/SSN/001_RET | RETRIEVE | 2000 (OK) |
| TP/oneM2M/CSE/SSM/SSN/001_UPD | UPDATE | 2004 (UPDATED) |
| TP/oneM2M/CSE/SSM/SSN/001_DEL | DELETE | 2002 (DELETED) |

TP/oneM2M/CSE/SSM/SSN/CRE/001

| TP Id | TP/oneM2M/CSE/SSM/SSN/CRE/001 |
| --- | --- |
| Test objective | Check that the IUT rejects CREATE request If the ruleLinks attribute is present in the resource representation, but the CSE-ID attribute is not present in the resource representation of <serviceSubscribedNode> resource |
| Reference | TS-0001 [1], clauses 9.6.20, TS-0004 [2], clause 7.4.20.2.1 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_IN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE OPERATION on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to authorized AE-ID Content containing serviceSubscribedNode resource containing ruleLinks attribute set to valid value and CSE-ID attribute Not set } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status set to 4000 (BAD Request) } | IUT  AE |

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4-------------------------------------------

##### 7.2.2.3.5	BASIC Operation

TP/oneM2M/CSE/DMR/001

| TP Id | TP/oneM2M/CSE/DMR/001 |
| --- | --- |
| Test objective | Check that the IUT retargets the request to the hosting CSE when the To parameter contains the hosting CSE-ID which is known by the IUT (a descendant CSE or its Registrar CSE) |
| Reference | TS-0001 [1], clause 8.2.1.1 |
| Config Id | CF02 |
| Parent Release | Release 2 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered to a Hosting CSE and the IUT having registered the AE and the Hosting CSE containing a resource representation on TARGET_RESOURCE_ADDRESS and the AE having privileges to perform OPERATION on the Hosting CSE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Request from the AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID } | IUT  AE |
|  | then { the IUT sends a OPERATION Request to the Hosting CSE } | IUT  CSE |

| TP Id | OPERATION |
| --- | --- |
| TP/oneM2M/CSE/DMR/001_CRE | CREATE |
| TP/oneM2M/CSE/DMR/001_RET | RETRIEVE |
| TP/oneM2M/CSE/DMR/001_UPD | UPDATE |
| TP/oneM2M/CSE/DMR/001_DEL | DELETE |

TP/oneM2M/CSE/DMR/002

| TP Id | TP/oneM2M/CSE/DMR/002 |
| --- | --- |
| Test objective | Check that the IUT retargets the response from the hosting CSE after retargeting an OPERATION Request |
| Reference | TS-0001 [1], clause 8.2.1.1 |
| Config Id | CF02 |
| Parent Release | Release 2 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered to the Hosting CSE and the IUT having registered the AE and the Hosting CSE containing a resource representation on TARGET_RESOURCE_ADDRESS and the AE having privileges to perform OPERATION on the Hosting CSE and the IUT having received a valid OPERATION Request from the AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and the IUT sends the OPERATION Request to the Hosting CSE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Response from the Hosting CSE } | IUT  CSE |
|  | then { the IUT sends a valid Response to the AE } | IUT  AE |

| TP Id | OPERATION |
| --- | --- |
| TP/oneM2M/CSE/DMR/002_CRE | CREATE |
| TP/oneM2M/CSE/DMR/002_RET | RETRIEVE |
| TP/oneM2M/CSE/DMR/002_UPD | UPDATE |
| TP/oneM2M/CSE/DMR/002_DEL | DELETE |

TP/oneM2M/CSE/DMR/003

| TP Id | TP/oneM2M/CSE/DMR/003 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the AE not having service subscription tries to perform OPERATION on the resource TARGET_RESOURCE_ADDRESS |
| Reference | TS-0004 [2], clause 7.3.2.1, clause 7.3.2.7 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT not having a m2mServiceSubscriptionProfile resource For the AE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to authorized AE-ID } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status set to 4128 (SERVICE_SUBSCRIPTION_NOT_ESTABLISHED) } | IUT  CSE |

TP/oneM2M/CSE/DMR/004

| TP Id | TP/oneM2M/CSE/DMR/004 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the AE having inactive service subscription tries to perform OPERATION on the resource TARGET_RESOURCE_ADDRESS |
| Reference | TS-0004 [2], clause 7.3.2.1, clause 7.3.2.7 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having a m2mServiceSubscriptionProfile resource For the AE containing status attribute set to INACTIVE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Requests from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to authorized AE-ID } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status set to 4139 (SERVICE_SUBSCRIPTION_NOT_ACTIVE) } | IUT  CSE |

TP/oneM2M/CSE/DMR/005

| TP Id | TP/oneM2M/CSE/DMR/005 |
| --- | --- |
| Test objective | Check that the IUT successfully performs OPERATION on the resource TARGET_RESOURCE_ADDRESS for an authorized AE having an active service subscription |
| Reference | TS-0004 [2], clause 7.3.2.1 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a m2mServiceSubscriptionProfile resource For the AE containing status attribute set to ACTIVE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to authorized AE-ID } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status set to RESPONSE_STATUS_CODE } | IUT  CSE |

| TP Id | OPERATION | RESPONSE_STATUS_CODE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/005_CRE | CREATE | 2001 (CREATED) |
| TP/oneM2M/CSE/DMR/005_RET | RETRIEVE | 2000 (OK) |
| TP/oneM2M/CSE/DMR/005_UPD | UPDATE | 2004 (UPDATED) |
| TP/oneM2M/CSE/DMR/005_DEL | DELETE | 2002 (DELETED) |

TP/oneM2M/CSE/DMR/006

| TP Id | TP/oneM2M/CSE/DMR/006 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the authorized AE exceeds the request rate limit specified in its service subscription profile |
| Reference | TS-0004 [2], clause 7.3.2.x |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a m2mServiceSubscriptionProfile resource For the AE containing maxRequestRate attribute set to MAX_REQUEST_RATE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Request at a rate higher than MAX_REQUEST_RATE from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to authorized AE-ID } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status set to 413x (SERVICE_SUBSCRIPTION_LIMITS_EXCEEDED) } | IUT  CSE |

TP/oneM2M/CSE/DMR/007

| TP Id | TP/oneM2M/CSE/DMR/007 |
| --- | --- |
| Test objective | Check that the IUT responds successfully when the authorized AE sends requests within the request rate limit specified in its service subscription profile |
| Reference | TS-0004 [2], clause 7.3.2.x |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a m2mServiceSubscriptionProfile resource For the AE containing maxRequestRate attribute set to MAX_REQUEST_RATE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Request at a rate less than MAX_REQUEST_RATE from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to authorized AE-ID } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status set to RESPONSE_STATUS_CODE } | IUT  CSE |

| TP Id | OPERATION | RESPONSE_STATUS_CODE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/007_CRE | CREATE | 2001 (CREATED) |
| TP/oneM2M/CSE/DMR/007_RET | RETRIEVE | 2000 (OK) |
| TP/oneM2M/CSE/DMR/007_UPD | UPDATE | 2004 (UPDATED) |
| TP/oneM2M/CSE/DMR/007_DEL | DELETE | 2002 (DELETED) |

TP/oneM2M/CSE/DMR/008

| TP Id | TP/oneM2M/CSE/DMR/008 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the authorized AE having exceeded the limit for ATTRIBUTE_NAME in its m2mServiceSubscriptionProfile resource tries to perform OPERATION on the resource TARGET_RESOURCE_ADDRESS |
| Reference | TS-0004 [2], clause 7.3.3.x |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a m2mServiceSubscriptionProfile resource For the AE containing ATTRIBUTE_NAME attribute set to MAX_VALUE and the IUT having the current limit with CURRENT_VALUE corresponding to this ATTRIBUTE_NAME more than MAX_VALUE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to authorized AE-ID } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status set to 413x (SERVICE_SUBSCRIPTION_LIMITS_EXCEEDED) } | IUT  CSE |

| TP Id | ATTRIBUTE_NAME |
| --- | --- |
| TP/oneM2M/CSE/SSM/SSP/UPD/008_MAE | maxNumAEs |
| TP/oneM2M/CSE/SSM/SSP/UPD/008_MND | maxNumNodes |
| TP/oneM2M/CSE/SSM/SSP/UPD/008_MNB | maxNumBytes |
| TP/oneM2M/CSE/SSM/SSP/UPD/008_MNU | maxNumUsers |
| TP/oneM2M/CSE/SSM/SSP/UPD/008_MRR | maxRequestRate |
| TP/oneM2M/CSE/SSM/SSP/UPD/008_MNC | maxNumContainers |
| TP/oneM2M/CSE/SSM/SSP/UPD/008_MIC | maxNumInstancesPerContainer |
| TP/oneM2M/CSE/SSM/SSP/UPD/008_MNT | maxNumTimeSeries |
| TP/oneM2M/CSE/SSM/SSP/UPD/008_MIT | maxNumInstancesPerTimeSeries |
| TP/oneM2M/CSE/SSM/SSP/UPD/008_MMG | maxMembersPerGroup |
| TP/oneM2M/CSE/SSM/SSP/UPD/008_MNR | maxNotificationRate |
| TP/oneM2M/CSE/SSM/SSP/UPD/008_MNF | maxNumFlexContainers |
| TP/oneM2M/CSE/SSM/SSP/UPD/008_MIF | maxNumInstancesPerFlexContainer |

TP/oneM2M/CSE/DMR/009

| TP Id | TP/oneM2M/CSE/DMR/009 |
| --- | --- |
| Test objective | Check that the IUT responds successfully when the authorized AE having not exceeded the limit for ATTRIBUTE_NAME in its m2mServiceSubscriptionProfile resource tries to perform OPERATION on the resource TARGET_RESOURCE_ADDRESS |
| Reference | TS-0004 [2], clause 7.3.3.x |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a m2mServiceSubscriptionProfile resource For the AE containing ATTRIBUTE_NAME attribute set to MAX_VALUE and the IUT having the current limit corresponding to this ATTRIBUTE_NAME with CURRENT_VALUE less than MAX_VALUE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to authorized AE-ID } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status set to RESPONSE_STATUS_CODE } | IUT  CSE |

| TP Id | ATTRIBUTE_NAME |
| --- | --- |
| TP/oneM2M/CSE/SSM/SSP/UPD/009_MAE | maxNumAEs |
| TP/oneM2M/CSE/SSM/SSP/UPD/009_MND | maxNumNodes |
| TP/oneM2M/CSE/SSM/SSP/UPD/009_MNB | maxNumBytes |
| TP/oneM2M/CSE/SSM/SSP/UPD/009_MNU | maxNumUsers |
| TP/oneM2M/CSE/SSM/SSP/UPD/009_MRR | maxRequestRate |
| TP/oneM2M/CSE/SSM/SSP/UPD/009_MNC | maxNumContainers |
| TP/oneM2M/CSE/SSM/SSP/UPD/009_MIC | maxNumInstancesPerContainer |
| TP/oneM2M/CSE/SSM/SSP/UPD/009_MNT | maxNumTimeSeries |
| TP/oneM2M/CSE/SSM/SSP/UPD/009_MIT | maxNumInstancesPerTimeSeries |
| TP/oneM2M/CSE/SSM/SSP/UPD/009_MMG | maxMembersPerGroup |
| TP/oneM2M/CSE/SSM/SSP/UPD/009_MNR | maxNotificationRate |
| TP/oneM2M/CSE/SSM/SSP/UPD/009_MNF | maxNumFlexContainers |
| TP/oneM2M/CSE/SSM/SSP/UPD/009_MIF | maxNumInstancesPerFlexContainer |

### -----------------------End of change 4---------------------------------------------

### -----------------------Start of change 5-------------------------------------------

##### 7.2.2.2.2	CREATE Operation

……..

TP/oneM2M/CSE/REG/CRE/031

| TP Id | TP/oneM2M/CSE/REG/CRE/031 |
| --- | --- |
| Test objective | Check that the IUT accepts an AE registration (S-AE-ID-STEM not provided by AE), communication between MN-CSE and IN-CSE |
| Reference | TS-0001 [1], clause 10.1.1.2.2 case a, TS-0004 [2], clause 7.4.5.2.1 |
| Config Id | CF04 |
| Parent Release | Release 2 |
| PICS Selection | PICS_IN_CSE |
| Initial conditions | with { the IUT being in the "initial state" } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from MN-CSE containing Resource Type set to 10002 (AEAnnc) and From set to SP-RELATIVE-AE-ID and Content containing AEAnnc resource containing link attribute set to SP-RELATIVE-AE-ID and labels indicating ‘Credential-ID:None’ } | IUT ( MN-CSE |
|  | then { the IUT creates the AEANNC_RESOURCE_ADDRESS resource and the IUT sends a valid Response to CSE containing Response Status Code set to 2001 (CREATED) and Content containing AEAnnc resource containing link attribute set to SP-RELATIVE-AE-ID* and labels indicating ‘Credential-ID:None’ } | IUT ( MN-CSE |
| NOTE: SP-RELATIVE-AE-ID = {SP-RELATIVE-CSE-ID}/{AE-ID-STEM} SP-RELATIVE-AE-ID* = {SP-RELATIVE-CSE-ID}/{S-AE-ID-STEM} AE-ID-STEM = “S” S-AE-ID-STEM = Valid AE-ID-Stem starting with “S” |

TP/oneM2M/CSE/REG/CRE/032

| TP Id | TP/oneM2M/CSE/REG/CRE/032 |
| --- | --- |
| Test objective | Check that the IUT rejects an AE registration for CSEs for which the associated <serviceSubscribeNode> resource is not linked with the <serviceSubscribedAppRule> via the ruleLinks attribute of the <serviceSubscribedNode> resource |
| Reference | TS-0001 [1], clause 10.2.2.1 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having the serviceSubscribedNode resource For the CSE containing ruleLinks attribute not set } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing Resource Type set to 2 (AE) } | IUT ( AE |
|  | then { the IUT does not create the AE resource and the IUT sends a valid Response containing Response Status Code set to 4126(APP_RULE_VALIDATION_FAILED) } | IUT ( AE |

### -----------------------End of change 5---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?