| CHANGE REQUEST |
| --- |
| Meeting ID:* | TDE 50.3 |
| Source:* | oneM2M-TF |
| Date:* | 2021-08-05 |
| Reason for Change/s:* | Process Management test purposes |
| CR against: Release* | Rel-4 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018 v4.3.0 |
| Clauses * | New clause |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2019 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution introduces test case for Process Management resources as per TS-0004 and TS-0001 documents.

----------------------- Start of change 1 -----------------------

#### 7.2.2.x	Process Management(PMG)

- 7.2.2.x.y 	Create Operation

- TP/oneM2M/CSE/PMG/CRE/001

| TP Id | TP/oneM2M/CSE/PMG/CRE/001 |
| --- | --- |
| Test objective | Check that the IUT creates <processManagement> resource. |
| Reference | TS-0004 [2] clause 7.4.XX.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <cseBase> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to XX (processManagement) and From set to AE-ID and Content containing processManagement resource } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 2001 (CREATED) and Content containing processManagement resource containing processStatus attribute set to value “Disabled” and currentState set to NULL. } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/002

| TP Id | TP/oneM2M/CSE/PMG/CRE/002 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <state> resource when processStatus attribute of parent <processManagement> has value not equal to “Disabled”. |
| Reference | TS-0004 [2] clause 7.4.XX.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <processManagement> resource at TARGET_RESOURCE_ADDRESS having processStatus attribute set to value not equal to “Disabled” and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to XX (state) and From set to AE-ID and Content containing state resource } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/003

| TP Id | TP/oneM2M/CSE/PMG/CRE/003 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <state> resource when some referenced <state> resources in stateTransitions attribute don’t exist. |
| Reference | TS-0004 [2] clause 7.4.XX.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <processManagement> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to XX (state) and From set to AE-ID and Content containing state resource having stateTransitions attribute set to some non-existing state resources } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/004

| TP Id | TP/oneM2M/CSE/PMG/CRE/004 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <state> resource when for some referenced <state> resources in stateTransitions attributes Originator don’t have retrieve privilege. |
| Reference | TS-0004 [2] clause 7.4.XX.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <processManagement> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to XX (state) and From set to AE-ID and Content containing state resource having stateTransitions attribute set to some state resources Originator don’t have retrieve privilege. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/005

| TP Id | TP/oneM2M/CSE/PMG/CRE/005 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <state> resource when some referenced <state> resources in stateTransitions attributes are not child resources of parent <processManagement>. |
| Reference | TS-0004 [2] clause 7.4.XX.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <processManagement> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to XX (state) and From set to AE-ID and Content containing state resource having stateTransitions attribute set to some state resources not child resources of TARGET_RESOURCE_ADDRESS resource. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/006

| TP Id | TP/oneM2M/CSE/PMG/CRE/006 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <action> resource when resource referenced by subjectResourceID attribute doesn’t exist. |
| Reference | TS-0004 [2] clause 7.4.73.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <cseBase> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 63 (action) and From set to AE-ID and Content containing action resource having subjectResourceID set to not-existing resourceID. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/007

| TP Id | TP/oneM2M/CSE/PMG/CRE/007 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <action> resource when resource referenced by subjectResourceID attribute is not accessible to it. |
| Reference | TS-0004 [2] clause 7.4.73.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <cseBase> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 63 (action) and From set to AE-ID and Content containing action resource having subjectResourceID set to non-accessible resourceID. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/008

| TP Id | TP/oneM2M/CSE/PMG/CRE/008 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <action> resource when resource referenced by objectResourceID attribute doesn’t exist. |
| Reference | TS-0004 [2] clause 7.4.73.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <cseBase> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 63 (action) and From set to AE-ID and Content containing action resource having objectResourceID set to not-existing resourceID. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/009

| TP Id | TP/oneM2M/CSE/PMG/CRE/009 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <action> resource when resource referenced by objectResourceID attribute is not accessible to it. |
| Reference | TS-0004 [2] clause 7.4.73.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <cseBase> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 63 (action) and From set to AE-ID and Content containing action resource having objectResourceID set to non-accessible resourceID. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/010

| TP Id | TP/oneM2M/CSE/PMG/CRE/010 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <action> resource when From parameter in actionPrimitive attribute is not same as Originator of create request. |
| Reference | TS-0004 [2] clause 7.4.73.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <cseBase> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 63 (action) and From set to AE-ID and Content containing action resource having actionPrimitive set having From parameter not same as Originator of create request. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/011

| TP Id | TP/oneM2M/CSE/PMG/CRE/011 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <action> resource when evalMode attribute has value either “off” or “once” and evalControlParam attribute is also set. |
| Reference | TS-0004 [2] clause 7.4.73.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <cseBase> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 63 (action) and From set to AE-ID and Content containing action resource having evalMode set to “off” or “once” and evalControlParam also set. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/012

| TP Id | TP/oneM2M/CSE/PMG/CRE/012 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <action> resource when subject element of evalCriteria attribute is not an attribute of resource type referenced by subjectResourceID attribute. |
| Reference | TS-0004 [2] clause 7.4.73.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <cseBase> resource at TARGET_RESOURCE_ADDRESS and the IUT having child <container> resource at CHILD_ADDRESS and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 63 (action) and From set to AE-ID and Content containing action resource having subjectResourceID set to CHILD_ADDRESS evalCriteria attribute set having subject element not matching CHILD_ADDRESS attributes. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/013

| TP Id | TP/oneM2M/CSE/PMG/CRE/013 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <action> resource when subjectResourceID attribute not set and subject element of evalCriteria attribute is not an attribute of the parent resource type. |
| Reference | TS-0004 [2] clause 7.4.73.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <cseBase> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 63 (action) and From set to AE-ID and Content containing action resource having subjectResourceID not set evalCriteria attribute set having subject element not matching TARGET_RESOURCE_ADDRESS attributes. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/014

| TP Id | TP/oneM2M/CSE/PMG/CRE/014 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <action> resource when threshold element of evalCriteria is outside value space of data type of subject element. |
| Reference | TS-0004 [2] clause 7.4.73.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <cseBase> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 63 (action) and From set to AE-ID and Content containing action resource having evalCriteria attribute set and subject element set and threshold element set outside value space of data type of subject attribute. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/015

| TP Id | TP/oneM2M/CSE/PMG/CRE/015 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <action> resource when operator element of evalCriteria has invalid value. |
| Reference | TS-0004 [2] clause 7.4.73.2.1, Table 6.3.4.2.86-1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <cseBase> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 63 (action) and From set to AE-ID and Content containing action resource having evalCriteria attribute set and operator set to invalid value. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/016

| TP Id | TP/oneM2M/CSE/PMG/CRE/016 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <dependency> resource when resource defined by referencedResourceID attribute doesn’t exist. |
| Reference | TS-0004 [2] clause 7.4.74.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <action> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Resource Type set to 64 (dependency) and Content containing dependency resource having referencedResourceID set to not-existing resourceID. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/017

| TP Id | TP/oneM2M/CSE/PMG/CRE/017 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <dependency> resource when Originator doesn’t have retrieve privilege on resource defined by referencedResourceID attribute. |
| Reference | TS-0004 [2] clause 7.4.74.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <action> resource at TARGET_RESOURCE_ADDRESS and the IUT having <container> resource at CHILD_ADDRESS not accessible to AE and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Resource Type set to 64 (dependency) and Content containing dependency resource having referencedResourceID set to CHILD_ADDRESS. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/018

| TP Id | TP/oneM2M/CSE/PMG/CRE/018 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <dependency> resource when attribute referenced by subject element of evalCriteria attribute of request is not an attribute of resource type referenced by referencedResourceID attribute. |
| Reference | TS-0004 [2] clause 7.4.74.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <action> resource at TARGET_RESOURCE_ADDRESS and the IUT having <container> resource at CHILD_ADDRESS accessible to AE and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Resource Type set to 64 (dependency) and Content containing dependency resource having referencedResourceID set to CHILD_ADDRESS and evalCriteria set having subject element set not to one of the attributes of CHILD_ADDRESS } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/019

| TP Id | TP/oneM2M/CSE/PMG/CRE/019 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <dependency> resource when value of threshold element of evalCriteria attribute is outside the value space of data type of subject element of evalCriteria. |
| Reference | TS-0004 [2] clause 7.4.74.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <action> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Resource Type set to 64 (dependency) and Content containing dependency resource having evalCriteria set having subject element set and threshold element set to value outside value range of referenced attribute data type of subject element. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/020

| TP Id | TP/oneM2M/CSE/PMG/CRE/020 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <dependency> resource when value of operator element is invalid. |
| Reference | TS-0004 [2] clause 7.4.74.2.1, Table 6.3.4.2.86 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <action> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Resource Type set to 64 (dependency) and Content containing dependency resource having evalCriteria set having operator element set to invalid value. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

7.2.2.x.y 	Update Operation

TP/oneM2M/CSE/PMG/UPD/001

| TP Id | TP/oneM2M/CSE/PMG/UPD/001 |
| --- | --- |
| Test objective | Check that the IUT rejects update of activateConditions attribute of <processManagement> resource when the processStatus attribute has value not equal to “Disabled”. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and and the IUT having a <processManagement> at TARGET_RESOURCE_ADDRESS having processStatus attribute set value not equal to “Disabled” and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing activateConditions attribute having value set. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/002

| TP Id | TP/oneM2M/CSE/PMG/UPD/002 |
| --- | --- |
| Test objective | Check that the IUT rejects update of endConditions attribute of <processManagement> resource when the processStatus attribute has value not equal to “Disabled”. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <processManagement> at TARGET_RESOURCE_ADDRESS having processStatus attribute set to value not equal to “Disabled” and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing endConditions attribute having value set. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/003

| TP Id | TP/oneM2M/CSE/PMG/UPD/003 |
| --- | --- |
| Test objective | Check that the IUT rejects update of initialState attribute of <processManagement> resource when the processStatus attribute has value not equal to “Disabled”. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <processManagement> at TARGET_RESOURCE_ADDRESS having processStatus attribute set not equal to “Disabled” and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing initialState attribute having value set. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/004

| TP Id | TP/oneM2M/CSE/PMG/UPD/004 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when originator don’t have retrieve privilege on the resources or attributes referred by subject element of the evalCriteria of activateConditions attribute . |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <processManagement> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform UPDATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing activateConditions attribute having evalCriteria attribute having subject attribute set to resource not having retrieve privilege to originator. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/005

| TP Id | TP/oneM2M/CSE/PMG/UPD/005 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when the resources or attributes referred by subject attribute of evalCriteria parameters of activateConditions attribute do not exist. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <processManagement> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform UPDATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing activateConditions attribute having evalCriteria attribute having subject attribute set to non-existing resource } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/006

| TP Id | TP/oneM2M/CSE/PMG/UPD/006 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when originator don’t have retrieve privilege on the resources or attributes referred by subject attribute of evalCriteria parameters of endConditions attribute . |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <processManagement> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform UPDATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing endConditions attribute having evalCriteria attribute having subject attribute set to resource not having retrieve privilege to the originator. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/007

| TP Id | TP/oneM2M/CSE/PMG/UPD/007 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when the resources or attributes referred by subject attribute of evalCriteria parameters of endConditions attribute do not exist. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <processManagement> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform UPDATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing endConditions attribute having evalCriteria attribute having subject attribute set to non-existing resource } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/008

| TP Id | TP/oneM2M/CSE/PMG/UPD/008 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when the evalCriteria of activateConditions has threshold parameter value not within the value space of the data type of the subject parameter. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <processManagement> resource at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing activateConditions attribute having evalCriteria attribute having threshold set to out of range value. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/009

| TP Id | TP/oneM2M/CSE/PMG/UPD/009 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when the evalCriteria of activateConditions has invalid value in operator attribute. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3, Table 6.3.4.2.86-1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource <processManagement> at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing activateConditions attribute having evalCriteria attribute having operator set to invalid value. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/010

| TP Id | TP/oneM2M/CSE/PMG/UPD/010 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when the evalCriteria of endConditions has threshold parameter value not within the value space of the data type of the subject parameter. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource <processManagement> at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing endConditions attribute having evalCriteria attribute having threshold set to out of range value. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/011

| TP Id | TP/oneM2M/CSE/PMG/UPD/011 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when the evalCriteria of endConditions has invalid value in operator attribute. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 , Table 6.3.4.2.86-1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource <processManagement> at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing endConditions attribute having evalCriteria attribute having operator set to invalid value. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/012

| TP Id | TP/oneM2M/CSE/PMG/UPD/012 |
| --- | --- |
| Test objective | Check that the IUT rejects update of initialState attribute of <processManagement> resource when referred <state> resource doesn’t exist. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource <processManagement> at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing initialState set to not-existing state resourceID. . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/013

| TP Id | TP/oneM2M/CSE/PMG/UPD/013 |
| --- | --- |
| Test objective | Check that the IUT rejects update of initialState attribute of <processManagement> resource when Originator don’t have retrieve privilege on referenced <state> resource. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource <processManagement> at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing initialState set to state resourceID on which originator don’t have retrieve privilege. . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/014

| TP Id | TP/oneM2M/CSE/PMG/UPD/014 |
| --- | --- |
| Test objective | Check that the IUT rejects update of initialState attribute of <processManagement> resource when the referred resource is not the child resource of <processManagement>. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource <processManagement> at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing initialState set to state resourceID which is not child resource of TARGET_RESOURCE_ADDRESS resource. . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/015

| TP Id | TP/oneM2M/CSE/PMG/UPD/015 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when the value of the processControl attribute in the request is equal to “Enable” and the value of the processStatus attribute of the <processManagement> resource is not equal to “Disabled”. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having resource <processManagement> at TARGET_RESOURCE_ADDRESS ,processStatus set not equal to “Disabled” and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing processControl set to value “Enable”. . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/016

| TP Id | TP/oneM2M/CSE/PMG/UPD/016 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when the value of the processControl attribute in the request is equal to “Disable” and the value of the processStatus attribute of the <processManagement> resource is equal to “Disabled”. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having resource <processManagement> at TARGET_RESOURCE_ADDRESS, processStatus set to “Disabled” and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing processControl set to value “Disable”. . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/017

| TP Id | TP/oneM2M/CSE/PMG/UPD/017 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when the value of the processControl attribute in the request is equal to “Pause” and the value of the processStatus attribute of the <processManagement> resource is not equal to “Activated”. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource <processManagement> at TARGET_RESOURCE_ADDRESS, processStatus set not equal to “Activated” and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing processControl set to value “Pause”. . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/018

| TP Id | TP/oneM2M/CSE/PMG/UPD/018 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when the value of the processControl attribute in the request is equal to “Reactivate” and the value of the processStatus attribute of the <processManagement> resource is not equal to “Paused”. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource <processManagement> at TARGET_RESOURCE_ADDRESS, processStatus set not equal to “Paused” and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing processControl set to value “Reactivate”. . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/019

| TP Id | TP/oneM2M/CSE/PMG/UPD/019 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when the value of the processControl attribute in the request is equal to “Enable” and the value of the processStatus attribute of the <processManagement> resource is equal to “Disabled” when any of the referenced child resources is not available . |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having resource <processManagement> at TARGET_RESOURCE_ADDRESS, processStatus set to “Disable” and the IUT having <state> resource as child resource of TARGET_RESOURCE_ADDRESS and referenced in initialState attribute and the resource referenced by stateAction attribute is not available and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing processControl set to value “Enable”. . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/020

| TP Id | TP/oneM2M/CSE/PMG/UPD/020 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when the value of the processControl attribute in the request is equal to “Enable” and the value of the processStatus attribute of the <processManagement> resource is equal to “Disabled” but Originator don’t have required privileges on any of the referenced child resources. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having resource <processManagement> at TARGET_RESOURCE_ADDRESS, processStatus set to “Disable” and the IUT having <state> resource at STATE as child resource of TARGET_RESOURCE_ADDRESS and referred in initialState attribute and the IUT having <action> resource at ACTION as child of STATE and referenced in stateAction attribute and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS but not on all child resources. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing processControl set to value “Enable”. . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/021

| TP Id | TP/oneM2M/CSE/PMG/UPD/021 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when the value of the processControl attribute in the request is equal to “Enable” and the value of the processStatus attribute of the <processManagement> resource is equal to “Disabled” but any of referenced resources are not descendent resource of <processManagement>. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having resource <processManagement> at TARGET_RESOURCE_ADDRESS, processStatus set to “Disabled” and the IUT having <state> resource at STATE and referred in initialState attribute and the IUT having <action> resource at ACTION and referenced in stateAction attribute and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing processControl set to value “Enable”. . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION). } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/022

| TP Id | TP/oneM2M/CSE/PMG/UPD/022 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <state> resource when the processStatus attribute of parent <processManagement> has value not equal to “Disabled”. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and and the IUT having a <processManagement> resource at PARENT_RESOURCE_ ADDRESS, processStatus attribute set not equal to “Disabled” and and the IUT having a child <state> resource at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing state resource containing ATTRIBUTE attribute having value set. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  AE |

| TP Id | ATTRIBUTE |
| --- | --- |
| TP/oneM2M/CSE/PMG/UPD/022_STAC | stateAction |
| TP/oneM2M/CSE/PMG/UPD/022_STTRS | stateTransitions |

TP/oneM2M/CSE/PMG/UPD/023

| TP Id | TP/oneM2M/CSE/PMG/UPD/023 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <state> resource when the resource referenced by stateAction attribute does not exist. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <state> resource at PARENT_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing state resource containing stateAction attribute value set to non-existing resource. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/024

| TP Id | TP/oneM2M/CSE/PMG/UPD/024 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <state> resource when the Originator don’t have retrieve privilege on resource referenced by stateAction attribute. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <state> resource at PARENT_RESOURCE_ADDRESS and the IUT having a child <action> resource ACTION_ADDRESS Originator not having retrieve privilege of and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing state resource containing stateAction attribute value set to ACTION_ADDRESS. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/025

| TP Id | TP/oneM2M/CSE/PMG/UPD/025 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <state> resource when the resource referenced by stateAction attribute is not a child resource. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <state> resource at PARENT_RESOURCE_ADDRESS and the IUT having a non-child <action> resource ACTION_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing state resource containing stateAction attribute value set to ACTION_ADDRESS. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/026

| TP Id | TP/oneM2M/CSE/PMG/UPD/026 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <state> resource when the any of <state> resources referenced by stateTransitions attribute doesn’t exist. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <state> resource at PARENT_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing state resource containing stateTransitions attribute value set but some referenced <state> resources don’t exist. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/027

| TP Id | TP/oneM2M/CSE/PMG/UPD/027 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <state> resource when for any of <state> resources referenced by stateTransitions attribute Originator doesn’t have retrieve privilege. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <state> resource at PARENT_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing state resource containing stateTransitions attribute value set but for some referenced <state> resources Originator doesn’t have retrieve privilege. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/028

| TP Id | TP/oneM2M/CSE/PMG/UPD/028 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <state> resource when any of <state> resources referenced by stateTransitions attribute is not child resource of parent <processManagement>. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <processManagement> resource at PARENT_ADDRESS having the IUT having a child <state> resource at STATE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to STATE_ADDRESS and From set to AE-ID and Content containing state resource containing stateTransitions attribute value set but some referenced <state> resources are not child of PARENT_ADDRESS. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/029

| TP Id | TP/oneM2M/CSE/PMG/UPD/029 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <state> resource when any of resources and attributes referenced by subject element of evalCriteria of stateTransitions attribute doesn’t exist. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <state> resource at PARENT_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to PARENT_RESOURCE_ADDRESS and From set to AE-ID and Content containing state resource containing stateTransitions attribute set having some evalCriteria’ subject element set to non-existing resources and attributes. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/030

| TP Id | TP/oneM2M/CSE/PMG/UPD/030 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <state> resource when Originator doesn’t have retrieve privilege on any of resources and attributes referenced by subject element of evalCriteria of stateTransitions attribute. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <state> resource at PARENT_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to PARENT_RESOURCE_ADDRESS and From set to AE-ID and Content containing state resource containing stateTransitions attribute set having some evalCriteria’ subject element set to resources and attributes Originator not having retrieve privilege. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/031

| TP Id | TP/oneM2M/CSE/PMG/UPD/031 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <state> resource when threshold element of evalCriteria of stateTransitions attribute have value outside the value spaces of the data type of subject element. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <state> resource at PARENT_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to PARENT_RESOURCE_ADDRESS and From set to AE-ID and Content containing state resource containing stateTransitions attribute having some evalCriteria’ threshold element set to outside range spaces of the data type of subject element. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/032

| TP Id | TP/oneM2M/CSE/PMG/UPD/032 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <state> resource when operator element of evalCriteria of stateTransitions attribute have invalid value. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3, Table 6.3.4.2.86-1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <state> resource at PARENT_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to PARENT_RESOURCE_ADDRESS and From set to AE-ID and Content containing state resource containing stateTransitions attribute having some evalCriteria’ operator element set to invalid value. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/033

| TP Id | TP/oneM2M/CSE/PMG/UPD/033 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when resource referenced by subjectResourceID attribute doesn’t exist. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing subjectResourceID attribute set to non-existing resourceID. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/034

| TP Id | TP/oneM2M/CSE/PMG/UPD/034 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when resource referenced by subjectResourceID attribute is not accessible by Originator. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS and the IUT having child <container> at CHILD_ADDRESS not accessible by AE and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing subjectResourceID attribute set to CHILD_ADDRESS. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/035

| TP Id | TP/oneM2M/CSE/PMG/UPD/035 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when resource referenced by dependencies attribute doesn’t exist. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing dependencies attribute set to non-existing resourceID. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/036

| TP Id | TP/oneM2M/CSE/PMG/UPD/036 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when resource referenced by dependencies attribute is not accessible by Originator. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS and the IUT having child <dependency> at CHILD_ADDRESS not accessible by AE and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing dependencies attribute set to CHILD_ADDRESS. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/037

| TP Id | TP/oneM2M/CSE/PMG/UPD/037 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when resource referenced by objectResourceID attribute doesn’t exist. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing objectResourceID attribute set to non-existing resourceID. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/038

| TP Id | TP/oneM2M/CSE/PMG/UPD/038 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when resource referenced by objectResourceID attribute is not accessible by Originator. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS and the IUT having a <container> at OBJECT_ADDRESS not accessible by AE and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing objectResourceID attribute set to OBJECT_ADDRESS. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/039

| TP Id | TP/oneM2M/CSE/PMG/UPD/039 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when any of <dependency> resources referenced by dependencies attribute are not child resources. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing dependencies attribute refers some non-child <dependency>. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/040

| TP Id | TP/oneM2M/CSE/PMG/UPD/040 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when From parameter contained in actionPrimitive attribute not equal to Originator. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing actionPrimitive attribute’s From element not equal AE-ID. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/041

| TP Id | TP/oneM2M/CSE/PMG/UPD/041 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when request evalMode attribute has value “off” or “once” and request evalControlParam attribute is also set. |
| Reference | TS-0004 [2] clause 7.4.73is .2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS, evalControlParam attribute not set and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing evalMode set to “off” or “once” and evalControlParam is set. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/042

| TP Id | TP/oneM2M/CSE/PMG/UPD/042 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when request evalMode attribute has value “off” or “once” ,request evalControlParam attribute not set but evalControlParam within <action> resource has value set. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS, evalControlParam attribute set and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing evalMode set to “off” or “once” and evalControlParam is not set. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/043

| TP Id | TP/oneM2M/CSE/PMG/UPD/043 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when value of subject element of evalCriteria attribute of request is not one of the attribute of referenced resource of subjectResourceID attribute of request. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS, subjectResourceID not set and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing subjectResourceID set and evalCriteria set having subject element value not found in subjectResourceID referred resource attributes. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/044

| TP Id | TP/oneM2M/CSE/PMG/UPD/044 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when value of subject element of evalCriteria attribute of request is not one of the attribute of referenced resource of subjectResourceID attribute of <action>. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS, subjectResourceID set and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing subjectResourceID not set and evalCriteria set having subject element value set to value not found in attributes of subjectResourceID attribute of targeted <action> resource. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/045

| TP Id | TP/oneM2M/CSE/PMG/UPD/045 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when value of subject element of evalCriteria attribute of request is not one of the attribute of parent resource. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a child <action> at TARGET_RESOURCE_ADDRESS, subjectResourceID not set and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing subjectResourceID not set and evalCriteria set having subject element value set to value not found in attributes of parent AE resource. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/046

| TP Id | TP/oneM2M/CSE/PMG/UPD/046 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when value of subject element of evalCriteria attribute of target <action> resource is not one of the attribute of resource referenced by request subjectResourceID attribute.. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS, evalCriteria set and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing subjectResourceID set to resourceID not having attribute referenced by target <action> resource’s subject element of evalCriteria attribute. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/047

| TP Id | TP/oneM2M/CSE/PMG/UPD/047 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when value of threshold element of evalCriteria is not within value space of the data type of subject element of evalCriteria attribute. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing evalCriteria set having subject element set and threshold element value outside value range of subject element data type. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/048

| TP Id | TP/oneM2M/CSE/PMG/UPD/048 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when value of operator element of evalCriteria has invalid value. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 , Table 6.3.4.2.86-1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing evalCriteria set having operator element set to invalid value. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/049

| TP Id | TP/oneM2M/CSE/PMG/UPD/049 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <dependency> resource when value present in subject element of evalCriteria of request is not an attribute of resource type referenced by referencedResourceID attribute. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <dependency> at TARGET_RESOURCE_ADDRESS, referencedResourceID set and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing dependency resource containing evalCriteria set having subject element set to value not available as attribute referenced by referencedResourceID attribute. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/050

| TP Id | TP/oneM2M/CSE/PMG/UPD/050 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <dependency> resource when value present in threshold element of evalCriteria attribute of request is not within value space of data type of subject element. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <dependency> at TARGET_RESOURCE_ADDRESS, referencedResourceID set and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing dependency resource containing evalCriteria set having subject element value set and threshold element value set to value outside value range of data type of subject attribute. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/051

| TP Id | TP/oneM2M/CSE/PMG/UPD/051 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <dependency> resource when value of operator element of evalCriteria attribute of request is invalid. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 , Table 6.3.4.2.86 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <dependency> at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing dependency resource containing evalCriteria set having operator set to invalid value. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

7.2.2.x.y 	Delete Operation

TP/oneM2M/CSE/PMG/DEL/001

| TP Id | TP/oneM2M/CSE/PMG/DEL/001 |
| --- | --- |
| Test objective | Check that the IUT rejects delete of <processManagement> resource when the value of the processStatus attribute is not equal to “Disabled”. |
| Reference | TS-0004 [2] clause 7.4.XX.2.4 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource <processManagement> at TARGET_RESOURCE_ADDRESS, processStatus set not equal to “Disabled” and the AE have privilege to perform DELETE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid DELETE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  AE |

TP/oneM2M/CSE/PMG/DEL/002

| TP Id | TP/oneM2M/CSE/PMG/DEL/002 |
| --- | --- |
| Test objective | Check that the IUT rejects delete of <state> resource when the value of the stateActive attribute is equal to “true”. |
| Reference | TS-0004 [2] clause 7.4.XX.2.4 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource <state> at TARGET_RESOURCE_ADDRESS, stateActive set to “true” and the AE have privilege to perform DELETE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid DELETE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  AE |

TP/oneM2M/CSE/PMG/DEL/003

| TP Id | TP/oneM2M/CSE/PMG/DEL/003 |
| --- | --- |
| Test objective | Check that the IUT rejects delete of <state> resource when the value of the processStatus attribute of parent <processManagement> is not equal to “Disabled”. |
| Reference | TS-0004 [2] clause 7.4.XX.2.4 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource <processManagement> at PARENT_RESOURCE_ADDRESS, processStatus set not equal to “Disabled and the IUT having a resource <state> at TARGET _RESOURCE_ADDRESS and the AE have privilege to perform DELETE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid DELETE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  AE |

- ----------------------- End of change 1 -----------------------