| CHANGE REQUEST |
| --- |
| Meeting ID:* | TDE 50.3 |
| Source:* | oneM2M-TF |
| Date:* | 2021-08-05 |
| Reason for Change/s:* | Process Management test purposes |
| CR against: Release* | Rel-4 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018 v4.3.0 |
| Clauses * | New clause |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2019 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution introduces test case for Process Management resources as per TS-0004 and TS-0001 documents.

R03:

As discussed in the last call, the CR is split into 3 CRs. This CRs contains test purposes for CREATE and DELETE of process management CSF.

TARGET_RESOURCE_ADDRESS was modified to CSEBASE_RESOURCE_ADDRESS. But the changes is reverted as <action> resource may have CSEBase, remoteCSE, node, AE, container, flexContainer, group, timeSeries, transaction, state as its parent. Similary <processManagment> may have CSEBase, remoteCSE, AE as parent.

Some of the TPs are merged.

----------------------- Start of change 1 -----------------------

#### 7.2.2.x	Process Management(PMG)

- 7.2.2.x.y 	Create Operation

- TP/oneM2M/CSE/PMG/CRE/001

| TP Id | TP/oneM2M/CSE/PMG/CRE/001 |
| --- | --- |
| Test objective | Check that the IUT creates <processManagement> resource on the TARGET_RESOURCE_ADDRESS of type PARENT_RESOURCE_TYPE |
| Reference | TS-0004 [2] clause 7.4.XX.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to XX (processManagement) and From set to AE-ID and Content containing processManagement resource } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 2001 (CREATED) and Content containing processManagement resource containing processStatus attribute set to value “Disabled” and currentState set to NULL. } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/002

| TP Id | TP/oneM2M/CSE/PMG/CRE/002 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <state> resource when processStatus attribute of parent <processManagement> has value not equal to “Disabled”. |
| Reference | TS-0004 [2] clause 7.4.XX.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <processManagement> resource at TARGET_RESOURCE_ADDRESS having processStatus attribute set to value not equal to “Disabled” and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to XX (state) and From set to AE-ID and Content containing state resource } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/003

| TP Id | TP/oneM2M/CSE/PMG/CRE/003 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <state> resource when some referenced <state> resources in stateTransitions attribute don’t exist. |
| Reference | TS-0004 [2] clause 7.4.XX.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <processManagement> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to XX (state) and From set to AE-ID and Content containing state resource containing stateTransitions attribute set to non-existing state resources } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/004

| TP Id | TP/oneM2M/CSE/PMG/CRE/004 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <state> resource when for some referenced <state> resources in stateTransitions attributes Originator don’t have retrieve privilege. |
| Reference | TS-0004 [2] clause 7.4.XX.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <processManagement> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to XX (state) and From set to AE-ID and Content containing state resource containing stateTransitions attribute set to state resources on which Originator don’t have retrieve privilege. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/005

| TP Id | TP/oneM2M/CSE/PMG/CRE/005 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <state> resource when some referenced <state> resources in stateTransitions attributes are not child resources of parent <processManagement>. |
| Reference | TS-0004 [2] clause 7.4.XX.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <processManagement> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to XX (state) and From set to AE-ID and Content containing state resource containing stateTransitions attribute set to some state resources not child resources of TARGET_RESOURCE_ADDRESS resource. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/006

| TP Id | TP/oneM2M/CSE/PMG/CRE/006 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <action> resource when resource referenced by ATTRIBUTE attribute doesn’t exist. |
| Reference | TS-0004 [2] clause 7.4.73.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 63 (action) and From set to AE-ID and Content containing action resource containing ATTRIBUTEset to not-existing resourceID. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

| TP Id | ATTRIBUTE |
| --- | --- |
| TP/oneM2M/CSE/PMG/CRE/006_SRI | subjectResourceID |
| TP/oneM2M/CSE/PMG/UPD/006_ORI | objectResourceID |

- TP/oneM2M/CSE/PMG/CRE/007

| TP Id | TP/oneM2M/CSE/PMG/CRE/007 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <action> resource when resource referenced by subjectResourceID attribute is not accessible to it. |
| Reference | TS-0004 [2] clause 7.4.73.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource. at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 63 (action) and From set to AE-ID and Content containing action resource containing subjectResourceID set to non-accessible resourceID. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/008

- TP/oneM2M/CSE/PMG/CRE/009

| TP Id | TP/oneM2M/CSE/PMG/CRE/009 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <action> resource when resource referenced by objectResourceID attribute is not accessible to it. |
| Reference | TS-0004 [2] clause 7.4.73.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 63 (action) and From set to AE-ID and Content containing action resource containing objectResourceID set to non-accessible resourceID. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/010

| TP Id | TP/oneM2M/CSE/PMG/CRE/010 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <action> resource when From parameter in actionPrimitive attribute is not same as Originator of create request. |
| Reference | TS-0004 [2] clause 7.4.73.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 63 (action) and From set to AE-ID and Content containing action resource containing valid value set in actionPrimitive containing From parameter not same as Originator of create request. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/011

| TP Id | TP/oneM2M/CSE/PMG/CRE/011 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <action> resource when evalMode attribute has value either “off” or “once” and evalControlParam attribute is also set. |
| Reference | TS-0004 [2] clause 7.4.73.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource.at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 63 (action) and From set to AE-ID and Content containing action resource containing evalMode set to “off” or “once” and evalControlParam also set. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/012

| TP Id | TP/oneM2M/CSE/PMG/CRE/012 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <action> resource when subject element of evalCriteria attribute is not an attribute of resource type referenced by subjectResourceID attribute. |
| Reference | TS-0004 [2] clause 7.4.73.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having child <container> resource at CHILD_ADDRESS and the AE having privileges to perform CREATE operation on the resource.at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 63 (action) and From set to AE-ID and Content containing action resource containing subjectResourceID set to CHILD_ADDRESS valid value set in evalCriteria attribute containing subject element not matching CHILD_ADDRESS attributes. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/013

| TP Id | TP/oneM2M/CSE/PMG/CRE/013 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <action> resource when subjectResourceID attribute not set and subject element of evalCriteria attribute is not an attribute of the parent resource type. |
| Reference | TS-0004 [2] clause 7.4.73.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 63 (action) and From set to AE-ID and Content containing action resource containing subjectResourceID not set valid value set in evalCriteria attribute containing subject element not matching TARGET_RESOURCE_ADDRESS attributes. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/014

| TP Id | TP/oneM2M/CSE/PMG/CRE/014 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <action> resource when threshold element of evalCriteria is outside value space of data type of subject element. |
| Reference | TS-0004 [2] clause 7.4.73.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 63 (action) and From set to AE-ID and Content containing action resource containing evalCriteria attribute set and subject element set and threshold element set outside value space of data type of subject attribute. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/015

| TP Id | TP/oneM2M/CSE/PMG/CRE/015 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <action> resource when operator element of evalCriteria has invalid value. |
| Reference | TS-0004 [2] clause 7.4.73.2.1, Table 6.3.4.2.86-1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE on the resource at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 63 (action) and From set to AE-ID and Content containing action resource containing evalCriteria attribute set and operator set to invalid value. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/016

| TP Id | TP/oneM2M/CSE/PMG/CRE/016 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <dependency> resource when resource defined by referencedResourceID attribute doesn’t exist. |
| Reference | TS-0004 [2] clause 7.4.74.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <action> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Resource Type set to 64 (dependency) and Content containing dependency resource containing referencedResourceID set to not-existing resourceID. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/017

| TP Id | TP/oneM2M/CSE/PMG/CRE/017 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <dependency> resource when Originator doesn’t have retrieve privilege on resource defined by referencedResourceID attribute. |
| Reference | TS-0004 [2] clause 7.4.74.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <action> resource at TARGET_RESOURCE_ADDRESS and the IUT having <container> resource at CHILD_ADDRESS not accessible to AE and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Resource Type set to 64 (dependency) and Content containing dependency resource containing referencedResourceID set to CHILD_ADDRESS. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/018

| TP Id | TP/oneM2M/CSE/PMG/CRE/018 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <dependency> resource when attribute referenced by subject element of evalCriteria attribute of request is not an attribute of resource type referenced by referencedResourceID attribute. |
| Reference | TS-0004 [2] clause 7.4.74.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <action> resource at TARGET_RESOURCE_ADDRESS and the IUT having <container> resource at CHILD_ADDRESS accessible to AE and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Resource Type set to 64 (dependency) and Content containing dependency resource containing referencedResourceID set to CHILD_ADDRESS and valid value set in evalCriteria containing subject element set not to one of the attributes of CHILD_ADDRESS } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/019

| TP Id | TP/oneM2M/CSE/PMG/CRE/019 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <dependency> resource when value of threshold element of evalCriteria attribute is outside the value space of data type of subject element of evalCriteria. |
| Reference | TS-0004 [2] clause 7.4.74.2.1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <action> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Resource Type set to 64 (dependency) and Content containing dependency resource containing valid value set in evalCriteria containing subject element set and threshold element set to value outside value range of referenced attribute data type of subject element. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- TP/oneM2M/CSE/PMG/CRE/020

| TP Id | TP/oneM2M/CSE/PMG/CRE/020 |
| --- | --- |
| Test objective | Check that the IUT rejects create of <dependency> resource when value of operator element is invalid. |
| Reference | TS-0004 [2] clause 7.4.74.2.1, Table 6.3.4.2.86 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <action> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Resource Type set to 64 (dependency) and Content containing dependency resource containing valid value set in evalCriteria containing operator element set to invalid value. } | IUT  AE |
|  | then { the IUT sends valid Response to AE containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

7.2.2.x.y 	Delete Operation

TP/oneM2M/CSE/PMG/DEL/001

| TP Id | TP/oneM2M/CSE/PMG/DEL/001 |
| --- | --- |
| Test objective | Check that the IUT rejects delete of <processManagement> resource when the value of the processStatus attribute is not equal to “Disabled”. |
| Reference | TS-0004 [2] clause 7.4.XX.2.4 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource <processManagement> at TARGET_RESOURCE_ADDRESS, processStatus set not equal to “Disabled” and the AE have privilege to perform DELETE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid DELETE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  AE |

TP/oneM2M/CSE/PMG/DEL/002

| TP Id | TP/oneM2M/CSE/PMG/DEL/002 |
| --- | --- |
| Test objective | Check that the IUT rejects delete of <state> resource when the value of the stateActive attribute is equal to “true”. |
| Reference | TS-0004 [2] clause 7.4.XX.2.4 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource <state> at TARGET_RESOURCE_ADDRESS, stateActive set to “true” and the AE have privilege to perform DELETE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid DELETE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  AE |

TP/oneM2M/CSE/PMG/DEL/003

| TP Id | TP/oneM2M/CSE/PMG/DEL/003 |
| --- | --- |
| Test objective | Check that the IUT rejects delete of <state> resource when the value of the processStatus attribute of parent <processManagement> is not equal to “Disabled”. |
| Reference | TS-0004 [2] clause 7.4.XX.2.4 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource <processManagement> at PARENT_RESOURCE_ADDRESS, processStatus set not equal to “Disabled and the IUT having a resource <state> at TARGET _RESOURCE_ADDRESS and the AE have privilege to perform DELETE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid DELETE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  AE |

- ----------------------- End of change 1 -----------------------

# Comments

RSC to be replaced here when defined by SDS.

RSC to be replaced when SDS finalize it.

cseBASE modify.

CSEBase, remoteCSE, node, AE, container, flexContainer, group, timeSeries, transaction, state could be parents of <action> resource hence we should use TARGET_RESOURCE_ADDRESS

cseBASE changes ..

cseBASE changes…

cseBase changes…

cseBase changes…

cseBase changes…

cseBase changes…