| CHANGE REQUEST |
| --- |
| Meeting ID:* | TDE 50.3 |
| Source:* | oneM2M-TF |
| Date:* | 2021-09-09 |
| Reason for Change/s:* | Process Management test purposes |
| CR against: Release* | Rel-4 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018 v4.3.0 |
| Clauses * | New clause |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2019 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution introduces test case for Update of  Process Management CSF resources  as per TS-0004 and TS-0001 documents.

----------------------- Start of change 1 -----------------------

#### 7.2.2.x	Process Management(PMG)

7.2.2.x.y 	Update Operation

TP/oneM2M/CSE/PMG/UPD/001

| TP Id | TP/oneM2M/CSE/PMG/UPD/001 |
| --- | --- |
| Test objective | Check that the IUT rejects update of ATTRIBUTE attribute of <processManagement> resource when the processStatus attribute has value not equal to “Disabled”. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and and the IUT having a <processManagement> at TARGET_RESOURCE_ADDRESS having processStatus attribute set value not equal to “Disabled” and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing ATTRIBUTE attribute containing valid value. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  AE |

| TP Id | ATTRIBUTE |
| --- | --- |
| TP/oneM2M/CSE/PMG/UPD/001_AC | activateConditions |
| TP/oneM2M/CSE/PMG/UPD/001_EC | endConditions |
| TP/oneM2M/CSE/PMG/UPD/001_IS | InitialState |

TP/oneM2M/CSE/PMG/UPD/002

| TP Id | TP/oneM2M/CSE/PMG/UPD/002 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when originator don’t have retrieve privilege on the resources or attributes referred by subject element of the evalCriteria of ATTRIBUTE attribute . |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <processManagement> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform UPDATE operation at TARGET_RESOURCE_ADDRESS and the IUT having a resource at SUBJECT_RESOURCE_ADDRESS and the AE not having privileges to perform RETRIEVE operation at SUBJECT_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing ATTRIBUTE attribute containing evalCriteria attribute containing subject parameter set to SUBJECT_RESOURCE_ADDRESS } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

| TP Id | ATTRIBUTE |
| --- | --- |
| TP/oneM2M/CSE/PMG/UPD/002_AC | activateConditions |
| TP/oneM2M/CSE/PMG/UPD/002_EC | endConditions |

TP/oneM2M/CSE/PMG/UPD/003

| TP Id | TP/oneM2M/CSE/PMG/UPD/003 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when the resources or attributes referred by subject attribute of evalCriteria parameters of ATTRIBUTE attribute do not exist. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <processManagement> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform UPDATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing ATTRIBUTE attribute containing evalCriteria attribute containing subject parameter set to UNAVAILABLE_RESOURCE } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

| TP Id | ATTRIBUTE |
| --- | --- |
| TP/oneM2M/CSE/PMG/UPD/003_AC | activateConditions |
| TP/oneM2M/CSE/PMG/UPD/003_EC | endConditions |

TP/oneM2M/CSE/PMG/UPD/004

| TP Id | TP/oneM2M/CSE/PMG/UPD/004 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when the evalCriteria of ATTRIBUTE has threshold element value not within the value space of the data type of the subject element. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <processManagement> resource at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing ATTRIBUTE attribute containing evalCriteria element containing threshold element set to invalid value } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

| TP Id | ATTRIBUTE |
| --- | --- |
| TP/oneM2M/CSE/PMG/UPD/004_AC | activateConditions |
| TP/oneM2M/CSE/PMG/UPD/004_EC | endConditions |

TP/oneM2M/CSE/PMG/UPD/005

| TP Id | TP/oneM2M/CSE/PMG/UPD/005 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when the evalCriteria of ATTRIBUTE has invalid value in operator attribute. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3, Table 6.3.4.2.86-1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource <processManagement> at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing ATTRIBUTE attribute containing evalCriteria attribute having operator parameter set to invalid value. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

| TP Id | ATTRIBUTE |
| --- | --- |
| TP/oneM2M/CSE/PMG/UPD/005_AC | activateConditions |
| TP/oneM2M/CSE/PMG/UPD/005_EC | endConditions |

TP/oneM2M/CSE/PMG/UPD/006

| TP Id | TP/oneM2M/CSE/PMG/UPD/006 |
| --- | --- |
| Test objective | Check that the IUT rejects update of initialState attribute of <processManagement> resource when referred <state> resource doesn’t exist. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource <processManagement> at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing initialState set to UNAVAILABLE STATE RESOURCE. . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/007

| TP Id | TP/oneM2M/CSE/PMG/UPD/007 |
| --- | --- |
| Test objective | Check that the IUT rejects update of initialState attribute of <processManagement> resource when Originator does not have retrieve privilege on referenced <state> resource. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource <processManagement> at TARGET_RESOURCE_ADDRESS and the AE having privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS and the IUT having a <state> resource at STATE_RESOURCE_ADDRESS and the AE not having privileges to perform RETRIEVE operation at STATE_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing initialState attribute set to STATE_RESOURCE_ADDRESS. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/008

| TP Id | TP/oneM2M/CSE/PMG/UPD/008 |
| --- | --- |
| Test objective | Check that the IUT rejects update of initialState attribute of <processManagement> resource when the referred resource is not the child resource of <processManagement>. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource <processManagement> at TARGET_RESOURCE_ADDRESS and the AE having privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS and the IUT having <state> resource at STATE_RESOURCE_ADDRESS not being child resource of TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing initialState attribute set to STATE_RESOURCE_ADDRESS . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/009

| TP Id | TP/oneM2M/CSE/PMG/UPD/009 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when the value of the processControl attribute in the request is equal to “Enable” and the value of the processStatus attribute of the <processManagement> resource is equal to PROCESS_STATUS_VALUE |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having resource <processManagement> at TARGET_RESOURCE_ADDRESS having,processStatus set equal to “PROCESS_STATUS_VALUEand the AE having privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing processControl attribute set to value “Enable”. . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  AE |

| TP Id | PROCESS_STATUS_VALUE |
| --- | --- |
| TP/oneM2M/CSE/PMG/UPD/009_EN | Enabled |
| TP/oneM2M/CSE/PMG/UPD/009_AC | Activated |
| TP/oneM2M/CSE/PMG/UPD/009_PU | Paused |
| TP/oneM2M/CSE/PMG/UPD/009_CM | Completed |
| TP/oneM2M/CSE/PMG/UPD/009_AB | Aborted |

TP/oneM2M/CSE/PMG/UPD/010

| TP Id | TP/oneM2M/CSE/PMG/UPD/010 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when the value of the processControl attribute in the request is equal to “Disable” and the value of the processStatus attribute of the <processManagement> resource is equal to “Disabled”. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having resource <processManagement> at TARGET_RESOURCE_ADDRESS, processStatus set to “Disabled” and the AE having privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing processControl attribute set to value “Disable”. . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/011

| TP Id | TP/oneM2M/CSE/PMG/UPD/011 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when the value of the processControl attribute in the request is equal to “Pause” and the value of the processStatus attribute of the <processManagement> resource is equal to “PROCESS_STATUS_VALUE |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource <processManagement> at TARGET_RESOURCE_ADDRESS, processStatus attribute set equal to PROCESS_STATUS_VALUE and the AE having privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing processControl attribute set to value “Pause”. . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  AE |

| TP Id | PROCESS_STATUS_VALUE |
| --- | --- |
| TP/oneM2M/CSE/PMG/UPD/011_EN | Enabled |
| TP/oneM2M/CSE/PMG/UPD/011_DS | Disabled |
| TP/oneM2M/CSE/PMG/UPD/011_PU | Paused |
| TP/oneM2M/CSE/PMG/UPD/011_CM | Completed |
| TP/oneM2M/CSE/PMG/UPD/011_AB | Aborted |

TP/oneM2M/CSE/PMG/UPD/012

| TP Id | TP/oneM2M/CSE/PMG/UPD/012 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when the value of the processControl attribute in the request is equal to “Reactivate” and the value of the processStatus attribute of the <processManagement> resource is equal to “PROCESS_STATUS_VALUE”. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource <processManagement> at TARGET_RESOURCE_ADDRESS, processStatus set equal to “PROCESS_STATUS_VALUE” and the AE having privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing processControl attribute set to value “Reactivate”. . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  AE |

| TP Id | PROCESS_STATUS_VALUE |
| --- | --- |
| TP/oneM2M/CSE/PMG/UPD/012_EN | Enabled |
| TP/oneM2M/CSE/PMG/UPD/012_DS | Disabled |
| TP/oneM2M/CSE/PMG/UPD/012_AC | Activated |
| TP/oneM2M/CSE/PMG/UPD/012_CM | Completed |
| TP/oneM2M/CSE/PMG/UPD/012_AB | Aborted |

TP/oneM2M/CSE/PMG/UPD/013

| TP Id | TP/oneM2M/CSE/PMG/UPD/013 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when the value of the processControl attribute in the request is equal to “Enable” and the value of the processStatus attribute of the <processManagement> resource is equal to “Disabled” when any of the referenced child resources is not available . |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having resource <processManagement> at TARGET_RESOURCE_ADDRESS, processStatus attribute set to “Disabled” and the IUT having <state> resource as child resource of TARGET_RESOURCE_ADDRESS and referenced in initialState attribute and the resource referenced by stateAction attribute is not available and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing processControl attribute set to value “Enable”. . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/014

| TP Id | TP/oneM2M/CSE/PMG/UPD/014 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when the value of the processControl attribute in the request is equal to “Enable” and the value of the processStatus attribute of the <processManagement> resource is equal to “Disabled” but Originator don’t have required privileges on any of the referenced child resources. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having resource <processManagement> at TARGET_RESOURCE_ADDRESS containing processStatus attribute set to “Disabled” and initialState attribute set to child <state> resource at STATE_ADDRESS containing stateAction attribute set to child <action> resource at ACTION_ADDRESS and the AE having privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS and but AE not having privilege on STATE_ADDRESS and ACTION_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing processControl set to value “Enable”. . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/015

| TP Id | TP/oneM2M/CSE/PMG/UPD/015 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <processManagement> resource when the value of the processControl attribute in the request is equal to “Enable” and the value of the processStatus attribute of the <processManagement> resource is equal to “Disabled” but any of referenced resources are not descendent resource of <processManagement>. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <state> resource at STATE and the IUT having <action> resource at ACTION and the IUT having resource <processManagement> at TARGET_RESOURCE_ADDRESS containing processStatus set to “Disabled” and initialState attribute set to STATE and stateAction attribute set to ACTION the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing processManagement resource containing processControl set to value “Enable”. . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx(INVALID_PROCESS_CONFIGURATION). } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/016

| TP Id | TP/oneM2M/CSE/PMG/UPD/016 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <state> resource when the processStatus attribute of parent <processManagement> has value not equal to “Disabled”. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and and the IUT having a <processManagement> resource at PARENT_RESOURCE_ ADDRESS containing processStatus attribute set not equal to “Disabled” and and the IUT having a child <state> resource at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing state resource containing ATTRIBUTE attribute containing valid value. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT  AE |

| TP Id | ATTRIBUTE |
| --- | --- |
| TP/oneM2M/CSE/PMG/UPD/016_STAC | stateAction |
| TP/oneM2M/CSE/PMG/UPD/016_STTRS | stateTransitions |

TP/oneM2M/CSE/PMG/UPD/017

| TP Id | TP/oneM2M/CSE/PMG/UPD/017 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <state> resource when the resource referenced by stateAction attribute does not exist. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <state> resource at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing state resource containing stateAction attribute value set to NON EXISTENT ACTION RESOURCE. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/018

| TP Id | TP/oneM2M/CSE/PMG/UPD/018 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <state> resource when the Originator don’t have retrieve privilege on resource referenced by stateAction attribute. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <state> resource at PARENT_RESOURCE_ADDRESS and the IUT having a child <action> resource ACTION_ADDRESS Originator not having retrieve privilege of and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing state resource containing stateAction attribute value set to ACTION_ADDRESS. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/019

| TP Id | TP/oneM2M/CSE/PMG/UPD/019 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <state> resource when the resource referenced by stateAction attribute is not a child resource. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <state> resource at PARENT_RESOURCE_ADDRESS and the IUT having a non-child <action> resource ACTION_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing state resource containing stateAction attribute value set to ACTION_ADDRESS. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/020

| TP Id | TP/oneM2M/CSE/PMG/UPD/020 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <state> resource when the any of <state> resources referenced by stateTransitions attribute doesn’t exist. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <state> resource at PARENT_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing state resource containing stateTransitions attribute set to NON EXISTENT STATE RESOURCE. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/021

| TP Id | TP/oneM2M/CSE/PMG/UPD/021 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <state> resource when for any of <state> resources referenced by stateTransitions attribute Originator doesn’t have retrieve privilege. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <state> resource at STATE_ADDRESS1 and the IUT having a <state> resource at STATE_ADDRESS2 and the AE having privilege to perform UPDATE operation on STATE_ADDRESS1 AE not having privileges to perform RETRIEVE operation on STATE_ADDRESS2 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to STATE_ADDRESS1and From set to AE-ID and Content containing state resource containing stateTransitions attribute value set to STATE_ADDRESS2. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/022

| TP Id | TP/oneM2M/CSE/PMG/UPD/022 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <state> resource when any of <state> resources referenced by stateTransitions attribute is not child resource of parent <processManagement>. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <processManagement> resource at PARENT_ADDRESS having the IUT having a child <state> resource at STATE_ADDRESS and the IUT having a non-child <state> resource at STATE_ADDRESS2 and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to STATE_ADDRESS and From set to AE-ID and Content containing state resource containing stateTransitions attribute indicating nextState element set to STATE_ADDRESS2 . } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/023

| TP Id | TP/oneM2M/CSE/PMG/UPD/023 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <state> resource when any of resources and attributes referenced by subject element of evalCriteria of stateTransitions attribute doesn’t exist. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <state> resource at PARENT_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to PARENT_RESOURCE_ADDRESS and From set to AE-ID and Content containing state resource containing stateTransitions attribute set having some evalCriteria’ subject element set to NON-EXISTING RESOURCES AND ATTRIBUTES. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/024

| TP Id | TP/oneM2M/CSE/PMG/UPD/024 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <state> resource when Originator doesn’t have retrieve privilege on any of resources and attributes referenced by subject element of evalCriteria of stateTransitions attribute. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <state> resource at PARENT_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS and the AE not having privileges to perform RETRIEVE operation at SUBJECT_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to PARENT_RESOURCE_ADDRESS and From set to AE-ID and Content containing state resource containing stateTransitions attribute containing evalCriteria’ subject element set to SUBJECT_RESOURCE_ADDRESS } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/025

| TP Id | TP/oneM2M/CSE/PMG/UPD/025 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <state> resource when threshold element of evalCriteria of stateTransitions attribute have value outside the value spaces of the data type of subject element. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <state> resource at PARENT_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to PARENT_RESOURCE_ADDRESS and From set to AE-ID and Content containing state resource containing stateTransitions attribute containing evalCriteria’ threshold element set to outside range spaces of the data type of subject element. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

- ----------------------- End of change 1 -----------------------

# Comments

RSC to be replaced when decided by SDS

RSC to be replaced when decided by SDS.

RSC to be replaced when decided by SDS

RSC to be replaced when decided by SDS

RSC to be replaced when decided by SDS

Same changes