| CHANGE REQUEST |
| --- |
| Meeting ID:* | TDE 50.3 |
| Source:* | oneM2M-TF |
| Date:* | 2021-09-09 |
| Reason for Change/s:* | Process Management test purposes |
| CR against: Release* | Rel-4 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018 v4.3.0 |
| Clauses * | New clause |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2019 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution introduces test case for Update of  Process Management CSF resources  as per TS-0004 and TS-0001 documents.

----------------------- Start of change 1 -----------------------

TP/oneM2M/CSE/PMG/UPD/026

| TP Id | TP/oneM2M/CSE/PMG/UPD/026 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <state> resource when operator element of evalCriteria of stateTransitions attribute have invalid value. |
| Reference | TS-0004 [2] clause 7.4.XX.2.3, Table 6.3.4.2.86-1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <state> resource at PARENT_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to PARENT_RESOURCE_ADDRESS and From set to AE-ID and Content containing state resource containing stateTransitions attribute containing evalCriteria’ operator element set to invalid value. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 41xx (INVALID_PROCESS_CONFIGURATION) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/027

| TP Id | TP/oneM2M/CSE/PMG/UPD/027 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when resource referenced by ATTRIBUTE attribute doesn’t exist. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing ATTRIBUTE attribute set to non-existing resourceID. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

| TP Id | ATTRIBUTE |
| --- | --- |
| TP/oneM2M/CSE/PMG/UPD/027_SRI | subjectResourceID |
| TP/oneM2M/CSE/PMG/UPD/027_DEP | dependencies |
| TP/oneM2M/CSE/PMG/UPD/027_ORI | objectResourceID |

TP/oneM2M/CSE/PMG/UPD/028

| TP Id | TP/oneM2M/CSE/PMG/UPD/028 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when resource referenced by ATTRIBUTE attribute is not accessible by Originator. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS and the IUT having child <container> at CHILD_ADDRESS not accessible by AE and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing ATTRIBUTE attribute set to CHILD_ADDRESS. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

| TP Id | ATTRIBUTE |
| --- | --- |
| TP/oneM2M/CSE/PMG/UPD/028_SRI | subjectResourceID |
| TP/oneM2M/CSE/PMG/UPD/028_DEP | Dependencies |
| TP/oneM2M/CSE/PMG/UPD/028_ORI | objectResourceID |

TP/oneM2M/CSE/PMG/UPD/029

| TP Id | TP/oneM2M/CSE/PMG/UPD/029 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when any of <dependency> resources referenced by dependencies attribute are not child resources of this <action> resource. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS and the IUT having another <action> at TARGET_RESOURCE_ADDRESS2 and and IUT having <dependency> resource at DEPENDENCY_RESOURCE_ADDRESS as child resource of TARGET_RESOURCE_ADDRESS2. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing dependencies attribute set to DEPENDENCY_RESOURCE_ADDRESS. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/030

| TP Id | TP/oneM2M/CSE/PMG/UPD/030 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when From parameter contained in actionPrimitive attribute not equal to Originator. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing actionPrimitive attribute’s From element not equal AE-ID. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/031

| TP Id | TP/oneM2M/CSE/PMG/UPD/031 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when request evalMode attribute has value “off” or “once” and request evalControlParam attribute is also set. |
| Reference | TS-0004 [2] clause 7.4.73is .2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS havingevalControlParam attribute not set and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing evalMode set to “off” or “once” and evalControlParam is set. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/032

| TP Id | TP/oneM2M/CSE/PMG/UPD/032 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when request evalMode attribute has value “off” or “once” ,request evalControlParam attribute not set but evalControlParam within <action> resource has value set. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS, evalControlParam attribute set and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing evalMode set to “off” or “once” and evalControlParam is not set. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/033

| TP Id | TP/oneM2M/CSE/PMG/UPD/033 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when value of subject element of evalCriteria attribute of request is not one of the attribute of referenced resource of subjectResourceID attribute of request. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS, subjectResourceID not set and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS and IUT having a resource at RESOURCE_ADDRESS not having attribute ATTRIBUTE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing subjectResourceID set to RESOURCE_ADDRESS and valid value set in evalCriteria containing subject set to ATTRIBUTE. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/034

| TP Id | TP/oneM2M/CSE/PMG/UPD/034 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when value of subject element of evalCriteria attribute of request is not one of the attribute of referenced resource of subjectResourceID attribute of <action>. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and IUT having a resource at RESOURCE_ADDRESS not having attribute ATTRIBUTE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS, subjectResourceID set to RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS and } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing valid value set in evalCriteria containing subject element set to ATTRIBUTE } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/035

| TP Id | TP/oneM2M/CSE/PMG/UPD/035 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when value of subject element of evalCriteria attribute of request is not one of the attribute of parent resource. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and AE not having attribute ATTRIBUTE and the AE having a child <action> at TARGET_RESOURCE_ADDRESS, subjectResourceID not set and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing subjectResourceID not set and valid value set in evalCriteria containing subject element value set to ATTRIBUTE } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/036

| TP Id | TP/oneM2M/CSE/PMG/UPD/036 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when value of subject element of evalCriteria attribute of target <action> resource is not one of the attribute of resource referenced by request subjectResourceID attribute.. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource at RESOURCE_ADDRESS not having attribute ATTRIBUTE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS, evalCriteria set having subject element set to ATTRIBUTE and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing subjectResourceID set to RESOURCE_ADDRESS } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/037

| TP Id | TP/oneM2M/CSE/PMG/UPD/037 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when value of threshold element of evalCriteria is not within value space of the data type of subject element of evalCriteria attribute. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing valid value set in evalCriteria containing subject element set and threshold element value outside value range of subject element data type. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/038

| TP Id | TP/oneM2M/CSE/PMG/UPD/038 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <action> resource when value of operator element of evalCriteria has invalid value. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 , Table 6.3.4.2.86-1 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <action> at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing action resource containing valid value set in evalCriteria containing operator element set to invalid value. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/039

| TP Id | TP/oneM2M/CSE/PMG/UPD/039 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <dependency> resource when value present in subject element of evalCriteria of request is not an attribute of resource type referenced by referencedResourceID attribute. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource at RESOURCE_ADDRESS not having attribute ATTRIBUTE and the IUT having a <dependency> at TARGET_RESOURCE_ADDRESS, referencedResourceID set to RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing dependency resource containing valid value set in evalCriteria containing subject element set to ATTRIBUTE } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/040

| TP Id | TP/oneM2M/CSE/PMG/UPD/040 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <dependency> resource when value present in threshold element of evalCriteria attribute of request is not within value space of data type of subject element. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <dependency> at TARGET_RESOURCE_ADDRESS, referencedResourceID set and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing dependency resource containing valid value set in evalCriteria containing subject element value set and threshold element value set to value outside value range of data type of subject attribute. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

TP/oneM2M/CSE/PMG/UPD/041

| TP Id | TP/oneM2M/CSE/PMG/UPD/041 |
| --- | --- |
| Test objective | Check that the IUT rejects update of <dependency> resource when value of operator element of evalCriteria attribute of request is invalid. |
| Reference | TS-0004 [2] clause 7.4.73.2.3 , Table 6.3.4.2.86 |
| Parent Release | Release 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <dependency> at TARGET_RESOURCE_ADDRESS and the AE have privilege to perform UPDATE operation on TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing dependency resource containing evalCriteria set containing operator set to invalid value. } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT  AE |

- ----------------------- End of change 1 -----------------------