| CHANGE REQUEST |
| --- |
| Meeting:* | TDE #51.1 |
| Source:* | TF-oneM2M |
| Date:* | 2021-10-07 |
| Contact:* | Neeta Meshram, C-DOT, neeta@cdot.in Poornima Shandilya, C-DOT, poornima@cdot.in |
| Reason for Change/s:* | New TPs for 3GPP Interworking SCEF NIDD |
| CR against: Release* | Rel-4 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018-V-4.2.0 |
| Clauses/Sub Clauses* | 7.2.2.12 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution introduces new TPs for 3GPP Interworking for SCEF-based NIDD functionality as per TS-0001 and TS-00026 documents.

----------------------- Start of new text 1 -----------------------

7.2.2.12	3GPP interworking

7.2.2.12.2        SCEF-based NIDD

TP/oneM2M/CSE/3GPP/NIDD/001

| TP Id | TP/oneM2M/CSE/3GPP/NIDD/001 |
| --- | --- |
| Test objective | Check that the IUT sends NIDD configuration request when it receives create request of <serviceSubscribedNode> resource associated with a UE hosting an ADN-AE with niddRequired attribute set to TRUE. |
| Reference | TS-0026 [5], clause 7.1.1.1 |
| Parent Release | Release 3 |
| Config Id | CF05 |
| PICS Selection | PICS_IN_CSE, PICS_3GPP |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Resource Type set to 20(serviceSubscribedNode) and Content containing valid serviceSubscribedNode resource representation containing niddRequired attribute set to TRUE and nodeID attribute set to M2M-Ext-ID of UE hosting an AND-AE } | IUT  AE |
|  | then { the IUT sends a valid Request to the SCEF containing NIDD configuration Request message containing a valid NIDD configuration Request } | IUT ( SCEF |

TP/oneM2M/CSE/3GPP/NIDD/002

| TP Id | TP/oneM2M/CSE/3GPP/NIDD/002 |
| --- | --- |
| Test objective | Check that the IUT issues NIDD configuration request when it receives update request of <serviceSubscribedNode> resource associated with a UE hosting an ADN-AE to set niddRequired attribute TRUE. |
| Reference | TS-0026 [5], clause 7.1.1.1 |
| Parent Release | Release 3 |
| Config Id | CF05 |
| PICS Selection | PICS_CSE, PICS_3GPP |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a <serviceSubscribedNode> resource at TARGET_RESOURCE_ADDRESS containing niddRequired attribute set to False and nodeID attribute set to M2M-Ext-ID of UE hosting an AND-AE and the AE having privileges to perform UPDATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content containing valid serviceSubscribedNode resource representation containing niddRequired attribute set to TRUE } | IUT  AE |
|  | then { the IUT sends a valid Request to the SCEF containing NIDD configuration Request message containing A NIDD configuration Request } | IUT ( SCEF |

TP/oneM2M/CSE/3GPP/NIDD/003

| TP Id | TP/oneM2M/CSE/3GPP/NIDD/003 |
| --- | --- |
| Test objective | Check that the IUT issues NIDD configuration delete request when it receives update request of <serviceSubscribedNode> resource associated with a UE hosting an ADN-AE to set niddRequired attribute False. |
| Reference | TS-0026 [5], clause 7.1.1.1 |
| Parent Release | Release 3 |
| Config Id | CF05 |
| PICS Selection | PICS_IN_CSE, PICS_3GPP |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a <serviceSubscribedNode> resource at TARGET_RESOURCE_ADDRESS containing niddRequired attribute set to True and nodeID attribute set to M2M-Ext-ID of UE hosting an AND-AE and the AE having privileges to perform UPDATE operation on the resource TARGET_RESOURCE_ADDRESS and IUT having established NIDD configuration for M2M-Ext-ID } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content containing valid serviceSubscribedNode resource representation containing niddRequired attribute set to FALSE } | IUT  AE |
|  | then { the IUT sends a valid Request to the SCEF containing NIDD configuration delete Request message containing A NIDD configuration delete Request } | IUT ( SCEF |

TP/oneM2M/CSE/3GPP/NIDD/004

| TP Id | TP/oneM2M/CSE/3GPP/NIDD/004 |
| --- | --- |
| Test objective | Check that the IUT issues NIDD configuration delete request when it receives delete request of <serviceSubscribedNode> resource associated with a UE hosting an ASN/MN-CSE or ADN-AE. |
| Reference | TS-0026 [5], clause 7.1.1.1 |
| Parent Release | Release 3 |
| Config Id | CF05 |
| PICS Selection | PICS_IN_CSE, PICS_3GPP |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a <serviceSubscribedNode> resource at TARGET_RESOURCE_ADDRESS containing niddRequired attribute set to True and nodeID attribute set to M2M-Ext-ID of UE hosting an AND-AE and the AE having privileges to perform DELETE operation on the resource TARGET_RESOURCE_ADDRESS IUT having established NIDD configuration for M2M-Ext-ID } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid DELETE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and } | IUT  AE |
|  | then { the IUT sends a valid Request to the SCEF containing NIDD configuration delete Request message containing A NIDD configuration delete Request } | IUT ( SCEF |

TP/oneM2M/CSE/3GPP/NIDD/005

| TP Id | TP/oneM2M/CSE/3GPP/NIDD/005 |
| --- | --- |
| Test objective | Check that the IUT issues SCEF-based Mobile Terminated (MT) NIDD Downlink Data Transfer Request if the size of the oneM2M request primitive to be sent in the MT NIDD Request is less than or equal to the maximumPacketSize defined in the NIDD Configuration response. |
| Reference | TS-0026 [5], clause 7.1.1.2 |
| Parent Release | Release 3 |
| Config Id | CF05 |
| PICS Selection | PICS_IN_CSE, PICS_3GPP |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having done successful NIDD Configuration Request for the targeted ADN-AE hosted on a UE and size of the oneM2M request primitive to be sent in the MT NIDD Request is less than or equal to the maximumPacketSize defined in the NIDD Configuration response. and the IUT having registered the IN-AE and the IUT having registered the AE1 hosted on AND-AE containing valid M2M-Ext-ID attribute and the IN-AE having created the container resource CONTAINER_RESOURCE_ADDRESS containing subscription child resource containing notificationURI attribute set to AE1 and notificationEventType attribute set to 3 and the IN-AE having privileges to perform CREATE operation on the resource CONTAINER_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from IN-AE containing To set to CONTAINER_RESOURCE_ADDRESS and From set to IN-AE and Content containing valid contentInstance resource } | IUT  IN-AE |
|  | then { the IUT sends a valid MT NIDD Downlink Data Transfer Request to the SCEF containing Non-IP data containing oneM2M request primitive containing Content containing valid Notification } | IUT ( SCEF |

TP/oneM2M/CSE/3GPP/NIDD/006

| TP Id | TP/oneM2M/CSE/3GPP/NIDD/006 |
| --- | --- |
| Test objective | Check that the IUT does not issue SCEF-based Mobile Terminated (MT) NIDD Downlink Data Transfer Request if the size of the oneM2M request primitive to be sent in the MT NIDD Request is more than the maximumPacketSize defined in the NIDD Configuration response. |
| Reference | TS-0026 [5], clause 7.1.1.2 |
| Parent Release | Release 3 |
| Config Id | CF05 |
| PICS Selection | PICS_IN_CSE, PICS_3GPP |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having done successful NIDD Configuration Request for the targeted ADN-AE hosted on a UE and size of the oneM2M request primitive to be sent in the MT NIDD Request is more than the maximumPacketSize defined in the NIDD Configuration response. and the IUT having registered the IN-AE and the IUT having registered the AE1 hosted on AND-AE containing valid M2M-Ext-ID attribute and the IN-AE having created the container resource CONTAINER_RESOURCE_ADDRESS containing subscription child resource containing notificationURI attribute set to AE1 and notificationEventType attribute set to 3 and the IN-AE having privileges to perform CREATE operation on the resource CONTAINER_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from IN-AE containing To set to CONTAINER_RESOURCE_ADDRESS and From set to IN-AE and Content containing valid contentInstance resource } | IUT  IN-AE |
|  | then { the IUT does not send a MT NIDD Downlink Data Transfer Request to the SCEF } |  |

TP/oneM2M/CSE/3GPP/NIDD/007

| TP Id | TP/oneM2M/CSE/3GPP/NIDD/007 |
| --- | --- |
| Test objective | Check that the IUT issues SCEF-based Mobile Terminated (MT) NIDD Downlink Data Transfer Request if the size of the oneM2M response primitive to be sent in the MT NIDD Request is less than or equal to the maximumPacketSize defined in the NIDD Configuration response. |
| Reference | TS-0026 [5], clause 7.1.1.2 |
| Parent Release | Release 3 |
| Config Id | CF05 |
| PICS Selection | PICS_IN_CSE, PICS_3GPP |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having done successful NIDD Configuration Request for the targeted ADN-AE hosted on a UE and size of the oneM2M response primitive to be sent in the MT NIDD Request is less than or equal to the maximumPacketSize defined in the NIDD Configuration response. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid MO(Mobile Originated) request from AE1 containing Non-IP data containing valid oneM2M request containing To set to AE1 and From set to AE1 and Content containing valid AE resource } | IUT  AE1 |
|  | then { the IUT sends a valid MT NIDD Downlink Data Transfer Request to the SCEF containing Non-IP data containing valid oneM2M response primitive } | IUT ( SCEF |

TP/oneM2M/CSE/3GPP/NIDD/008

| TP Id | TP/oneM2M/CSE/3GPP/NIDD/008 |
| --- | --- |
| Test objective | Check that IUT responds with a 204 NO CONTENT acknowledging the notification when SCEF sends MT NIDD Downlink Data Delivery Status Notification. |
| Reference | TS-0026 [5], clause 7.1.1.2, step 7 |
| Parent Release | Release 3 |
| Config Id | CF05 |
| PICS Selection | PICS_CSE, PICS_3GPP |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered AE1 hosted on a 3GPP UE and the IUT having sent a MT Downlink data transfer request } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid MT NIDD Downlink Data Delivery Status Notification from SCEF containing valid NiddDownlinkDataDeliveryStatusNotification | IUT ( SCEF |
|  | then { the IUT sends a 204 NO CONTENT acknowledging the notification } | IUT ( SCEF |

TP/oneM2M/CSE/3GPP/NIDD/009

| TP Id | TP/oneM2M/CSE/3GPP/NIDD/009 |
| --- | --- |
| Test objective | Check that IUT responds with a 204 NO CONTENT acknowledging the notification when SCEF sends MO NIDD Uplink Data Notification. |
| Reference | TS-0026 [5], clause 7.1.1.2, step 7 |
| Parent Release | Release 3 |
| Config Id | CF05 |
| PICS Selection | PICS_IN_CSE, PICS_3GPP |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having register an AE1 hosted on a 3GPP UE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid MO NIDD Uplink Data Notification from SCEF containing NiddUplinkDataNotification containing Non_IP data containing a valid oneM2M response primitive } | IUT ( SCEF |
|  | then { the IUT sends a 204 NO CONTENT acknowledging the notification } | IUT ( SCEF |

---------------------- End of new text 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

Raise an issue in issue tracker about what will happen in this case