| CHANGE REQUEST |
| --- |
| Meeting:* | TDE #52 |
| Source:* | TF-oneM2M |
| Date:* | 2021-12-02 |
| Contact:* | Siddharth Trikha, C-DOT, strikha@cdot.in Poornima Shandilya, C-DOT, poornima@cdot.in |
| Reason for Change/s:* | New TPs for SUB & NOTIF notificationContentType/notificatonEventType |
| CR against: Release* | Rel-4 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018-V-4.5.0 |
| Clauses/Sub Clauses* | 7.2.2.4.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution introduces new TPs for SUB & NOTIF CSF based on notificationContentType and notificatonEventType attributes as per TS-0001.

As per TS-0001 the set of valid combination allowed for these attributes are:

Table 9.6.8-4: Default and allowed values of notificationContentType

| notificationEventType notificationContentType | A | B | C | D | E | F | G | H |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| "modified attributes"; | valid | n/a | n/a | n/a | n/a | n/a | valid (default) | n/a |
| "all attributes"; | valid (default) | valid (default) | valid (default) | valid (default) | valid (default) | n/a | n/a | n/a |
| "ID" of the resource indicated in the notificationEventType condition. | valid | valid | valid | valid | valid | n/a | n/a | n/a |
| "Trigger Payload" | n/a | n/a | n/a | n/a | n/a | valid (default) | n/a | n/a |
| "TimeSeries notification" | n/a | n/a | n/a | n/a | n/a | n/a | n/a | valid (default) |

where A, B, C, D, E, F, G, H are defined as follows:

| notificationEventType | 0..5 | The type of event that shall trigger a notification. If multiple notificationEventType tags are present, a notification shall be triggered if any of the configured events occur. Note that not all combinations of event type are meaningful. Possible notification event type values are: Update to attributes of the subscribed-to resource Deletion of the subscribed-to resource, Creation of a direct child of the subscribed-to resource, Deletion of a direct child of the subscribed-to resource An attempt to retrieve a <contentInstance> direct-child-resource of a subscribed-to <container> resource is performed while this <contentInstance> child resource is an obsolete resource or the reference used for retrieving this resource is not assigned. This retrieval is performed by a RETRIEVE request targeting the subscribed-to resource with the Result Content parameter set to either "child-resources" or "attributes+child-resources". This value for the notificationEventType tag implies that the subscribed-to resource shall be an <container> resource. Otherwise this setting is not valid. Trigger Received targeting the MN/ASN-AE associated with the <AE> parent resource. This implies that the subscribed-to resource shall be an <AE> resource instance. Otherwise this setting is not valid. Update to attributes of the subscribed-to resource with blocking of the triggering UPDATE operation. For this notificationEventType value setting, only one single Notification Target shall be present in the notificationURI attribute – see notificationURI attribute definition. This value for the notificationEventType tag shall not be combined with any other notificationEventType tag value. This value for notificationEventType establishes a subscription that is triggered for the same events as for the value "Update to attributes of the subscribed-to resource". However, upon occurrence of a triggering UPDATE operation that has been validated and results in an authorized UPDATE operation, the triggering UPDATE operation shall be blocked by the Hosting CSE until a notification request was sent out and a corresponding response message was received or a timeout happens. When the response status code of the notification response message indicates a successful notification reception in combination with a successful notification action taken by the Notification Target entity, the triggering UPDATE operation shall be completed with a successful update of the targeted attribute(s). If the notification response message indicates an unsuccessful notification reception or a successful notification reception with unsuccessful notification action by the targeted entity or times out, the blocked UPDATE operation shall be completed with no success and no change of the targeted attribute(s). For any subscribed-to resource there shall exist a maximum of one subscription with this setting of notificationEventType. All other notification policies shall not be allowed when this setting of notificationEventType is used. The notificationContentType shall be "modified attributes". When an UPDATE operation has been blocked due to triggering this type of notification, any other occurring UPDATE or DELETE requests to the same resource shall be handled only after the blocked UPDATE operation has been completed. Report on missing data points. This notificationEventType value shall not be combined with any other notificationEventType value. The other conditions in eventNotificationCriteria conditions apply within the scope of the selected notificationEventType. For example, if notificationEventType is "Creation of a direct child of the subscribed-to resource" then other eventNotificationCriteria conditions is applied to the direct child resources of the subscribed-to resource. If this condition is not specified, the default value is "Update to attributes of the subscribed-to resource". This default value shall apply only if operationMonitor is not present in the resource. The notion of "obsolete resource" is defined in clause 9.6.1.3.2 (Common attributes). For a list of the default and allowed values of notificationContentType for each of the supported values of notificationEventType refer to Table 9.6.8-4. |
| --- | --- | --- |

and

Table 6.3.4.2.18-1: Interpretation of notificationContentType

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | All Attributes |  |
| 2 | Modified Attributes |  |
| 3 | ResourceID |  |
| 4 | Trigger Payload |  |
| 5 | TimeSeries notification |  |
| NOTE: See clause 7.4.8 "Resource Type subscription". |

----------------------- Start of new text 1 -----------------------

TP/oneM2M/CSE/SUB/CRE/015

| TP Id | TP/oneM2M/CSE/SUB/CRE/015 |
| --- | --- |
| Test objective | Check that the IUT rejects a CREATE request when the notificationEventType is set to NOTIFICATION_EVENT_TYPE and notificationContentType set to 3 (ResourceID) |
| Reference | TS-0001 [1], clause 9.6.8 and clause 10.2.10.2, TS-0004 [2], clause 7.4.8.2.1, 6.3.4.2.18-19 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource as TARGET_RESOURCE_ADDRESS which is subscribable and the Originator having privileges to perform CREATE operation on TARGET_RESOURCE_ADDRESS resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing Resource Type set to subscription and To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing subscription resource containing eventNotificationCriteria attribute containing notificationEventType element set to NOTIFICATION_EVENT_TYPE and notificationContentType attribute set to 3 (ResourceID) } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) and no Content } | IUT  AE |

| TP Id | NOTIFICATION_EVENT_TYPE |
| --- | --- |
| TP/oneM2M/CSE/SUB/CRE/015_NET/6 | 6 (Trigger_Received_For_AE_Resource) |
| TP/oneM2M/CSE/SUB/CRE/015_NET/7 | 7 (Blocking_Update ) |
| TP/oneM2M/CSE/SUB/CRE/015_NET/8 | 8 (Report_on_missing_data_points) |

TP/oneM2M/CSE/SUB/CRE/016

| TP Id | TP/oneM2M/CSE/SUB/CRE/016 |
| --- | --- |
| Test objective | Check that the IUT rejects a CREATE request when the notificationEventType is set to NOTIFICATION_EVENT_TYPE and notificationContentType set to 5 (TimeSeries notification) |
| Reference | TS-0001 [1], clause 9.6.8 and clause 10.2.10.2, TS-0004 [2], clause 7.4.8.2.1, 6.3.4.2.18-19 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource as TARGET_RESOURCE_ADDRESS which is subscribable and the Originator having privileges to perform CREATE operation on TARGET_RESOURCE_ADDRESS resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing Resource Type set to subscription and To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing subscription resource containing eventNotificationCriteria attribute containing notificationEventType element set to NOTIFICATION_EVENT_TYPE and notificationContentType attribute set to 5 (TimeSeries notification) } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) and no Content } | IUT  AE |

| TP Id | NOTIFICATION_EVENT_TYPE |
| --- | --- |
| TP/oneM2M/CSE/SUB/CRE/016_NET/1 | 1 (Update_of_Resource) |
| TP/oneM2M/CSE/SUB/CRE/016_NET/2 | 2 (Delete_of_Resource) |
| TP/oneM2M/CSE/SUB/CRE/016_NET/3 | 3 (Create_of_Direct_Child_Resource) |
| TP/oneM2M/CSE/SUB/CRE/016_NET/4 | 4 (Delete_of_Direct_Child_Resource ) |
| TP/oneM2M/CSE/SUB/CRE/016_NET/5 | 5 (Retrieve_of_Container_Resource_With_No_Child_Resource) |
| TP/oneM2M/CSE/SUB/CRE/016_NET/6 | 6 (Trigger_Received_For_AE_Resource) |
| TP/oneM2M/CSE/SUB/CRE/016_NET/7 | 7 (Blocking_Update ) |

TP/oneM2M/CSE/SUB/CRE/017

| TP Id | TP/oneM2M/CSE/SUB/CRE/017 |
| --- | --- |
| Test objective | Check that the IUT rejects a CREATE request when the notificationEventType is set to NOTIFICATION_EVENT_TYPE and notificationContentType set to 1 (All Attributes) |
| Reference | TS-0001 [1], clause 9.6.8 and clause 10.2.10.2, TS-0004 [2], clause 7.4.8.2.1, 6.3.4.2.18-19 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource as TARGET_RESOURCE_ADDRESS which is subscribable and the Originator having privileges to perform CREATE operation on TARGET_RESOURCE_ADDRESS resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing Resource Type set to subscription and To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing subscription resource containing eventNotificationCriteria attribute containing notificationEventType element set to NOTIFICATION_EVENT_TYPE and notificationContentType attribute set to 1 (All Attributes) } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) and no Content } | IUT  AE |

| TP Id | NOTIFICATION_EVENT_TYPE |
| --- | --- |
| TP/oneM2M/CSE/SUB/CRE/017_NET/6 | 6 (Trigger_Received_For_AE_Resource) |
| TP/oneM2M/CSE/SUB/CRE/017_NET/7 | 7 (Blocking_Update ) |
| TP/oneM2M/CSE/SUB/CRE/017_NET/8 | 8 (Report_on_missing_data_points) |

---------------------- End of new text 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?