| CHANGE REQUEST |
| --- |
| Meeting ID:* | TDE 55 |
| Source:* | Rahul Kumar, C-DOT, krahul@cdot.in Anupama Chopra, C-DOT, anupama@cdot.in Poornima Shandilya, C-DOT, poornima@cdot.in |
| Date:* | 2022-07-14 |
| Reason for Change/s:* | See the introduction |
| CR against: Release* | Release 4 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018 V4.6.0 |
| Clauses * | 7.2.2.18.2.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2020 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

If this is  a correction, and the change applies to previous releases, a separate “mirror CR” should be posted at the same time as this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made e.g. a change impacting 5 tables should not only include a proposal to change only 3 tables. Include any changes to references, definitions, and abbreviations in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar.

Use change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the proposed new clause is located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to the content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This proposes to modify TPs of <m2mServiceSubscriptionProfile> resource in order to provide linking of AE and <m2mServiceSubscriptionProfile> resource.

### -----------------------Start of change 1-------------------------------------------

##### 7.2.2.18.2	Service Subscription Profile(SSP)

###### 7.2.2.18.2.1	Basic Operation

TP/oneM2M/CSE/SSM/SSP/001

| TP Id | TP/oneM2M/CSE/SSM/SSP/001 |
| --- | --- |
| Test objective | Check that the IUT successfully performs operations on resource m2mServiceSubscriptionProfile for authorized AE |
| Reference | TS-0001 [1], clauses 9.6.19 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_IN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform OPERATION on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to authorized AE-ID } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to RESPONSE_STATUS_CODE } | IUT  AE |

| TP Id | OPERATION | RESPONSE_STATUS_CODE |
| --- | --- | --- |
| TP/oneM2M/CSE/SSM/SSP/001_CRE | CREATE | 2001 (CREATED) |
| TP/oneM2M/CSE/SSM/SSP/001_RET | RETRIEVE | 2000 (OK) |
| TP/oneM2M/CSE/SSM/SSP/001_UPD | UPDATE | 2004 (UPDATED) |
| TP/oneM2M/CSE/SSM/SSP/001_DEL | DELETE | 2002 (DELETED) |

TP/oneM2M/CSE/SSM/SSP/002

| TP Id | TP/oneM2M/CSE/SSM/SSP/002 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the AE not having service subscription tries to perform OPERATION on the resource TARGET_RESOURCE_ADDRESS |
| Reference | TS-0004 [2], clause 7.3.2.1, clause 7.3.2.7 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT not having a m2mServiceSubscriptionProfile resource For the AE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Request from AE } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4128 (SERVICE_SUBSCRIPTION_NOT_ESTABLISHED) } | IUT  CSE |

| TP Id | OPERATION |
| --- | --- |
| TP/oneM2M/CSE/SSM/SSP/002_CRE | CREATE |
| TP/oneM2M/CSE/SSM/SSP/002_RET | RETRIEVE |
| TP/oneM2M/CSE/SSM/SSP/002_UPD | UPDATE |
| TP/oneM2M/CSE/SSM/SSP/002_DEL | DELETE |

TP/oneM2M/CSE/SSM/SSP/003

| TP Id | TP/oneM2M/CSE/SSM/SSP/003 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the AE having inactive service subscription tries to perform a request |
| Reference | TS-0004 [2], clause 7.3.2.1, clause 7.3.2.7, 7.4.20.2.1 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" the IUT having a registration resource containing M2M-Sub-ID attribute set to M2M_SUB_ID originatorID attribute set to AE_ID and the IUT having a m2mServiceSubscriptionProfile resource For the AE_ID containing M2M-Sub-ID attribute set to M2M_SUB_ID status attribute set to INACTIVE} |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Request from AE_ID To set to TARGET_RESOURCE_ADDRESS } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4139 (SERVICE_SUBSCRIPTION_NOT_ACTIVE) } | IUT  CSE |

| TP Id | OPERATION |
| --- | --- |
| TP/oneM2M/CSE/SSM/SSP/003_CRE | CREATE |
| TP/oneM2M/CSE/SSM/SSP/003_RET | RETRIEVE |
| TP/oneM2M/CSE/SSM/SSP/003_UPD | UPDATE |
| TP/oneM2M/CSE/SSM/SSP/003_DEL | DELETE |

TP/oneM2M/CSE/SSM/SSP/004

| TP Id | TP/oneM2M/CSE/SSM/SSP/004 |
| --- | --- |
| Test objective | Check that the IUT processes the request when the AE having an active service subscription tries to perform a request |
| Reference | TS-0004 [2], clause 7.3.2.1, 7.4.20.2.1 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE the IUT having a registration resource containing M2M-Sub-ID attribute set to M2M_SUB_ID originatorID attribute set to AE_ID and the IUT having a m2mServiceSubscriptionProfile resource For the AE_ID containing M2M-Sub-ID attribute set to M2M_SUB_ID status attribute set to ACTIVE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request from AE_ID To set to TARGET_RESOURCE_ADDRESS } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000(OK) } | IUT  CSE |

TP/oneM2M/CSE/SSM/SSP/005

| TP Id | TP/oneM2M/CSE/SSM/SSP/005 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the authorized AE exceeds the request rate limit specified in its service subscription profile |
| Reference | TS-0004 [2], clause 7.3.2.10, 7.4.20.2.1 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE the IUT having a registration resource containing M2M-Sub-ID attribute set to M2M_SUB_ID originatorID attribute set to AE_ID and the IUT having a m2mServiceSubscriptionProfile resource For the AE AE_ID containing M2M-Sub-ID attribute set to M2M_SUB_ID maxRequestRate attribute set to MAX_REQUEST_RATE} |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Request at a rate higher than MAX_REQUEST_RATE from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to authorized AE_ID } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 413x (SERVICE_SUBSCRIPTION_LIMITS_EXCEEDED) } | IUT  CSE |

| TP Id | OPERATION |
| --- | --- |
| TP/oneM2M/CSE/SSM/SSP/005_CRE | CREATE |
| TP/oneM2M/CSE/SSM/SSP/005_RET | RETRIEVE |
| TP/oneM2M/CSE/SSM/SSP/005_UPD | UPDATE |
| TP/oneM2M/CSE/SSM/SSP/005_DEL | DELETE |

TP/oneM2M/CSE/SSM/SSP/006

| TP Id | TP/oneM2M/CSE/SSM/SSP/006 |
| --- | --- |
| Test objective | Check that the IUT processes the request when the authorized AE sends requests within the request rate limit specified in its service subscription profile |
| Reference | TS-0004 [2], clause 7.3.2.10, 7.4.20.2.1 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE the IUT having a registration resource containing M2M-Sub-ID attribute set to M2M_SUB_ID originatorID attribute set to AE_ID and the IUT having a m2mServiceSubscriptionProfile resource For the AE_ID containing M2M-Sub-ID attribute set to M2M_SUB_ID maxRequestRate attribute set to MAX_REQUEST_RATE} |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request at a rate less than MAX_REQUEST_RATE from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to authorized AE_ID } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000(OK) } | IUT  CSE |

TP/oneM2M/CSE/SSM/SSP/007

| TP Id | TP/oneM2M/CSE/SSM/SSP/007 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the authorized AE tries to perform OPERATION on the resource TARGET_RESOURCE_ADDRESS and it exceeds the limit for ATTRIBUTE_NAME in its m2mServiceSubscriptionProfile resource |
| Reference | TS-0004 [2], clause 7.3.3.21, 7.4.20.2.1 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE the IUT having a registration resource containing M2M-Sub-ID attribute set to M2M_SUB_ID originatorID attribute set to AE_ID and the IUT having a m2mServiceSubscriptionProfile resource For the AE_ID containing M2M-Sub-ID attribute set to M2M_SUB_ID ATTRIBUTE_NAME attribute set to MAX_VALUE and the IUT having the current limit with CURRENT_VALUE corresponding to this ATTRIBUTE_NAME equal MAX_VALUE} |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to authorized AE_ID } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 413x (SERVICE_SUBSCRIPTION_LIMITS_EXCEEDED) } | IUT  CSE |

| TP Id | ATTRIBUTE_NAME | OPERATION |
| --- | --- | --- |
| TP/oneM2M/CSE/SSM/SSP/007_MAE | maxNumAEs | CREATE |
| TP/oneM2M/CSE/SSM/SSP/007_MND | maxNumNodes | CREATE |
| TP/oneM2M/CSE/SSM/SSP/007_MNB | maxNumBytes | CREATE |
| TP/oneM2M/CSE/SSM/SSP/007_MNU | maxNumUsers | CREATE |
| TP/oneM2M/CSE/SSM/SSP/007_MNC | maxNumContainers | CREATE |
| TP/oneM2M/CSE/SSM/SSP/007_MIC_CRE | maxNumInstancesPerContainer | CREATE |
| TP/oneM2M/CSE/SSM/SSP/007_MIC_UPD | maxNumInstancesPerContainer | UPDATE |
| TP/oneM2M/CSE/SSM/SSP/007_MNT | maxNumTimeSeries | CREATE |
| TP/oneM2M/CSE/SSM/SSP/007_MMG_CRE | maxMembersPerGroup | CREATE |
| TP/oneM2M/CSE/SSM/SSP/007_MMG_UPD | maxMembersPerGroup | UPDATE |
| TP/oneM2M/CSE/SSM/SSP/007_MNF | maxNumFlexContainers | CREATE |

TP/oneM2M/CSE/SSM/SSP/008

| TP Id | TP/oneM2M/CSE/SSM/SSP/008 |
| --- | --- |
| Test objective | Check that the IUT processes the request when the authorized AE having not exceeded the limit for ATTRIBUTE_NAME in its m2mServiceSubscriptionProfile resource tries to perform OPERATION on the resource TARGET_RESOURCE_ADDRESS |
| Reference | TS-0004 [2], clause 7.3.3.21, 7.4.20.2.1 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE the IUT having a registration resource containing M2M-Sub-ID attribute set to M2M_SUB_ID originatorID attribute set to AE_ID and the IUT having a m2mServiceSubscriptionProfile resource For the AE_ID containing M2M-Sub-ID attribute set to M2M_SUB_ID ATTRIBUTE_NAME attribute set to MAX_VALUE and the IUT having the current limit corresponding to this ATTRIBUTE_NAME with CURRENT_VALUE less than MAX_VALUE} |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to authorized AE_ID } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to RESPONSE_STATUS_CODE } | IUT  CSE |

| TP Id | RESOURCE_TYPE | OPERATION | RESPONSE_STATUS_CODE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/SSM/SSP/008_MAE | maxNumAEs | CREATE | 2001 (CREATED) |
| TP/oneM2M/CSE/SSM/SSP/008_MND | maxNumNodes | CREATE | 2001 (CREATED) |
| TP/oneM2M/CSE/SSM/SSP/008_MNB | maxNumBytes | CREATE | 2001 (CREATED) |
| TP/oneM2M/CSE/SSM/SSP/008_MNU | maxNumUsers | CREATE | 2001 (CREATED) |
| TP/oneM2M/CSE/SSM/SSP/008_MNC | maxNumContainers | CREATE | 2001 (CREATED) |
| TP/oneM2M/CSE/SSM/SSP/008_MIC_CRE | maxNumInstancesPerContainer | CREATE | 2001 (CREATED) |
| TP/oneM2M/CSE/SSM/SSP/008_MIC_UPD | maxNumInstancesPerContainer | UPDATE | 2004 (UPDATED) |
| TP/oneM2M/CSE/SSM/SSP/008_MNT | maxNumTimeSeries | CREATE | 2001 (CREATED) |
| TP/oneM2M/CSE/SSM/SSP/008_MMG_CRE | maxMembersPerGroup | CREATE | 2001 (CREATED) |
| TP/oneM2M/CSE/SSM/SSP/008_MMG_UPD | maxMembersPerGroup | UPDATE | 2004 (UPDATED) |
| TP/oneM2M/CSE/SSM/SSP/008_MNF | maxNumFlexContainers | CREATE | 2001 (CREATED) |

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?