| CHANGE REQUEST |
| --- |
| Meeting ID:* | TDE 56 |
| Source:* | Siddharth Trikha, C-DOT, strikha@cdot.in Poornima Shandilya, C-DOT, poornima@cdot.in Anupama Chopra, C-DOT, anupama@cdot.in |
| Date:* | 2022-09-23 |
| Reason for Change/s:* | See the introduction |
| CR against: Release* | Release 4 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018 V4.6.0 |
| Clauses * | 7.2.2.18.3, 7.2.2.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2020 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

If this is  a correction, and the change applies to previous releases, a separate “mirror CR” should be posted at the same time as this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made e.g. a change impacting 5 tables should not only include a proposal to change only 3 tables. Include any changes to references, definitions, and abbreviations in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar.

Use change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the proposed new clause is located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to the content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposes to add validation in Create and Update procedure of <serviceSubscribedAppRule> resource for attribute allowedApp-IDs. This CR also adds validation in AE Registration request for App-ID attribute.

### -----------------------Start of change 1-------------------------------------------

7.2.2.18.3	Service Subscribed App Rule(SSAR)TP/oneM2M/CSE/SSM/SSAR/001

| TP Id | TP/oneM2M/CSE/SSM/SSAR/001 |
| --- | --- |
| Test objective | Check that the IUT successfully performs operations on resource seriviceSubscribedAppRule for authorized AE |
| Reference | TS-0001 [1], clauses 9.6.29, TS-0004, clauses 7.4.29 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_IN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform OPERATION on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to authorized AE-ID } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to RESPONSE_STATUS_CODE } | IUT  AE |

| TP Id | OPERATION | RESPONSE_STATUS_CODE |
| --- | --- | --- |
| TP/oneM2M/CSE/SSM/SSAR/001_CRE | CREATE | 2001 (CREATED) |
| TP/oneM2M/CSE/SSM/SSAR/001_RET | RETRIEVE | 2000 (OK) |
| TP/oneM2M/CSE/SSM/SSAR/001_UPD | UPDATE | 2004 (UPDATED) |
| TP/oneM2M/CSE/SSM/SSAR/001_DEL | DELETE | 2002 (DELETED) |

TP/oneM2M/CSE/SSM/SSAR/002

| TP Id | TP/oneM2M/CSE/SSM/SSAR/002 |
| --- | --- |
| Test objective | Check that the IUT rejects a <serviceSubscribedAppRule> OPERATION of the AE if allowedApp-IDs attribute is set to LIST_OF_APP_IDS and this list contains the INVALID_APP_ID_PATTERN. |
| Reference | TS-0001 [1], clauses 9.6.29, TS-0004, clauses 7.4.29.2.1 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_IN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform OPERATION on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid OPERATION Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to authorized AE-ID and Content containing serviceSubscribedAppRule resource containing allowedApp-IDs set to LIST_OF_APP_IDS containing INVALID_APP_ID_PATTERN } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to RESPONSE_STATUS_CODE } | IUT  AE |
| NOTE: INVALID_APP_ID_PATTERN = Pattern starting with other than ‘*’, 'R' or 'N' |

| TP Id | OPERATION | RESPONSE_STATUS_CODE |
| --- | --- | --- |
| TP/oneM2M/CSE/SSM/SSAR/002_CRE | CREATE | 4000 (BAD_REQUEST) |
| TP/oneM2M/CSE/SSM/SSAR/002_UPD | UPDATE | 4000 (BAD_REQUEST) |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

#### 7.2.2.2	Registration (REG)

##### 7.2.2.2.2	CREATE Operation

TP/oneM2M/CSE/REG/CRE/001

| TP Id | TP/oneM2M/CSE/REG/CRE/001 |
| --- | --- |
| Test objective | Check that the IUT accepts a create request of <AE> resource with attributes multiplicity equals to 1 and provided preprovisioned SP_RELATIVE_ AE_ID |
| Reference | TS-0001 [1], clause 10.1.1.2.2 case b, TS-0004 [2], clause 7.4.5.2.1 |
| Config Id | CF01 |
| Parent Release | PARENT_RELEASE |
| PICS Selection | PICS SELECTION |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having preconfigured AE_ID_stem } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to CSEBASE_RESOURCE_ADDRESS and From set to SP_RELATIVE_AE_ID and Resource Type set to 2(AE) and Content containing AE resource representation } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) and Content containing AE resource representation } | IUT ( AE |

| TP Id | PARENT_RELEASE | SP_RELATIVE_ AE_ID | PICS SELECTION |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/REG/CRE/001_CAE | Release 1 | Starting with “C” | PICS_CSE |
| TP/oneM2M/CSE/REG/CRE/001_SAE | Release 2 | Starting with “S” | PICS_IN_CSE |

### …….

TP/oneM2M/CSE/REG/CRE/032

| TP Id | TP/oneM2M/CSE/REG/CRE/032 |
| --- | --- |
| Test objective | Check that the IUT rejects an AE registration for CSEs for which the associated <serviceSubscribeNode> resource is not linked with the <serviceSubscribedAppRule> via the ruleLinks attribute of the <serviceSubscribedNode> resource |
| Reference | TS-0001 [1], clause 10.2.2.1 |
| Config Id | CF01 |
| Parent Release | Release 4 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having the serviceSubscribedNode resource For the CSE containing ruleLinks attribute not set } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing Resource Type set to 2 (AE) } | IUT ( AE |
|  | then { the IUT does not create the AE resource and the IUT sends a valid Response containing Response Status Code set to 4126(APP_RULE_VALIDATION_FAILED) } | IUT ( AE |

TP/oneM2M/CSE/REG/CRE/033

| TP Id | TP/oneM2M/CSE/REG/CRE/033 |
| --- | --- |
| Test objective | Check that the IUT rejects an AE registration request if supportedReleaseVersions attribute is set to a value indicating release version 4 or above and App-ID attribute is set to a INVALID_APP_ID |
| Reference | TS-0001 [1], clause 10.2.2.1 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having preconfigured AE_ID_stem } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing Resource Type set to 2 (AE) and From set to AE_ID_STEM and Content containing AE resource containing supportedReleaseVersions set to 4 or above App-ID attribute set to INVALID_APP_ID } | IUT ( AE |
|  | then { the IUT does not create the AE resource and the IUT sends a valid Response containing Response Status Code set to 4000(BAD_REQUEST) } | IUT ( AE |
| Note: INVALID_APP_ID: value starting with other than ‘R’ or ‘N’ |

TP/oneM2M/CSE/REG/CRE/034

| TP Id | TP/oneM2M/CSE/REG/CRE/034 |
| --- | --- |
| Test objective | Check that the IUT rejects an AE registration request if supportedReleaseVersions attribute is set to a value indicating release version 3 or below and App-ID attribute is set to a value starting with other than ‘r’, ‘R’ or ‘N’ |
| Reference | TS-0001 [1], clause 10.2.2.1 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having preconfigured AE_ID_stem } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing Resource Type set to 2 (AE) and From set to AE_ID_STEM and Content containing AE resource containing supportedReleaseVersions set to 3 or below App-ID attribute set to INVALID_APP_ID } | IUT ( AE |
|  | then { the IUT does not create the AE resource and the IUT sends a valid Response containing Response Status Code set to 4000(BAD_REQUEST) } | IUT ( AE |
| Note: INVALID_APP_ID: value starting with other than ‘r’, ‘R’ or ‘N’ |

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

Conflicts with TS-0001 clause 7.2 “the format of AE-ID or CSE-ID in the From parameter shall be set in a shortest format by the Originator in the initial request” It should be AE-ID-Stem.