| CHANGE REQUEST |
| --- |
| Meeting ID:* | TDE #60 |
| Source:* | JaeSeung Song, Sejong University, jssong@sejong.ac.kr |
| Date:* | 2023-06-28 |
| Reason for Change/s:* | Intoduce a new product profile for lightweight MN |
| CR against: Release* | Release 4 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0025-V3.0.1 |
| Clauses * | 5.9 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2020 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

If this is  a correction, and the change applies to previous releases, a separate “mirror CR” should be posted at the same time as this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made e.g. a change impacting 5 tables should not only include a proposal to change only 3 tables. Include any changes to references, definitions, and abbreviations in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar.

Use change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the proposed new clause is located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to the content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposes to add a new product profile for lightweight MN.

### -----------------------Start of change 1 -------------------------------------------

## 5.8	Gateway as MN

### 5.8.1	Profile description

The profile defines gateways that may support multiple different area network technologies and connect devices from the corresponding area networks. The devices may be oneM2M defined ADNs,  ASNs or NoDNs which are not defined by oneM2M. The gateway hosts resources to enforce common services that devices in the area network may utilize the enable local services without the dependency of the platform and the wide area network.

### 5.8.2	Profile usage examples

Home gateways deployed in the home for smart home:

Sensors, actuators and home appliances are connected with the home gateway. Applications can be connected through the platfrom to access the smart home service as well as applications can be directly connected with the gateway to do the same thing.

Head unit in connected vehicles:

Sensors and actuators in the car are connected with the head unit. The sensed data and control command are reported to delivered through the head unit. Applications may access the head unit and monitor the car state via the platform. Applications may also access the head unit once connected directly with the head unit via area network such as Wifi or Bluetooth.

### 5.8.3	Fundamental feature sets

#### …

## 5.9	Lightweight MN Profile

### 5.9.1	Profile description

IoT services can be provided in various environments, and one of them could involve an independent IoT service offered in a localized area where small sensors are interconnected and managed via an edge node. The edge node is a place where data is collected and processed, rather than sending data back to a centralized cloud IoT platform. For instance, a company that runs a small smart factory might manage its own lightweight IoT platform server on an edge node at a gateway, without relying on a cloud-based IoT service. In such cases, it is possible to deploy and manage the IoT platform solely with small-scale MN profile functionalities. These could include supporting only a single binding such as HTTP and supporting only the structured identifier option.

### 5.9.2	Profile usage examples

An IoT gateway with small number of IoT sensors and actuators that runs in a small size smart factory.

An IoT gateway that runs on an edge/fog node.

### 5.9.3	Fundamental feature sets

Editor’s note: feature sets for lightweight MN will be specified later after discussion.

## 5.10 Field configurable oneM2M Entity Hosted on a 3GPP Device

### 5.10.1	Profile description

The profile defines the features required for a oneM2M entity hosted on a 3GPP device. This profile is intended to add required features to those specified in other profiles. For example, a temperature sensor hosted on an CIoT device would required the features described in this section plus the features described for a Constrained Sensor device.

### 5.10.2	Profile usage examples

The profile applies to CIoT devices that can receive trigger messages via a 3GPP core network. The trigger messages are used provision the device with enrolment credentials, register the device to a oneM2M CSE and re-establish a connection to the Registrar CSE.

### ----------------------- End of change 1 -------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?