| CHANGE REQUEST |
| --- |
| Meeting ID:* | TDE 62 |
| Source:* | Akash, TSDSI, akash@tsdsi.in |
| Date:* | 2023-12-07 |
| Reason for Change/s:* | Test purposes covering requestaggregation attribute |
| CR against: Release* | Release 4 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018 V4.7.0 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2020 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

If this is  a correction, and the change applies to previous releases, a separate “mirror CR” should be posted at the same time as this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made e.g. a change impacting 5 tables should not only include a proposal to change only 3 tables. Include any changes to references, definitions, and abbreviations in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar.

Use change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the proposed new clause is located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to the content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution presents test purposes for the requestaggregation attribute of the polling channel resource.

### -----------------------Start of change 1-------------------------------------------

| TP Id | TP/oneM2M/AE/PCH/003 |
| --- | --- |
| Test objective | Check that the IUT sends an RETRIEVE Request to <pollingChannelURI> of a <pollingChannel> resource with requestAggregation attribute set to true |
| Reference | TS-0001 - clause 10.2.5.12, 10.2.5.13, TS-0004 – 7.4.22.1, 7.4.22.2.2 |
| Config Id | CF02 |
| Parent Release | Release 4 |
| PICS Selection | PICS_PCH |
| Initial conditions | with { the IUT being registered with CSE and the IUT being switched on and the IUT having created <pollingChannel> resource with CSE containing its requestAggregation attribute set to true } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a valid RETRIEVE Request containing To set to POLLINGCHANNELURI _RESOURCE_ADDRESS } | NA |
|  | then { the IUT sends a valid RETRIEVE Request containing To set to POLLINGCHANNELURI _RESOURCE_ADDRESS From set to AE_ID } | IUT ( CSE |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

| TP Id | TP/oneM2M/CSE/PCH/007 |
| --- | --- |
| Test objective | Check that the IUT which hosts <pollingChannel> resource containing several requests for AE sends an RETRIEVE response containing all requests after IUT has received a long polling request from AE. |
| Reference | TS-0001 - clause 10.2.5.18, TS-0004 – 7.4.22.2.2 |
| Config Id | CF02 |
| Parent Release | Release 4 |
| PICS Selection | PICS_PCH |
| Initial conditions | with { the IUT being in the “initial state” and the IUT having registered an AE containing and the AE having a child <pollingChannel> resource containing requestaggregation attribute set to true and the IUT storing several requests for the AE and the IUT having received a NOTIFY Request from CSE containing To set to AE_RESOURCE_ADDRESS and From set to CSE_ID } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request containing To set to POLLINGCHANNELURI _RESOURCE_ADDRESS From set to AE_ID } | AE ( IUT |
|  | then { the IUT sends a valid RETRIEVE response containing To set to AE_ID From set to CSE_ID and Content containing aggregatedRequestPrimitive element containing requests in order } | AE ( IUT |

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?