## Slide 1: oneM2M High Level Overview
Current Status of Standardization in M2M – September 2014 Nicolas Damour, ndamour@sierrawireless.com

## Slide 2: Landscape of M2M Applications 1/5
Payment
Energy
Health
Automotive

## Slide 3: Landscape of M2M Applications 2/5
Payment
Energy
Health
Automotive
Communication Devices & Hardware

## Slide 4: Landscape of M2M Applications 3/5
Payment
Energy
Health
Automotive
Communication Devices & Hardware
Communication Technologies & Protocols

## Slide 5: Landscape of M2M Applications 4/5
Payment
Energy
Health
Automotive
Communication Devices & Hardware
Communication Technologies & Protocols
Application
Application
Application
Application

## Slide 6: Landscape of M2M Applications 5/5
Home
Energy
Health
Automotive
Communication Devices & Hardware
Communication Technologies & Protocols
Application
Application
Application
Application
M2M Horizontal Platform

## Slide 7: What is oneM2M – www.onem2m.org
  Seven institutional regional SDOs* (so-called “partners type 1”) involved:
    ATIS Alliance for Telecommunications Industry Solutions USA
    ARIB Association of Radio Industries and Businesses Japan
    CCSA China Communication Standards Association China
    ETSI European Telecommunications Standards Institute European Union
    TIA Telecommunications Industry Association USA
    TTA Telecommunications Technology Association Korea
    TTC Telecommunication Technology Committee Japan
  Secondary partners “partners type 2” from the technology and industry side
    Open Mobile Alliance
    Home Gateway Initiative
  It is a partnership project for M2M standards, much like 3GPP
  Aimed at producing “globally applicable, access-independent Technical Specifications and Technical Reports to define and specify a common, efficient, easily and widely available M2M Service Layer”.
  See the partnership agreement on the OneM2M website: http://onem2m.org/docs/Partnership_Agreement_FINAL.pdf
    BroadBand Forum
    Continua Health Alliance
* Standards Development Organization

## Slide 8: Timeline of oneM2M
  2009 Jan. ETSI M2M started to work
  2010 Feb. TIA TR-50 started to work
  2011 Aug. Release 1 of ETSI M2M standard published
  2011 Sep. Start of discussions to form oneM2M globally
  2012 Sep. First Technical Plenary meeting of oneM2M
  2013 Oct. Approval of Technical Specification on Requirements
  2014 Jun. Approval of Technical Specification on Architecture
  2014 Aug. Approval of candidate oneM2M release 1
  2014 Dec. oneM2M “Launch Event” with oneM2M demos
  2014 Dec. Approval of final oneM2M release 1

## Slide 9: oneM2M – Organization
TECHNICAL PLENARY Chair: Peter Nurse (Qualcomm) Vice-chairs: N. Yamasaki (KDDI); Y. Chang (Samsung)
  <Vacant chairmanship>
  J. Swetina (NEC) R. Bhalla (ZTE)
WG1 Requirements
WG2 Architecture
WG3 Protocols
WG4 Security
WG5 Management, Abstraction, Semantics
  F. Ennesser (Gemalto)
  D. Vujcic (Oberthur)
  T. MacAuley (MacAffee)
  R. Forbes (Ericsson) P. Jacobs (Cisco) S. Fujimoto (Fujitsu)
  Y. Zhang (Huawei)
  P. Martigne (Orange)
  T. Carey (Alcatel-Lucent)
STEERING COMMITTEE Chair: Fran O'Brien (Cisco, TIA) Vice-chairs: P. Jain (Intel, ATIS); T. Li (Huawei, CCSA); E. Scarrone (Telecom Italia, ETSI)
  O. Elloumi (Alcatel-Lucent) N. Damour (Sierra Wireless) M. Tseng (Huawei)
Finance Committee
Marketing & Communication
Legal Subcommittee
Methods & Processes
Ad-Hoc Group Work Program Management
N. Damour (Sierra Wireless)
Ad-Hoc Group Methods of Work
E. Scarrone (Telecom Italia)

## Slide 10: Use Cases Technical Report Overview
Energy | Wide area energy related measurement & control system for transmission and distribution | Analytics for oneM2M | Smart Meter Reading | Environmental Monitoring for Hydro-Power Generation using Satellite M2M | Oil and Gas Pipeline Cellular/Satellite Gateway |  | 
Enterprise | Smart building |  |  |  |  |  | 
Healthcare | M2M Healthcare Gateway | Wellness services |  |  |  |  | 
Public Services | Street Light Automation | Devices, Virtual devices and Things | Car/Bicycle Sharing Services | Smart parking |  |  | 
Residential | Home Energy Management | Home Energy Management System | Plug-In Electrical Charging Vehicles and power feed in home scenario | Real-time Audio/Video Communication | Event Triggered Task Execution |  | 
Transportation | Vehicle Diagnostic & Maintenance Report | Remote Maintenance services | Neighborhood Alerting on Traffic Accident | Fleet management service using Digital Tachograph |  |  | 
Other | Extending the M2M Access Network using Satellites | Peer communication between M2M devices | M2M data traffic management by underlying network operator | Collection of M2M system data | Optimizing connectivity management parameters with mobile networks | Optimizing mobility management parameters with mobile networks | Sleepy nodes

## Slide 11: Requirements Overview
  Functional Requirements in TS-0002 on Requirements
    OSR 72 agreed requirements Overall System Requirements
    MGR 17 agreed requirements Management Requirements
    ABR 03 agreed requirements Abstraction Requirements
    SMR 07 agreed requirements Semantics Requirements
    SER 26 agreed requirements Security Requirements
    CHG 06 agreed requirements Charging Requirements
    OPR 06 agreed requirements Operational Requirements
    CRPR 05 agreed requirements Comm. Request Processing Requirements
    NFR 02 agreed requirements Non Functional Requirements
  Examples of requirements
    [OSR-001] The M2M System shall be able to allow communication between M2M Applications in the Network Domain & M2M Applications in the Device Domain by using multiple communication means based on IP access.
    [MGR-007] The M2M System shall provide the capability for monitoring and diagnostics of M2M Gateways/Devices in M2M Area Networks.
    [SER-008] The M2M system shall support countermeasures against unauthorized access to M2M services and M2M application services.

## Slide 12: Architecture Overview
Underlying Network
Underlying Network
Node: Logical equivalent of a physical (or possibly virtualized, especially on the server side) device
Application Service Node
Middle Node
Infrastructure Node

## Slide 13: Architecture Overview 1/3
Underlying Network
Underlying Network
Node: Logical equivalent of a physical (or possibly virtualized, especially on the server side) device
Network Services Entity: Provides services to the CSEs besides the pure data transport needed for Mcc. Examples: device management, location services, device triggering...
NSE
NSE
NSE
NSE
Application Service Node
Middle Node
Infrastructure Node
Network Layer

## Slide 14: Architecture Overview 2/3
Underlying Network
Underlying Network
Node: Logical equivalent of a physical (or possibly virtualized, especially on the server side) device
Network Services Entity: Provides services to the CSEs besides the pure data transport needed for Mcc. Examples: device management, location services, device triggering...
Application Entity: Provides application logic for the end-to-end M2M solutions. Examples: fleet tracking application, blood sugar monitoring application, power metering application.
NSE
NSE
NSE
NSE
Application Service Node
Middle Node
Infrastructure Node
Network Layer
AE
AE
AE
Application Layer

## Slide 15: Architecture Overview 3/3
A
Underlying Network
Underlying Network
Node: Logical equivalent of a physical (or possibly virtualized, especially on the server side) device
Network Services Entity: Provides services to the CSEs besides the pure data transport needed for Mcc. Examples: device management, location services, device triggering...
Application Entity: Provides application logic for the end-to-end M2M solutions. Examples: fleet tracking application, blood sugar monitoring application, power metering application.
Common Services Entity: Provides the set of "service functions" that are common to the M2M environments.
Reference Points: Mcc (CSE-CSE), Mca (CSE-AE), Mcn (CSE-NSE) and Mcc’ (between 2 service providers). Mch, for charging, is also defined (but not shown here) between the IN-CSE and a charging server.
CSE
AE
NSE
CSE
AE
NSE
CSE
AE
NSE
NSE
Application Service Node
Middle Node
Infrastructure Node
Application Layer
Service Layer
Network Layer
Mca
Mcn
Mca
Mca
Mcn
Mcn
Mcn
Mcc
Mcc

## Slide 16: OneM2M Complete Architecture Overview
A
Underlying Network
Underlying Network
Node: Logical equivalent of a physical (or possibly virtualized, especially on the server side) device
Network Services Entity: Provides services to the CSEs besides the pure data transport needed for Mcc. Examples: device management, location services, device triggering...
Application Entity: Provides application logic for the end-to-end M2M solutions. Examples: fleet tracking application, blood sugar monitoring application, power metering application.
Common Services Entity: Provides the set of "service functions" that are common to the M2M environments.
Reference Points: Mcc (CSE-CSE), Mca (CSE-AE), Mcn (CSE-NSE) and Mcc’ (between 2 service providers). Mch, for charging, is also defined (but not shown here) between the IN-CSE and a charging server.
CSE
AE
NSE
CSE
AE
NSE
CSE
AE
NSE
NSE
Application Service Node
Middle Node
Infrastructure Node
Application Layer
Service Layer
Network Layer
IN (other SP)
CSE
Mca
Mcn
Mca
Mca
Mcn
Mcn
Mcn
Mcc
Mcc
Mcc’

## Slide 17: Common Services
  Identification Identity management of the entities (AEs, CSEs, NSEs, …)
  Registration CSE-CSE Registration, AE-CSE Registration, …
  Discovery Discovery of entities and information/resources
  Security confidentiality, integrity, availability, credential/key management, encryption, privacy, authentication, authorization
  Group Management Management of groups, support of bulk operations and access
  Device Management Firmware updates, configuration settings, topology management, Software installation, logging, monitoring, diagnostics, Reuse of existing DM technologies
  Subscribe / Notify Support of event-related notifications (change of values)
  Network Exposure Abstraction of the underlying network interface, (eg. usage of remote device triggering, location services, …)
  Comm. Management Selection of communications channels, scheduling, Store-and-forward, reachability status awareness
  Location Manages and provides location information services
Note: this is a non-exhaustive list and provides only the most important defined common services

## Slide 18: Information Modeling: Resources
  Information is stored in the system as “Resources” addressable via a URI
  A given Resource has a one of the defined Resource Types, defining the semantics of the information contained in the resource, including the attributes of the resource
  Resources can be Created, Read, Updated or Deleted to manipulate the information
  Resources are addressable through a tree-like structure, with links that can be either “hard-coded” in the tree hierarchy (plain lines below) or freely reference another part or the tree (dotted lines below)

## Slide 19: Resource Types & Flows
  The following resource types are defined:
    CSEBase, remoteCSE: information about the Common Services Entity
    node: information about the node containing the entities
    application: information about the Application Entities
    container, instance: applicative data created and used by the Application Entities
    accessControlPolicy: information about access control policies
    subscription: information about subscription/notification mechanisms
    delivery, request, schedule, pollingChannel: information about synch/asynch message flows
    locationPolicy: information about location policies
    group, members: information used for group management
    mgmtObj, parameters, mgmtCmd, execInstance: information used for device management
    m2mServiceSubscription, nodeInfo: information about the service-layer subscription
    cmdhPolicy, cmdhDefaults, cmdhDefEcValue, cmdhEcDefParamValues, cmdhLimits, cmdhNetworkAccessRules, cmdhNwAccessRule, cmdhBuffer: comm. scheduling info
    statsConfig, eventConfig, statsCollect: information used for service-layer charging
    announcement: information used to proxy resources into another CSE
  The following flow schemes are defined:
    Blocking (synchronous) request-response, either local, over 1 hop or (routed) multi-hops
    Non-blocking (synchronous) request-response, with regular polling from the requester
    Non-blocking (asynchronous) request-response, with callback from the receiver to the requester

## Slide 20: OneM2M Service Oriented internal architecture
Work defined in the Technical Specification TS-0007 – Service Component Architecture Supported by Alcatel-Lucent and Ericsson

## Slide 21: WG3 – Protocols 1/2
  Study TR-0009 Technical Report on candidate protocols complete
  Candidate protocols that were studied for Service and Data Management are:
    HTTP
    CoAP
    MQTT
    TIA TR-50
    XMPP
    WebSocket
    Bluetooth
    DDS
    Modbus
    DNP3

## Slide 22: WG3 – Protocols 2/2
  Core Protocol TS-0004 Technical Specification
  Retained main protocols on Mca and Mcc are HTTP, CoAP and MQTT (for transport)
  Data payload considered is XML and JSON
  Specific features for each protocol are defined in a dedicated:
    oneM2M-TS-0008 for CoAP (RESTful request/response protocol over UDP or DTLS)
    oneM2M-TS-0009 for HTTP (RESTful request/response protocol over TCP or TLS)
    oneM2M-TS-0010 for MQTT (Connected Publish/Subscribe protocol over TCP or TLS)
  HTTP example (with filter criteria, for resource discovery)
    GET http://airvantage.net/oneM2M/root?label=one&label=two&createdBefore=2014-01-01
  MQTT example
    All entities first connect to an MQTT broker and subscribe to “their topic”
    Topics identify the entities (AEs and CSEs) that communicate over Mca and Mcc. Example: /oneM2M/req/CSE-45678
    The messages used for actual communication are then PUBLISH messages
    The payload identifies the details of the operation. Example (in JSON): {“op”: “RETRIEVE”, “fr”: “AE-ID”, “to”: “CSE-ID/resource”}

## Slide 23: WG4 – Security
  The Technical Report TR-0008 compiles a study on security threats
  22 different threats on M2M systems have been listed
  26 possible countermeasures have been proposed and evaluated
  The Technical Specification TS-0003 defines the security mechanisms
  Security is one of the Common Services Functions (see slides 20 and 21).
  The retained functionalities so far are:
    Access Management (Authentication, Authorization, Access Control)
    Security Transport Layer
    Sensitive Data Handling (Sensitive Functions protection, Secure Storage)
    Security Association Establishment (Secure Connection via secure session establishment, Secure Connection via object security)
    Security Administration (including security bootstrapping)
    Identity Protection
  Supported features
    Security Bootstrapping through PSK (based on shared keys or based on the SIM) or PKI
    Channel encryption based on TLS or DTLS

## Slide 24: WG5 – Device Management & Semantics
  Two main areas of work
  Reuse of existing Device Management technologies
  Supported dedicated technologies: OMA DM 1.3, DM 2.0, LWM2M and BBF TR069.
  Mapping of defined management objects onto oneM2M resources
  Support for data semantics: not part of the release 1
  Study in Technical Report has been carried out, but no specification yet.