| oneM2M Technical Specification |
| --- |
| Document Number | oneM2M-TS-0005-V-0.1.0 |
| Document Name: | Management Enablement (OMA) |
| Date: | 2014-04-21 |
| Abstract: | Specifies the usage of OMA DM and OMA LWM2M resources and the corresponding message flows including normal cases as well as error cases to fulfil the oneM2M management requirements. Mapping between the oneM2M management related resources and the resources from OMA. Protocol translation between the oneM2M service layer and OMA. The Mca reference point, ms interface and la interface are possibly involved in this protocol translation. Resource definitions in OMA to fulfil the oneM2M management requirements. |

This Specification is provided for future development work within oneM2M only. The Partners accept no liability for any use of this Specification.

The present document has not been subject to any approval process by the oneM2M Partners Type 1.  Published oneM2M specifications and reports for implementation should be obtained via the oneM2M Partners' Publications Offices.

About oneM2M

The purpose and goal of oneM2M is to develop technical specifications which address the need for a common M2M Service Layer that can be readily embedded within various hardware and software, and relied upon to connect the myriad of devices in the field with M2M application servers worldwide.

More information about oneM2M may be found at:  http//www.oneM2M.org

Copyright Notification

No part of this document may be reproduced, in an electronic retrieval system or otherwise, except as authorized by written permission.

The copyright and the foregoing restriction extend to reproduction in all media.

© 2013, oneM2M Partners Type 1 (ARIB, ATIS, CCSA, ETSI, TIA, TTA, TTC).

All rights reserved.

Notice of Disclaimer & Limitation of Liability

The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations. No recommendation as to products or vendors is made or should be implied.

NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE, GOVERNMENTAL RULE OR REGULATION, AND FURTHER, NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS. NO oneM2M PARTNER TYPE 1 SHALL BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY THAT PARTNER FOR THIS DOCUMENT, WITH RESPECT TO ANY CLAIM, AND IN NO EVENT SHALL oneM2M BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES. oneM2M EXPRESSLY ADVISES ANY AND ALL USE OF OR RELIANCE UPON THIS INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER.

# Contents

Contents	3

1	Scope	4

2	References	4

2.1	Normative references	4

2.2	Informative references	4

3	Definitions, symbols, abbreviations and acronyms	4

3.1	Definitions	4

3.2	Symbols	5

3.3	Abbreviations	5

3.4	Acronyms	5

4	Conventions	5

5.	OMA DM 1.3 and OMA DM 2.0	5

5.1	Mapping of basic data types	5

5.2	Mapping of Identifiers	6

5.3	Mapping of resources	6

5.3.1	General Mapping Assumptions	6

5.3.2	Resource [firmware]	6

5.3.3	Resource [software]	7

5.3.4	Resource [memory]	7

5.3.5	Resource [areaNwkInfo]	7

5.3.6	Resource [areaNwkDeviceInfo]	7

5.3.7	Resource [battery]	8

5.3.8	Resource [deviceInfo]	8

5.3.9	Resource [deviceCapability]	8

5.3.10	Resource [reboot]	9

5.3.11	Resource [eventLog]	9

6.	OMA Lightweight M2M 1.0	10

6.1	Mapping of basic data types	10

6.2	Mapping of Identifiers	10

6.3	Mapping of resources	10

6.3.1	General Mapping Assumptions	11

6.3.2	Resource [memory]	11

6.3.3	Resource [battery]	11

6.3.4	Resource [deviceInfo]	11

6.3.5	Resource [reboot]	11

7	Mapping of procedures for management	12

8	Server Interactions	12

8.1	Server interaction management	12

8.2	Authorization	12

9	New Management Technology Specific Resources	12

Proforma copyright release text block	12

Annexes	13

Annex <y>: Bibliography	13

History	14

# 1	Scope

The present document specifies the protocol translation and mappings between the oneM2M Service layer and management technologies specified by OMA such as OMA DM 1.3, OMA DM 2.0 and OMA LightweightM2M. Note that OMA DM 1.3 and OMA DM 2.0 are collectively called as OMA DM in this document.

# 2	References

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references,only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M TS-0001: “oneM2M Functional Architecture”

[2]	oneM2M TS-0004: “oneM2M Protocol Specification”

[3]	oneM2M TR-0004: “Definitions and Acronyms”

[4]	“OMA Device Management Protocol”, Version 1.3, Open Mobile Alliance™, http://www.openmobilealliance.org/

[5]	“OMA Device Management Protocol”, Version 2.0, Open Mobile Alliance™, http://www.openmobilealliance.org/

[6]	"OMA LightweightM2M”, Version 1.0, Open Mobile Alliance™, http://www.openmobilealliance.org/

## 2.2	Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

# 3	Definitions, symbols, abbreviations and acronyms

For the purposes of the present document, the terms and definitions given in TR-0004 [3] apply. In addition, the terms and definitions defined in this section apply.

## 3.1	Definitions

Definition format

<defined term>: <definition>

<defined term>[N]: <definition>

example 1: text used to clarify abstract rules by applying them literally

NOTE:	This may contain additional information.

## 3.2	Symbols

Symbol format

<symbol>	<Explanation>

<2nd symbol>	<2nd Explanation>

<3rd symbol>	<3rd Explanation>

## 3.3	Abbreviations

Abbreviation format

<ABREVIATION1>	<Explanation>

<ABREVIATION2>	<Explanation>

<ABREVIATION3>	<Explanation>

## 3.4	Acronyms

Acronym format

<ACRONYM1>	<Explanation>

<ACRONYM2>	<Explanation>

<ACRONYM3>	<Explanation>

# 4	Conventions

The key words “Shall”, ”Shall not”, “May”, ”Need not”, “Should”, ”Should not” in this document are to be interpreted as described in the oneM2M Drafting Rules [i.1]

# 5.	OMA DM 1.3 and OMA DM 2.0

## 5.1	Mapping of basic data types

oneM2M has defined the data types that describe the format of the value stored at the attribute. Those oneM2M data types are listed in the below table, and mapped to the data types specified by OMA DM Protocol [4], [5]. Note that OMA DM 1.3 [4] and OMA DM 2.0 [5] uses the same data types.

| oneM2M Data Types | Mapping to data types in OMA DM | description |
| --- | --- | --- |
| TBD | null |  |
| TBD | b64 |  |
| TBD | bin |  |
| TBD | bool |  |
| TBD | chr |  |
| TBD | int |  |
| TBD | xml |  |
| TBD | date |  |
| TBD | time |  |
| TBD | float |  |

Note: there is one more data type in OMA DM, which is not listed in the above table. It is the 'node' data type that describes the format of the Interior Node that can have child Nodes. oneM2M release 1 may not support the hierarchical structure for <mgmtObj> resource; hence it may not be able to have a mapping for the 'node' data type in OMA DM.

## 5.2	Mapping of Identifiers

OMA DM 1.3 and OMA DM 2.0 specifies many identifiers including device identifier, server identifier, client version identifier, manufacturer identifier, etc. To enable the device management using OMA DM Protocol, oneM2M identifiers needs to be mapped to identifiers specified by OMA DM Protocol. Below table shows the oneM2M identifiers that needs to be mapped to OMA DM Protocol.

| oneM2M | Mapping to OMA DM Identifiers | Description |
| --- | --- | --- |
| M2M-Node-ID. | Device Identifier (i.e., DevId node in DevInfo MO) | In OMA DM, the device identifier is a unique identifier for the device. This value is globally unique and MUST be formatted as a URN. OMA DM Gateways and OMA DM enabled devices are assigned with the device identifiers, and each can be mapped to the M2M-Node-ID. Note: In case that the notion of the device identifier is not supported by the device, the DM Gateway can assign the local identifier for the device, and the M2M-Node-ID should be mapped to this local identifier. |
| The objectID attribute in <mgmtObj> resource. | MOID | A unique identifier of the management object. Each MO is characterized by a unique MOID, which is generally a URN. |
| The objectPath attribute in <mgmtObj> resource | URI for the local path in the device where the relevant Management Object is located | Management Objects in the device are uniquely addressed by a URI that is stored in the objectPath attribute. Note that DM 1.3 and DM 2.0 uses different Addressing scheme, but they are transparent to the oneM2M service layer. |

## 5.3	Mapping of resources

This section describes how to map <mgmtObj> resources specified in the Annex D of [1] to the relevant management objects as defined by OMA DM ([4], [5]). Since OMA DM 1.3 and OMA DM 2.0 use the same management objects except standard management objects, the resource mappings can be considered regardless of the specific version of the OMA DM Protocol.

### 5.3.1	General Mapping Assumptions

OMA DM Protocol implements the management functionaligies by using the Management Objects. Management Object is a collection of Nodes which are related for providing certain management functionalities. For example, SCOMO is for the software management, and FUMO is for the firmware update, and so on. The individual management operations such as firmware update, software management can be achieved by manipulating the corresponding Management Object. Since oneM2M <mgmtObj> Resources are for providing specific management functionalities, oneM2M <mgmtObj> Resources shall be mapped to Management Objects specified by OMA DM [4], [5].

### 5.3.2	Resource [firmware]

The resource [firmware] is for firmware management in the service layer. Regardless of OMA DM 1.3 and OMA DM 2.0,, the resource shall be mapped to FUMO (urn:oma:mo:omafumo:1.0). The attributes of the resource shall be mapped to nodes of the MO as the follows.

| Attribute Name of [firmware] | Mapping to Nodes in Management Object |
| --- | --- |
| version | <x>/PkgVersion |
| name | <x>/PkgName |
| URL | <x>/DownloadAndUpdate/PkgURL |
| update | <x>/DownloadAndUpdate |
| updateStatus | <x>/State |

### 5.3.3	Resource [software]

The resource [software] is for software management in the service layer. Regardless of OMA DM 1.3 and OMA DM 2.0,, the resource shall be mapped to SCOMO (urn:oma:mo:omascomo:1.0). The attributes of the resource shall be mapped to nodes of the MO as the follows.

| Attribute Name of [software] | Mapping to Nodes in Management Object |
| --- | --- |
| version | <x>/Inventory/Deployed/<x>/Version |
| name | <x>/Download/<x>/Name (when the software package is not ready for install) <x>/Inventory/Delivered/<x>/Name (when the software package is ready for install) <x>/Deployed/<x>/Name (when the software package is already installed) |
| URL | <x>/Download/<x>/PkgURL |
| install | <x>/Download/<x>/Operations/DownloadInstall (when the software package is not yet available) <x>/Inventory/Delivered/<x>/Operations/Install (when the software package has already been downloaded) |
| installStatus | <x>/Download/<x>/Status (started install when the software package is not yet available) <x>/Inventory/Delivered/<x>/Status (started install when the software package has already been downloaded) |
| activate | <x>/Inventory/Deployed/<x>/Operations/Activate |
| deactivate | <x>/Inventory/Deployed/<x>/Operations/Deactivate |
| activeStatus | <x>/Inventory/Deployed/<x>/Status |

### 5.3.4	Resource [memory]

The resource [memory] is for acquire information about the total memory or available memory of the device. Regardless of OMA DM 1.3 and OMA DM 2.0,, the resource shall be mapped to memory information of DiagMO (urn:oma:mo:omadiag:memory:1.0). The attributes of the resource shall be mapped to nodes of the MO as the follows.e

| Attribute Name of [memory] | Mapping to Nodes in Management Object |
| --- | --- |
| memAvailable | <x>/DiagMonData/RAMAvail |
| memTotal | <x>/DiagMonData/RAMTotal |

### 5.3.5	Resource [areaNwkInfo]

The resource [areaNwkInfo] is for managing the area network. Regardless of OMA DM 1.3 and OMA DM 2.0, the resource shall be mapped to MANMO (urn:oma:mo:ext-etsi-manmo:1.0). The attributes of the resource shall be mapped to nodes of the MO as the follows.

| Attribute Name of [areaNwkInfo] | Mapping to Nodes in Management Object |
| --- | --- |
| areaNwkType | M2MAreaNwkInfo/AreaNwks/<x>/AreaNwkType |
| listOfDevices | M2MAreaNwkInfo/AreaNwks/<x>/ListOfDevices |

### 5.3.6	Resource [areaNwkDeviceInfo]

The resource [areaNwkDeviceInfo] is for managing the device of the area network as well as acquiring information about devices in the area network. Regardless of OMA DM 1.3 and OMA DM 2.0, the resource shall be mapped to MANDMO (urn:oma:mo:ext-etsi-mandmo:1.0). The attributes of the resource shall be mapped to nodes of the MO as the follows.

| Attribute Name of [areaNwkDeviceInfo] | Mapping to Nodes in Management Object |
| --- | --- |
| devId | DevInfo/DevId |
| devType | DevDetail/DevType |
| areaNwkId | <x>/AreaNwks/<x>/AreaNwkID |
| sleepInterval | <x>/AreaNwks/<x>/SleepInterval |
| sleepDuration | <x>/AreaNwks/<x>/SleepDuration |
| status | <x>/AreaNwks/<x>/Status |
| listOfNeighbors | <x>/AreaNwks/<x>/Groups/ListOfDeviceNeighbors |

Editor’s Note: The description of which procedures are used to maintain the resource is FFS.

### 5.3.7	Resource [battery]

The Resource [battery] is to provide battery related information. Regardless of OMA DM 1.3 and OMA DM 2.0, this Resource shall be mapped to Battery Info Management Object (MOID: "urn:oma:mo:oma-diag:batteryinfo:1.0"). The attributes of this Resource shall be mapped to Nodes in the Management Object as follows:

| Attribute Name of [battery] | Mapping to Nodes in Management Object |
| --- | --- |
| batteryLevel | "<x>/DiagMonData/<x>/BatteryLevel" Node |
| batteryStatus | "<x>/DiagMonData/<x>/BatteryStatus" Node |

### 5.3.8	Resource [deviceInfo]

The Resource [deviceInfo] is to provide device related information. For OMA DM 1.3, this Resource shall be mapped to DevInfo MO (MOID: "urn:oma:mo:oma-dm-devinfo:1.1") and DevDetail MO (MOID: "urn:oma:mo:oma-dm-devdetail:1.1"). The attributes of this Resource shall be mapped to Nodes in two Management Objects as follows:

| Attribute Name of [deviceInfo] | Mapping to Nodes in Management Object |
| --- | --- |
| deviceLabel | "DevInfo/DevId" Node in DevInfo MO |
| Manufacturer | "DevInfo/Man" Node in DevInfo MO |
| Model | "DevInfo/Mod" Node in DevInfo MO |
| deviceType | "DevDetail/DevType" Node in DevDetail MO |
| fwVersion | "DevDetail/FwV" Node in DevDetail MO |
| swVersion | "DevDetail/SwV" Node in DevDetail MO |
| hwVersion | "DevDetail/HwV" Node in DevDetail MO |

For OMA DM 2.0, this Resource shall be mapped to DevInfo MO (MOID: "urn:oma:mo:oma-dm-devinfo:1.2"). The attributes of this Resource shall be mapped to Nodes in the Management Object as follows:

| Attribute Name of [deviceInfo] | Mapping to Nodes in Management Object |
| --- | --- |
| deviceLabel | "<x>/DevID" Node |
| Manufacturer | "<x>/Man" Node in DevInfo MO |
| Model | "<x>/Mod" Node in DevInfo MO |
| deviceType | "<x>/DevType" Node in DevInfo MO |
| fwVersion | "<x>/FwV" Node in DevInfo MO |
| swVersion | "<x>/SwV" Node in DevInfo MO |
| hwVersion | "<x>/HwV" Node in DevInfo MO |

### 5.3.9	Resource [deviceCapability]

The Resource [deviceCapability] is to manage the device capabilities such USB, camera, etc. Regardless of OMA DM 1.3 and OMA DM 2.0, this Resource shall be mapped to Device Capability Management Object (MOID: "urn:oma:mo:oma-dcmo:1.0"). The attributes of this Resource shall be mapped to Nodes in the Management Object as follows:

| Attribute Name of [deviceCapability] | Mapping to Nodes in Management Object |
| --- | --- |
| capabilityName | "<x>/Property" Node in DCMO |
| attached | "<x>/Attached" Node in DCMO |
| capabilityActionStatus | "<x>/Enabled" Node in DCMO |
| enable | "<x>/Operations/Enable" Node in DCMO |
| disable | "<x>/Operations/Disable" Node in DCMO |

### 5.3.10	Resource [reboot]

The Resource [reboot] is to reboot the device. Regardless of OMA DM 1.3 and OMA DM 2.0, this Resource shall be mapped to Restart Management Object (MOID: "urn:oma:mo:oma-diag:restart:1.0") that is specified in Diag Mon [ref] and Lock and Wipe Management Object (MOID: "urn:oma:mo:oma-lawmo:1.0"). The attributes of this Resource shall be mapped to Nodes in the Management Objects as follows:

| Attribute Name of [reboot] | Mapping to Nodes in Management Object |
| --- | --- |
| reboot | "<x>/Operations/Start" Node in Restart MO. The restarting level described at the "<x>/DiagMonConfig/ConfigParms/RestartLevel" Node is up to the implementation. |
| factoryReset | "<x>/Operations/FactoryReset" Node in LAWMO |

Note: which procedures shall be invoked when the "reboot" is TBD and shall be specified (better if handled in a general way)

Note: access right mapping needs to be resolved in a general manner in TS-0005.

### 5.3.11	Resource [eventLog]

The Resource [eventLog] is to record the event log for the device. Regardless of OMA DM 1.3 and OMA DM 2.0, this Resource shall be mapped to several Management Objects according to the logTypeId attribute of this Resource as follows:

- Trap Event Logging Function Management Object (MOID: "urn:oma:mo:oma-diag:trapeventlogging:1.1") if the logTypeId attribute is set to "TBD"

- Trace Logs Management Object (MOID: "urn:oma:mo:oma-diag:tracelog:1.0") if the logTypeId attribute is set to "TBD"

- Panic Logs Management Object (MOID: "urn:oma:mo:oma-diag:paniclog:1.1") if the logTypeId attribute is set to "TBD"

The attributes of this Resource shall be mapped to Nodes in above Management Objects as follows:

| Attribute Name of [eventLog] | Mapping to Nodes in Management Object |
| --- | --- |
| logTypeId | This attribute is not mapped to Nodes in Management Object. Instead, this attribute specifies the log type, and based on the log type, the actual Management Object mapped to this Resource is decided. |
| logData | "<x>/DiagMonData/log" Node for Trap Event Logging Function MO and Trace Logs MO. "<x>/DiagMonData/PanicLog" Node for Panic Logs MO |
| logActionStatus | "<x>/Status" Node for Trap Event Logging Function MO, Trace Logs MO and Panic Logs MO |
| logStart | "<x>/Operations/Start" Node for Trap Event Logging Function MO, Trace Logs MO and Panic Logs MO |
| logStop | "<x>/Operations/Stop" Node for Trap Event Logging Function MO, Trace Logs MO and Panic Logs MO |

# 6.	OMA Lightweight M2M 1.0

## 6.1	Mapping of basic data types

oneM2M has defined the data types that describe the format of the value stored at the attribute. Those oneM2M data types are listed in the below table, and mapped to the data types specified by OMA Lightweight M2M 1.0 (shortened in LWM2M)

| oneM2M Data Types | description | Mapping to data types in OMA LWM2M |
| --- | --- | --- |
| TBD |  | Boolean |
| TBD |  | Float |
| TBD |  | Integer |
| TBD |  | Opaque |
| TBD |  | String |
| TBD |  | Time |

## 6.2	Mapping of Identifiers

The LWM2M 1.0 enabler defines specific identifiers for entities (e.g. End Point Client Name, Server Identifier, Objects identifiers ..) To enable the device management using OMA LWM2M enabler, oneM2M identifiers needs to be mapped to identifiers specified by OMA LWM2M [6]. Below table shows the oneM2M identifiers that needs to be mapped to OMA LWM2M identifiers:

| oneM2M | Mapping to LWM2M Identifiers | Description |
| --- | --- | --- |
| M2M-Node-ID. | Endpoint Client Name | A unique identifier for the device. This value is globally unique and MUST be formatted as a URN. |
| The objectID attribute in <mgmtObj> resource. | Object ID | A unique identifier of Object. Each Object is characterized by a unique ObjectID, which is represented as an integer.In OMNA Object URN is registered as : urn:oma:lwm2m:{oma,ext, x}:{Object ID} |
| The objectPath attribute in <mgmtObj> resource | URI for the local path in the device where the Object Instance is located | Objects Instances are uniquely addressed by a URI that is stored in the objectPath attribute. |

## 6.3	Mapping of resources

This section describes how to map the <mgmtObj> resources specified in the Annex D of [1] to the relevant Objects specified  in OMA LWM2M [6] enabler.

### 6.3.1	General Mapping Assumptions

OMA LWM2M Enabler implements the functionalities of the device management and M2M service enablement as  Objects.  An Object is a collection of resources which are related to a specific management functionality. For example the Firmware Update Object contains all the Resources used for firmware update purpose. Before to be able of  fulfilling its role, an Object shall be firstly instantiated into an Object Instance. Since oneM2M <mgmtObj> Resources are for providing specific management functionalities, oneM2M <mgmtObj> Resources shall be mapped to Object Instances specified by OMA LWM2M [6]. The attributes of a oneM2M <mgmtObj> Resource shall be mapped to the resources of the  associated LWM2M Object Instance.

### 6.3.2	Resource [memory]

The Resource [memory] provides memory related information. For OMA LWM2M, this oneM2M Resource shall be mapped to an Instance of LWM2M Device Object (LWM2M ObjectID: 3) . The attributes of this oneM2M Resource shall be mapped to specific resources of the LWM2M Device Object Instance as follows:

| Attribute Name of [memory] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| memAvailable | 10 : estimated current available amount of memory |

### 6.3.3	Resource [battery]

The Resource [battery] provides battery related information. For  OMA LWM2M, this oneM2M Resource shall be mapped to an Instance of LWM2M Device Object (LWM2M ObjectID: 3). The attributes of this oneM2M Resource shall be mapped to specific resources of the LWM2M Device Object Instance  as follows:

| Attribute Name of [battery] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| batteryLevel | /9 : current battery level as percentage |

### 6.3.4	Resource [deviceInfo]

The Resource [deviceInfo] provides device related information. For OMA LWM2M, this oneM2M Resource shall be mapped to an Instance of LWM2M Device Object (LWM2M ObjectID: 3).The attributes of this oneM2M Resource shall be mapped to specific resources of the LWM2M Device Object Instance  as follows:

| Attribute Name of [deviceInfo] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| deviceLabel | /2 : Serial Number |
| Manufacturer | /0 : Manufacturer name |
| Model | /1 : Model Number |
| fwVersion | /3 : Firmware Version |

### 6.3.5	Resource [reboot]

The Resource [reboot] is used for rebooting the device. For  OMA LWM2M, this oneM2M Resource shall be mapped to an Instance of LWM2M Device Object (LWM2M ObjectID: 3).The attributes of this Resource shall be mapped to  LWM2M Device Object Instance  as follows:

| Attribute Name of [reboot] | Mapping to resources in LWM2M Object Instance |
| --- | --- |
| reboot | /4 : reboot the LWM2M Device to restore the Device from unexpected firmware failure |
| factoryReset | /5 : Perform Factory Reset : the LWM2M device return to the same configuration as at the initial deployment. |

# 7	Mapping of procedures for management

Editor’s Note: The section specifies the mapping between oneM2M operation (i.e, Create, Retrieve, Update and Delete) and DM Commands defined in OMA DM, and logical operations defined in LWM2M. The mapping includes the handling of normal cases and error cases.

# 8	Server Interactions

Editor’s Note: The section specifies the action taken for the DMG CSE to communicate with the Management Server by using the ms interface. The server interaction can be different depending on the device management technology (i.e. OMA DM, OMA LWM2M). The server interaction might include the establishment, maintainance, usage and termination of communication to the Management Server defined in OMA DM and OMA LWM2M.

## 8.1	Server interaction management

Editor’s Note: Describes the management of communication between oneM2M service layer and DM Server, and LWM2M Server. The management includes the establishment and termination of session when needed. The management also includes necessary procedure to utilize the existing sessions.

## 8.2	Authorization

Editor’s Note: The section specifies the mapping of authorization rules defined in oneM2M and OMA standards.

# 9	New Management Technology Specific Resources

Editor’s Note: The section specifies the definition of new data models if needed based on the requirements of oneM2M. The definition of new data models in this section need to be liaised to OMA to create corresponding MOs or Objects in OMA DM or OMA LWM2M.

The following text is to be used when appropriate:

# Proforma copyright release text block

This text box shall immediately follow after the heading of an element (i.e. clause or annex) containing a proforma or template which is intended to be copied by the user. Such an element shall always start on a new page.

Notwithstanding the provisions of the copyright clause related to the text of the present document, oneM2M grants that users of the present document may freely reproduce the <proformatype> proforma in this {clause|annex} so that it can be used for its intended purposes and may further publish the completed <proformatype>.

<PAGE BREAK>

## Annexes

Each annex shall start on a new page (insert a page break between annexes A and B, annexes B and C, etc.).

Use the Heading 9 style for the title and the Normal style for the text.

Annex <A> (Informative/Normative):Remove Informative or Normative as appropriatTitle of annex (style H9)

<Text>

<PAGE BREAK>

Annex <B>(Informative/Normative): Remove Informative or Normative as appropriateTitle of annex (style H9)

<Text>

B.1	First clause of the annex (style H1)

<Text>

B.1.1	First subdivided clause of the annex (style H2)

<Text>

<PAGE BREAK>

The following text is to be used when appropriate:

Annex <y>:
Bibliography

The annex entitled "Bibliography" is optional.

It shall contain a list of standards, books, articles, or other sources on a particular subject which are not mentioned in the document itself

It shall not include references mentioned in the document.

Use the Heading 9 style for the title and B1+ or Normal for the text.

<Publication>: "<Title>".

OR

<Publication>: "<Title>".

<PAGE BREAK>

# History

This clause shall be the last one in the document and list the main phases (all additional information will be removed at the publication stage).

| Publication history |
| --- |
| V1.1.1 | <dd-Mmm-yyyy> | <Milestone> |

| Draft history (to be removed on publication) |
| --- |
| V.0.0.1 | 28-2-2014 | Initial skeleton of the TS |
| V 0.1.0 | 21-4-2014 | Incoporated contributions: MAS-2014-0351R02-Resource_Mapping_for_OMA_DM MAS-2014-0352R04-DataType_Identification_Mapping_for_OMA_DM MAS-2014-0355R01-resource-mapping-for-management MAS-2014-0366R03-DataType_Identification_Mapping_for_OMA_LWM2M MAS-2014-0367R03-Resource_Mapping_for_OMA_LWM2M Other editorial update: Format adjustments Clause numbers |