| oneM2M Technical Specification |
| --- |
| Document Number | TS-0006-Management_Enablement_(BBF)-V0_2_0 |
| Document Name: | Management Enablement (BBF) |
| Date: | 2014-05-12 |
| Abstract: | Specifies the usage of the BBF TR-069 protocol and the corresponding message flows including normal cases as well as error cases to fulfil the oneM2M management requirements. Protocol mapping between the oneM2M service layer and BBF TR-069 protocol. The Mca reference point, ms interface and la interface are possibly involved in this protocol mapping. Mapping between the oneM2M management related resources and the TR-069 protocol RPCs and TR-181i2 data model. Specification of new TR-181 data model elements to fulfil oneM2M specific management requirements that cannot be currently translated. |

This Specification is provided for future development work within oneM2M only. The Partners accept no liability for any use of this Specification.

The present document has not been subject to any approval process by the oneM2M Partners Type 1.  Published oneM2M specifications and reports for implementation should be obtained via the oneM2M Partners' Publications Offices.

About oneM2M

The purpose and goal of oneM2M is to develop technical specifications which address the need for a common M2M Service Layer that can be readily embedded within various hardware and software, and relied upon to connect the myriad of devices in the field with M2M application servers worldwide.

More information about oneM2M may be found at:  http//www.oneM2M.org

Copyright Notification

No part of this document may be reproduced, in an electronic retrieval system or otherwise, except as authorized by written permission.

The copyright and the foregoing restriction extend to reproduction in all media.

© 2014, oneM2M Partners Type 1 (ARIB, ATIS, CCSA, ETSI, TIA, TTA, TTC).

All rights reserved.

Notice of Disclaimer & Limitation of Liability

The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations. No recommendation as to products or vendors is made or should be implied.

NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE, GOVERNMENTAL RULE OR REGULATION, AND FURTHER, NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS. NO oneM2M PARTNER TYPE 1 SHALL BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY THAT PARTNER FOR THIS DOCUMENT, WITH RESPECT TO ANY CLAIM, AND IN NO EVENT SHALL oneM2M BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES. oneM2M EXPRESSLY ADVISES ANY AND ALL USE OF OR RELIANCE UPON THIS INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER.

# Contents

Contents	3

1	Scope	5

2	References	5

2.1	Normative references	5

2.2	Informative references	5

3	Definitions, symbols, abbreviations and acronyms	5

3.1	Definitions	5

3.2	Symbols	5

3.3	Abbreviations	6

3.4	Acronyms	6

4	Conventions	6

5	Mapping of basic data types	6

6	Mapping of identifiers	6

6.1	Mapping of Device identifiers to the Node Resource	7

6.2	Identifier of an object instance	7

7	Mapping of resources	7

7.1	General mapping assumptions	8

7.2	Resource deviceInfo	8

7.3	Resource memory	8

7.4	Resource battery	8

7.5	Resource areaNwkInfo	9

7.6	Resource areaNwkDeviceInfo	9

7.7	Resource eventLog	10

7.8	Resource deviceCapability	11

7.9	Resource firmware	11

7.10	Resource software	12

7.11	Resource reboot	13

8	Mapping of procedures for management	14

8.1	MgmtObj primitive mappings	14

8.1.1	Create primitive mapping	14

8.1.1.1	M2M Service Layer Resource Instance Identifier mapping	14

8.1.2	Delete primitive mapping	14

8.1.2.1	Delete primitive mapping for deletion of Object Instances	14

8.1.2.2	Delete primitive mapping for software un-install operation	15

8.1.3	Update primitive mapping	16

8.1.3.1	Update primitive mapping for Parameter modifications	16

8.1.3.2	Update primitive mapping for upload file transfer operations	17

8.1.3.3	Update primitive mapping for download file transfer operations	18

8.1.3.4	Update primitive mapping for reboot operation	20

8.1.3.5	Update primitive mapping for factory reset operation	20

8.1.3.6	Update primitive mapping for software install operation	20

8.1.4	Retrieve primitive mapping	22

8.1.5	Notify primitive mapping	22

8.1.5.1	Procedure for subscribed Resource attributes.	22

8.1.5.2	Notification mapping	23

9	Server Interactions	23

9.1	Communication Session Establishment	23

9.1.1	IN-CSE to ACS Communication Session Establishment	23

9.1.2	ACS to IN-CSE Communication Session Establishment	24

9.2.3	ACS and IN-CSE Communication Session Requirements	24

9.2	Processing of Requests and Responses	24

9.2.1	Request and Notification Formatting	24

9.2.2	ACS Request Processing Requirements	24

9.2.3	ACS Notification Processing Requirements	24

9.3	Discovery and Synchronization of Resources	25

9.4	Access Management	25

9.4.1	Access Management Requirements	25

10	New Management Technology Specific Resources	25

Proforma copyright release text block	25

Annexes	26

Annex <y>: Bibliography	26

History	27

# 1	Scope

The present document describes the protocol mappings between the management Resources for oneM2M and the BBF TR-181i2 Data Model [6].

# 2	References

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M TS-0001: “oneM2M Functional Architecture”.

[2]	oneM2M TS-0004: “oneM2M Protocol Specification”.

[3]	oneM2M TR-0004: “Definitions and Acronyms”.

Editors Note: naming of TR-0004 to the new TS name.

[4]	BBF: “TR-069 CPE WAN Management Protocol” Issue: 1 Amendment 5, November 2013.

[5]	BBF: “TR-106 Data Model Template for TR-069-Enabled Devices”, Issue 1, Amendment 7,
September 2013.

[6]	BBF: “TR-181 Device Data Model for TR-069, Issue 2 Amendment 7”, November 2013.

[7]	BBF: “TR-131 ACS Northbound Interface Requirements, Issue:1”, November 2009.

[8]	IETF/RFC 3986: “Uniform Resource Identifier (URI): Generic Syntax”.

[9]	POSIX.1-2008: “The Open Group Technical Standard Base Specifications”, Issue 7.

## 2.2	Informative references

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

# 3	Definitions, symbols, abbreviations and acronyms

Delete from the above heading the word(s) which is/are not applicable.

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in TR-0004 [3] apply.

## 3.2	Symbols

Clause numbering depends on applicability.

For the purposes of the present document, the [following] symbols [given in ... and the following] apply:

Symbol format

<symbol>	<Explanation>

<2nd symbol>	<2nd Explanation>

<3rd symbol>	<3rd Explanation>

## 3.3	Abbreviations

For the purposes of the present document, the following abbreviations apply:

CPE	Customer Premise Equipment

DU	Deployment Unit

OUI	Organizationally Unique Identifier

PC	Product Class

RPC	Remote Procedure Call

SN	Serial Number

## 3.4	Acronyms

For the purposes of the present document, the acroynms given in TR-0004 [3] apply.

# 4	Conventions

The key words “Shall”, ”Shall not”, “May”, ”Need not”, “Should”, ”Should not” in this document are to be interpreted as described in the oneM2M Drafting Rules [i.1]

# 5	Mapping of basic data types

TR-106 [5] specifies the object structure supported by TR-069 enabled devices and specifies the structural requirements for the data hierarchy. This includes the mapping attribute data types to TR-181 [6] parameters which follows the conventions of section 3 of TR-106 [5] and data types described in Table 4 of TR-106 [5].

Specifically the following conventions shall be used when mapping data types:

String: Maps directly to the “string” data type

Long: Maps directly to the “long” data type

UnsignedLong: Maps directly to the “unsignedLong” data type

UnsignedInt: Maps directly to the “unsignedInt” data type

Lists of Strings: When a data structure is represented by comma separated list of type "string", any whitespace or comma characters  contained in an item of such a list MUST be escaped using percent as defined in Section 3.2.3 of TR-106 [5].

# 6	Mapping of identifiers

The TR-069 [4] specification defines three (3) types of devices, known as CPEs, that are capable of being managed from the perspective of the TR-069 agent:

CPE that hosts the TR-069 agent: Section A.3.3.1 Inform of TR-069 [4] defines the required fields for a CPE to be identified. These fields include the OUI and Serial Number of the CPE assigned by the CPE manufacturer. Optionally the manufacturer may assign a Product Class to the CPE. The format of the identifier is as follows: OUI-[PC-]SN.

Virtual Device: This type of device is addressed as a CPE. The Virtual Device has its own OUI-[PC-]SN.

Embedded Device: This type of device is addressed as one or more objects within the data model of the CPE that hosts the TR-069 agent.

The objectPath attribute of the <mgmtObj> Resource contains the CPE identifier that hosts the TR-069 agent in the form OUI-[PC-]-SN. The Product Class (PC) is an optional field. All elements of the CPE identifier is assigned by the manufacturer of the CPE.

## 6.1	Mapping of Device identifiers to the Node Resource

Node Resources are identified for each instance of an ADN, ASN and MN node and are identified using the M2M Node Identifier (M2M-Node-ID) defined in the oneM2M Functional Architecture [1].

CPE Device identifiers shall map to the Node Identifier. The CPE Device identifiers is obtained from the contents of the following attributes:

- Device.DeviceInfo.ManufacturerOUI

- Device.DeviceInfo.{i}.ProductClass

- Device.DeviceInfo.{i}.SerialNumber

Virtual Device identifiers shall map to the Node Identifier. The Virtual Device identifiers are obtained from the proxier CPE using the contents of the attributes:

- Device.ManagementServer.VirtualDevice.{i}.ManufacturerOUI

- Device.ManagementServer.VirtualDevice.{i}.ProductClass

- Device.ManagementServer.VirtualDevice.{i}.SerialNumber

Embedded Device identifiers shall map to the Node Identifier using the containing CPE or Virtual Device identifiers along with the contents of the attributes of the:

- Device.ManagementServer.EmbeddedDevice.{i}.ControllerID

- Device.ManagementServer.EmbeddedDevice.{i}.ProxiedDeviceID

## 6.2	Identifier of an object instance

The TR-069 [4] permits objects to have multiple object instances where each object instance is contained within the objectPath attribute of the Resource within the context of the Resource’s objectId as defined in clause 7.1.

In order to allow the AE or CSE that originated the request that manipulates a Resource to easily align the M2M Service Layer with the Resource’s external technology identifier, the value of the object instance “{i}” should be a part of the identifier of the  Resource in the M2M Service Layer where possible. For example if the areaNetwork Resource has an object instance identifier of “Device.X_oneM2M_CSE.1.M2MAreaNetworkDevice.[foo]” then the M2M Service Layer Resource should be identified using the object instance of the underlying technology (e.g., “/foo” for the Resource type areaNetwork). Resource.

# 7	Mapping of resources

This clause contains all information on how to map subtypes of the <mgmtObj> resource to their equivalent managed object and parameters as defined in the TR-181 [6] data model or the Remote Procedure Call (RPC) in TR-069 [4].

Editors Note: Resource attributes need to be rechecked to ensure all attribles of the mgmtObj resources are in the mapping tables (e.g., DeviceInfo:deviceId).

## 7.1	General mapping assumptions

TR-069 [4] specifies a protocol for communication between a CPE (Customer Premises Equipment) and an ACS (Auto-Configuration Server).  Any TR-069 enabled device has to follow the data model as described in the TR-106 [5] and TR-181 [6] as well as RPCs described in TR-069 [4].

As TR-181 [6] is the model that the Resources are mapped, all Resources shall have the objectId of the TR-181[6] namespace (e.g., "urn:broadband-forum-org:TR-181-2-7-0”).

## 7.2	Resource deviceInfo

The Resource deviceInfo is a read-only Resource that shall map to the Device.DeviceInfo object of TR-181 [6].

The information shall be retrieved using the GetParameterValues RPC of TR-069 [4].

| Attribute Name of deviceInfo | TR-181 Parameter |
| --- | --- |
| deviceLabel | Device.DeviceInfo.Description |
| manufacturer | Device.DeviceInfo.Manufacturer |
| model | Device.DeviceInfo.ModelNumber |
| deviceType | Device.DeviceInfo.ProductClass |
| fwVersion | Device.DeviceInfo.SoftwareVersion if the device supports only 1 software version. If the device support multiple software versions this would map to Device.DeviceInfo.AdditionalSoftwareVersion |
| swVersion | Device.DeviceInfo.SoftwareVersion |
| hwVersion | Device.DeviceInfo.HardwareVersion |

## 7.3	Resource memory

The Resource memory is a read-only Resource that shall map to the Device.DeviceInfo.MemoryStatus object of TR-181 [6].

The information shall be retrieved using the GetParameterValues RPC of TR-069 [4].

Attempts to modify the attributes of the memory Resource causes an error code “operation unsupported” to be returned.

| Attribute Name of memory | TR-181 Parameter |
| --- | --- |
| memAvailable | Device.DeviceInfo.MemoryStatus.Free |
| memTotal | Device.DeviceInfo.MemoryStatus.Total |

## 7.4	Resource battery

The Resource battery  is a read-only Resource that shall map to an instance of Device.DeviceInfo.X_oneM2M_BatteryStatus.Battery.{i} object.

The information shall be retrieved using the GetParameterValues RPC of TR-069 [4].

| Attribute Name of battery | TR-181 Parameter |
| --- | --- |
| batteryLevel | Device.DeviceInfo.X_oneM2M_BatteryStatus.Battery.{i}.Level |
| batteryStatus | Device.DeviceInfo.X_oneM2M_BatteryStatus.Battery.{i}.Status |

## 7.5	Resource areaNwkInfo

The Resource areaNwkInfo is a multi-instance Resource where each instance of the Resource shall map to an instance of Device.X_oneM2M_CSE.{i}.M2MAreaNetwork.{i} object.

As the areaNwkInfo Resource is a multi-instance Resource, the M2MAreaNetwork object is an multi-object instance that can be created and deleted.

The M2MAreaNetwork instance shall be created  using the Add Object RPC of TR-069 [4].

The M2MAreaNetwork instance shall be deleted  using the Delete Object RPC of TR-069 [4].

The information of a M2MAreaNetwork shall be retrieved using the GetParameterValues RPC of TR-069 [4].

The information of a M2MAreaNetwork shall be modified using the SetParameterValues RPC of TR-069 [4].

| Attribute Name of areaNwkInfo | X_oneM2M Parameter |
| --- | --- |
| areaNwkType | Device.X_oneM2M_CSE.{i}.M2MAreaNetwork.{i}.Type |
| listOfDevices | Device.X_oneM2M_CSE.{i}.M2MAreaNetwork.{i}.ListOfDevices |

## 7.6	Resource areaNwkDeviceInfo

The Resource areaNwkDeviceInfo is a multi-instance Resource where each instance of the Resource shall map to an instance of Device.X_oneM2M_CSE.{i}.AreaNetworkDevice.{i} object.

As the areaNwkDeviceInfo Resource is a multi-instance Resource, the AreaNetworkDevice object is an multi-object instance that can be created and deleted.

Instances of the areaNwkDeviceInfo Resource is referenced in the listOfDevices attribute of the associated AreaNwkInfo Resource.

The M2MAreaNetworkDevice instance shall be created  using the Add Object RPC of TR-069 [4].

The M2MAreaNetworkDevice instance shall be deleted  using the Delete Object RPC of TR-069 [4].

The information of a M2MAreaNetworkDevice shall be retrieved using the GetParameterValues RPC of TR-069 [4].

The information of a M2MAreaNetworkDevice shall be modified using the SetParameterValues RPC of TR-069 [4].

| Attribute Name of areaNwkDeviceInfo | X_oneM2M Parameter |
| --- | --- |
| devId | Device.X_oneM2M_CSE.{i}.M2MAreaNetworkDevice.{i}.Host |
| devType | Device.X_oneM2M_CSE.{i}.M2MAreaNetworkDevice.{i}.Type |
| areaNwkId | Reference to Device.X_oneM2M_CSE.{i}.M2MAreaNetworkDevice.{i}.M2MAreaNetwork |
| sleepInterval | Device.X_oneM2M_CSE.{i}.M2MAreaNetworkDevice.{i}.SleepInterval |
| sleepDuration | Device.X_oneM2M_CSE.{i}.M2MAreaNetworkDevice.{i}.SleepDuration |
| status | Device.X_oneM2M_CSE.{i}.M2MAreaNetworkDevice.{i}.Status |
| listOfNeighbors | Device.X_oneM2M_CSE.{i}.M2MAreaNetworkDevice.{i}.Neighbors |

## 7.7	Resource eventLog

The Resource eventLog is a multi-instance Resource where each instance of the Resource shall map to an instance of Device.DeviceInfo.VendorLogFile.{i} object.

While the eventLog Resource is a multi-instance Resource, the VendorLogFile is a read-only object where only the CPE is able to create and delete instances of the VendorLogFile.

The contents of a VendorLogFile instance shall be retrieved using the Upload RPC of TR-069 [4].

The VendorLogFile.Name parameter does not support the capability to set the name. Attempts to modify the TypeId attribute of the eventLog Resource causes an error code “operation unsupported” to be returned.

The VendorLogFile object instance does not support action capabilities to start or stop the log. As such, the following mappings are used:

logStart: The value shall be set to “True” when the Resource is created. An error code “unsupported value” shall be returned for an attempt to set the values of logStart attribute to any other value.

logStop: When set to “True” the CSE shall initiate the “Upload” operation where the results of the VendorLogFile is placed in the logData attribute. When the logStop attribute is set to “True”, the CSE shall initiate the “Upload” operation where the results of the Upload operation are placed in the logData attribute.  Once the logStop attribute is set to “True” it cannot be set to “False”. An attempt to set the logStop attribute to “False” once it has been set to “True” shall result in an  error code “operation unsupported” to be returned.

logActionStatus: The value shall be set to “Started” when the Resource is created and shall be set to “Stopped” when the logStop is set to “True”

| Attribute Name of eventLog | TR-181 Parameter |
| --- | --- |
| logTypeId | Device.DeviceInfo.VendorLogFile.{i}.Name |
| logData | Upload RPC using the Device.DeviceInfo.VendorLogFile.{i} as the FileType. Results are placed in this attribute. |
| logActionStatus | Always returns the value of “Started” upon creation and the value “Stopped” upon a success transfer of the VendorLogFile.{i} Instance. |
| logStart | Set to “True” upon creation of the Resource. |
| logStop | Invoke the Upload RPC when set to “True”. |

RPC Upload Argument

URL: URL of the Server that M2M Node uses to uplod the event log in order to retrieve the contents of the eventLog.

FileType: “4 Vendor Log File <i>”

Username: Username credential of the Server that the M2M Node uses to receive the event log.

Password: Password credential of the Server that the M2M Node uses to receive the event log.

CommandKey: Automatically set by the M2M node in order to correlate the TransferComplete response.

DelaySeconds: 0 (immediate)

## 7.8	Resource deviceCapability

The deviceCapability Resource represents a capabilility of device that can be administratively enabled or disabled. The list of capabilities that are managed are defined in the enumeration of the capabilityName attribute.  The TR-181 [6] data model defines a subset of capabilities listed in the deviceCapability enumeration. The supported device capabilities within TR-181 [6] include:

LAN Interfaces: USB, Wifi, HomePlug, MoCA, UPA

Hardware Capabilities: SmartCardReader

The information shall be retrieved using the GetParameterValues RPC of TR-069 [4].

The capabilities shall be enabled and disabled using the SetParameterValues RPC of TR-069 [4].

| Attribute Name of capabilityInstance | TR-181 Parameter |
| --- | --- |
| capabilityName | This attribute is fixed baed on the value of the capablityName attribute. |
| attached | Returns “True” |
| capabilityActionStatus | No direct mapping exists. The progress indicator of the capabilityActionStatus is set to 0% as soon as the request to enable or disable the capability is performed by the M2M Service Layer. After completion of the request, the progress indicator is set to 100%. |
| enable | USB: Device.USB.Interface.(i).Enable WiFi: Device.WiFi.Radio.{i}.Enable HomePlug: Device.HomePlug.Interface.{i}.Enable MoCA: Device.MoCA.Interface.{i}.Enable UPA: Device.UPA.Interface.{i}.Enable SmartCardReader: Device.SmartCardReaders.SmartCardReader.{i}.Enable |
| disable | Same parameter is used to disable a capability as the enable attribute. |

## 7.9	Resource firmware

The firmware Resource represents a firmware instance and  is not considered a TR-069 managed entity within the device until the the firmware Resource’s update attribute has been written a value of “True”. When this occurs, the TR-069 Download RPC shall be invoked.

Note: In many instances, the server from which the firmware is downloaded requires authentication in the form of Username and Password credentials. The CSE that executes firmware download shall maintain the a mapping of the username and password of the download server needed to download the firmware outside the lifecycle of the specific firmware

| Attribute Name of firmware | RPC Download Arguments |
| --- | --- |
| URL | URL |
| update | When set to the value of “True” executes the Download operations with a FileType “1 Firmware Upgrade Image” is performed. |
|  | Username: Received from the CSE for the download server where the update is set to “True”. |
|  | Password: Received from the CSE for the download server where the update is set to “True”. |
|  | CommandKey: Automatically set by the CSE where the update is set to “True” in order to correlate the TransferComplete response. |
|  | FileSize: 0 (not used) |
|  | TargetFileName: <empty> (not used) |
|  | DelaySeconds: 0 (immediate) |
|  | SuccessURL: <empty> (not used) |
|  | FailureURL: <empty> (not used) |

## 7.10	Resource software

The Resource software is a multi-instance Resource where each instance of the Resource maps directly to an instance of Device.SoftwareModules.DeploymentUnit.{i} object for the deployment aspects (install, remove) of the software Resource.  The install and uninstall operation of software Resource is performed using a combination of the ChangeDUState and ChangeDUStateComplete RPCs.

Once a software Resource has been installed, the Resource shall be mapped to the associated Device.SoftwareModules.ExecutionUnit.{i} objects in order to activate and deactivate the associated execution unit.

The software Resource version and name shall be retrieved using the GetParameterValues RPC of TR-069 [4].

The activate and deactive operations of the software Resource shall be performed by manipulating the Device.SoftwareModules.ExecutionUnit.{i}.RequestedState parameter using the SetParameterValues RPC.

| Attribute Name of software | Description |
| --- | --- |
| version | Device.SoftwareModules.DeploymentUnit.{i.Version |
| name | Device.SoftwareModules.DeploymentUnit.{i}.Name |
| URL | Device.SoftwareModules.DeploymentUnit.{i}.URL |
| install | Use the ChangeDUState:InstallOpStruct |
| installStatus | Status is defined as 0% if the install operation has not been initiated or has failed. If the install operation has completed successfully, the value of 100% is used in indicate a successful completion of the installation. |
| activate | The action that activates software previously installed. |
| deactivate | The action that deactivates software. |
| activeStatus | Status is defined as 0% if the last operation has not been has failed or a new operation has been initiaited. If the current operation has completed successfully, the value of 100% is used in indicate a successful completion of the operation. |

RPC ChangeDUState:InstallOpStruct Argument

URL: URL of the Server that M2M Node uses to download the DU.

Username: Username credential of Server that the CPE uses to download the DU – Supplied by the CSE.

Password: Password credential of Server that the CPE uses to download the DU – Supplied by the CSE.

UUID: Supplied by the CSE and used to correlate the DU for the uninstall operation.

ExecurtionEnvRef: <empty> not used

RPC ChangeDUState:Uninstall OpStruct Argument

UUID: UUID of the DU that was installed – Maintained by the CSE.

ExecutionEnvRef: <empty> not used

## 7.11	Resource reboot

The Resource reboot maps to either the Reboot RPC or FactoryReset RPC of TR-069 [4].

When the reboot attribute of the reboot Resource is set to “True”, the CSE shall execute the Reboot RPC of TR-069[4].

When the factoryReset attribute of reboot Resource is set to “True”, the CSE shall execute the FactoryReset RPC of TR-069[4].

| Attribute Name of reboot | Description |
| --- | --- |
| reboot | Executes the Reboot RPC |
| factoryReset | FactoryReset RPC |

RPC Reboot Arguments

CommandKey: Automatically set by the CSE where the reboot is set to “True” in order to correlate the “M-Reboot” Event from the next Inform.

# 8	Mapping of procedures for management

## 8.1	MgmtObj primitive mappings

Editors Note: Need to flesh out the error codes for procedures.

### 8.1.1	Create primitive mapping

The  Create primitive shall map to the AddObject RPC. The AddObject RPC is defined in TR-069 [4] as a synchronous RPC and returns a successful response or one of the following fault codes in Table 8.1.1-1.

Table 8.1.1-1: AddObject Fault Code Mapping

| Fault code | Description | Primitive Error Code |
| --- | --- | --- |
| 9001 | Request denied (no reason specified) |  |
| 9002 | Internal error |  |
| 9003 | Invalid arguments |  |
| 9004 | Resources exceeded (when used in association with SetParameterValues, this MUST NOT be used to indicate Parameters in error) |  |
| 9005 | Invalid Parameter name (associated with Set/GetParameterValues, GetParameterNames, Set/GetParameterAttributes, AddObject, and DeleteObject) |  |

#### 8.1.1.1	M2M Service Layer Resource Instance Identifier mapping

When the Resource is a multi-instance Resource, the AddObject RPC should utilize the Alias-Based Addressing Mechanism (as defined in Section Error! Reference source not found.) of TR-069 [4] in order to use the Resource instance value of the URI.

The Alias-Based Addressing Mechanism mustbe supported by the ACS and CPE in order to map the M2M Service Layer identifier for the Resource instance to the CPE object instance. If the Alias-Based Addressing Mechanism feature is not supported by either the ACS or CPE, the CSE shall retain the mapping of the these instance identifiers.

### 8.1.2	Delete primitive mapping

#### 8.1.2.1	Delete primitive mapping for deletion of Object Instances

The  Delete primitive shall map to the DeleteObject RPC. The DeleteObject RPC is defined in TR-069 [4] as a synchronous RPC and returns a successful response or one of the following fault codes in Table 8.1.2.1-1.

Table 8.1.2.1-1: DeleteObject Fault Code Mapping

| Fault code | Description | Primitive Error Code |
| --- | --- | --- |
| 9001 | Request denied (no reason specified) |  |
| 9002 | Internal error |  |
| 9003 | Invalid arguments |  |
| 9005 | Invalid Parameter name (associated with Set/GetParameterValues, GetParameterNames, Set/GetParameterAttributes, AddObject, and DeleteObject) |  |

#### 8.1.2.2	Delete primitive mapping for software un-install operation

The  Delete primitive that results in a software un-install operation (e.g., Resource software) shall use the ChangeDUState mechanism defined in TR-069 [4]. The ChangeDUState mechanism is an asynchronous command that consists of the synchronous ChangeDUState RPC for the uninstallation request and the asynchronous ChangeDUStateComplete RPC.  The ChangeDUState RPC returns a successful response or one of the following fault codes in Table 8.1.2.2-1. A successful response means that the CPE has accepted the ChangeDUState RPC.

Table 8.1.2.2-1: ChangeDUState Fault Code Mapping

| Fault code | Description | Primitive Error Code |
| --- | --- | --- |
| 9000 | Method not supported |  |
| 9001 | Request denied (no reason specified) |  |
| 9002 | Internal error |  |
| 9004 | Resources exceeded (when used in association with SetParameterValues, this MUST NOT be used to indicate Parameters in error) |  |

Once the CPE has attempted to change the state of the deployment unit, the CPE reports the result of the state change operation using the ChangeDUStateComplete RPC. The ChangeDUStateComplete RPC indicates a successful operatoin or one of the following fault codes in Table 8.1.2.2-2.

Table 8.1.2.2-2: ChangeDUStateComplete Fault Code Mapping

| Fault code | Description | Primitive Error Code |
| --- | --- | --- |
| 9001 | Request denied (no reason specified) |  |
| 9003 | Invalid arguments |  |
| 9012 | File transfer server authentication failure (associated with Upload, Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9013 | Unsupported protocol for file transfer (associated with Upload, Download, ScheduleDownload, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9015 | File transfer failure: unable to contact file server (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9016 | File transfer failure: unable to access file (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9017 | File transfer failure: unable to complete download (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9018 | File transfer failure: file corrupted or otherwise unusable (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9022 | Invalid UUID Format (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install, Update, and Uninstall) |  |
| 9023 | Unknown Execution Environment (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install only) |  |
| 9024 | Disabled Execution Environment (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install, Update, and Uninstall) |  |
| 9025 | Deployment Unit to Execution Environment Mismatch (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install and Update) |  |
| 9026 | Duplicate Deployment Unit (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install only) |  |
| 9027 | System Resources Exceeded (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install and Update) |  |
| 9028 | Unknown Deployment Unit (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Update and Uninstall) |  |
| 9029 | Invalid Deployment Unit State (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install, Update and Uninstall) |  |
| 9030 | Invalid Deployment Unit Update – Downgrade not permitted (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Update only) |  |
| 9031 | Invalid Deployment Unit Update – Version not specified (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Update only) |  |
| 9032 | Invalid Deployment Unit Update – Version already exists (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Update only) |  |

### 8.1.3	Update primitive mapping

#### 8.1.3.1	Update primitive mapping for Parameter modifications

The  Update primitive that modifies the value of a Resource attribute shall map to the SetParameterValues RPC. The SetParametersValue RPC is defined in TR-069 [4] as a synchronous RPC and returns a successful response or one of the following fault codes in Table 8.1.3.1-1.

Table 8.1.3.1-1: SetParameterValues Fault Code Mapping

| Fault code | Description | Primitive Error Code |
| --- | --- | --- |
| 9001 | Request denied (no reason specified) |  |
| 9002 | Internal error |  |
| 9003 | Invalid arguments |  |
| 9004 | Resources exceeded (when used in association with SetParameterValues, this MUST NOT be used to indicate Parameters in error) |  |
| 9005 | Invalid Parameter name (associated with Set/GetParameterValues, GetParameterNames, Set/GetParameterAttributes, AddObject, and DeleteObject) |  |
| 9006 | Invalid Parameter type (associated with SetParameterValues) |  |
| 9007 | Invalid Parameter value (associated with SetParameterValues) |  |
| 9008 | Attempt to set a non-writable Parameter (associated with SetParameterValues) |  |

#### 8.1.3.2	Update primitive mapping for upload file transfer operations

The  Update primitive that results in a upload file transfer operation (e.g., logStop attribute of the eventLog Resource) shall use the Upload mechanism defined in TR-069 [4]. The Upload mechanism  is an asynchronous command that consists of the synchronous Upload RPC for the Upload and the asynchronous TransferComplete RPC.  The Upload RPC returns a successful response or one of the following fault codes in Table 8.1.3.2-1. A successful response means that the CPE has accepted the Upload RPC.

Table 8.1.3.2-1: Upload Fault Code Mapping

| Fault code | Description | Primitive Error Code |
| --- | --- | --- |
| 9000 | Method not supported |  |
| 9001 | Request denied (no reason specified) |  |
| 9002 | Internal error |  |
| 9003 | Invalid arguments |  |
| 9004 | Resources exceeded (when used in association with SetParameterValues, this MUST NOT be used to indicate Parameters in error) |  |
| 9011 | Upload failure (associated with Upload, TransferComplete or AutonomousTransferComplete methods). |  |
| 9012 | File transfer server authentication failure (associated with Upload, Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9013 | Unsupported protocol for file transfer (associated with Upload, Download, ScheduleDownload, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |

Once the CPE has attempted to Upload the file, the CPE reports the result of the Upload operation using the TransferComplete RPC. The TransferComplete RPC indicates a successful operatoin or one of the following fault codes in Table 8.1.3.2-2.

Table 8.1.3.2-2: TransferComplete Fault Code Mapping

| Fault code | Description | Primitive Error Code |
| --- | --- | --- |
| 9001 | Request denied (no reason specified) |  |
| 9002 | Internal error |  |
| 9010 | File transfer failure (associated with Download, ScheduleDownload, TransferComplete or AutonomousTransferComplete methods). |  |
| 9011 | Upload failure (associated with Upload, TransferComplete or AutonomousTransferComplete methods). |  |
| 9012 | File transfer server authentication failure (associated with Upload, Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9014 | File transfer failure: unable to join multicast group (associated with Download, TransferComplete or AutonomousTransferComplete methods). |  |
| 9015 | File transfer failure: unable to contact file server (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9016 | File transfer failure: unable to access file (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9017 | File transfer failure: unable to complete download (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9018 | File transfer failure: file corrupted or otherwise unusable (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9019 | File transfer failure: file authentication failure (associated with Download, TransferComplete or AutonomousTransferComplete methods). |  |
| 9020 | File transfer failure: unable to complete download within specified time windows (associated with TransferComplete method). |  |

#### 8.1.3.3	Update primitive mapping for download file transfer operations

The  Update primitive that results in a download file transfer operation (e.g., update attribute of Resource firmware) shall use the Download mechanism defined in TR-069 [4]. The Download mechanism is an asynchronous command that consists of the synchronous Download RPC for the Download and the asynchronous TransferComplete RPC.  The Download RPC returns a successful response or one of the following fault codes in Table 8.1.3.3-1. A successful response means that the CPE has accepted the Download RPC.

Table 8.1.3.3-1: Download Fault Code Mapping

| Fault code | Description | Primitive Error Code |
| --- | --- | --- |
| 9000 | Method not supported |  |
| 9001 | Request denied (no reason specified) |  |
| 9002 | Internal error |  |
| 9003 | Invalid arguments |  |
| 9004 | Resources exceeded (when used in association with SetParameterValues, this MUST NOT be used to indicate Parameters in error) |  |
| 9010 | File transfer failure (associated with Download, ScheduleDownload, TransferComplete or AutonomousTransferComplete methods). |  |
| 9012 | File transfer server authentication failure (associated with Upload, Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9013 | Unsupported protocol for file transfer (associated with Upload, Download, ScheduleDownload, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |

Once the CPE has attempted to Download the file, the CPE reports the result of the download operation using the TransferComplete RPC. The TransferComplete RPC indicates a successful operatoin or one of the following fault codes in Table 8.1.3.3-2.

Table 8.1.3.3-2: TransferComplete Fault Code Mapping

| Fault code | Description | Primitive Error Code |
| --- | --- | --- |
| 9001 | Request denied (no reason specified) |  |
| 9002 | Internal error |  |
| 9010 | File transfer failure (associated with Download, ScheduleDownload, TransferComplete or AutonomousTransferComplete methods). |  |
| 9011 | Upload failure (associated with Upload, TransferComplete or AutonomousTransferComplete methods). |  |
| 9012 | File transfer server authentication failure (associated with Upload, Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9014 | File transfer failure: unable to join multicast group (associated with Download, TransferComplete or AutonomousTransferComplete methods). |  |
| 9015 | File transfer failure: unable to contact file server (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9016 | File transfer failure: unable to access file (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9017 | File transfer failure: unable to complete download (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9018 | File transfer failure: file corrupted or otherwise unusable (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9019 | File transfer failure: file authentication failure (associated with Download, TransferComplete or AutonomousTransferComplete methods). |  |
| 9020 | File transfer failure: unable to complete download within specified time windows (associated with TransferComplete method). |  |

#### 8.1.3.4	Update primitive mapping for reboot operation

The  Update primitive that results in a reboot operation (e.g., reboot attribute of Resource reboot) shall use the Reboot RPC defined in TR-069 [4]. The Reboot RPC is a synchronous command.  The Reboot RPC returns a successful response or one of the following fault codes in Table 8.1.3.4-1.

Table 8.1.3.4-1: Reboot Fault Code Mapping

| Fault code | Description | Primitive Error Code |
| --- | --- | --- |
| 9001 | Request denied (no reason specified) |  |
| 9002 | Internal error |  |
| 9003 | Invalid arguments |  |

#### 8.1.3.5	Update primitive mapping for factory reset operation

The  Update primitive that results in a factory reset operation (e.g., factoryReset attribute of Resource reboot) shall use the FactoryReset RPC defined in TR-069 [4]. The FactoryReset RPC is a synchronous command.  The FactoryReset RPC returns a successful response or one of the following fault codes in Table 8.1.3.5-1.

Table 8.1.3.5-1: FactoryReset Fault Code Mapping

| Fault code | Description | Primitive Error Code |
| --- | --- | --- |
| 9000 | Method not supported |  |
| 9001 | Request denied (no reason specified) |  |
| 9002 | Internal error |  |
| 9003 | Invalid arguments |  |

#### 8.1.3.6	Update primitive mapping for software install operation

The  Update primitive that results in a software installation operation (e.g., install attribute of Resource software) shall use the ChangeDUState mechanism defined in TR-069 [4]. The ChangeDUState mechanism is an asynchronous command that consists of the synchronous ChangeDUState RPC for the download and the asynchronous ChangeDUStateComplete RPC.  The ChangeDUState RPC returns a successful response or one of the following fault codes in Table 8.1.3.6-1. A successful response means that the CPE has accepted the ChangeDUState RPC.

Table 8.1.3.6-1: ChangeDUState Fault Code Mapping

| Fault code | Description | Primitive Error Code |
| --- | --- | --- |
| 9000 | Method not supported |  |
| 9001 | Request denied (no reason specified) |  |
| 9002 | Internal error |  |
| 9004 | Resources exceeded (when used in association with SetParameterValues, this MUST NOT be used to indicate Parameters in error) |  |

Once the CPE has attempted to change the state of the deployment unit, the CPE reports the result of the state change operation using the ChangeDUStateComplete RPC. The ChangeDUStateComplete RPC indicates a successful operatoin or one of the following fault codes in Table 8.1.3.6-2.

Table 8.1.3.6-2: ChangeDUStateComplete Fault Code Mapping

| Fault code | Description | Primitive Error Code |
| --- | --- | --- |
| 9001 | Request denied (no reason specified) |  |
| 9003 | Invalid arguments |  |
| 9012 | File transfer server authentication failure (associated with Upload, Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9013 | Unsupported protocol for file transfer (associated with Upload, Download, ScheduleDownload, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9015 | File transfer failure: unable to contact file server (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9016 | File transfer failure: unable to access file (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9017 | File transfer failure: unable to complete download (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9018 | File transfer failure: file corrupted or otherwise unusable (associated with Download, TransferComplete, AutonomousTransferComplete, DUStateChangeComplete, or AutonomousDUStateChangeComplete methods). |  |
| 9022 | Invalid UUID Format (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install, Update, and Uninstall) |  |
| 9023 | Unknown Execution Environment (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install only) |  |
| 9024 | Disabled Execution Environment (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install, Update, and Uninstall) |  |
| 9025 | Deployment Unit to Execution Environment Mismatch (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install and Update) |  |
| 9026 | Duplicate Deployment Unit (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install only) |  |
| 9027 | System Resources Exceeded (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install and Update) |  |
| 9028 | Unknown Deployment Unit (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Update and Uninstall) |  |
| 9029 | Invalid Deployment Unit State (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Install, Update and Uninstall) |  |
| 9030 | Invalid Deployment Unit Update – Downgrade not permitted (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Update only) |  |
| 9031 | Invalid Deployment Unit Update – Version not specified (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Update only) |  |
| 9032 | Invalid Deployment Unit Update – Version already exists (associated with DUStateChangeComplete or AutonomousDUStateChangeComplete methods: Update only) |  |

### 8.1.4	Retrieve primitive mapping

The  Retrieve primitive shall map to the SetParameterValues RPC. The GetParametersValue RPC is defined in TR-069 [4] as a synchronous RPC and returns a successful response or one of the following fault codes in Table 8.1.4-1.

Table 8.1.4-1: GetParameterValues Fault Code Mapping

| Fault code | Description | Primitive Error Code |
| --- | --- | --- |
| 9001 | Request denied (no reason specified) |  |
| 9002 | Internal error |  |
| 9003 | Invalid arguments |  |
| 9004 | Resources exceeded (when used in association with SetParameterValues, this MUST NOT be used to indicate Parameters in error) |  |
| 9005 | Invalid Parameter name (associated with Set/GetParameterValues, GetParameterNames, Set/GetParameterAttributes, AddObject, and DeleteObject) |  |

### 8.1.5	Notify primitive mapping

The Notify primitive permits notifications to Originators that have subscribed to a Resource. TR-069 [4] has the capability to be notified when attributes of objects have been modified but not when any attribute of an object has been modified.

As such the procedure for mapping the Notify primitive for TR-069 is not possible within the TR-069 protocol unless the CSE subscribes to receive notification to all the attributes of a Resource.

Note: In many implementations, subscribing to all the attributes of an object associated with the Resource can cause performance issues in the CPE as well as the CSE. As such using the attribute based subscription capabilities of TR-069 [4] for subscription of Resources should be avoided when possible.

#### 8.1.5.1	Procedure for subscribed Resource attributes.

The Notify primitive shall map to the SetParameterAttributes RPC in the following manner:

TR-069 [4] provides the capability to subscribe to changes of a specific attribute through the use of the SetParameterAttributes RPC using the “Active” value for the Notification parameter.

TR-069 [4] provides the capability to un-subscribe to changes of a specific attribute through the use of the SetParameterAttributes RPC using the “None” value for the Notification parameter.

The SetParametersAttributes RPC is defined in TR-069 [4] as a synchronous RPC and returns a successful response or one of the following fault codes in Table 8.1.5.1-1.

Table 8.1.5.1-1: SetParameterAttributes Fault Code Mapping

| Fault code | Description | Primitive Error Code |
| --- | --- | --- |
| 9000 | Method not supported |  |
| 9001 | Request denied (no reason specified) |  |
| 9002 | Internal error |  |
| 9003 | Invalid arguments |  |
| 9004 | Resources exceeded (when used in association with SetParameterValues, this MUST NOT be used to indicate Parameters in error) |  |
| 9010 | File transfer failure (associated with Download, ScheduleDownload, TransferComplete or AutonomousTransferComplete methods). |  |

#### 8.1.5.2	Notification mapping

CPEs produce notifications for subscribed attributes using the TR-069 Inform method, the Inform method has an argument Event that has as one of the EvendCodes with the value "4 VALUE CHANGE" indicating that a subscribed parameter’s value has changed. The parameter(s) that have changed are included ParameterList argument of the Inform method.

The ParameterList argument  is list of  name-value pairs; the name is parameter name and shall be mapped to the objectPath attribute of the Resource while the value is the most recent value of the parameter.

Note: TR-069 CPEs do not report value change’s of parameters that were modified by the ACS.

# 9	Server Interactions

This clause specifies how the IN-CSE interacts with an ACS in order to manage the Resources described in this specification. The IN-CSE interaction with an ACS includes:

Establishment of the communication session between the IN-CSE and ACS

Processing of requests and notifications between the IN-CSE and the ACS

Discovery

Note: The Broadband Forum has not defined a protocol specification for the Northbound Interface of an ACS. As such, this document only describes the expectations of this interface in the form of requirements on the ACS.

## 9.1	Communication Session Establishment

## 9.1.1	IN-CSE to ACS Communication Session Establishment

When the IN-CSE detects that it has to delegate an interaction with the a device resource to an ACS, the IN-CSE establishes a communication session with the ACS. The establishment of a communication session between the IN-CSE and ACS  provides security dimensions for Access control, Authentication, Non-repudiation, Data confidentiality, Communication security, Data integrity and Privacy adhering to the following TR-131 [7] Architectural requirement A7.

The IN-CSE may establish multiple sessions with a ACS based on the security model utilized between the IN-CSE and the ACS.

## 9.1.2	ACS to IN-CSE Communication Session Establishment

When the ACS detects a change to resources it manages that the IN-CSE has expressed interest, the ACS  requests the IN-CSE to establish a session if a session doesn’t exist for the resource being managed. The establishment of a communication session between the IN-CSE and ACS  provides security dimensions for Access control, Authentication, Non-repudiation, Data confidentiality, Communication security, Data integrity and Privacy adhering to the following TR-131 [7] Architectural requirement A7.

The ACS may establish multiple sessions with a IN-CSE based on the security model utilized between the IN-CSE and the ACS.

While a session between the ACS and IN-CSE is not established, the AS retains any notifications or changes in the resources based on a Event retention policy (i.e., time, number of events).

When a ACS to IN-CSE interaction is required and a session does not exist, the ACS requests to initiate a session based on a Session Initiation Policy (i.e., Periodic contact establishment (schedule), upon event detection with timeframe window).

### 9.2.3	ACS and IN-CSE Communication Session Requirements

When establishing a session from the ACS to the IN-CSE:

If a session doesn’t exist between the IN-CSE and ACS, the ACS shall retain any notifications or changes in the resources based on a Event retention policy (i.e., time, number of events).

When an ACS to IN-CSE interaction is required and a session does not exist, the ACS shall be capable to initiate a session based on a Session Initiation Policy (i.e., Periodic contact establishment (schedule), upon event detection with timeframe window)

## 9.2	Processing of Requests and Responses

### 9.2.1	Request and Notification Formatting

Requests and Notifications mechanisms between the IN-CSE and the DM Server format the XML schema of the CPE methods defined in TR-069 [4] as an ACS would format the CPE methods that it would pass to the CPE. The IN-CSE would then also process the CPE methods as defined in TR-069 [4]. Likewise the ACS would send notifications in the format of the XML schema of the CPE for sending events using the Inform RPC.

### 9.2.2	ACS Request Processing Requirements

When receiving requests from the IN-CSE the ACS  shall be capable of defining mechanisms to support triggering of immediate operations to device. If the device is not available the ACS MUST return an appropriate error code.

The ACS shall provide capability for the IN-CSE to indicate request policies to include: Retry policy, Request Time out.

### 9.2.3	ACS Notification Processing Requirements

When sending notifications to the IN-CSE:

The ACS shall be capable of providing a mechanism for the IN-CSE  to subscribe to events.

The ACS shall be capable of providing a list of events for which the IN-CSE can subscribe.

The ACS shall be capable of providing a mechanism for the IN-CSE to unsubscribe from events.

The ACS shall be capable of providing an event delivery mechanism.

The ACS shall be capable of providing the capability for the IN-CSE to request event filters including: Event Code; Specific parameters changing value; Device; Any combination of the previous criteria.

The IN-CSE shall be capable of subscribing to be notified of changes to resources it manages.

The ACS  shall be capable of notifying the IN-CSE of changes to resources to which the client has subscribed.

## 9.3	Discovery and Synchronization of Resources

For devices under management, the IN-CSE  may discover resources of interest (metadata and values) within a device using the ACS.

For resources of interest, the IN-CSE may also express an interest to be notified of a resource if a resource is changed (added, deleted, updated).

The IN-CSE shall be capable to discover and subscribe to changes of resources in order to synchronize the IN-CSE with resources of interest of the ACS.

## 9.4	Access Management

Once a request has performed an Access Decision by the IN-CSE to allow the request, the IN-CSE must select the appropriate ACS along with elements the ACS would need to implement access management within the ACS. These would include the Identity of the subject (oneM2M Originator) of the request which is needed in scenarios where the original issuer of the request is needed to be known – this could be done by correlating principals (e.g., Roles, Accounts) used by the IN-CSE and ACS.

## 9.4.1	Access Management Requirements

The ACS shall be capable of providing a mechanism for the IN-CSE to discover the Access Management elements used to authorize and authenticate access to resources controlled by the ACS.

The IN-CSE shall be capable of correlating Access Management elements provided by the ACS to Access Management elements used by the IN-CSE.

The IN-CSE shall be capable of providing secured storage of Access Management elements within the IN-CSE.

# 10	New Management Technology Specific Resources

TR-181 [6] provides a list of management objects that have been standardized by the Broadband Forum and where possible, clause 7 provides a mapping of the Resources to standardized management objects. This clause provides the oneM2M vendor specific extensions to the TR-181 [6] data model as specified in the ts-0006-1-0.xml.

# Proforma copyright release text block

This text box shall immediately follow after the heading of an element (i.e. clause or annex) containing a proforma or template which is intended to be copied by the user. Such an element shall always start on a new page.

Notwithstanding the provisions of the copyright clause related to the text of the present document, oneM2M grants that users of the present document may freely reproduce the <proformatype> proforma in this {clause|annex} so that it can be used for its intended purposes and may further publish the completed <proformatype>.

<PAGE BREAK>

## Annexes

Each annex shall start on a new page (insert a page break between annexes A and B, annexes B and C, etc.).

Use the Heading 9 style for the title and the Normal style for the text.

Annex <A> (Informative/Normative):Remove Informative or Normative as appropriatTitle of annex (style H9)

<Text>

<PAGE BREAK>

Annex <B>(Informative/Normative): Remove Informative or Normative as appropriateTitle of annex (style H9)

<Text>

B.1	First clause of the annex (style H1)

<Text>

B.1.1	First subdivided clause of the annex (style H2)

<Text>

<PAGE BREAK>

The following text is to be used when appropriate:

Annex <y>:
Bibliography

The annex entitled "Bibliography" is optional.

It shall contain a list of standards, books, articles, or other sources on a particular subject which are not mentioned in the document itself

It shall not include references mentioned in the document.

Use the Heading 9 style for the title and B1+ or Normal for the text.

<Publication>: "<Title>".

OR

<Publication>: "<Title>".

<PAGE BREAK>

# History

This clause shall be the last one in the document and list the main phases (all additional information will be removed at the publication stage).

| Publication history |
| --- |
| V1.1.1 | <dd-Mmm-yyyy> | <Milestone> |

| Draft history (to be removed on publication) |
| --- |
| V.0.0.1 | 18 Feb 2014 | Initial Skeleton |
| V.0.1.0 | 12 Mar 2014 | Incorporate the following contributions: MAS-2014-0336R01-TS-0006_Updates |
| V.0.2.0 | 12 May 2014 | Incorporate the following contributions: MAS-2014-0371R03-TS-0006-Editorial_and_Section_6_Updates MAS-2014-0372R04-TS-0006-Section_7_and_10_Updates MAS-2014-0373R01-TS-0006-Section_8_Updates |