| oneM2M Technical Specification |
| --- |
| Document Number | TS-0022-Field_Device_Configuration-V0_4_0 |
| Document Name: | Field Device Configuration |
| Date: | 21-July -2016 |
| Abstract: | Field Device Configuration TS |
| Template Version:23 February 2015 (Dot not modify) |

This Specification is provided for future development work within oneM2M only. The Partners accept no liability for any use of this Specification.

The present document has not been subject to any approval process by the oneM2M Partners Type 1.  Published oneM2M specifications and reports for implementation should be obtained via the oneM2M Partners' Publications Offices.

About oneM2M

The purpose and goal of oneM2M is to develop technical specifications which address the need for a common M2M Service Layer that can be readily embedded within various hardware and software, and relied upon to connect the myriad of devices in the field with M2M application servers worldwide.

More information about oneM2M may be found at:  http//www.oneM2M.org

Copyright Notification

© 2016, oneM2M Partners Type 1 (ARIB, ATIS, CCSA, ETSI, TIA, TTA, TTC).

All rights reserved.

The copyright extends to reproduction in all media.

Notice of Disclaimer & Limitation of Liability

The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations. No recommendation as to products or vendors is made or should be implied.

NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE, GOVERNMENTAL RULE OR REGULATION, AND FURTHER, NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS. NO oneM2M PARTNER TYPE 1 SHALL BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY THAT PARTNER FOR THIS DOCUMENT, WITH RESPECT TO ANY CLAIM, AND IN NO EVENT SHALL oneM2M BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES. oneM2M EXPRESSLY ADVISES ANY AND ALL USE OF OR RELIANCE UPON THIS INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER.

# Contents

Contents	3

1.	Scope	4

2.	References	4

2.1.	Normative references	4

2.2.	Informative references	4

3.	Definitions	5

3.1.	Definitions	5

4.	Conventions	5

5.	Introduction	5

6.	Resource type and data format definitions	7

6.1.	<mgmtObj> Resource specializations	7

6.1.1.	Resource [registration]	7

6.1.1.1.	Introduction	7

6.1.1.2.	Resource specific procedure on CRUD operations	9

6.1.2.	Resource [dataCollection]	10

6.1.2.1.	Introduction	10

6.1.2.2.	Resource specific procedure on CRUD operations	11

6.2.	Data Formats for Device Configuration	11

6.2.1.	Introduction	11

6.2.2.	Enumeration types	11

6.2.2.1.	Introduction	11

6.2.2.2.	dcfg:authenticationDataFormatType	12

6.2.3.	Simple data types	12

7.	Procedures	13

7.1.	Device configuration generic procedures	13

7.1.1.	Setting configuration information on <mgmtObj> resource	13

7.1.2.	Loading configuration information for field device	13

7.2.	Initial registration procedure	16

7.3.	Enabling data collection by [dataCollection] resource	16

7.4.	Application Configuration	17

Proforma copyright release text block	18

Annexes	19

Annex <y>: Bibliography	19

History	20

# Scope

The present document will cover the specifications enabling to remotely configure oneM2M compliant Field Domain Devices (e.g. ADN or ASN) for operation with a chosen oneM2M SP.

The configuration information may include:

- The availability of protocol bindings

- The URI of registrar CSE that  receives Registration requests.

- The URI of registrar CSE that receives non-Registration requests.

- The address of target resource to use a oneM2M Service. [e.g. reconfigurable to add/delete service during operation]

- The credential data that is required for accessing the resource. [e.g. reconfigurable to grant/revoke authorization]

- The instructions for configuration of Field Device implementing specific information models.

# References

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references,only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

## Normative references

The following referenced documents are necessary for the application of the present document.

[1]	IETF RFC5280: "Internet X.509 Public Key Infrastructure Certification and Certificate Revocation List (CRL) Profile"

[2]	oneM2M TS-0001, Functional Architecture TS

[3]	oneM2M TS-0003, Security Solutions TS

[4]	oneM2M TS-0004, Service Layer Core Protocol TS

[5]	IETF RFC 2898, "PKCS#5: Password-Based Cryptography Specification Version 2.0"

[6]	IETF RFC 5652, "PKCS#7: Cryptographic Message Syntax (CMS)"

[7]	IETF RFC 7292, "PKCS#12: Personal Information Exchange Syntax v1.1"

[8]	IETF RFC 6920, "Naming Things with Hashes"

## Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

# Definitions

## Definitions

Configurator AE: the specialized AE which assist configuration both M2M Platform and the field device (e.g. AE or remote CSE in field domain.

Node Enrolment: the procedure to enable registration of AE or remote CSE in field domain

Application Configuration: the procedure to enable configuring M2M Application specific settings (including security profile associated with the application) on AE in field domain.

Configurator AE: a specialized AE which determines setting data for configuring device in the field domain.

Configuration Information  Serializer AE: a specialized AE which retrieves the <mgmtObj> resource and transfers it as serialized data stream to configuring device in the field domain.

# Conventions

The key words “Shall”, ”Shall not”, “May”, ”Need not”, “Should”, ”Should not” in this document are to be interpreted as described in the oneM2M Drafting Rules [i.1]

# Introduction

## 5.1. 	Roles for M2M Application and Field Device configuration

The oneM2M Functional Architecture TS [2] assumes all required information is shared between Registrar CSE and remote entities (e.g. AE or CSE) in field domain before Registration of the remote entity is performed.

Exchange of such information may be assisted by a third party AE, named as 'Configurator', since trust relation between registrar and remote entities are not established yet.

The Configurator is responsible to configure both the M2M Platform and the devices in the field domain to operate properly.

## 5.2.	High level procedure

There are two phase on the M2M Application and field device configuration.

Phase-1: Node Enrolment: Sharing the information to register the entity on the specific registrar CSE.

Phase-2: Application Configuration: Configuring M2M Application specific parameters including the security parameters.

### 5.2.1.	Introduction

There are two categories on the M2M Application and field device configuration.

Category-1: Device Management regarding Initializing M2M Service
Sharing the configuration information to establish the connectivity and to register the entity (AE or CSE in the field domain) on the specific registrar CSE.

Category-2: Service management regarding Application Enrolment (see oneM2M TS-0001 [2] clause 11.2.2)
Configuring M2M Application specific configuration information. This procedure can be performed on AE only.

The specialized AE which is named ‘Configurator AE’, may takes a role of responsible to configure device in field domain.

The setting information shall be set on specializations of oneM2M <mgmtObj> resource by the Configurator AE, and the data is reflected to the Field Device.

Field Device may choose one of three ways to reflect the configuration information:

[Type-1] Device Management: (note: use same term of TS-0001)[applicable for Category1 & Category-2]
The configuration information is shared as a management object using remote device management technologies (e.g. OMA-DM, BBF TR-069) (case 2a in Figure 5.2.1-1).

[Type-2] Application Configure through oneM2M native access [applicable for Category-2 only]
Once Field Device is registered, and the device can receive setting information for Application Configuration purpose (case 2b in Figure 5.2.1-1).

[Type-3] Interworked Device Management  [applicable for Category-1 & Category-2]
The configuration information is retrieved by ‘Configuration Information Serializer AE’, then it is transferred to the Field Device as data stream (case 2c & 3 in Figure 5.2.1-1).

Figure 5.2.1-1: Device Configuration Overview

### 5.2.2.	Initializing M2M Service procedure

The field device shall receive from the M2M Service Provider the initial settings to install for performing Registration.

The initial settings for each CSE or AE shallcontain following information:

Connectivity settings: protocol binding, PoA information of Registrar CSE (IP address or DNS name, port)

Authentication credential: Pre-shared symmetric key with associated identifier, or public-key pair with digital certificate(See oneM2M TS-0003 [3])

From parameter of Registration request: CSE-ID or AE-ID

Note: The choice of delivery method of the configuration information may be implementation depended.

### 5.2.3.	Application Configuration procedure

The possible configuratio information for Application Configuration are:

The address of targeted containers (e.g. <container> or <flexContainer> resource) to use.

Data format and other meta-information to apply on storing data on targeted containers.

Frequency of data collections

# Resource type and data format definitions

## <mgmtObj> Resource specializations

The present clause specifies <mgmtObj> resource specializations used for device configuration.

Following table shows summary of defined <mgmtObj> resource specializations in present document.

| mgmtDefinition | Intended use | Note |
| --- | --- | --- |
| registration | Install configuration regarding registration procedure. |  |
| dataCollection | Install configuration regarding data collection using <container> and <contentInstance> resource. |  |

### Resource [registration]

#### Introduction

This specialization of <mgmtObj> is used to convey setting parameter to enable registration procedure by field devices (e.g. AE or CSE).

Figure 6.1.1.1-1: Structure of [registration] resource

Table 6.1.1.1-1: Data Type Definition of [registration]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| registration | DCFG-registration-v1_0.xsd |  |

Table 6.1.1.1-2: Resource specific attributes of [registration]

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| mgmtDefinition | M | NP | See clause 7.4.15of oneM2M TS-0004. | "registration" |
| objectID | O | NP | See clause 7.4.15 of oneM2M TS-0004. |  |
| objectPaths | O | NP | See clause 7.4.15 of oneM2M TS-0004. |  |
| description | O | O | See clause 7.4.15 of oneM2M TS-0004. |  |
| originatorID | O | O | m2m:ID | AE-ID or CSE-ID to be used on registration request. If the setting is for CSE, then this attribute shall be present. |
| poA | M | O | xs:AnyURI | the URI for point of acess address of registrar CSE. Protocol binding is determined from the protol in this URI. |
| resourcePath | M | O | m2m:ID | The path of <CSEBase> resource to create <AE> or <remoteCSE> resource. |
| credentialID | O | O | dcfg:credentialID | Identifier to be used for authentication on registration procedure. See clause 10.4 of oneM2M TS-0003 [3] for detail specification of "credential-ID" (NOTE-1). |
| authenticationDataFormat | O | O | dcfg:authenticationDataFormatType | Indicates the data format of authenticationData attribute. See clause 6.2.2.2 for definition. |
| authenticationData | O | O | xs:base64Binary | Data which is used for authentication. The interpretation procedure of this data is determined by the value of authenticationDataType. |
| NOTE-1: optionality on authenticationDataFormat and authenticationData attribute depends on Type-ID part of credentialID. |

#### Resource specific procedure on CRUD operations

When management is performed using technology specific protocols, the procedures defined in clause 7.4.15.2 on oneM2M TS-0004,'<mgmtObj> specific procedures' shall be used. There are no change from the generic procedures in clause 7.2.2 of oneM2M TS-0004 for operations on this resource.

### Resource [dataCollection]

#### Introduction

This specialization of <mgmtObj> is used to convey setting parameter to enable data collection using <container> and <contentInstance> resource by field devices (e.g. AE).

Figure 6.1.2.1-1: Structure of [registration] resource

Table 6.1.2.1-1: Data Type Definition of [dataCollection]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| dataCollection | DCFG-dataCollection-v1_0.xsd |  |

Table 6.1.2.1-2: Resource specific attributes of [dataCollection]

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| mgmtDefinition | M | NP | See clause 7.4.15 of oneM2M TS-0004. | "dataCollection" |
| objectID | O | NP | See clause 7.4.15 of oneM2M TS-0004. |  |
| objectPaths | O | NP | See clause 7.4.15 of oneM2M TS-0004. |  |
| description | O | O | See clause 7.4.15 of oneM2M TS-0004. |  |
| containerPath | M | O | m2m:ID | The resource address of <container> resource to store the data from the device. |
| reportFrequency | O | O | xs:integer | The seconds to upload next data. |
| measurementFrequency | O | O | xs:integer | The seconds to measure next data. |

#### Resource specific procedure on CRUD operations

When management is performed using technology specific protocols, the procedures defined in clause 7.4.15.2 on oneM2M TS-0004,'<mgmtObj> specific procedures' shall be used. There are no change from the generic procedures in clause 7.2.2 of oneM2M TS-0004 for operations on this resource.

## Data Formats for Device Configuration

### Introduction

The following clauses define data formats of resource attributes and parameters used in present document.

Any data types of XML elements defined for use in present document shall be one of name spaces in Table 6.2.1-1.

Table 6.2.1-1: Namespaces used in present document

| Name space | prefix | Name space definition |
| --- | --- | --- |
| oneM2M protocol CDT | m2m: | http://www.onem2m.org/xml/protocol |
| Device Configuration | dcfg: | http://www.onem2m.org/xml/deviceConfig |

### Enumeration types

### Introduction

The following clauses define various enumeration types as extension from ‘oneM2M Enumeration Types’ which is defined in oneM2M TS-0004[x].

Each enumeration type is defined as table like below.

Table 6.2.2.1-1: Example of oneM2M Enumeration Type Definition

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Interpretation-1 |  |
| 2 | Interpretation-2 |  |
| 3 | Interpretation-3 |  |
| NOTE: See clause x.x.x "title of clause" |

The enumeration type definition in present document shall be implemented as part of ‘DCFG-CommonTypes-<version_of_specification>.xsd’. Figure 6.2.2.1-1 shows the example of XSD representation of
 'dcfg:fooType'.

Figure 6.2.2.1-1: Example of XSD version of oneM2M Enumeration Type

##### dcfg:authenticationDataFormatType

Used for authenticationData attribute in [registration] resource.

The authenticationDataFormat attribute shall indicates data format of authenticationData attribute in [registration] resource.

Table 6.2.2.2-1: Interpretation of dcfg:authenticationDataFormatType

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | PSK_PLAIN_TEXT | Pre-shared key for (D)TLS-PSK in plain text. |
| 2 | PSK_PKCS5 | Pre-shared key for (D)TLS-PSK in PKCS5 data format [5]. |
| 3 | CERT_X509 | Digital certificate for Certificate-based authentication in X.509 DER format [1]. |
| 4 | CERT_KEY_PKCS12 | Digital certificate for Certificate-based authentication with associated private key in PKCS#12 format [7] |
| 5 | RAW_PUBLIC_KEY | one of the sha 256-120, sha-256-128 or sha-256 hash algorithms specified in IETF RFC 6920 [40]. |
| NOTE: Passphrase for encrypted data shall be shared in advance. |

### Simple data types

Table 6.2.3-1 describes Device Configuration specific simple data type definitions. XML Schema data type definitions for these data types can be found in the XSD file called DCFG-commonTypes-<version_of_specification>.xsd.

The types in table 6.2.3-1 are either:

- Atomic data types derived from XML Schema data types by restrictions other than enumeration

- List data types constructed from other XML Schema or oneM2M-defined atomic data types.

NOTE: The enumeration data types for Device Configuration TS are defined in clause 6.2.2.

Table 6.2.3-1: oneM2M Simple Data Types for Device Configuration

| XSD type name | Type Name | Examples | Description |
| --- | --- | --- | --- |
| dcfg:credentialID | credential ID | User1@example.com | KpsaId |
|  |  | 0x265357902fe1b7e2a04b897c6025d7a2 | one of the sha 256-120, sha-256-128 or sha-256 hash algorithms specified in IETF RFC 6920 [8]. |
|  |  | Sapplication00230 | SP assigned AE-ID |

# Procedures

## Device configuration generic procedures

## Setting configuration information on <mgmtObj> resource

Setting configuration information for  field device is achieved by setting value on [objectAttribute] attribute of the <mgmtObj> resource.

When the Configurator AE decided to configure a device, the Configurator AE searches <mgmtObj> resources which is created as child resource of <node> resource which is linked to the device.

If the targeted <mgmtObj> resource is found, the Configurator AE request to UPDATE the resource, otherwise the Configurator AE shall CREATE a <mgmtObj> resource as child resource of the <node> resource.

NOTE: Acceptance of  CREATE request for a specialization of  <mgmtObj> resource is implementation dependent.

Figure 7.1.1-1: Configuring setting parameters on <mgmtObj> resource

### Loading configuration information for field device

If the <mgmtObj> resource is configured to trigger device management technologies, remote device management to load configuration information  on the device is performed automatically when <mgmtObj> resource is CREATEed or UPDATEed. See clause 10.2.8 '<mgmtObj> Resource Procedures' of oneM2M TS-0001 for triggering external management technologies via <mgmtObj> resource. The Hosting CSE shall be IN-CSE in this case.

Procedures to load configuration information for field device (Type-1) using external management technologies are illustrated in Figure 7.1.2-1.

Figure 7.1.2-1: Configure setting parameter using external management technologies

- The Configurator AE shall issue CREATE or UPDATE request for <mgmtObj> resource which is associated field device by Hosting CSE.

Hosting CSE shall process CREATE or UPDATE request issued by Configurator AE.

The Hosting CSE shall execute Device Management command which is mapped from operation on <mgmtObj> resource to external management technologies.

The DM agent on targeted field device shall configure the setting parameters on the node, and returns the result of management.

If the <mgmtObj> resource is subscribed by the AE which resides on the targeted device, the AE shall configure setting parameters according to the Notification message. The Hosting CSE may be IN-CSE, MN-CSE, or ASN in this case.

Procedures to load configuration information for field device (Type-2) using oneM2M native access are illustrated in Figure 7.1.2-2.

Figure 7.1.2-2: Configure setting parameter using oneM2M native access

- As the preparation, the targeted field device shall subscribe <mgmtObj> resource which is associated with the specific M2M Application functionality on the targeted field device by requesting CREATE <subscription> resource.

When the Configurator AE decided to change M2M Application specific parameters, the Configurator AE shall issue UPDATE request on the <mgmtObj> resource with changed parameters.

The Hosting CSE of operated <mgmtObj> resource shall perform UPDATE procedure on the resource as Receiver.

The Hosting CSE shall issue NOTIFY request to deliver the changed parameter to targeted field device as the subscribed event message.

The targeted field device shall configure the M2M Application on the device using received parameter.

When the field device (Type-3) requested to receive the setting parameters in serialized data, the Setting Data Serializer AE shall RETRIEVE <mgmtObj> child resource of the <node> resource which is linked to the device.

Procedures to load configuration information for field device (Type-3) assisted by configuration information serialize AE are illustrated in Figure 7.1.2-3.

Figure 7.1.2-3: Configure setting parameter assisted by setting data serialize AE

- The Configurator AE shall issue CREATE or UPDATE request of <mgmtObj> resource which is associated with the functionality of targeted field device.

The Hosting CSE shall process CREATE or UPDATE request normally.

When the targeted field device determines some setting parameters to be loaded, the targeted filed device shall request the Configuration Information Serializer AE to retrieve configuration parameter as serialized data. 
Note: The communication method (ex. HTTP request) for this step is out of scope in this document.

The Configuration Information Serializer AE determines <mgmtObj> resource to refer as the source of configuration parameter for the targeted field device, and shall issue RETRIEVE operation on the <mgmtObj> resource.

When the RETRIEVE request is successfully performed, the Setting Data Serializer AE shall forward the <mgmtObj> resource in serialized form. See possible serialized forms of <mgmtObj> resource and MIME content types at clause 6.7 of TS-0004 'oneM2M specific MIME media types'.

The targeted field device shall configure setting parameters for the M2M Application referring parameters encoded in serialized data.

## Initial registration procedure

The field device shall perform registration procedure when it loaded setting data from [registration] resource.

If the field device node is CSE, then the CSE registration procedure which is defined in clause 10.1.1.2.1 of oneM2M TS-0001[2].  Otherwise (field device node is AE),the Application Entity Registration procedure which is defined in clause 10.1.1.2.2 of oneM2M TS-0001[2].

Required parameter for registration procedures are retrived as attribute value of [registration] resource.

Table 7.1-1: connectivity parameter mappings from [registration] resource

| attribute of [registration] | parameter in TS-0001/TS-0004 | Note |
| --- | --- | --- |
| originatorID | From primitive parameter | AE-ID or CSE-ID |
| PoA | CSE-PoA(Point of Access) | protocol binding choice and port number to establish connectivity with registrar CSE. |
| resourcePath | To primitive parameter | resource ID of <CSEBase> of registrar CSE. |

When credential information (see Table 7.1-2) are provided, the device shall use them for the registration procedure.

The present documents supports to configure security parameters for ‘Symmetric Key Security Framework’ (see clause 8.1.1 of oneM2M TS-0003), and ‘Certificate-Based Security Framework’ (see clause 8.1.2 of oneM2M TS-0003 [3]).

Table 7.1-2: security parameter mapping from [registration] resource

| attribute of [registration] | parameter in TS-0003 | Note |
| --- | --- | --- |
| credentialID | Credential-ID | See clause 10.4 of ‘Credential-ID detail’ of oneM2M TS-0003 [3]. |
| authenticationDataFormat | (not applicable) | Used to determine the data type of credentialID and authenticationData attribute |
| authenticationData | Kpsa (Provisioned Secure Connection Key) or ‘Credential Configuration’ | See oneM2M TS-0003[3] for Kpsa. See clause 8.1.2.3 of oneM2M TS-0003[3] for ‘Credential Configuration’. |

  - Enabling data collection by [dataCollection] resource

The field device shall be enabled to collect and report measured data to the instructed place by [dataCollection] resource.

The targeted field device shall be managed to configure necessary parameters regarding reporting measured data.

NOTE: this configuration is only applicable to M2M Applications.

Required parameter for reporting measured are retrived as attribute value of [dataCollection] resource.

Table 7.x-1: parameter mappings from [dataCollection] resource

| attribute of [registration] | parameter in TS-0001/TS-0004 | Note |
| --- | --- | --- |
| containerPath | To primitive parameter for CREATE operation for <contentInstance>. | The resource ID of <container> which is parent resource of targeted <contentInstance> |
| reportFrequency | N/A | Tme interval for requesting CREATE operation of <contentInstance>. |
| measurementFrequency | N/A | Tme interval for measurements. |

Once this application configuration is done, AE shall perform CREATE operation for new <contentInstance> resource as the child resource of <container> resource which is specified as 'containerPath' attribute of [registration] to report the measured value.

The frequency of measurement and report are specified as 'reportFrequency' and 'measuredFrequence' accordingly.

## Application Configuration

Application Configuration procedure is performed by synchronizing settings given by the Configurator AE with settings on the targeted AE, as continuation of Step 5 of "Registration Configuration" procesure:

Step 1: The Configurator AE sends CREATE request for the <flexContainer> resource which contains application specific settings in standardized data format.

Step 2: The targeted AE shall receive Notification message that contains settings regarding CREATEd <flexContainer> resource by Configurator AE.

Step 3: The targeted AE shall process the content of Notification message to load the application specific setting in the Notification message, and the targeted AE starts working with the given settings.

Step 4(optional): The Configurator AE determined to change the settings on the targeted AE.

Step 5(optional): The Configurator AE shall UPDATE the specialized <flexContainer> resource to modify the application-specific settings for the targeted AE.

Step 6(optional): The targeted AE shall process the content of Notification message to load updated setting in the Notification message, and the target AE starts working with new settings.

Figure 7.2-1: Application Enrollment procedure

Editor's Note: Figure 7.2-1 should be modified (from Francois's comment)

# Proforma copyright release text block

This text box shall immediately follow after the heading of an element (i.e. clause or annex) containing a proforma or template which is intended to be copied by the user. Such an element shall always start on a new page.

Notwithstanding the provisions of the copyright clause related to the text of the present document, oneM2M grants that users of the present document may freely reproduce the <proformatype> proforma in this {clause|annex} so that it can be used for its intended purposes and may further publish the completed <proformatype>.

<PAGE BREAK>

## Annexes

Each annex shall start on a new page (insert a page break between annexes A and B, annexes B and C, etc.).

Use the Heading 9 style for the title and the Normal style for the text.

Annex <A> (Informative/Normative):Remove Informative or Normative as appropriatTitle of annex (style H9)

<Text>

<PAGE BREAK>

Annex <B>(Informative/Normative): Remove Informative or Normative as appropriateTitle of annex (style H9)

<Text>

B.1	First clause of the annex (style H1)

<Text>

B.1.1	First subdivided clause of the annex (style H2)

<Text>

<PAGE BREAK>

The following text is to be used when appropriate:

Annex <y>:
Bibliography

The annex entitled "Bibliography" is optional.

It shall contain a list of standards, books, articles, or other sources on a particular subject which are not mentioned in the document itself

It shall not include references mentioned in the document.

Use the Heading 9 style for the title and B1+ or Normal for the text.

<Publication>: "<Title>".

OR

<Publication>: "<Title>".

<PAGE BREAK>

# History

This clause shall be the last one in the document and list the main phases (all additional information will be removed at the publication stage).

| Publication history |
| --- |
| V1.1.1 | <dd-Mmm-yyyy> | <Milestone> |

| Draft history (to be removed on publication) |
| --- |
| V.0.1.0 | 11-Sep-2015 | Initial Draft Version |
| v.0.2.0 | 22-Jan-2016 | Following CR was incorpolated: MAS-2015-0678R06 |
| v0.3.0 | 20-May-2016 | Following CR was incorpolated (agreed in MAS 22.0) MAS-2016-0082R03_CR_TS-0022_Editorial_improvements_and_clarifiations Following CR was incorpolated (agreed in MAS 23.0): MAS-2016-0086R02-CR_DevCfg_mgmtObj |
| V0.4.0 | 22-June-2016 | Following CR was incorporated (agreed in MAS 24.0) MAS-2016-0155R06-DevCfg_Basic_flows MAS-2016-0158R04-DevCfg_mgmtObj_registration MAS-2016-0184R04-DevCfg_mgmtObj_dataCollection |

# Text boxes

<xs:simpleType name="fooType">

<xs:restriction base="xs:integer">

<xs:enumeration value="1"/>

<xs:enumeration value="2"/>

<xs:enumeration value="3"/>

</xs:restriction>

</xs:simpleType>