| oneM2M Technical Report |
| --- |
| Document Number | oneM2M-TR-0044-V-0.5.0 |
| Document Name: | Physical object heterogeneous identification and tracking in oneM2M |
| Date: | 2019-03-18 |
| Abstract: | This technical report investigates the various IoT ID standards and application requirements, discussion on how to be compatible with the IoT ID standards, and providing the heterogeneous identification and tracking services. |
| Template Version:23 February 2015 (Dot not modify) |

This Specification is provided for future development work within oneM2M only. The Partners accept no liability for any use of this Specification.

The present document has not been subject to any approval process by the oneM2M Partners Type 1.  Published oneM2M specifications and reports for implementation should be obtained via the oneM2M Partners' Publications Offices.

About oneM2M

The purpose and goal of oneM2M is to develop technical specifications which address the need for a common M2M Service Layer that can be readily embedded within various hardware and software, and relied upon to connect the myriad of devices in the field with M2M application servers worldwide.

More information about oneM2M may be found at:  http//www.oneM2M.org

Copyright Notification

© 2016, oneM2M Partners Type 1 (ARIB, ATIS, CCSA, ETSI, TIA, TSDSI, TTA, TTC).

All rights reserved.

The copyright and the foregoing restriction extend to reproduction in all media.

Notice of Disclaimer & Limitation of Liability

The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations. No recommendation as to products or vendors is made or should be implied.

NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE, GOVERNMENTAL RULE OR REGULATION, AND FURTHER, NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS. NO oneM2M PARTNER TYPE 1 SHALL BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY THAT PARTNER FOR THIS DOCUMENT, WITH RESPECT TO ANY CLAIM, AND IN NO EVENT SHALL oneM2M BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES. oneM2M EXPRESSLY ADVISES ANY AND ALL USE OF OR RELIANCE UPON THIS INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER.

# Contents

Contents	3

1	Scope	5

2	References	5

2.1	Normative references	5

2.2	Informative references	5

3	Definitions, symbols and abbreviations	5

3.1	Definitions	5

3.2	Abbreviations	6

4	Conventions,	6

5	Introduction to Heterogeneous Identification Service	7

5.1	Concept of IoT identifier	7

5.1.1	Overview	7

5.1.2	Tangible identifier	7

5.1.3	Communication identifier	7

5.1.4	Application identifier	7

5.2	Concept of identification service	7

5.2.1	Introduction	7

5.2.2	Identification registration	7

5.2.3	Identification resolution	7

5.2.4	Identification discovery	8

5.2.4	Identification maintenance	8

5.3	Requirements of Heterogeneous Identification Service	8

6	Introduction on Existing Technologies	8

6.1	Overview	8

6.2	Electronic Product Code (EPC)	8

6.3	Handle Identifier	10

6.4	Ubiquitous Code (ucode)	10

6.5	Object Identifier (OID)	12

7	Use cases analysis	12

7.1	Overview	12

7.2 Use case for heterogeneous identification service	13

7.2.1	Description	13

7.2.2	Actors	13

7.2.3	Pre-conditions	14

7.2.4	Triggers	14

7.2.5	Normal Flow	14

7.2.6	Alternative flow	15

7.2.7	Post-conditions	15

7.2.8	High Level Illustration	15

7.2.9	Potential requirements	16

8	Potential enhancements to oneM2M	16

8.1	Scenarios analysis based on oneM2M architecture	16

8.1.1	Creation of physical object representation and repository	16

8.1.2	Providing associated tangible identifiers and mapping information	17

8.1.3	Identifier-based discovery of Physical Object at the CSE	18

8.1.4	Discovery of external identifiers based on interworking with external systems via IPEs	19

8.2	Potential solutions	21

8.2.1Resource Type <physicalObject>	21

8.2.x Discovery based on interworking with Handle system via IPE	22

Proforma copyright release text block	25

Annexes	25

Annex <y>: Bibliography	26

History	26

# 1	Scope

The present document studies IoT identifier, identification service, and analyses use cases and requirements of heterogeneous identification service. The document also studies and analyzes potential ways to support the heterogeneous identification and tracking services in oneM2M systems.

# 2	References

The following text block applies.

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]		oneM2M TS-0001: "Functional Architecture".

[2]		oneM2M TS-0011: "Common Terminology".

[3]		GS1 Object Name Service (ONS) V.2.0.1. 2013.

[4]		GS1 EPC Tag Data Standard 1.6.2011.

[5]		 IETF RFC 3650 Handle System Overview

[6]		IETF RFC 3651 Handle System Namespace and Service Definition.

[7]		ISO/IEC 9834-1 Information technology – Open Systems Interconnection – Procedures for the operation of OSI Registration Authorities: General procedures and top arcs of the International Object Identifier tree.

## 2.2	Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules (http://www.onem2m.org/images/files/oneM2M-Drafting-Rules.pdf)

[i.2]	Ubiquitous Code: ucode, 930-S101-1.A0.10/UID-00010

[i.3]	Simplified ucode Resolution Protocol, 910-S202-01.A0.01/UID-00005-1.A0.01

# 3	Definitions, symbols and abbreviations

Delete from the above heading the word(s) which is/are not applicable.

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in TS-0011 [2] and the following apply.

EPCIS Server: EPCIS Server that provides capture and query interfaces for event and other data.

Global Handle Registry (GHR): mainly used to manage naming authority handles and to provide service information for every naming authority under the Handle System [6].

Local Handle Services (LHS): mainly used to manage handles under given sets of naming authorities [6].

Object Name Service (ONS): A resolution system that is based on DNS and responsible for discovering authoritative data and services related to a GS1 Identification Key as defined in EPC Tag Data Standard [4].

OID resolution system (ORS): A system that is responsible for implementation of the OID resolution process.

ONS Client: An application that wishes to use ONS to identify a service that may provide information related to a specific GS1 Identification Key as defined in EPC Tag Data Standard [4].

## 3.2	Abbreviations

For the purposes of the present document, the abbreviations given in TS-0011 [2] and the following apply.

AE		Application Entity

CSE		Common Services Entity

DNS		Domain Name System

EPC		Electronic Product Code

EPCIS	EPC Information Service

FQDN	Fully Qualified Domain Name

GHR	Global Handle Registry

GRAI 	Global Returnable Asset Identifier

IC		Identification Code

IP		Internet Protocol

IPE		Interworking Proxy Entity

LHS		Local Handle Services

OID		Object Identifier

ORS		OID Resolution System

ONS		Object Name Service

SDL 	Second Level Domain Code

SGLN 	Serialized Global Location Number

SGTIN	Serialized Global Trade Item Number

SLDc 	Second Level Domain Code

SSCC	Serial Shipping Container Code

TLD 	Top Level Domain Code

UC		Ubiquitous Communicator

URI     	Uniform Resource Identifier

URL		Uniform Resource Locator

# 4	Conventions,

The key words “Shall”, ”Shall not”, “May”, ”Need not”, “Should”, ”Should not” in this document are to be interpreted as described in the oneM2M Drafting Rules [i.1]

# 5	Introduction to Heterogeneous Identification Service

## 5.1	Concept of IoT identifier

### 5.1.1	Overview

An IoT identifier is used for uniquely identifying a physical entity or logical entity in a given context. The underlying networks or applications can control and manage an entity, as well as retrieve, transmit and exchange the relevant information by the identifier.

According to the different identified objects, scenarios, and technology characteristics, the identifier can be classified into three categories: tangible identifier, communication identifier, and application identifier.

### 5.1.2	Tangible identifier

A tangible identifier is used for uniquely identifying a physical entity (e.g. cup, human being, room, etc) not having network connectivity. The tangible identifier is generally coded within in a carrier, and the carrier is attached to the physical entity, so as that the tangible identifier can be read by other entities. The carrier types include barcodes (e.g. 1D barcode, 2D barcode), RFID and others (e.g. Network card, cellphone).

The common scenario of the usage of the tangible identifier is to retrieve the physical entity related information, and the tangible identifier is not used for communicating or addressing.

### 5.1.3	Communication identifier

A communication identifier is used for uniquely identifying network nodes with the communication capabilities (terminal, RFID reader, sensor, network device). Some example formats include E.164 number and IP address so on. The communication identifier can be a relative or absolute address that it is used for communicating or addressing and, establishing network connection to the identified object.

### 5.1.4	Application identifier

An application identifier is used for identifying the services in the application layer or service layer, logical entities and objects. For example, service access code or domain name. Some example formats include URI, and URL.

## 5.2	Concept of identification service

### 5.2.1	Introduction

An IoT identification service supports the mapping, management, maintenance, discovery, and retrieval of identifier related information.

### 5.2.2	Identification registration

Identification registration represents the procedures of establishment of mappings between different identifiers, as well as the establishment of an identifier and its related information.

### 5.2.3	Identification resolution

Identification resolution represents the procedures of resolving the associated identifier or information according to the mapping between the different identifiers (e.g. tangible identifier, communication identifier and application identifier), as well as the identifier and its related information, for example, the lookups are implemented by DNS, ONS, handle system and so on.

### 5.2.4	Identification discovery

Identification discovery represents the procedures of discovering all the related identifiers or information in large and complex resources, according to the mapping between the different identifiers (e.g. tangible identifier, communication identifier and application identifier), as well as the identifier and its related information. Commonly, more than one result will be retrieved.

### 5.2.4	Identification maintenance

Identification maintenance service represents the procedures of deletion and update of different identifiers, their related information and mappings between the different identifiers.

## 5.3	Requirements of Heterogeneous Identification Service

The IoT identifier is not globally unified due to political, commercial, and due to different kinds of IoT ID standardsdefining their own identifiers. Currently, the mainstream IoT identifier standards include “Electronic Product Code (EPC)”, “Object Identifier (OID)”, “Handle Identifier”, “ubiquitous code (ucode)”, “Mobile RFID Code (mCode)” and so on. Different application verticals adopt different IoT standards, and deploy different IoT identification technologies. As a result, there exists incompatibility between different IoT identification technologies.

The heterogeneous identification service supports interworking various identification systems, and allowing them to co-exist within one another.

# 6	Introduction on Existing Technologies

Editor’s Note: The clause describes various identifier technologies and identifier resolution technologies.

## 6.1	Overview

There are many existing mechanisms for identification, naming by assigning unique identifiers to various physical/virtual entities (e.g., devices, users, processes, data, services, applications, etc.). The identification system also includes the resolution mechanisms to resolve its corresponding identification type, and some of resolution mechanisms are not implemented based on DNS infrastructure.

## 6.2	Electronic Product Code (EPC)

EPC has its origins at Auto-ID Center of the Massachusetts Institute of Technology (MIT) since 1998. In 2003, the Auto-ID Center became EPCglobal, and all relevant studies, business, and management about EPC were transferred to GS1 US®. GS1 US® is founded in 1973, and it is a not-for-profit information standards organization. Currently, GS1 US® has more than 300,000 members, and GS1 Standards are the most widely-used supply chain standards in the world.

A fundamental principle of the EPCglobal Network Architecture is the assignment of a unique identifier for physical objects, loads, locations, assets, and other entities whose use is to be tracked. The EPC has a series of code fields, it uses an 8-bits “Header Value” field to identify specific encoding scheme, such as SSCC, SGTIN, SGLN, GRAI, etc [4]. Taking the “SGTIN” code as an example, the overall structure is shown in Figure 6.2-1. A company applies its own “CompanyPrefix” from GS1, and then it assigns the “Item Reference &Indicator Digit” and “Serial Number” fields for each item-level product. In information systems, an EPC is a Uniform Resource Identifier (URI) that is in text format. EPC is not restricted to data carriers.

Figure 6.2-1 The overall structure of an EPC

EPCglobal network architecture is comprised of ONS (Object Name Service), and EPCIS (EPC information service). ONS is designed for resolving information associated with a EPC identifier, which means other identification types can not be recognized and resolved by the system. ONS uses the Domain Name System (DNS) infrastructure and implementation, thus the item’s EPC identifier must be converted into a format that DNS can understand, which is the typical, “dot” delimited, left-to-right form of all domain names, so as to accomplish the identification resolution, and then retrieving the information about the item. The resolution procedure is specified in [3] and shown in Figure 6.2-2, and the detailed illustrations are as follows:

Figure 6.2-2 ONS resolution procedures

- A EPC identifier is read from a barcode or an RFID tag using an appropriate reader.

- The reader sends that sequence of data to an ONS application.

- The ONS application extracts the desired GS1 Identification Key type and the GS1 Identification
Key itself from the data. For example, a contained GTIN is 50614141322607.

- The ONS application sends the GS1 Identification Key type, the GS1 Identification Key itself,
and the optional codes that are the client language code and client country code to the ONS client. For
example, it is configured to operate in English in Canada: en|ca|gtin|50614141322607.

- The ONS client converts the GS1 Identification Key type and the GS1 Identification Key into an
appropriate FQDN as a DNS query, implementing“dot” delimited and left-to-right form, for example: 5.0.6.2.2.3.1.4.1.4.1.6.0.gtin.gs1.id.onsepc.com.

- The DNS infrastructure with contains service types and associated data, for example, the URLs point to one or more EPCIS.

- The ONS client extracts the service type and the service data and sends it to the ONS application.

- The application interprets the data and communicates the EPCIS server according to the resolved URL.

## 6.3	Handle Identifier

The Handle System was originally developed at CNRI (The corporation for National Research Initiatives). Each handle identifier is globally unique within the context of the Handle System. It consists of two parts: naming authority (prefix) and local name (suffix), as specified in [5], and the structure is as followed:
<Handle> ::= <Handle Naming Authority> "/" <Handle Local Name>

The naming authority and local name are separated by the ASCII character "/". The naming authorities are defined in a hierarchical tree structure, the root and nodes of the tree are separated by the ASCII character ".".

For example, "10.1045/january99-bearman" is a handle identifier for an article. Its naming authority is "10.1045", there into “10” is the root naming authority, and “1045” is the subordinate naming authority. Its local name is "january99-bearman".

The Handle System defines a hierarchical service model. The Global Handle Registry (GHR) is at the top level, which can be used to manage any handle namespace, and the Local Handle Services (LHS) is at the lower level, which can be used to manage any handle namespace.

A typical handle resolution procedure is specified in [5] and shown in Figure 6.3-1, and the detailed illustrations are as follows:

- The client sends a query to Global Handle Registry to resolve the handle “10.123/456”.

- The Global Handle Registry returns the service information of the Local Handle Service A that is responsible for 	the handles under the naming authority “10.123”.

- The client sends a query to the Local Handle Service A to resolve the handle “10.123/456”.

- The Local Handle Service A resolves the Handle, and then responses the result.

Figure 6.3-1 Handle system resolution procedures

## 6.4	Ubiquitous Code (ucode)

ucode is supported by the uID center, which is a non-profit organization based in Japan. A ucode is an identifier based on an encoding strategy to uniquely identify individual “objects”, “places” and “concepts” in the real world. "Objects" include tangible objects (e.g. industrial products, agricultural crops) and intangible objects (e.g. Internet content, programs). “Places” include the real world features such as roads and buildings. “Concepts” include the relationships between "objects" and "places" and the information which can be the real world context.

The ucode consists of five fields as specified in [i.2]: Version, Top Level Domain Code, Class Code, Second Level Domain Code, and Identification Code. The basic ucode width is 128 bits, and it can extend the width in 128-bit units. The structure is shown in the Table 6.4-1.

Table 6.4-1: the structure of ucode

|  | version | TLD Code | Class Code | SDL Code | Identification Code |
| --- | --- | --- | --- | --- | --- |
| ucode-128 | 4bits | 16bits | 4bits | 20-40bits | 24-4bits |

The version indicates a ucode version number. The Class Code indicates the boundary between the Second Level Domain Code (SLDc) and the Identification Code (ic). The TLD is a domain allocated to organizations authorized by Ubiquitous ID Center. The SLD is a domain allocated to organizations authorized by the TLD management organizations.

The ucode server architecture is a multilevel hierarchical structure. In the architecture, the ubiquitous communicator (UC) retrieves the ucode and then gets the information server address by ucodeRP (ucode resolution protocol), and accesses the information associated with the identified “objects/places”.

A typical ucodeRP resolution procedure is specified in [i.3], and shown in Figure 6.4-1, and the detailed illustrations are as follows:

- UC captures a ucode from a tag.

- UC sends a request that containing the ucode to the ucode resolution server, and gets the location information 		(e.g. 192.168.1.1) of the ucode resolution server for managing a CC field.

- UC sends a request that containing the ucode to the ucode resolution server for managing a CC field and gets the 	location information (e.g. 192.168.2.1) of the ucode resolution server for managing an SLD.

- UC sends a request that containing the ucode to the ucode resolution server for managing an SLD and gets the 	location information (e.g. http://www.uidcenter.org/getinfo.cgi) of the information server.

- UC sends the ucode to the information server and gets content.

Figure 6.4-1 ucodeRP resolution procedures

## 6.5	Object Identifier (OID)

OID is jointly developed by both ISO/IEC and ITU-T. It is an encoding strategy and used to unambiguously identify an object (physical/virtual objects) uniquely in the global context. It ensures that the object can be addressed and managed absolutely.

OID uses a hierarchical tree structure. An OID consists of several segments called arcs which provide placeholders for identification and description in the hierarchical tree. In the OID tree as specified in [7], the first arc represents the organization code and is used to manage and allocate its corresponding lower arc. The first arc (nodes under the root) can be the value “itu-t (0)”, “iso (1)” and “joint-iso-itu-t (2)”, and the arcs from each node can be infinite. The OID structure is shown in the figure. OID resolution system (ORS) is a DNS-based protocol.

Figure 6.5-1 the structure of OID

# 7	Use cases analysis

## 7.1	Overview

A heterogeneous identification service is a common technology widely used in various IoT industries.  For example, supply chain management and logistics, product traceability, and energy management.

There are three requirements related to the heterogeneous identification service that are not yet supported by the oneM2M system.

| Requirement ID | Description | Release |
| --- | --- | --- |
| OSR-111 See REQ-2017-0018R01 | The oneM2M system shall be able to support heterogeneous identification services, the recognition of external identification systems and converting an object identifier to a compatible identifier recognized by the oneM2M system. |  |
|  | The oneM2M system shall be able to support the traceability linking service which provides a mapping that relates a product identifier to product related traceability information. Traceability information consists of: Logs Information on ID service nodes, such as: servers that provide access to traceability information, and devices (sensors and gateways) that gather traceability information |  |
|  | The oneM2M system shall be able to enable applications to retrieve the traceability information related to product identifiers. |  |

## Use case for heterogeneous identification service

### 7.2.1	Description

In an industrial internet environment, a physical entity (e.g. raw material, component, intermediate product and finished product ...) is given a unique tangible identifier via a labelling technology (e.g. RFID tag, barcode, etc.). The tangible identifier can aid a device (e.g. barcode reader) in identifing, monitoring, and proxying on behalf of a physical entity. The same physical entity can be assigned multiple tangible identifiers.

Based on various identification standards (e.g. EPC, OID, ucode) to allow different devices and applications compatible with the various identification standards to identify, monitor and proxy on behalf of the same physical entity.

To help manage the multiple tangible identifiers that is assigned to a physical entity, a M2M service platform supports a heterogeneous identification service. When it receives a request with a tangible identifier, the M2M service platform detects the standard which the tangible identifier is compliant to, and interworks with the corresponding resolution server to resolve the tangible identifier to a communication identifier (e.g. IP address, FQDN) of the device that interworks to the physical entity.

### 7.2.2	Actors

- M2M service platform

- The entity that provides a heterogeneous identification service.

- Discovery application

- The discovery request initiator (e.g. vendor, processor, operator or the third party).

- Device

- The entity that interworks to the physical entity and reads its tangible identifier. It can be a sensor, actuator, RFID reader, or application server.

- Resolution server

- The resolution server (e.g. ONS, Handle system) is an entity to resolve the tangible identifier of the physical entity to the communication identifier of the device that interworks to the physical entity.

- Physical entity

The physical entity does not have the capability to communicate with other entities. It is tagged with a tangible identifier a device (e.g. RFID reader) can use to identify and record information about the physical entity.

### 7.2.3	Pre-conditions

The application registers to the M2M service platform. The M2M service platform supports a heterogenous identification service that interworks with one or more identification resolution servers.

### 7.2.4	Triggers

The application initiates a request to discovery a physical entity via a tangible identifier.

### 7.2.5	Normal Flow

Figure 7.2.5-1 normal flow of heterogeneous identification service use case

- The discovery application initiates a request to discover a physical entity via its tangible identifier such that it can find the communication identifier of the device that interworks to the physical entity.

- The M2M service platform receive the request from the discovery application, identifies the standards which the tangible identifier is complaint with.

- The M2M service platform sends the tangible identifier to a request to resolve the tangible identifier to a corresponding resolution server.

- The resolution servers resolve the tangible identifier to the communication identifier of the device.

- The resolution servers respond with the communication identifier of the device to the M2M service platform.

- The M2M service platform forwards the communication identifier to the discovery application.

- The discovery application sends a request to the device that is interworked to the physical entity and includes the tangible identifier of the physical entity.

- The device processes the request.

- The device responds with information about the physical entity to the discovery application.

### 7.2.6	Alternative flow

None

### 7.2.7	Post-conditions

None.

### 7.2.8	High Level Illustration

Figure 7.2.8-1 high level illustration of heterogeneous identification service

### 7.2.9	Potential requirements

- The oneM2M system shall be able to support heterogeneous identification services, the recognition of external identification systems resolving a tangible identifier of a physical entity to a communication identifier of device.

# 8	Potential enhancements to oneM2M

## 8.1	Scenarios analysis based on oneM2M architecture

### 8.1.1	Creation of physical object representation and repository

A oneM2M AE captures physical/passive object using specialized resources (e.g. <physicalObject> type) with information that describes it for use in within the system. These specialized resources can be stored at CSEs in a location associated with the AE or in repositories.

The creation procedure is described at a high level in Figure 8.1.1-1. Various attributes of the specialized resource can be populated at the time of creation or provided via updates. The details related to attribute creation are to be provided with the resource definitions in clause 8.2.

Figure 8.1.1-1 Creation procedures for the <physicalObject> resource

The oneM2M platform can interwork with external systems or databases based on different identification mechanisms and technologies such as ONS, Handle system, uCodeRP, etc. In order to enable interworking with these systems and access to the associated physical object information, the resource definitions in clause 8.2. provide links to these external resources.

## 8.1.2	Providing associated tangible identifiers and mapping information

A oneM2M AE captures the tangible identifiers (e.g. from tags attaching to a physical entity) and also captures other related information (e.g. location, time). The procedures are shown in Figure 8.1.2-1 and assume that specific attributes of the resource representing the physical object (e.g. <physicalObject>) are used to capture this information.  Assuming the <physicalObject> resources have already been created, the tangible identifiers can be provided via UPDATE operations to the associated physical object resource and operation details are to be provided with the resource definitions in clause 8.2.

Figure 8.1.2-1 Update procedures

- AEs (AE1, AE2) capture the tangible identifiers and potentially other information (e.g. location, time) associated with the physical entities.

- <physicalObject> resources have already been created (e.g. by an inventory application ) the AEs optionally update the resources with the tangible identifiers and identifier type. The AEs can also update other information (e.g. location, time) related to the physical entities.  The AEs can also provide their own communication identifier to be associated with the physical object at the CSE. Alternatively, the AEs can start by first creating the necessary <physicalObject>.

## 8.1.3	Identifier-based discovery of Physical Object at the CSE

When an application wants to discover Physical Object information based on the tangible identifier associated with a <physicalObject> hosted by a CSE there are two cases as follows:

Case 1: When the discovery request response requires only information maintained by the CSE, as shown in	Figure 8.1.3-1.

Figure 8.1.3-1 Discovery procedures for case 1

- The discovery application AE initiates a request (e.g. to discover  IDServiceCommAddrList of a device that interworks to the particular physical entity. The tangible identifier of the physical entity is included in the request.

- The CSE receives and processes the request. If the identifier type is not included in the request, the CSE can recognize the type of tangible identifier from the tangibleID. The CSE resolves the tangible identifier to a <physicalObject> and discovers the communication identifier (IDServiceCommAddrList) of the device that interworks to the physical entity.

- The CSE forwards the discovery results to the requesting AE.

Case 2: When the discovery request response requires additional information which is not maintained on the queried CSE. The CSE can interwork with external identification	resolution system(s) to assist with the identification resolution. The discovery procedure is shown in figure 8.1.3-2.

Figure 8.1.3-2 Discovery procedures for case 2

- The discovery application AE initiates (e.g. request to discover the communication identifier of a device that can be used to identify the particular physical entity.  The tangible identifier of the physical entity is included in the request.

- The CSE receives the request. If the identifier type is not included in the request, the CSE can recognize the type of tangible identifier from the tangibleID.

- The CSE sends the tangible identifier (tangibleID) to the corresponding external resolution system (e.g. Handle system). For this purpose, the PO management functionality is pre-provisioned with clients using standardized interfaces and protocols to communicate with the identification resolution system servers.

The CSE uses the identifier type to choose the corresponding external identification resolution system server and the corresponding protocol, based on pre-provisioned information about the systems supported. For example, a tangibleID representing an EPC is sent to the ONS server via the corresponding standardized protocol request. The ONS server responds with information which can be used to identify and describe the physical entity. The result is stored by the hosting CSE in the corresponding attribute of the <physicalObject> resource.

Note: The mapping between oneM2M attributes and the requests used by the CSE to communicate with the external identification resolution systems is in scope of TS-0004 and corresponds to each external resolution system supported by oneM2M, as well as oneM2M resource structure types (e.g. <physicalObject>).

- The CSE can store the information received locally and responds with the discovery results to the requesting AE.

### 8.1.4	Discovery of external identifiers based on interworking with external systems via IPEs

As described in case 2 of clause 8.1.3, CSEs may maintain tangible identifier information for physical entities using identification resolution systems such as ONS, Handle system and uCodeRP.

The interworking between a CSE and the external identification resolution systems may also be implemented through an IPE. IPEs for identification resolution systems generally consist of two components: clients and interworking modules. Each identification resolution system has its corresponding client that has specific functions and standardized interface and protocol to communicate with the server of an identification resolution system. The interworking module translates the external entities into oneM2M resources (e.g. <physicalObject>) and exposes the resources via the oneM2M reference point.

Figure 8.1.4-1: IPE registration for interworking with Identification resolution systems

As a pre-requisite to assisting the CSE in interworking, it is assumed that IPE discovers the external identification resolution systems proactively or is pre-previsioned accordingly. The IPE registers to the CSE using generic registration procedures and creates a corresponding <AE> resource. In addition, the IPE may create <physicalObject> resources for capturing tangible identifier information. This initial step is shown in Figure 8.1.4-1.

The discovery procedure when the interworking with external systems uses IPEs is further described below and in figure 8.1.4-2.

Figure 8.1.4-2: Discovery procedure using IPEs for interworking with external systems

Step 1: AE (e.g. a query application) sends a RETRIEVE request to CSE (e.g. a service platform) to discover the information related to a tangible identifier. In the request, filterUsage is set to 'IPEOnDemandDiscovery' and filterCriteria to the necessary conditions, e.g. “tangibleID = 10.01000.1011”.

Step 2: If there are no matches for the tangible identifier, based on filterUsage being set to 'IPEOnDemandDiscovery', the CSE checks whether identification resolution IPEs may be used. For this purpose, the CSE may check which IPEs are registered to the CSE and whether they support the type of tangible identifier needed by the discovery request. If a corresponding identification resolution IPE is registered, the CSE sends Notify request to the IPE. The CSE includes the tangibleID, AE-ID and the Filter Criteria in the Notify request, indicating a request for on-demand discovery in the interworked system.

Step 3: The IPE interworks with external identification resolution system(s) to resolve the tangible identifier, e.g. the result may include the communication identifier (IDServiceCommAddrList) of a device that interworks to the physical entity.

NOTE 1: The IPE interworks with the external identification resolution system (server) through the corresponding client that identifies according to the identifier type. For example, an EPC (e.g. 10.01000.1001011101) is input to the ONS client, and the client sends the EPC to the ONS server in a request with standardized protocol. The ONS server may interact with the client several times before it finally responds with the communication identifier (e.g. IP address 10.101.101.193).

Step 4: The IPE creates physical entity resource(s) including the information received and sends the Notify response including the list of created resource(s).

Step 5: The CSE sends the discovery result to the AE with the list of the resources matching the query.

## 8.2	Potential solutions

This section includes the changes needed in TS-0001 in existing resources, Figures and Tables to support the above scenarios.

## 8.2.1Resource Type <physicalObject>

The <physicalObject> resource represents information about a physical object data instances. It is used to share information with other entities and potentially to track the physical object.

Table 8.2.1-1 : Child Resources of <physicalObject> resource

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to in Resource Type Definition |
| --- | --- | --- | --- |
| <semanticDescriptor> | [variable] | 0..n | Clause 9.6.30 |
| <subscription> | [variable] | 0..n | Clause 9.6.8 |
| <flexContainer> | [variable] | 0..n | Clause 9.6.34 |

Table 8.2.1.-2: Attributes of <physicalObject> resource

| Attributes of <physicalObject> | Multiplicity | RW/ RO/ WO | Description | <physicalObjectAnnc> Attributes |
| --- | --- | --- | --- | --- |
| poID | 0..1 | RW | This attribute is a oneM2M identifier of the physical object | OA |
| tangibleID | 0..1(L) | RW | This parameter is a list of tangible identifiers associated with the specific physical entities. It is described as a list of tangible identifiers (e.g. 86.1000.11/70140703307739, 1.2.156.20000.2010319). | OA |
| IDType | 0..1(L) | RW | It shall be present in case tangibleID parameter is null. If the tangibleID parameter is present, it represents the corresponding type of the tangible identifiers. If the tangibleID parameter is not present, it represents the identifier type that is supported by the creation originator. The identifier type is expressed in string： epc; handle; oid; ucode; mcode; ecode. | OA |
| IDServiceCommAddrList | 0..1 (L) | RW | It represents the physical address used by devices or applications that interworks to the physical entity for the purpose of providing identification services. For oneM2M devices, it represents the pointOfAccess attribute of AEs or CSEs. For non-oneM2M devices it represents physical address information (e.g. IP address, FQDN) for such devices, as provided by an external identification system. This information may be derived from the tangibleID or may be pre-provisioned at the CSE. | OA |
| auxiliaryAEList | 0..1(L) | RW | List of AEs which provide services (e.g. object recognition camera) associated with this physical entity | OA |
| associatedPoIDList | 0..1(L) | RW | A list of associated physical objects. | OA |
| associatedPoIDAssocType | 0..1(L) | RW | A list of qualifiers describing the type of association between this Physical Object and each of the Physical Objects in associatedPoIDList, e.g. component-of, sub-component, etc. | OA |
| externalDatabaseList | 0..1(L) | RW | A list of associated external databases containing additional information | OA |
| poDefinition | 0..1 | WO | This contains an identifier reference (URI) to a schema definition which is used by the CSE to validate the syntax of the resource, if one or more [customAttributes] are used. If this attribute is not present, no [customAtrribute] specialized attributes are defined. |  |
| [customAttribute] | 0..n | RW | Specialization-specific attribute(s) used to create a specialization of the resource. Name and data type pairs are defined in the the schema provided in the poDefinition attribute. | OA |

## 8.2.x Discovery based on interworking with Handle system via IPE

This clause provides details for implementing interworking with an external system using Handle Identifiers via an IPE. More information about the Handle Identifier system is provided in clause 6.3.

Figure 8.2.x-1: Discovery based on interworking with Handle system via IPE

Step 1: An Originator (e.g. an AE) sends a request to the CSE to discover information related to a tangible identifier. The parameters in the request are set as follows:

Operation: Retrieve

To: <CSEBase> or <physicalObject> by pre-provisioning

Filter Criteria: set the attribute (e.g. “tangibleID = 21.86101/t-93”) and filterUsage to‘IPEOnDemandDiscovery’, and other necessary conditions

Step 2a: If there are no matched results found, the CSE checks if the IPE supports the Handle system. The type of tangible identification system may be identified by the heterogenous identification recognition functionality of the CSE from the tangibleID or may be provided in the request of AE.

Editor’s Note: It is FFS how the CSE heterogenous identification function discovers if the IPE supports a specific identification system (e.g. Handle).

Step 2b: If the type of tangible identifier is Handle and a corresponding identification resolution IPE for Handle system is found, the CSE sends Notify request to the IPE. The Notify request contains the ID of the orginator and the filterCriteria parameters, including the tangibleID condition.

Step 3a: The IPE consists of a Handle Client which has specific functions and standardized interface and protocol to communicate with Handle server. When IPE receives the request from CSE, the client is responsible to encapsulate a new request message, the main common elements of request are shown in Table 8.2.x-1.

Step 3b: The Client sends the request to the GHR, see [6] for request implementation specification.

NOTE: It is assumed that the IPE/ Handle Client software is pre-provisioned with GHR service information that includes the IP address, port number and so on.

Step 3c: GHR responds with the service information of the responsible LHS “21.86101”. The service information includes the IP address, transmission protocol (e.g. TCP, UDP and HTTP), port number used by the interface (e.g. the default port number is 2641) and so on.

Step 3d: According to the received service information, the Client sends the same request as Step 3b to the LHS to query Handle Identifier "21.86101/t-93".

Step 3e: Optionally, Client authentication is implemented and invoked between the LHR and Client.

Step 3f: LHS searches for the Handle Identifier "21.86101/t-93" related information. Each Handle Identifier may have a set of values assigned to it. These Handle Identifier values use a common data structure for its data. Figure 8.2.x-2 shows the Handle Identifier "21.86101/t-93" with a set of three Handle Identifier values.

Step 3g: LHS responds to the query result. The main elements of the response are shown in Table 8.2.x-2.

Step 4a: The IPE creates physical entity resource(s) based on the information received. How the IPE mapps the received information to the physical entity resource depends on the specific implementation of the used system. For example, a system may assign Handle identifiers to oneM2M physicalObject resources. The corresponding IPE will create a local physicalObject resource with the exact representation received. In another implementation, the values returned may be mapped to a single attribute of the corresponding physicalObject resource.

Step 4b: The IPE sends the Notify response to the CSE including the list of created physicalObject resource(s).

Step 5: CSE responds with the query result to the Originator AE.

Table 8.2.x-1: Request Message Element

| Element | Description |
| --- | --- |
| OpCode | It stands for operation code, which is a four-byte unsigned integer that specifies the intended operation. In the case of resolution operation, the <OpCode> is set to OC_RESOLUTION. |
| Handle | It represents the tangible ID. In the Handle system, it is a UTF8-String that specifies the Handle Identifier to be resolved. |
| IndexList | It is a 4-byte unsigned integer followed by an array of 4-byte unsigned integers. The first integer indicates the number of integers in the integer array. Each number in the integer array is a Handle Identifier value index and refers to a Handle Identifier value to be retrieved. The client sets the first integer to zero (followed by an empty array) to ask for all the Handle Identifier values regardless of their index. |
| TypeList | It is a 4-byte unsigned integer followed by a list of UTF8- Strings. The first integer indicates the number of UTF8-Strings in the list that follows. Each UTF8-String in the list specifies a data type. This tells the server to return all Handle Identifier values whose data type is listed in the list. The <TypeList> may contain no UTF8-String if the first integer is 0. In this case, the server must return all Handle Identifier values regardless of their data type.e.g. URL. |

Table 8.2.x-2: Successful Response Message Element

| Element | Description |
| --- | --- |
| Handle | It represents the tangible ID. In the Handle system, it is a UTF8-String that specifies the Handle Identifier queried by the client. |
| ValueList | A 4-byte unsigned integer followed by a list of Handle Identifier values. The integer specifies the number of Handle Identifier values in the list. The integer is set to zero if there is no Handle Identifier value that satisfies the query. Each Handle Identifier may have a set of values assigned to it. For example, in the Figure 8.2.x-2, the <data> parameter describes the resource identified by the Handle Identifier, e.g. http://www.dlib.org/dlib. |

Figure 8.2.x-2: set of values for Handle Identifier "21.86101/t-93"

# Proforma copyright release text block

This text box shall immediately follow after the heading of an element (i.e. clause or annex) containing a proforma or template which is intended to be copied by the user. Such an element shall always start on a new page.

Notwithstanding the provisions of the copyright clause related to the text of the present document, oneM2M grants that users of the present document may freely reproduce the <proformatype> proforma in this {clause|annex} so that it can be used for its intended purposes and may further publish the completed <proformatype>.

<PAGE BREAK>

## Annexes

Each annex shall start on a new page (insert a page break between annexes A and B, annexes B and C, etc.).

Use the Heading 9 style for the title and the Normal style for the text.

Annex <A>:
Title of annex (style H9)

<Text>

<PAGE BREAK>

Annex <B>:
Title of annex (style H9)

<Text>

B.1	First clause of the annex (style H1)

<Text>

B.1.1	First subdivided clause of the annex (style H2)

<Text>

<PAGE BREAK>

Annex <y>:
Bibliography

The annex entitled "Bibliography" is optional.

It shall contain a list of standards, books, articles, or other sources on a particular subject which are not mentioned in the document itself.

It shall not include references mentioned in the document.

Use the Heading 9 style for the title and B1+ or Normal for the text.

<Publication>: "<Title>".

OR

<Publication>: "<Title>".

<PAGE BREAK>

# History

This clause shall be the last one in the document and list the main phases (all additional information will be removed at the publication stage).

| Publication history |
| --- |
| V.1.1.1 | <dd Mmm yyyy> | <Milestone> |

| Draft history (to be removed on publication) |
| --- |
| V.0.1.0 | 2017-07-10 | Incorporated contributions agreed at ARC#27 and ARC#29: ARC-2017-0043R01-Skeleton_of_heterogeneous_identification_service ARC-2017-0203R01-TR-0044_Introduction_to_heterogeneous_identification_service ARC-2017-0204-TR-0044_Existing_technologies ARC-2017-0205R01-TR-0044_Use_cases_analysis ARC-2017-0206R01-TR-0044_Potential_enhancements |
| V.0.2.0 | 2018-03-13 | Incorporated contributions agreed at ARC#32.2 and ARC#33: ARC-2017-0431R04-CR-TR-0044-Potential_solution ARC-2018-0004-TR-0044_clean_up |
| V.0.3.0 | 2018-11-08 | Incorporated contributions agreed at ARC#35.3 ARC-2018-0107R04-TR-0044_PO_resource_solution |
| V.0.4.0 | 2019-02-18 | Incorporated contributions agreed at ARC#37.2 and ARC#38: ARC-2018-0271R02-TR-0044 PO resource solution update; ARC-2018-0252R02-CR TR-0044 Discovery based on interworking with external systems; ARC-2018-0325R01-TR-0044 Adding references and abbreviations. |
| V.0.5.0 | 2019-03-28 | Incorporated contributions agreed at SDS #39: SDS-2019-0073R02-CR TR-0044 Discovery based on interworking with handle system |