| oneM2M Technical Report |
| --- |
| Document Number | oneM2M-TR-0056-V-0.1.0 |
| Document Name: | Summary of Differences between Rel-2A & Rel-3 |
| Date: | 2018-11-08 |
| Abstract: | Provides summary of differences oneM2M Rel-2A and Rel-3 including major updates, benefits of each releases and short guides for users. |
| Template Version: January 2017 (Do not modify) |

The present document is provided for future development work within oneM2M only. The Partners accept no liability for any use of this report.

The present document has not been subject to any approval process by the oneM2M Partners Type 1.  Published oneM2M specifications and reports for implementation should be obtained via the oneM2M Partners' Publications Offices.

About oneM2M

The purpose and goal of oneM2M is to develop technical specifications which address the need for a common M2M Service Layer that can be readily embedded within various hardware and software, and relied upon to connect the myriad of devices in the field with M2M application servers worldwide.

More information about oneM2M may be found at:  http//www.oneM2M.org

Copyright Notification

© 2017, oneM2M Partners Type 1 (ARIB, ATIS, CCSA, ETSI, TIA, TSDSI, TTA, TTC).

All rights reserved.

The copyright and the foregoing restriction extend to reproduction in all media.

Notice of Disclaimer & Limitation of Liability

The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations. No recommendation as to products or vendors is made or should be implied.

NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE, GOVERNMENTAL RULE OR REGULATION, AND FURTHER, NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS. NO oneM2M PARTNER TYPE 1 SHALL BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY THAT PARTNER FOR THIS DOCUMENT, WITH RESPECT TO ANY CLAIM, AND IN NO EVENT SHALL oneM2M BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES. oneM2M EXPRESSLY ADVISES ANY AND ALL USE OF OR RELIANCE UPON THIS INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER.

# Contents

Contents	3

1	Scope	4

2	References	4

2.1	Normative references	4

2.2	Informative references	4

3	Definitions, symbols and abbreviations	5

3.1	Definitions	5

3.2	Symbols	6

3.3	Abbreviations	6

4	Conventions	6

5	Features of Each Releases	6

5.1	Introduction	6

5.2	Release-2A	6

5.3	Release-3	7

6	Updated and NewTSs	7

6.1	Introduction	7

6.2	Updated TSs	8

6.2.1	TS-0001	8

6.2.2	TS-0003	8

6.2.3	TS-0004	8

6.2.4　	TS-0005	8

6.2.5　	TS-0006	8

6.2.6　	TS-0008	8

6.2.7　	TS-0009	8

6.2.8　	TS-0011	8

6.2.9　	TS-0012	8

6.2.10	TS-0014	8

6.2.11　	TS-0016	8

6.2.12	TS-0022	8

6.2.13	TS-0023	8

6.2.14	TS-0024	8

6.2.15	TS-0025	8

6.2.14	TS-0026	8

6.2.16	TS-0031	8

6.2.17	TS-0032	8

6.3	New TSs	8

6.3.1	TS-0017	9

6.3.2	TS-0018	9

6.3.3	TS-0019	9

6.3.4	TS-0026	9

6.3.5	TS-0030	9

6.3.6	TS-0033	9

6.3.7	TS-0034	9

6.3.8	TS-0036	9

Proforma copyright release text block	9

Annexes	9

Annex <y>: Bibliography	10

History	10

# 1	Scope

The present document …

EXAMPLE:	The present document provides the necessary adaptions to the endorsed document.

The Scope shall not contain requirements.

# 2	References

The following text block applies.

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references,only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

## 2.1	Normative references

As a Technical Report (TR) is entirely informative it shall not list normative references.

The following referenced documents are necessary for the application of the present document.

Not applicable.

## 2.2	Informative references

Clause 2.2 shall only contain informative references which are cited in the document itself.

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

- oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

- oneM2M TS-0001: “Functional Architecture

- oneM2M TS-0002: “ Requirements ”

- oneM2M TS-0003: “ Security Solutions ”

- oneM2M TS-0004: “ Service Layer Core Protocol”

- oneM2M TS-0005: “ Management Enablement (OMA) ”

- oneM2M TS-0006: “ Management enablement (BBF) ”

- oneM2M TS-0007: “ Service Components ”

- oneM2M TS-0008: “ CoAP Protocol Binding”

- oneM2M TS-0009: “ HTTP Protocol Binding ”

- oneM2M TS-0010: “ MQTT protocol binding ”

- oneM2M TS-0011: “ Common Terminology”

- oneM2M TS-0012: “ Base Ontology”

- oneM2M TS-0013: “ Interoperability Testing”

- oneM2M TS-0014: “ LWM2M Interworking”

- oneM2M TS-0015: “ Testing Framework ”

- oneM2M TS-0016: “ Secure Environment Abstraction ”

- oneM2M TS-0017: “ Implementation Conformance Statements”

- oneM2M TS-0018: “ Test Suite Structure and Test Purposes ”

- oneM2M TS-0019: “ Abstract Test Suite & implementation eXtra Information for Test”

- oneM2M TS-0020: “ WebSocket Protocol Binding”

- oneM2M TS-0021: “ oneM2M and AllJoyn Interworking ”

- oneM2M TS-0022: “ Field Device Configuration”

- oneM2M TS-0023: “ Home Appliances  Information Model and Mapping ”

- oneM2M TS-0024: “ OIC Interworking”

- oneM2M TS-0025: “ Product Profiles”

- oneM2M TS-0026: “ 3GPP Interworking ”

- oneM2M TS-0027: “ Security Implementation Conformance Statements”

- oneM2M TS-0028: “ Security Test Suite Structure and Test Purposes”

- oneM2M TS-0029: “ Security Abstract Test Suite and Implementation extra Information for Test ”

- oneM2M TS-0030: “ Ontology based Interworking”

- oneM2M TS-0031: “ Feature Catalogue”

- oneM2M TS-0032: “ MAF and MEF Interface Specification”

- oneM2M TS-0033: “ Proximal IoT Interworking ”

- oneM2M TS-0034: “ Semantics Support”

- oneM2M TS-0035: “ OSGi Interworking”

- oneM2M TS-0036: “ Advanced Vehicular Domain Enablement”

# 3	Definitions, symbols and abbreviations

Delete from the above heading the word(s) which is/are not applicable.

## 3.1	Definitions

Clause numbering depends on applicability.

A definition shall not take the form of, or contain, a requirement.

The form of a definition shall be such that it can replace the term in context. Additional information shall be given only in the form of examples or notes (see below).

The terms and definitions shall be presented in alphabetical order.

For the purposes of the present document, the [following] terms and definitions [given in ... and the following] apply:

Definition format

<defined term>: <definition>

If a definition is taken from an external source, use the format below where [N] identifies the external document which must be listed in Section 2 References.

<defined term>[N]: <definition>

example 1: text used to clarify abstract rules by applying them literally

NOTE:	This may contain additional information.

## 3.2	Symbols

Clause numbering depends on applicability.

For the purposes of the present document, the [following] symbols [given in ... and the following] apply:

Symbol format

<symbol>	<Explanation>

<2nd symbol>	<2nd Explanation>

<3rd symbol>	<3rd Explanation>

## 3.3	Abbreviations

Abbreviations should be ordered alphabetically.

Clause numbering depends on applicability.

For the purposes of the present document, the [following] abbreviations [given in ... and the following] apply:

Abbreviation format

<ABBREVIATION1>	<Explanation>

<ABBREVIATION2>	<Explanation>

<ABBREVIATION3>	<Explanation>

# 4	Conventions

The key words “Shall”, ”Shall not”, “May”, ”Need not”, “Should”, ”Should not” in this document are to be interpreted as described in the oneM2M Drafting Rules [i.1]

# 5	Features of Each Releases

## 5.1	Introduction

## This clause summarizes features of both Release-2A and Release-3.5.2	Release-2A

Release-2A is an updated version of Release-2.

Home domain enablement

TS-0023 defines the Home Appliance Information Model (HAIM) for  home domain devices based on HGI SDT 3.0.

Industrial domain enablement

Considering requirements from industrial domain, the number of oneM2M resource types increases in Release-2A.

Semantic Interoperability

The first Semantic function in oneM2M is <semanticDescriptor> in Release-2.

Base Ontology is newly introduced  in TS-0012.

Dynamic authorizations and end to end security

The Dynamic Authorization reference model and processes including Dynamic Authorization System (DAS) are described in TS-0003

Authorization parameters and their transport are described in TS-0001 and TS-0004.

oneM2M as generic interworking framework

Some TSs express how to interwork between oneM2M and other specifications such as Alljoyn / AllSeen (TS-0021) , OIC (TS-0024) and LightWeight M2M (LWM2M) (TS-0014).

Application developer APIs and guidelines

Eight Developer Guides have been under development and will be released as Technical Reports.

## 5.3	Release-3

Smart City with Automotive Enablement

Industrial Domain Enablement

Management

Semantics

Security

oneM2M Interworking framework

Market Adoption (Developer Guide)

# 6	Updated and NewTSs

## 6.1	Introduction

Clause 6.2, ‘Updated TSs’ introduces TSs which are included in both Release-2A and Release-3.TSs which are included in Release-3 only are described in clause 6.3, ‘New TSs’.

## 6.2	Updated TSs

### 6.2.1	TS-0001

22 resource types like <transaction> and <semanticMashupInstance> are newly added in Release-3.

Release-3 has less gaps with TS-0004 because of the gap analysis activity.

There is no resource tree pictures at Release-3 because of optimisation of space.

Concept of transaction is introduced and many resource types become to be able to have <transaction> resource as a child in Release-3.

About <node> resource, hostedAELinks attribute and hostedAServiceLinks attributes are added in Release-3.

Relating this, figures expressing relationship between IN/MN (Fig.9.6.18-1in Release-3) and ADN and between IPE  (Fig.9.6.18-2 in Release-3) are modified.

<trafficPattern> resource type is deleted in Release-3, so the general procedure for configuration of traffic patterns (clause 8.3.5.3) is changed to the procedure without using <trafficPattern>.

### 6.2.2	TS-0003

### 6.2.3	TS-0004

6.2.4　	TS-0005

6.2.5　	TS-0006

6.2.6　	TS-0008

6.2.7　	TS-0009

6.2.8　	TS-0011

6.2.9　	TS-0012

### 6.2.10	TS-0014

6.2.11　	TS-0016

### 6.2.12	TS-0022

### 6.2.13	TS-00236.2.14	TS-0024

### 6.2.15	TS-0025

### 6.2.14	TS-0026

### 6.2.16	TS-0031

### 6.2.17	TS-0032

## 6.3	New TSs

### 6.3.1	TS-0017

### 6.3.2	TS-0018

### 6.3.3	TS-0019

### 6.3.4	TS-0026

### 6.3.5	TS-0030

### 6.3.6	TS-0033

### 6.3.7	TS-0034

### 6.3.8	TS-0036

# Proforma copyright release text block

This text box shall immediately follow after the heading of an element (i.e. clause or annex) containing a proforma or template which is intended to be copied by the user. Such an element shall always start on a new page.

Notwithstanding the provisions of the copyright clause related to the text of the present document, oneM2M grants that users of the present document may freely reproduce the <proformatype> proforma in this {clause|annex} so that it can be used for its intended purposes and may further publish the completed <proformatype>.

<PAGE BREAK>

## Annexes

Each annex shall start on a new page (insert a page break between annexes A and B, annexes B and C, etc.).

Use the Heading 9 style for the title and the Normal style for the text.

Annex <A>:
Title of annex (style H9)

<Text>

<PAGE BREAK>

Annex <B>:
Title of annex (style H9)

<Text>

B.1	First clause of the annex (style H1)

<Text>

B.1.1	First subdivided clause of the annex (style H2)

<Text>

<PAGE BREAK>

Annex <y>:
Bibliography

The annex entitled "Bibliography" is optional.

It shall contain a list of standards, books, articles, or other sources on a particular subject which are not mentioned in the document itself.

It shall not include references mentioned in the document.

Use the Heading 9 style for the title and B1+ or Normal for the text.

<Publication>: "<Title>".

OR

<Publication>: "<Title>".

<PAGE BREAK>

# History

This clause shall be the last one in the document and list the main phases (all additional information will be removed at the publication stage).

| Publication history |
| --- |
| V1.1.1 | <yyyy-mm-dd> | <Milestone> |

| Draft history (to be removed on publication) |
| --- |
| V0.0.1 | 2018-07-20 | Skelton is defined based on ARC-2018-0195R02 |
| V0.1.0 | 2018-11-08 | Include agreed contributions at ARC#37 meeting: 1. ARC-2018-0268R01 |