## Slide 1: OIC INTERWORKING Operational Procedure (addressing and Discovery)
Group Name: Architecture WG
Source: Kiran Vedula, Samsung Electronics, kiran.vedula@samsung.com
Jieun Keum, Samsung Electronics, je.keum@samsung.com
Jinhyeock Choi, Samsung Electronics, jinchoe@samsung.com
Sungchan Choi, KETI, sungchan.keti@gmail.com
SeonHyang Kim, DT&C, shkim@dtnc.net
Meeting Date: <2015-10-20>
Agenda Item: <WI 44: oneM2M-OIC interworking >
Notes: Other suggested titles:
“Benefits of oneM2M Standardization”

## Slide 2: Introduction
This presentation introduces possible initialization setup of different entities for oneM2M OIC Interworking
Also details of how oneM2M device can discover OIC entities is depicted. There can be 2 alternatives
  Automatic Bootstrap Mode
  Need Based Mode
Also how entities are addressed is described

## Slide 3: Initialization of Entities
The IN supports a CSE. An ADN AE (Smartphone) is registered to the IN CSE. Similarly MN already supports a CSE
IN CSE also registers with MN CSE
Intermediary Device is installed with an IPE AE based on an out of band mechanism
  Triggered by a user action e.g. user subscribing to some service or
  Based on business logic of service provider
The installed IPE AE registers with MN CSE

## Slide 4: Discovery (Automatic bootstrap Mode)
The IPE AE discovers OIC devices using its OIC Client functionality as soon as it is installed on MN and registered to MN CSE. It uses OIC mechanisms for the discovery
After the discovery, IPE AE uses its translator function to map the discovered OIC devices and resources into oneM2M resources and creates them on MN
For each discovered OIC Device an OIC AE is created and registered with MN CSE
After that the ADN through an IN CSE can anytime discover OIC AE resources by sending a RETRIEVE request with appropriate filter criteria to the MN CSE where they are registered
The MN CSE responds to IN CSE with the OIC AE’s information which in turn is sent to the ADN
Also, Instead of step 4 and 5, directly the MN CSE can notify IN CSE of the discovered information based on subscription
NOTE: In this mode, OIC AE’s are formed before any discovery request

## Slide 5: Discovery (Need Based Mode)
The ADN through IN CSE sends a RETRIEVE request to MN CSE with filter criteria to search for IPE AE (if possible OIC IPE AE)
Trigger could be sent to IPE from MN CSE to perform the OIC discovery
Based on that IPE AE sends discovery request using OIC mechanisms
After the discovery, IPE AE uses its translator function to map the discovered OIC devices and resources into oneM2M resources and creates them
For each discovered OIC Device an OIC AE is created and registered with MN CSE
The MN CSE responds to ADN through IN CSE with the newly registered OIC AE’s information
NOTE: In this mode, OIC AE’s are formed after discovery request in real time

## Slide 6: Comparative Analysis
Mode | PROs | CONs
Automatic Bootstrap Mode | Quick discovery | OIC AE is created even before its usage. Occupies memory
 |  | OIC AE information could become stale if not updated regularly. To keep updated further resources need to be used
Need Based Mode | OIC AE created only after discovery request from any oneM2M entity. Memory efficient | Slow discovery
 | OIC AE information is up to date. | 
 | OIC AE could be deleted after sometime | 

## Slide 7: Addressing
The “To” parameter in a request/ notification is used as a target for the request/ notification
Resource-ID: The originator of the request is recommended to use “Absolute” or “SP-relative” format of addressing when sending requests. This is just to ensure that the MN-CSE hosting OIC AE resources receives the request
Request Target
  Requests are targeted to AEs but via CSE which hosts them
  The MN CSE-PoA is used by IN to reach the CSE which is hosting the OIC AE resource
  Specific AE under the MN CSE is addressed using the AE-ID attribute of the <AE>
Notification Target
  Notifications are usually targeted to AEs
  A hosting CSE which receives notification request, can retarget the request to AE-PoA