## Slide 1: Introduction to 3GPP cellular IoT interworking
Group Name: ARC WG, ARC-2018-0055
Source: F. Sang-Eon Kim, KT (TTA), kim.sangeon@kt.com
Meeting Date: 2018-03-04 (ARC34)
Notes: Other suggested titles:
“Benefits of oneM2M Standardization”

## Slide 2: Problem
Reference: TS 0026 V0.7.0 Clause 5.1
It uses mixed concepts among reference point (Tsp, SGi), communication scheme (SMS, NAS), wrong reference point (API) and missing several reference point to develop interworking oneM2M with 3GPP
Figure 5.1-1: 3GPP IoT Related Interfaces

## Slide 3: Problem
Reference: TS 0001 V3.10.0 Clause 6.2
Some CSFs are not considered at TS 0026 which is for 3GPP interworking.
Figure 6.2.0-1: Common Services Functions

## Slide 4: Review 3GPP TSs
Purpose:
  To develop architecture for interworking oneM2M and 3GPP
Lists of TSs
  3GPP TS 23.401
  3GPP TS 23.682
  3GPP TS 23.246
  3GPP TS 29.468
  3GPP TS 23.271
  3GPP TS 23.203
  3GPP TS 24.011
  3GPP TS 23.272
  3GPP TS 23.060

## Slide 5: Architecture for 3GPP Access
Reference: 3GPP TS 23.401 Clause 4.2
Non-roaming architecture for 3GPP accesses.
Single gateway configuration option

## Slide 6: 3GPP Architecture for MTC
Reference: 3GPP TS 23.682 Clause 4.2

## Slide 7: Proposal 3GPP interworking
Green line is for 3G network.
Blue line is for evolved packet system (EPS).
Red line is for major interworking reference point in 3GPP domain.
Black line is for core interworking 3GPP with oneM2M.
Yellow line is for SMS related reference point.

## Slide 8: MBMS
3GPP 23.246 Clause 4.2.2
Figure 1b

## Slide 9: 3GPP reference model for Group comm.
Reference: 3GPP TS 29.468
Figure 4.1-1

## Slide 10: Proposal 3GPP interworking to add Group function
Violet line is for MBMS related reference point.
Issues: interworking method for option A, B and C
A: BM-SC – SCEF – SCS
B: BM-SC – SCS
C: BM-SC – P-GW - SCS
ⓐ
ⓑ
ⓒ

## Slide 11: Group message delivery using MBMS
3GPP TS 23.682
Figure 5.5.1-1

## Slide 12: Proposal 3GPP interworking to add Group function
MBMS for group resource may use SCEF for interworking

## Slide 13: 3GPP LCS architecture
Reference: 3GPP TS 23.271 Figure 6.1-1
LCS: Location service
GMLC: Gateway MLC
MLC: Mobile Location Centre
PPR: Privacy Profile Register
LIMS-IWF: Location IMS – Interworking Function
PMD: Pseudonym mediation device functionality

## Slide 14: 3GPP LCS architecture
Reference: 3GPP TS 31.271 Figure 4.1.1

## Slide 15: Proposal 3GPP interworking to add location function
Brown line is for LCS related reference point.
Issues: interworking method for option A, B and C
A: GMLC – LIMS-IWF – SCEF - SCS
B: GMLC – LIMS IWF -SCS
C: GMIC - SCS
ⓐ
ⓑ
ⓒ
TS 23.271 5.4.2.6
The Location IMS – Interworking Function (LIMS-IWF) in the requesting network provides the capability to route LCS service requests based on an IMS Public User Identity (SIP-URI) to the home network of the target user. The LIMS-IWF in the home network of the target user is responsible to determine the appropriate HSS and to obtain the MSISDN associated with a IMS Public User Identity from the HSS.

## Slide 16: Proposal 3GPP interworking to add location function
GMLC for location resource may use SCS directly

## Slide 17: PCC in 3GPP
Pink is for policy and charging control (PCC) related reference point.
Issues: oneM2M specifies charging related resource.
3GPP 23.203
Figure 5.1-1

## Slide 18: Proposal 3GPP interworking to add PCC function

## Slide 19: SMS in TS 24.011
SM‑AL Short Message Application Layer
SM‑TL Short Message Transfer Layer
SM‑RL Short Message Relay Layer
SM‑RP Short Message Relay Protocol
SMR Short Message Relay (entity)
CM‑sub Connection Management sublayer
SM‑CP Short Message Control Protocol
SMC Short Message Control (entity)
MM‑sub Mobility Management sublayer
GMM-sub GPRS Mobility Management sublayer
RR‑sub Radio Resource Management sublayer
LLC-sub Logical Link Control sublayer
GRR-sub GPRS Radio Resource sublayer in GSM
EMM-sub EPS Mobility Management sublayer

## Slide 20: SMS in MME (TS23.272)
Figure C.2-1: SMS in MME Architecture
Figure C.2-2: SMS in MME architecture using IWF

## Slide 21: SMS in GPRS General Packet Radio Service
Clause 5.4 in 3GPP TS 23.060
3GPP TS 29.338
Diameter based protocols to support Short Message Service (SMS) capable Mobile Management Entities (MMEs)

## Slide 22: Proposal 3GPP interworking including messaging

## Slide 23: 3GPP UE
Reference: 3GPP TS 31.271 Figure 4.1.1
TS 23.101 Figure 1a
TS 23.101 Figure 1b
ME Mobile Equipment
MT Mobile Termination
MExE Mobile Station Application Execution Environment
TE Terminal Equipment

## Slide 24: 3GPP UE
Reference: 3GPP TS 31.271 Figure 4.1.1
TS 27.060 Figure 1
ME Mobile Equipment
MT Mobile Termination
MExE Mobile Station Application Execution Environment
TE Terminal Equipment

## Slide 25: Proposal 3GPP interworking architecture

## Slide 26: Optimized EPS architecture for CIoT
Reference: 3GPP TS 23.401 Annex L
Non-Roaming Architecture
Roaming architecture

## Slide 27: C-SGN
Reference: 3GPP TS 23.401 Annex L
An EPS optimized for CIoT can be enabled by having sub-set of functionalities implemented in single logical entity C-SGN (CIoT Serving Gateway Node).
C-SGN is decribed in L.4. Mobility and Attach procedures are performed as described in other clauses for corresponding entities MME, S-GW and P-GW.

## Slide 28: Simplied Proposal 3GPP interworking architecture
C-SGN introduces for MME, S-GE and P-GW

## Slide 29: Revised Proposal 3GPP interworking architecture (1/2)
Le interface is for between SCEF and GMLC

## Slide 30: Revised Proposal 3GPP interworking architecture (2/2)
Specific interfaces are removed
The TS-0026 has PCRF, BM-SC which is not described at Figure 5.1-1

## Slide 31: Protocol stack for T8 and Tsp
T8 uses API
Every resource needs to convert Diameter in case of Tsp interworking.

## Slide 32: Protocol stack for T8 and Tsp
4.3.17.8 Support for Non-IP Data Delivery (NIDD)
4.3.17.8.1 General
The support of Non-IP data is part of the CIoT EPS optimisations. A PDN Type "Non-IP" is used for Non-IP data. The Non-IP data delivery to SCS/AS is accomplished by one of two mechanisms:
- Delivery using SCEF as defined in clause 4.3.17.8.3.2.
- Delivery using a Point-to-Point (PtP) SGi tunnel as defined in clause 4.3.17.8.3.3.
Non-IP data in-sequence delivery cannot be guaranteed and data PDUs may be lost requiring higher protocol layers to ensure guaranteed delivery when needed.
The SMS service may also be used to deliver data without use of the IP protocol. The SMS service is always supported for CIoT EPS optimisations, i.e. can be used simultaneously with Non-IP and IP data. When only the SMS service is needed, an attach without PDN connection establishment can be used, see clause 5.3.2.
Dedicated bearers are not supported for the Non-IP data.
3GPP TS 23.401

## Slide 33: T8 (3GPP TS 29.122)
T8 reference points supports the following procedures:
  Monitoring Procedures (7.4)
  Procedures for resource management of Background Data Transfer
  Procedures for changing the chargeable party
  Procedures for Non-IP Data Delivery (7.1)
  Procedures for Device Triggering (7.5)
  Procedures for Group Message Delivery (7.7)
  Procedures for Reporting of Network Status
  Procedures for Communication Pattern Parameters Provisioning
  Procedures for PFD Management
  Procedures for Enhanced Coverage Restriction Control
  Procedures for Network Parameter Configuration (7.6)
  Procedures for setting up an AS session with required QoS
  Procedures for MSISDN-less Mobile Originated SMS

## Slide 34: CIoT optimization
TS 23.402 Clause 4.10
UE support:
  User Plane CIoT EPS Optimisation
  Control Plane CIoT EPS Optimisation
EPC support:
  User Plane CIoT EPS Optimisation
  Control Plane CIoT EPS Optimisation
    Transport oneM2M message via MME by encapsulating in NAS
    SMS message via MME by encapsulating in NAS