## Slide 1: Partial Update
Group Name: ARC/PRO, ARC-2018-0125
Source: F. Sang-Eon Kim, KT (TTA), kim.sangeon@kt.com
Meeting Date: 2018-05-14 (ARC35)
Notes: Other suggested titles:
“Benefits of oneM2M Standardization”

## Slide 2: Introduction
HTTP PATCH method
  defined in IETF RFC 5789
  allows for a partial update of previously sent data, e.g. resources.
HTTP PUT method
  complete replacement of previously sent data
Inconsistency
    WG2 introduces partial update at TS-0026
    WG3 has not specified for partial update at TS-0009

## Slide 3: Background Data Transfer
A PATCH method for partial update is introduced at clause 7.10.3.1 in TS-0026 V0.8.1
Step 8: Confirm the transfer policy
If more than one transfer policy was offered in step-4, for the transfer policy selected Step 6, the IN-CSE informs the SCEF of the selected transfer policy identifier and the Reference-ID mappings to the Background-Data-Transfer-Request (BTR) on the Nt reference point as defined in 3GPP TS 29.154 [i.16]. For this purpose, the SCS/AS shall use the PATCH request to modify the existing resource at the SCEF.
Step 10: Response to IN-CSE
Once the underlying network has recorded the confirmed transfer policy, the SCEF returns a response to the IN-CSE.
For this purpose, the SCEF provides a PATCH response message with the appropriate response code

## Slide 4: PATCH method at 29.122 V1.1.0
4.4.2.2 Monitoring Events Configuration
4.4.3 Background Data Transfer
4.4.4 Changing the chargeable party
4.4.5.2 NIDD Configuration
4.4.7.2 Group Message Delivery via MBMS
4.4.12.1 Network Parameter Configuration
4.4.13 Setting up an AS session with required QoS
The TS-0026 needs to consider following features that uses PATCH method in 3GPP.

## Slide 5: HTTP Method mapping
oneM2M Operation | HTTP Method
Create | POST
Retrieve | GET
Update | PUT
Delete | DELETE
Notify | POST
There is no PATCH method in oneM2M protocol at clause 6.2.1 in TS-0009.
  V1.10.0
  V2.13.0
  V3.0.0

## Slide 6: Discussion
Option A
  Architecture TS support only full update
  Protocol TS keeping i.e. no need to be revised
Option B
  Architecture TS keeping i.e. no need to be revised
  Protocol TS introduces partial update
    It needs to re-open PRO-2015-0833