## Slide 1: Node discussion
Group Name: ARC
Source: Catalina Mladin (Convida)
Meeting Date: 2018-09-16
Notes: Other suggested titles:
“Benefits of oneM2M Standardization”

## Slide 2: Introduction
This contribution seeks to bring clarity to specifications regarding the following <node> resource-related questions:
  Who creates it? When? Where?
  <node> relationship with resources and entities:
    Managed entity
    Hosting CSE
    Registrar
Initially ARC-2018-0143 was needed for cleanup of device management. R01 contains solutions for the issues presented here, this is a summary.

## Slide 3: <mgmtObj> @ IN, ADN implications
Existing specification texts for ADN <node> location :
TS-0001 10.2.8.7:
  If technology specific protocols are used for management,….<mgmtObj> resources are hosted on the IN-CSE
  TS-0022 and TS-0001 Figure 9.6.18-1 suggest that for ADN <node> is on the registrar.
  …..where the <mgmtObj> resource does not utilize an external management technology but instead uses the M2M Service Layer … If the managed entity is an ADN node …the <mgmtObj> resource is hosted on the registrar CSE of the managed entity
  Issue: If an ADN is registered to ASN/MN, we cannot use technology specific protocols for management.

## Slide 4: Management of 3GPP UEs
Currently 2 specifications for UE <node> location contradict each other:
TS-0026 6.3 (and others) UE attach:
  <node> resource created at the IN
TS-0001 10.2.8.7:
  In the scenario where the <mgmtObj> resource does not utilize an external management technology but instead uses the M2M Service Layer to perform the management request, the <mgmtObj> resource is hosted on the CSE of the managed entity when the managed entity is an ASN, MN or IN.
Issue: 3GPP UEs or are limited to use ONLY technology specific protocols OR UEs can be only ADNs (not ASN/ MN)

## Slide 5: <schedule> clarifications
TS-0001 9.6.9 Resource Type schedule
  A child <schedule> resource of the <node> resource shall indicate the time periods when the node can communicate via the Underlying Network.
    Note: The node shall obey the communication schedule indicated for the Underlying Network. If the schedule information is modified, the node shall ensure that the change of schedule is detected..
  A child <schedule> resource of the <CSEBase> resource shall indicate the anticipated time periods when the CSE is available for processing.
  An Originator shall have the same access control privileges to the <schedule> resource as it has to its parent resource.
Issues:
<node> is not mandatory (other than for 3GPP UEs), what are the <schedule> implications?
confusion by keeping <schedule> under CSEBase as well… Is that necessary?
Access control to <schedule> limited to “DM entities” (with <node> resource privileges)… Is that necessary?

## Slide 6: Other text for clarification (1)
10.2.8.3 Create <node>
This procedure shall be used for creating a <node> resource.
NOTE: The creation of the <node> resource is on discretion of the Originator. In general the resource is created when the Originator is not always reachable and therefore it is convenient that the entity that the Originator is registered to is aware of the characteristic of the node.
<node> CREATE | 
Associated Reference Point | Mca, Mcc and Mcc'
Information in Request message | All parameters defined in table 8.1.2-3 apply with the specific details for: Content: The representation of the <node> resource described in clause 9.6.18 The following attributes from clause 9.6.18 are mandatory for the request: resourceType which shall be set to the appropriate tag that identify the <node> resource as defined in clause 9.6.1.3 (see note)
Processing at Originator before sending Request | According to clause 10.1.2
Processing at Receiver | According to clause 10.1.2
Information in Response message | All parameters defined in table 8.1.3-1 apply with the specific details for: Content: Address of the created <node> resource, according to clause 10.1.2
Processing at Originator after receiving Response | According to clause 10.1.2
Exceptions | According to clause 10.1.2
NOTE: If the Originator is a CSE, it could take the information that is stored in the <node> resource under its own <CSEBase> resource and provide the information in the Content. | 
Table 10.2.8.3-1: <node> CREATE

## Slide 7: Other text for clarification (2)
TS-0001 10.2.8.7:
  “If the managed entity is an ADN node or the managed entity is co-located on an ASN, MN or IN, the <mgmtObj> resource is hosted on the registrar CSE of the managed entity”
  This means that if we have ASN + another entity on the same node, mgmgtObj for ASN are on ASN and mgmgtObj for other entity on registrar
Issues from pervious slide:
Is the yellow highlighted statement still true? It is not for 3GPP UEs, <node> is specified in that case to be created at attachment time
The blue highlighted statement should be clarified
Issue from this slide:
This doesn’t allow ASN + another entity to be managed together, which seems to be the intent of the text

## Slide 8: Issue clarification and Proposal

## Slide 9: Issue at a glance:
Node has been changed to include 2 different logical constructs:
  nodeDM,
  For device management
  nodeComm
  For communication management
  The following slides show where the information is NEEDED

## Slide 10: ADN @ IN (applies to 3GPP UEs)
Ext DM or oneM2M DM

## Slide 11: ADN @ ASN/MN
oneM2M DM
Ext DM

## Slide 12: ASN/MN @ IN (applies to 3GPP UEs)
oneM2M DM
Ext DM

## Slide 13: ASN@ MN
oneM2M DM
Ext DM

## Slide 14: Proposal (ARC-2018-0143R01)
Keep <node> containing only nodeComm info:
  nodeID
  [cmdhPolicy], [activeCmdhPolicy]
  <schedule>
  roamingStatus, networkID
  <semanticDescriptor>, <transaction>, <subscription>
<node> under own CSEBase of registrar always, created by either Registrar, Registree, DM entity.
Clearly show <node> management in relationship to registration

## Slide 15: Proposal (cont)
New <managedNode> resource type for DM purposes only (created by DM entity/manager):
  includes all other mgmtObj specializations, nodeID, <subscription>
<managedNode> location:
  ASN/MN: under own CSEBase for SL-based DM or CSEBase (IN?) for other technologies (like today)
  ADN: under registrar CSEBase for SL-based DM or CSEBase (IN?) for other technologies (like today)

## Slide 16: Proposal (cont)
Remove <schedule> from CSEBase, remaining only under <node>.
Change <schedule> to include own ACPs
Clarify that external technology DM can be done with <mgmtObj> at MN as well.