## Slide 1: oneM2M Architecture Adaptations for Semantics
Group Name: MAS WG
Source: Martin Bauer, martin.bauer@neclab.eu, NEC Europe Ltd. (ETSI)
Meeting Date: 2015-03-16
Agenda Item: TBD

## Slide 2: Common Service Functions(CSF)

## Slide 3: Semantics Engine
Provides core semantic functionality
  management of ontologies
    Relation to Data management & Repository?
  management of semantic information
    Relation to Data management & Repository?
  semantic queries (e.g. SPARQL)
    on what information? Relation to discovery?
  semantic reasoning
  (support for) analytics, e.g. deployment within platform
  (support for) mash-ups, e.g. connecting sensors to analytics
CSF is about functionality being exposed to AEs, so which of the above are being exposed (in Rel. 2)?

## Slide 4: Data Management and Repository (DMR)
One of the purposes of CSEs is to enable AEs to exchange data with each other.
The Data Management and Repository (DMR) CSF is responsible for providing data storage and mediation functions. It includes the capability of collecting data for the purpose of aggregating large amounts of data, converting this data into a specified format, and storing it for analytics and semantic processing. The data can be either raw data transparently retrieved from an M2M Device, or processed data which is calculated and/or aggregated by M2M entities.
The following are examples of DMR CSF functionalities:
  Ability to store data in an organized fashion so it is discernible. This includes storage of contextual information such as data types, semantic information, time stamps, location, etc., to complement the data stored in order to access and search the data based on a set of parameters.
  Provides the means to aggregate data received from different entities.
  Ability to grant access to data from remote CSEs and AEs based on defined access control policies, and trigger data processing based on data access.
  Ability to provide the means to perform data analytics on large amount of data to allow service providers to provide value-added services.

## Slide 5: Discovery (DIS)
The Discovery (DIS) CSF searches information about applications and services as contained in attributes and resources. The result of a discovery request from an Originator depends upon the filter criteria and is subject to access control policy allowed by M2M Service Subscription. An Originator could be an AE or another CSE. The scope of the search could be within one CSE, or in more than one CSE. The discovery results are returned back to the Originator.
The DIS CSF uses the Originator provided filter criteria (e.g. a combination of keywords, identifiers, location and semantic information) that can limit the scope of information returned to the Originator.
The discovery request indicates the address of the resource where the discovery is to be performed. Upon receiving such request, the DIS CSF discovers, identifies, and returns the matching information regarding discovered resources according to the filter criteria.
A successful response includes the discovered information or address(es) pertaining to the discovered resources. In the latter case the Originator can retrieve the resources using such discovered address. Based on the policies or Originator request, the CSE which received the discovery request can forward the request to other registered ASN-CSEs, MN-CSEs or IN-CSEs.

## Slide 6: Location (LOC)
The Location (LOC) CSF allows AEs to obtain geographical location information of Nodes (e.g. ASN, MN) for location-based services. Such location information requests can be from an AE residing on either a local Node or a remote Node.
  NOTE: Geographical location information can include more than simply the longitude and the latitude information.
The LOC CSF obtains and manages geographical location information based on requests from AEs residing on either a local Node or a remote Node. The LOC CSF interacts with any of the following:
  a location server in the Underlying Network;
  a GPS module in an M2M device; or
  information for inferring location stored in other Nodes.
In order to update the location information, an AE can configure an attribute (e.g. update period). Based on such defined attributes, the LOC CSF can update the location information using one of the location retrieval mechanisms listed above.
Location information is inherently semantic information and may be modelled semantically

## Slide 7: Registration
The Registration (REG) CSF processes a request from an AE or another CSE to register with a Registrar CSE in order to allow the registered entities to use the services offered by the Registrar CSE.
Registration could possibly include semantic information about the AE / CSE (tbd)
Access to semantic information as a service? (tbd)

## Slide 8: Security
The Security (SEC) CSF comprises the following functionalities:
  Sensitive data handling;
  Security administration;
  Security association establishment;
  Access control including identification, authentication and authorization;
  Identity management.
Sensitive data handling may be required for certain semantic information (tbd)
Semantic information may be relevant for security policies, e.g. access control (tbd)

## Slide 9: Group Management
The Group Management (GMG) CSF is responsible for handling group related requests. The request is sent to manage a group and its membership as well as for the bulk operations supported by the group. When adding or removing members to/from a group, it is necessary to validate whether the group member complies with the purpose of the group. Bulk operations include read, write, subscribe, notify, device management, etc. Whenever a request or a subscription is made via the group, the group is responsible for aggregating its responses and notifications. The members of a group can have the same role with regards to access control policy control towards a resource. In this case, access control is facilitated by grouping. When the Underlying Network provides broadcasting and multicasting capability, the GMG CSF is able to utilize such capability.
Semantics could play a role in defining group membership (tbd)
Semantics may play a role in aggregating responses and notifications (tbd)

## Slide 10: Subscription and Notification
The Subscription and Notification (SUB) CSF provides notifications pertaining to a subscription that tracks event changes on a resource (e.g. deletion of a resource). A subscription to a resource is initiated by an AE or a CSE, and is granted by the Hosting CSE subject to access control policies. During an active resource subscription, the Hosting CSE sends a notification regarding a notification event to the address(es) where the resource subscriber wants to receive it.
Subscription could be based on semantic information (tbd)