## Slide 1: Ontology Architectural Support Options
Group Name: MAS WG
Source: Catalina Mladin, Lijun Dong, InterDigital
Meeting Date: 2015-05-16
Agenda Item: TBD

## Slide 2: Overview
TS-0012 oneM2M Base Ontology is under development to define a set of concepts, relationships and properties that are mainly used for defining oneM2M resources
  There are other ontologies defined addressing individual namespaces rated to M2M and agreed requirements to support simultaneous usage of multiple ontologies for the same M2M resource
There are proposals/discussions (MAS-2015-0551R01) under way on modelling approaches when dealing with concepts from different ontologies
  RE-USE (concepts from existing ontologies) where possible and extend the oneM2M Base ontology where needed
  RE-DEFINITION ( of similar concepts)

## Slide 3: Re-use vs. Mapping
by Nicolas Seydoux, LAAS-CNRS, from NEC MAS-2015-0551
 Re-use
Mapping 

## Slide 4: Next
Independent of the answer to the modeling approach to move forward on functionality addressing the existing requirements, we need to determine architectural support needed for Ontology storage and management.
Consider a e-Health Use Case to highlight the Open Issues to address next

## Slide 5: eHealth Use Case
eHealth
Monitoring
System
Service Provider
(IN-CSE)
Smart
Watch
Blood
Pressure Meter
Smart Scale
Ontology Repository
Semantic
Repository
(Triple Store)
Semantic
Engine
Resource
Repository
3rd Party
(e.g., insurance company)
Home
Gateway
(MN-CSE)
Q1: How to input (E-health) Ontology for oneM2M system use.
Q 2. How to create semantic descriptions and annotate resources
Q 3: Enable Semantic Repository (TripleStore)
to store RDF triples?
Q 4: How to enable use of the Semantic Repository (TripleStore) for queries
Illustrate questions/proposals via Blood Pressure reading use-case flows

## Slide 6: Questions
We propose for discussion the four steps identified in this use-case in order to address the following questions
How to store multiple ontologies such that they can be discovered and re-used by the M2M system
What the ontology repository resources should look like to enable use for semantic annotation
How to enable semantic queries using the given annotation

## Slide 7: Architectural support assumptions
There are three architectural elements which have been discussed/proposed to support both the oneM2M Base Ontology and any extensions:
  ontologyRef attribute ( Release 1 agreement)
    For AE, container, contentInstance resources
    URI of the ontology used to represent the information that is managed and understood for that resource
  Semantic descriptor attribute ( several proposals)
    semantic descriptor with relationships and values for the parent resource
    RDF annotation or similar
  Ontology repository (MAS-2015-0528 NEC proposal)
    Supports Management of ontologies
    Supports CRUD, SPARQL query on ontology (as special retrieve)

## Slide 8: Ontology Repository Assumption MAS-2015-0528 NEC proposal
Ontologies
  Create
    Provide ontology directly
    Download ontology from URL
  Retrieve
    List of supported ontologies
<ontology>
  Retrieve
    Read complete ontology
    Retrieve parts based on (SPARQL) query (e.g. subclasses)
  Update
    Complete ontology
    Partial update???
  Delete
ontologies
oneM2M base ontology
SSN ontology
Smart home ontology
Proposal for discussion – neither final nor complete

## Slide 9: Q1: Example Definition: Class
rdfs:Class – declare a resource as a class for other resources
rdf:type – specify that a resource is an instance of a specific RDFS class
rdfs:subClassOf – declare hierarchies of classes
Define Concepts such as “Patient”, “Blood Pressure Meter”, etc.

## Slide 10: Q1: Example Definition: Property
rdfs:Property – declare the class of properties
rdfs:domain – mean that when the specified property is used in a triple, the subject of the triple will always be an instance of the class specified by the rdfs:domain property in the ontology.
rdfs:range -- mean that when the specified property is used in a triple, the object of the triple will always be an instance of the class specified by the rdfs:range property in the ontology.
sValue: systolic value
dValue: diastolic value

## Slide 11: Q2: Creating Semantic Annotations & Triples
Create the real measurement data
Create the semantic descriptions about the measurement data
Create RDF triples and submit/store them in Semantic Repository

## Slide 12: Q2: Resource Representation examples
Resource
Repository
Semantic
Repository
(Triple Store)
Corresponding RDF triples stored in…
semantic descriptor
Example: Resource Representation for Blood Pressure Measurements and its Semantic Descriptor

## Slide 13: Q3: Example Query on TripleStore

## Slide 14: Q3: SPARQL Query example
Select ?sample ?sValue_var ?dValue_var
Where
{
?sample ex:sValue ?sValue_var.
?sample ex:dValue ?dValue_var.
FILTER ( (?sValue_var >= 120) || (?sValue_var < 90)
|| (?dValue_var >= 80) || (?dValue_var < 60) )
}
Find blood pressure samples that are abnormal

## Slide 15: Annex: Assumed Functional architecture