## Slide 1: AppID Registry FUNTION AppID Profile Data to Identity, Verify and AutHenticate applications REGISTERing FOR services.
Ian Deakin, iconectiv 3rd July 2017
ideakin@iconectiv.com
oneM2M www.oneM2M.org

## Slide 2: Challenges for the CSE connecting unknown IoT applications.
When an IoT application is unknown to the oneM2M system attempts to connect, the current workflow will not provide a mechanism to enable the oneM2M system to access the APPID Registry Function data to identify and verify the identity of the connecting application.
Why would you want to verify the AppID with the AppID registry:-
Today onboarding of IoT applications is a manual process, this limits the scaling of the services for application enrolment at mass scale.
Know if the IoT application is certified to be used for the purpose.
How can the IoT application be authenticated , if using a public CA , can the CA be trusted.
What will be the data it produces and how it is mapped to a oneM2M ontology

## Slide 3: Smart City Challenges Limitations due to IoT application onboarding
Smart City
CSE
Smart City
CSE
Manual AEID onboarding provides limited scope to enroll IoT applications that you have no prior knowledge of:-
Cannot detect rogue or counterfeit applications from entering the systems.
Unknown applications cannot be identified and profiled to know how to enroll them.
No reference to know if the data provided is valid and can be trusted.
Without using AppID identity and authorization management, severely limits the smart city business :
Scale of service due to security controls.
Protection from data compromise
Interoperability to share trusted data
Ability to monetization services
?
?
?
IoT
Applications
IoT
Applications
Unknown &
Uncontrolled
IoT applications
Passive Device Data
?
?
Contracted Device Data
Contracted Devices Data

## Slide 4: Smart City oneM2M service Using an AppID Registry Function
AppID Registry Function provides information to the smart city IoT Platform to enable it to identify and manage any connecting IoT application
Identify any connecting IoT application and characterize its properties before allowing it provide any data.
Using AppID profile data to decide if and how to enroll the application onto the IoT platform.
Description of mapping of application data.
Have reference data to know if the application is certified for use and is fit for purpose.
Cost efficiencies to manage plethora of connected IoT applications
Trust framework to share and commercialize data securely
Trusted open environment to crowd source uncontrolled IoT data at scale
Protect from data breeches and rogue applications
All Known and identified to be trusted
AppID Registry
Function
Smart City
CSE
Smart City
CSE
Passive Device Data
Contracted Device Data
Contracted Devices Data
IoT
Applications
IoT
Applications
Unknown &
Uncontrolled
IoT applications

## Slide 5: AppID Registry Function Identify connecting Applications
The AppID Registry data can be interrogated in REAL-TIME to provide a central trusted repository of IoT application identities and profiles to enable a oneM2M system to trust and securely connect IoT application layer, though an automated process:
IoT Application Registration ( AppID) :
  A unique identity to enable an IoT platform to authorize the connecting application
  A trusted data model for the registered IoT application
  Data privacy policy specific for the application type and its use
  Certificate Authority identity used to authenticate the AE-ID
IoT AppID Identity verification:
  Verify that the IoT application and its AE-ID is valid and can be supported according to the application registration profile (e.g., healthcare applications not connecting to a smart city)
IoT AppID Authentication:
  Provide the identity of the Certificate Authority with the root certificate used to authenticate the IoT application identity. data is valid and can be trusted by the IoT platform.

## Slide 6: AppID Registry Function Value Benefits to all stakeholders
IoT Application Vendors:
  Ability for IoT applications to be broadly adopted by any IoT service provider. Improves reach
  Provides confidence to the community that the IoT applications are secure and can be trusted
IoT Platform and System Integrators:
  Automated onboarding and enrolment, integration with broader range of IoT applications, reduce cost of management
  Security built in by design architecture
  Inclusion of IoT data for application integration and privacy is harmonized
  Maximizing the use of the platform and ability to create service offering
IoT Service Providers:
  Open access, inclusion for a broader range of IoT data to be more innovative
  Reduce cost of vertically integrated sponsors
  Broader adoption, increasing return on investment and opens new revenue possibilities
  Underpins a trust framework to share or commercialize IoT Data
  Supports compliance with data protection
Consumers and End Users:
  Ease of access to participate in service using own IoT applications
  Participation in broader range of services offering better value and choice
  Ensure privacy controls over use of data

## Slide 7
An IoT AppID Security Registry for the industry:
Provides the foundation for IoT security across the ecosystem, for all stakeholders.
Ensures that IoT applications and the data they produce can be trusted.
Underpins secure interoperability as a trust framework to share and commercialize IoT data.
Benefiting the IoT economy for all:
Enables broader inclusion for IoT application manufacturers and consumers
Lowers cost of integration and maximizes service innovation possibilities.
Creates data that can be trusted, while protecting privacy of the customers.
Maximizes revenue and limits IoT security vulnerabilities through trusted open IoT services for service providers.
Anticipates innovative services, knowing that those services are secure.
Using AppID Registry Function data to enable
oneM2M system authenticate unknown applications

## Slide 8: Possible scenario for AppID Registry Function Integration

## Slide 9: CSE to check AppID data in real time from the AppID Registry Function
As a Common Service Entity, I want to query the App-ID Registry so I can determine if an App-ID exists and is registered and use its data to enroll the application.
  When an Application Entity (AE) attempts to register with a common service entity (CSE), it passes its App-ID as a parameter of the CREATE request made to the registrar CSE.
  The CSE may wish to check (OPTIONALLY) if the App-ID exists in the App-ID Registry Funtion before it allows the AE resource instance to be enrolled.
AE
CSE
NSE
AE
CSE
NSE
Field Domain
Infrastructure Domain
Infrastructure Domain of other Service Provider
Mca
Mca
Mca
Mcn
Mcn
Mcc
AppID
Registry
Function
Mcr
Mcr
Standalone AppID Registry Function (ARF)
The AppID Registry function is defined as part of the oneM2M architecture.
Defining a new interface for the CSE to query the ARF

## Slide 10: AppID Registry Function AppID Registration process
Registry determines availability of the requested App-ID.
Option’s to provide the meta data for characterizing the application for enrolment. .
1
2
3
IoT App Developer
Developer requests to register an App-ID , with metadata.
The developer is assigned the App-ID
AppID Registry
Function
Certification
Body
Option for Certification of the IoT application conformity with oneM2M. Verifies the profile is valid.
4
5
The developer is assigned the App-ID CA
Option to provide the Certificate Authority of the AppID / AE-ID certificates.

## Slide 11: AppID Registry Function AppID Application Auto Identity Enrolment using AppID
CSE
HPE
oneM2M
CSE
AppID Registry
Function
  When IoT application connects, it presents its AppID.
  The CSE verifies the IoT AppID with the AppID Registry Function
    AppID and Unique instance
  If the AppID is registered, provide AppID profile data:-
    Meta data to enable the CSE verify the authenticity of the connecting IoT application.
    How to authenticate the application.
    Data model description
    If the application is certified for use
  Providing AppiID profile is acceptable to the IoT platform , the application is allowed connection to share data.
IoT application Identity
Verified and authorized to be used on the CSE
Automated Onboarding of IoT applications.
IoT
application
1
2
3
4

## Slide 12: Enrolment using AppID Registry Meta Data
Where the AE-ID/AppID are unknown to the CSE. Using the AppID registry will enable the service subscription to be auto-populated.
The <serviceSubscribedAppRule> resource represents a rule that defines allowed Role-ID, App-ID and AE-ID combinations that are acceptable for registering an AE on a Registrar CSE
The rule contained in a <serviceSubscribedAppRule> resource defines a mapping between:
  a) one or more Credential-ID(s); and
  b) combinations of one or more Role-ID(s), one or more App-ID(s) and one or more AE-ID(s) which are allowed to be used for registering AE(s) that issued a registration request via a Security Association established with the credentials associated with the Credential-ID(s)

## Slide 13: AppID Registry Function Discovery/Data Model Onboarding a new application
When representing the same kinds of devices from different vendors on M2M platforms application developers may create completely different resource trees without common understanding of the meaning of the data
Example: Light Switch
“On” / “Off”
1 / 0 … or maybe 0 / 1 ?
TRUE / FALSE
… which one is it ?
Data Validation
– Uses “Smart Device Template” (SDT) from HGI as a
flexible and extensible tool for specifying the
abstract information model
– The abstract information model is made concrete
(as resources in the oneM2M system) by
mapping rules
– who is allowed to see it
How the fields relate to action and manageable data for privacy
Privacy management
Ensures IoT data format is valid and can be trusted

## Slide 14: AppID Registry Function Discovery/Data Model Onboarding a new application
IoT Platform
HPE
oneM2M
CSE
AppID Registry
Function
  The IoT application provider, provides the data definition and ontology ID for the specific AppID on the registry.
  At AE registration request, the CSE makes a request to the AppID registry for the data definition of the AppID.
  Informs platform what the data model is
  The IoT platform can auto generate the data model
IoT
Application
1
2
Automated data model discover and mapping to ontology
3

## Slide 15: AppID Registry Meta Data
Proposal to have AppID Meta Data as XML defined characteristics to enable CSE easily configure the resources and mapping of the data to ontology for use within applications.
Examples Including but not limited to :-
  Type of IoT application – Sensor, Application, gateway
  Vertical application – Home, Healthcare, Industry
  Security Capabilities – None, Identity, Communication,
  Native communications – CoAP, MQTT, 3GPP
  Data type – Low Burst , Stream
  Data mapping to ontology
    Ontology Reference
    W3C Mapping ?

## Slide 16: AppID registry Function Digital Certificate – CA Trust
Where an AppID is using a AE-ID public key to provide authentication with a CSE
- How will a CSE know that a Certificate Authority can be trusted that has assigned a certificate for an AE-ID.
- The AppID Registry Function enables the CSE to verify if the IoT application AE-ID digital certificate is authentic.
Inform the CSE that the AE-ID has obtained a digital certificate from a Trusted Public CA
Advantages:
- CSE can connect any IoT application using any digital certificate authority that is trusted by the AppID Registry Function.
- The CSE can choose to revoke attachment of an AE-ID if the CA is not to be trusted.
- Digital certificates can be revoked for a misbehaving AE-IDs, which immediately stops the application from communicating with the CSE.

## Slide 17: AppID registry Function Digital Certificate – CA Trust
CSE
HPE
oneM2M
CSE
AppID Registry
Function
  The CSE, requests the AppID Registry the Root Certificate for the AE-ID CA. ( Could be part of MAF flow ? )
  The AppID registry provides the public and root certificate for the CA
  CSE verifies the AE-ID with the Root certificate for the CA
  Once authenticated, the IoT application has secure connectivity.
1
2
3
Public CA
4
Authenticated
and secure
5
Certificate Authority
IoT
application
AppID
AE-ID CA = xxx
Root Certificate
Trust Level

## Slide 18: Thank You