## Slide 1: oneM2M Sustainability Case Study
4/27/2022
Dale Seed
Convida Wireless

## Slide 2: Outline
  Review of oneM2M specifications to identify aspects/features that are already well-aligned with IoT sustainability and that can provide value-add sustainability.
    E.g., Aspects/features that can make IoT deployments more sustainable
    E.g., Aspects/features that can help society reach sustainability goals
  Review of oneM2M specifications to identify aspects/features where there may be opportunities for further improvements / enhancements to enable implementations of the standard to be deployed more sustainably or to enable the standard to further help society meet its sustainability goals.

## Slide 3: First, a quick refresher on oneM2M entities
temp
AE-2
AE: Application Entity
AE-1
temp
AE-3
temp
AE-4
AE-1
CSEBase
AE-3
AE-4
AE-2
CSE
CSE: Common Services Entity
CSE resource tree for storing metadata/data of applications and devices

## Slide 4
  oneM2M features that enable more sustainable IoT deployments

## Slide 5: Summary of oneM2M features enabling more sustainable IoT deployments
Streamlining of IoT message sizes [<primitiveProfile>]
Offloading processes to IoT service layer [<state>, <processManagement>]
Time synchronization management [<timeSyncBeacon>]
Digital twins [<AE>, <node>, <container>, <contentInstance>, <flexContainer>, etc.]
Subscription and notifications [<subscription>, <crossResourceSubscription>]
Managing sleep schedules and wake-up of devices [<schedule>, <triggerRequest>]
IoT message delivery scheduling and aggregation [<schedule>, <delivery>]
Interworking to different IoT technologies [IPEs]
Performing optimized operations on groups of devices [<group>, <fanoutPoint>]
Managing end-to-end sessions between applications [<e2eQosSession>]
Offloading a software management campaign targeting a set of devices from an application to service layer [<softwareCampaign>, <mgmtObj>]
Assist with managing congestion in underlying network transports [<nwMonitoringRequest>]
Offloading semantic reasoning operations from applications to service layer [<reasoningRules>, <reasoningJobInstance>]
Offloading and managing data storage and brokering on behalf of devices and applications (e.g., storage, discovery, authorization, stats collection, charging of data) [data management resources, <accessControlPolicy>, <statsConfig>, <eventConfig>, <statsCollect>]
Offloading the execution of individual requests from applications to service layer [<mgmtCmd>, <action>, <dependency>, <transactionMgmt>, <transaction>]
Offloading data analytics operations from devices and applications to service layer [<timeSeries>, <timeSeriesInstance>]
Offloading semantic mashup operations from applications to service layer [<semanticMashupJobProfile>, <semanticMashupInstance>, <semanticMashupResult>]
Sending requests to 3GPP devices using Non-IP Data Delivery (use of 3GPP control plane to deliver messages)
Detect network congestion and throttle messages to help alleviate congestion
Managing network connectivity used to communicate with devices [CMDH]
* Features that have been added to the slide deck but not yet been reviewed and discussed with SSC group members
* Features that still need to be added to the slide deck

## Slide 6: 1. Streamlining IoT message sizes
Registration
Registration
Group Management
Security
Discovery
Data Management & Repository
Application & Service Management
Device Management
Subscription & Notification
Communication Management
Service Charging & Accounting
Location
Network Service Exposure
Semantics
Transaction Management
Service Layer
Time
Management
Session
Management
Process
Management
Feature: A message profile is used to reduce the size of messages IoT devices transmit and receive. Message profile is used by service layer to enrich message with additional metadata after message is received from a device (e.g., static information elements in messages).
Sustainability Impact: Size of messages transmitted and received by devices can be reduced. Results in reduced energy consumption by devices and reduced load on networks without sacrificing useful information within messages.

## Slide 7: 1. Streamlining IoT message sizes
temp
AE-1
CSE
AE: Application Entity
CSE: Common Services Entity
primitiveProfile
resourceTypes = contentInstance
operations = CREATE
additions =
labels=temperature,
creator=AE-1, contentInfo=application/xml:1 …
AE-1
CSEBase
1) Request to create contentInstance resource
[content = 32]
CSE
AE-2
2) CSE uses primitiveProfile to add additional useful metadata to message.
A primitiveProfile is used by a CSE to add, modify and delete attributes of messages flowing to/from constrained IoT devices. This helps minimize size of messages without sacrificing useful info needed by apps interacting with these devices
3) Request to Retrieve contentInstance
4) Rich set of information needed by AE-2 included in response
4) Response
[labels = temperature, creator = AE-1,
contentInfo = application/xml:1, content=32]
1) Only bare minimal amount of info needed in request (i.e., just the sensor reading)
container
contentInstance
labels = temperature
creator = AE-1
contentInfo = application/xml:1 …
content=32

## Slide 8: 2. Offloading processes to service layer
Registration
Registration
Group Management
Security
Discovery
Data Management & Repository
Application & Service Management
Device Management
Subscription & Notification
Communication Management
Service Charging & Accounting
Location
Network Service Exposure
Semantics
Transaction Management
Service Layer
Time
Management
Session
Management
Process
Management
Feature: Applications can offload application defined processes to the service layer to perform on their behalf.
Sustainability Impact: Offloading of processes reduces the amount of processing performed by devices/apps and the network traffic flowing between the devices/apps and service layer. For example, an app no longer needs to pull data from service layer and process it. Instead, service layer is instructed by app which operations to perform on the locally stored data and when to perform these operations.

## Slide 9: 2. Offloading processes to service layer
CSE
AE: Application Entity
CSE: Common Services Entity
processManagement
1. Create <processManagement>,
<state>, <action> resources
CSEBase
AE-1
state-1
state-2
action-1
…
…
5. While performing the process, CSE transitions to individual process states based on transition criteria and performs actions defined for each state.
3. CSE monitors start/stop conditions to determine if/when to perform the process
1.An AE can offload to a CSE a process that the CSE performs on the AE’s behalf.
2. A process consists of a set of states and actions much like a state machine
5. While performing the process, CSE transitions to individual process states based on transition criteria and performs actions defined for each state.
4. While performing the process, CSE transitions to individual process states based on transition criteria and performs actions defined for each state if/when specified conditions have been met.
AE-2
5. Unlock Door

## Slide 10
Registration
Registration
Group Management
Security
Discovery
Data Management & Repository
Application & Service Management
Device Management
Subscription & Notification
Communication Management
Service Charging & Accounting
Location
Network Service Exposure
Semantics
Transaction Management
Service Layer
Time
Management
Session
Management
Process
Management
Feature: Service layer detects time synchronization offset issues with devices and compensates for this offset by adjusting timestamp information within the messages to/from these devices.
Sustainability Impact: Complexity and overhead of performing time synchronization operations by devices themselves can be offloaded to the service layer to perform. This helps keep devices simple and streamlined such that they consume less energy.
3. Time synchronization management

## Slide 11: 3. Time synchronization management
temp
AE-1
CSE
AE: Application Entity
CSE: Common Services Entity
timeSeries
AE-1
CSEBase
1) Request to create timeSeriesInstance resource
[Originating Timestamp = 20201003T112432,
Data Generation Time = 20201003T112405
content = 32, …]
timeSeriesInstance1
dataGenerationTime = 20201003T113140,
content = 32
CSE
AE-2
.
.
.
2) Based on AE-1’s Originating Timestamp value, CSE detects time synchronization offset of +7mins 35secs
3) CSE compensates for time offset by adjusting Data Generation Time by 7mins 35secs
4) Request to Retrieve timeSeriesInstance resource
[Originating Timestamp = 20201003T161349]
5) Based on AE-2’s Originating Timestamp value, CSE detects time synchronization offset of +4mins 15secs and adjusts Data Generation Time to compensate for offset when responding to AE-2
6) Response
[Data Generation Time = 20201003T113555
content = 32, …]
6) CSE compensates for time offset by adjusting Data Generation Time by 11mins 50secs

## Slide 12: 4. Digital twins of devices
Registration
Registration
Group Management
Security
Discovery
Data Management & Repository
Application & Service Management
Device Management
Subscription & Notification
Communication Management
Service Charging & Accounting
Location
Network Service Exposure
Semantics
Transaction Management
Service Layer
Time
Management
Session
Management
Process
Management
Feature: Service layer hosts a digital twin representation of a device such that device can sleep but its information can still be accessed while it sleeps
Sustainability Impact: Devices can sleep longer and more often without impacting applications that require information from devices. This helps devices conserve more energy.

## Slide 13: 4. Digital twins of devices
temp
AE-1
CSE
AE: Application Entity
CSE: Common Services Entity
AE-1
CSEBase
1) Register to CSE
CSE
AE-2
4) Device goes to sleep
5) Retrieve contentInstance or flexInstance
7) Response (temp = 32 F, location = New York
container or flexContainer
contentInstance or flexInstance
temp = 32 F
location = New York
2) Create container or flexContainer
3) Create contentInstance or flexInstance
6) CSE services request without needing to wake and interact with device. CSE uses local oneM2M resources (i.e., digital twin of device) to service request.

## Slide 14: 5. Subscriptions and notifications
Registration
Registration
Group Management
Security
Discovery
Data Management & Repository
Application & Service Management
Device Management
Subscription & Notification
Communication Management
Service Charging & Accounting
Location
Network Service Exposure
Semantics
Transaction Management
Service Layer
Time
Management
Session
Management
Process
Management
Feature: Subscriptions and notifications enable devices and applications to offload the monitoring and detection of events of interest to the service layer to perform on their behalf.
Sustainability Impact: Subscriptions and notifications reduces the amount of processing performed by devices/apps and the network traffic flowing between the devices/apps and service layer. For example, an app no longer needs to pull data from service layer and analyze it to determine whether an event of interest has occurred. Instead, service layer is instructed by app which events to monitor on the locally stored data.

## Slide 15: 5. Subscriptions and notifications
AE-1
CSE
AE: Application Entity
CSE: Common Services Entity
AE-1
CSEBase
1) Register to CSE [reachability schedule]
CSE
AE-2
4) Subscribe to door lock status updates
8) Notification that door is unlocked
subscription to control
2) Create flexContainer for door lock
3) Subscribe to door lock control attribute
flexContainer for door lock
status = locked
control = lock
flexContainer for door lock
status = locked
control = unlock
flexContainer for door lock
status = unlocked
control = unlock
subscription to status
5) Request to unlock door
6) Notification of request to unlock door
7) Update door lock status as unlocked
Subscriptions and notifications reduces the amount of processing performed by devices/apps and the network traffic flowing between the devices/apps and service layer. For example, an app no longer needs to pull data from service layer and analyze it to determine whether an event of interest has occurred. Instead, service layer is instructed by app which events to monitor on the locally stored data.

## Slide 16: 6. Managing sleep schedules and wake-up of devices
Registration
Registration
Group Management
Security
Discovery
Data Management & Repository
Application & Service Management
Device Management
Subscription & Notification
Communication Management
Service Charging & Accounting
Location
Network Service Exposure
Semantics
Transaction Management
Service Layer
Time
Management
Session
Management
Process
Management
Feature: Devices can share their reachability status and schedules with service layer. If the device is not currently reachable (e.g., device is sleeping) service layer can trigger the device to wake up and reconnect to receive a high priority request.
Sustainability Impact: Devices can sleep longer and more often without impacting applications that require prioritized communication with devices. This helps devices conserve more energy.

## Slide 17: 6. Managing sleep schedules and wake-up of devices
AE-1
CSE
AE: Application Entity
CSE: Common Services Entity
node (smart meter)
CSEBase
1) Register to CSE [reachability schedule]
CSE
AE-2
4) Subscribe to smart meter software status
9) Notification software has been installed
subscription to control
2) Create node and software for smart meter
3) Subscribe to software install attribute
software
software
install = TRUE
…
software
installStatus = installed
…
subscription to status
5) Request to install software
7) Notification to install software
8) Update software install status
6) Service layer detects if/when device is not connected to the 3GPP network and sends a trigger request to have the 3GPP network trigger the device to re-establish a network connection to the service layer.
3GPP Network

## Slide 18: 7. IoT message delivery scheduling and aggregation
Registration
Registration
Group Management
Security
Discovery
Data Management & Repository
Application & Service Management
Device Management
Subscription & Notification
Communication Management
Service Charging & Accounting
Location
Network Service Exposure
Semantics
Transaction Management
Service Layer
Time
Management
Session
Management
Process
Management
Feature: Based on communication and message delivery handling (CMDH) policies, individual requests received during a scheduled time window can be aggregated into a single request and forwarded for delivery.
Sustainability Impact: The number of overall messages can be reduced, thereby reducing overall load on the system. This can reduce required size and scale of system resources and therefore energy and carbon footprints of systems.

## Slide 19: 7. IoT message delivery scheduling and aggregation
AE-1
CSE
AE: Application Entity
CSE: Common Services Entity
IN-CSE
4) Based on communication and message delivery handling (CMDH) policies configured on the Middle Node CSE (e.g., gateway), individual requests received during a scheduled time window are aggregated into a single request and forward to the Infrastructure CSE (e.g., Cloud)
AE-2
AE-3
MN-CSE
1) Create contentInstance A
2) Create contentInstance B
3) Create contentInstance C
5) Create contentInstances A, B and C
AE-1
CSEBase
contentInstance A
AE-2
contentInstance B
AE-3
contentInstance C

## Slide 20: 8. Interworking to different IoT technologies
Registration
Registration
Group Management
Security
Discovery
Data Management & Repository
Application & Service Management
Device Management
Subscription & Notification
Communication Management
Service Charging & Accounting
Location
Network Service Exposure
Semantics
Transaction Management
Service Layer
Time
Management
Session
Management
Process
Management
Feature: Capability to interwork legacy systems together with one another such that all devices and data can be shared across systems.
Sustainability Impact: Ability to re-use and extend deployment lifetimes of legacy systems (‘brownfield + greenfield’ ) and reduce e-waste.

## Slide 21: 8. Interworking to different IoT technologies
temp
CSE
AE: Application Entity
CSE: Common Services Entity
IPE: Interworking Proxy Entity
IPE-AE
Retrieve deviceThermometer1 Request
CSEBase
AE-1
AE-1 can retrieve the value of a temperature sensor without having to be aware it is a Modbus device
temp
temp
Response
(temperature = 72)
Modbus
Device 1
Modbus
Device 2
Modbus
Device 3
IPE
deviceThermometer1
deviceThermometer2
deviceThermometer3
Modbus devices represented as oneM2M devices

## Slide 22: 9. Performing optimized operations on groups of devices
Registration
Registration
Group Management
Security
Discovery
Data Management & Repository
Application & Service Management
Device Management
Subscription & Notification
Communication Management
Service Charging & Accounting
Location
Network Service Exposure
Semantics
Transaction Management
Service Layer
Time
Management
Session
Management
Process
Management
Feature: Capability to form groups of devices, receive a request targeting the group, fan out the request to the individual group members and aggregate responses.
Sustainability Impact: Using groups the number of overall messages can be reduced, thereby reducing overall load on the system. This can reduce required size and scale of system resources and therefore energy and carbon footprints of systems.

## Slide 23: 9. Performing optimized operations on groups of devices
AE-1
CSE
AE: Application Entity
CSE: Common Services Entity
CSEBase
CSE
AE-4
1) Request to fanout request to all devices in a group (e.g., lock all the doors)
4) Aggregate Response
fanoutPoint
group
members = AE-1, AE-2, AE-3
2a) Request to lock dock
3a) Response
Receive a request targeting a group, fan out the request to the individual group members and aggregate received responses.
AE-2
AE-3
2b) Request to lock dock
3b) Response
2c) Request to lock dock
3c) Response
Note – In addition to fanning out requests to all group members, anycast and somecast options are also supported

## Slide 24: 10. Managing end-to-end sessions between applications
Registration
Registration
Group Management
Security
Discovery
Data Management & Repository
Application & Service Management
Device Management
Subscription & Notification
Communication Management
Service Charging & Accounting
Location
Network Service Exposure
Semantics
Transaction Management
Service Layer
Time
Management
Session
Management
Process
Management
Feature: Capability to configure network QoS session between applications on different devices in the network.
Sustainability Impact: Support for different levels of QoS enables more efficient use of network resources. This can reduce required size and scale of network resources, thereby reducing the energy and carbon footprint of the network.

## Slide 25: 10. Managing end-to-end sessions between applications
temp
AE-2
CSE
AE: Application Entity
CSE: Common Services Entity
AE-1
CSEBase
3) E2E request from
AE-1 to AE-2 with QoS
e2eQosSession
e2eQosRequirements = QoS level, schedule, etc.
CSE
AE-1
2) CSE configures QoS session parameters between AE-1 and AE-2 in underlying 3GPP network
3GPP Network
Request to establish
E2E QoS Session between
AE-1 and AE-2
4) E2E request from
AE-1 to AE-2 with QoS
1) AE-1 needs to communicate with AE-2 with a guaranteed level of QoS (e.g., low latency)

## Slide 26: 11. Offloading a software management campaign
Registration
Registration
Group Management
Security
Discovery
Data Management & Repository
Application & Service Management
Device Management
Subscription & Notification
Communication Management
Service Charging & Accounting
Location
Network Service Exposure
Semantics
Transaction Management
Service Layer
Time
Management
Session
Management
Process
Management
Feature: Capability for offloading a software management campaign targeting a set of devices from an application.
Sustainability Impact: Offloading software campaigns to the service layer to perform on behalf of applications can reduce the amount of network messaging required between applications and devices. This can reduce required size and scale of network resources, thereby reducing the energy and carbon footprint of the network.

## Slide 27: 11. Offloading a software management campaign
AE: Application Entity
CSE: Common Services Entity
CSE
AE
CSEBase
softwareCampaign
version = 1.2.5
name = MN-CSE
targets = Node-2, Node-3, Node-4
softwareOperation = INSTALL
URL = http://images/MN-CSE
softwareTriggerCriteria = subjectResource123
CSE-1
AE
2) When software campaign trigger criteria are met, CSE-1 performs operations to manage CSE SW on targeted Edge nodes
CSE-2
CSE-3
CSE-4
3a) Install CSE software
AE offloads software management to CSE-1 using software campaigning to orchestrate CSEs deployed on Edge nodes
4) Response
[Aggregated software campaign results]
Node-2
Node-3
Node-4
1) Software Campaign Request
[targets, trigger criteria, operation, version, URL, …]
3b) Install CSE software
3c) Install CSE software

## Slide 28: 12. Assist with managing congestion in underlying network transports
Registration
Registration
Group Management
Security
Discovery
Data Management & Repository
Application & Service Management
Device Management
Subscription & Notification
Communication Management
Service Charging & Accounting
Location
Network Service Exposure
Semantics
Transaction Management
Service Layer
Time
Management
Session
Management
Process
Management
Feature: Capability for reducing / minimizing congestion in underlying transport networks.
Sustainability Impact: Minimizing congestion in underlying transport networks can reduce peak loads and required size and scale of networks, thereby reducing the energy and carbon footprint of the network.

## Slide 29: 12. Assist with managing congestion in underlying network transports
CSE
AE: Application Entity
CSE: Common Services Entity
AE-1
CSEBase
4) Notification of high
network congestion in New York
nwMonitoringReq
geographicArea = [40.71, -74.0]
CSE
AE-1
2) CSE subscribes to 3GPP network to receive notifications of high congestion level in a New York area
3GPP Network
AE-1 requests to be notified if network congestion in a New York area becomes high
temp
AE-2
temp
AE-3
temp
AE-4
Location: New York
[40.71, -74.0]
Location: New York
[40.71, -74.0]
Location: New York
[40.71, -74.0]
3) 3GPP network notifies CSE that network congestion in the specified New York area is high
5. AE-1 scales communication with devices in New York area to help reduce network congestion

## Slide 30: 12. Offloading semantic reasoning operations
Registration
Registration
Group Management
Security
Discovery
Data Management & Repository
Application & Service Management
Device Management
Subscription & Notification
Communication Management
Service Charging & Accounting
Location
Network Service Exposure
Semantics
Transaction Management
Service Layer
Time
Management
Session
Management
Process
Management
Feature: Capability to offload semantic reasoning operations from applications to the service layer.
Sustainability Impact: Offloading semantic reasoning operations to the service layer to perform on behalf of applications can reduce the amount of messaging between applications and the service layer. This can reduce required size and scale of network resources, thereby reducing the energy and carbon footprint of the network.

## Slide 31: 12. Offloading semantic reasoning operations
AE: Application Entity
CSE: Common Services Entity
Located in Area-A
Located in Area-B
AE-2
CSEBase
AE-3
semanticDescriptor2
“AE-2” “is-a” “Temperature Sensor”
“AE-2” “isLocatedIn” “Area-A”
semanticDescriptor1
Semantic Resource Discovery Request
temp
AE-2
CSE
AE-1
AE sends a semantic based resource discovery request
SELECT ?sensor
WHERE {
?sensor “is-a” “Temperature Sensor”
?sensor “isOwnedBy” “Organization-A”
}
temp
AE-3
semanticRuleRepository
reasoningRules
If X “isLocatedIn” “Area-A”  X “isOwnedBy” “Organization-A”
Response (AE-2)
CSE applies semantic reasoning rules to perform semantic discovery and determine that
“AE-2” “is-a” “Temperature Sensor”
that “isOwnedBy” “Organization-A”

## Slide 32
  Shortcomings / opportunities for further improvements and enhancements to oneM2M that could enable more sustainable IoT deployments

## Slide 33: Next Steps
Continue to add additional oneM2M features well-aligned with IoT sustainability (e.g., features 11 – 20 identified on slide 5)
Start to identify shortcomings / opportunities for further improvements and enhancements to oneM2M that could enable more sustainable IoT deployments