## Slide 1
HGI’s Approach to
Smart Home Abstraction Layer
Andreas Sayegh (Deutsche Telekom)
HGI Smart Home TF Chair
Andreas.Sayegh@telekom.de
Duncan Bees
Chief Technology and Business Officer HGI
www.homegateway.org
duncan.bees@homegateway.org

## Slide 2: HGI Smart Home Task Force - Scope
Smart Home use case analysis (in progress)
Reference architecture (RWD036)
Connectivity between home gateway and smart meter (RWD038)
Wireless Home Area Network (WHAN) technologies (RWD039)
Device Modeling Template (started: GWD042)
Device Models (started: RWD043)
2

## Slide 3: Reference architecture
HOME GATEWAY
3
RP1 – Abstraction Application Interface
RP2 – Device Application Interface
RP4 – Remote Representation (e. g. ETSI M2M)
RPx – Cloud API
There are more reference points for LAN side access and inter-app communication, but HGI focuses on RP1, RP2, RP4 and probably RPx.
RPx is not defined yet, but considered to be a cloud side API (i.e. for M2M platforms)
D1
D2
D3
Dx
Abstraction Layer
RP2
Remote Access Agent
App 1
App N
…
RP4
Remote Access Middleware
RPx
RP1

## Slide 4: Ordered goals of the abstraction layer
Provide unified APIs for application developers to command, control and query home appliances
Independence of underlying HAN technologies so that an application developer doesn’t need to know anything about Zigbee, Z-Wave, wireless m-bus etc.
Enable applications to be portable across different HGI compliant devices
Enable extendibility of the system with additional HAN technology support without service interruption
Applications should be able to use a pass-through mechanism to use technology-specific functions
4

## Slide 5: Why Standardise the Smart Home?
Oracle, Java (SE, EE) – Standardized APIs (JCP), accessible for any developer, no fees for developers
Apple, iOS – Proprietary APIs, accessible for any developer, fees if commercial rollout is desired
Google, Android – Proprietary APIs, accessible for any developer, no fees for developers
While API standardization is not always essential for successful acceptance by developer communities …
…. no player in the smart home market has comparable market power. HGI believes standardisation is key for smart home
5
Major smart phone manufacturers adopted Android
Apple controls this end to end value chain from hardware to app store

## Slide 6: Areas for standardisation
Should include device model semantics
  I.e. a switch should be defined to have operations called “on” and “off”, not “toggle”, nor “setSwitchState” etc.
  If implementations cannot be unified, mapping rules to a generic model have to be standardized
There are functions that could add a higher level of abstraction (for which business and functional requirements should be elaborated)
  Grouping (“all devices in the living room”), rules engine (“if TV is switched on change the light scene” etc.

## Slide 7: Device Model Template Document
Should be approved by all participating organizations (BBF, HGI, OneM2M, OSGi-A, …)
  Show high acceptance of the template
Template has an informal (text) and a formal section (machine-readable, probably XML based)
  The machine readable part shall be automatically and dynamically translatable into any API system (Java, REST, iOS, Android etc.)
Template must be instantiated for specific devices by domain specific organizations
  Wide industry acceptance is crucial to attract adopters and application developers
  Template may also be instantiated by vendors, even for proprietary models
7

## Slide 8: Aimed collaboration of organizations for a smart home abstraction layer eco-system
8
Joint work on ontology template document
Map ontology template to BBF TRs (if needed)
Jointly approaching domain specific organizations (verticals)
Joint work on GWD042
Map ontology template to OSGi technology
Jointly approaching domain specific organizations (verticals)
Instantiates GWD042 with their respective device characteristics
Joint work on ontology template document
Map ontology template to specific technologies:
ETSI M2M REST APIs
EEBus APIs
Jointly approaching domain specific organizations (verticals)
Edit and align a GWD042
Liaise template to domain specific organizations
Instantiates GWD042 with their respective device characteristics
This figure is not at all comprehensive; it only shows a possible starting point.

## Slide 9: Device Model Template - Process
Instantiation: Send template to domain organizations and request to fill out the template with the device models of their respective interest
Clearing: Classification, unified abstraction, or multiple models with mapping rules
Publication: Formal and informal device model descriptions on public servers
9

## Slide 10: Device Modeling Process (simplified)
PUBLICATION
INSTANTIATION
CLEARING
10
Domain specific org instantiates template for a set of devices
Send GWD042 to domain specific organization
Domain specific org returns instantiated templates
Merge differing models into a single unified model and circulate for approval
Agreement achieved?
Publish resulting domain specific and unified device models
YES
Define mapping rules between unified model and domain specific models
NO
Only 1 model for this device class?
NO
YES
Identify the device class

## Slide 11: Possible components of an abstract device model
11
DEVICE MODEL
DEVICE CLASS
name
SERVICE
SERVICE
SERVICE
name
SERVICE
SERVICE
ACTION
name
parameter value types
return value types
SERVICE
SERVICE
STATE
name
value type
SERVICE
SERVICE
EVENT
name
event type
payload
DEVICE CLASS still under discussion
How to deal with compound devices like i.e. a TV set which consists of a screen, an audio amplifier, most likely a tuner, sometimes also a hard disk recorder?
Formal language for the device model not selected yet
OWL, other XML scheme, or even TR-106 based?
Would formal semantic description have any benefit?

## Slide 12: Licensing and Publication of Device Models
License of Device Models should be BSD style (free of charge, free to use etc.)
  Agreement required
Publication of device models should be on
  Organization servers (BBF, HGI, OneM2M, OSGi-A etc.)
  Neutral platforms, e. g. sourceforge, pastebin etc.
12