## Slide 1: OCF Overview & Introduction
February 2016

## Slide 2: OCF Basics
The Open Interconnect Consortium (OCF) defines a common communication framework that connects and intelligently manages the flow of information among devices to address the emerging needs of the Internet of Things
  Regardless of form factor, operating system, vertical market, manufacturer or service provider
  Based on industry standard technologies
OCF certifies products for interoperability and compliance with the OCF specifications
OCF sponsors the IoTivity Project, an open source reference implementation of the OCF framework.
OCF promotes the goal of broad interoperability via collaboration with other organisations and standards

## Slide 3: Content
IoT & Comms Frameworks
Goals
Structure
Membership (& How to Join)
  Liaisons
IPR Policy
Technology
  Non-Technical Overview
  High Level Technical Information
  IoTivity
Latest Demos
Future Direction

## Slide 4: IoT & Communication Frameworks

## Slide 5
Apps
Services
Before IoT: Apps on Rich Devices communicate with Services in the Cloud or on Data Centers
Comms are relatively easy for developers
  Well defined standards, including security & identity
Services

## Slide 6: What Changed?
Moore’s Law marches on…
  Lower cost compute power
  Lower cost communications
Now realistic to put compute & comms in small, fixed-function devices
Devices you were already going to buy will now be smart & connected
  Very fast ramp in volume
  And some new types of devices too!
Explosion in the amount of data & number of control points

## Slide 7
Apps
Control Points
Data
Services
Services
A simplified model of the Internet of Things
Communications just got a lot more complicated!

## Slide 8
Cloud / Data Centres
Rich Devices / Gateways
Constrained Devices
Time
Isolated
Aggregated
Massively Connected
The architecture will need to achieve massive scale

## Slide 9: The challenge of IoT Communications
Value will be delivered by apps & services, and…
Apps & services need access to data & control points to deliver that value, but…
Developers find it difficult to access all the data and control points
Use cases are more complicated
The system and therefore comms needs to achieve massive scale
The solution must work across form factors, OSs, platforms, manufacturers, service providers and vertical markets.
The solution must also scale from constrained devices to smart devices to the Cloud.
OCF makes it easier to build the apps & services that deliver value

## Slide 10: Comms Framework - Simple IoT Layers Model
Applications & Services
Data & Control Points

## Slide 11: Comms Framework - Simple IoT Layers Model
Applications & Services
Transports
Data & Control Points
Transports
Method of Communication
(Letter, Phone, E-Mail)

## Slide 12: Comms Framework - Simple IoT Layers Model
Transports
Transports
Applications & Services
Comms Protocols
Data & Control Points
Comms Protocols
Language
(French, Chinese, English)
Method of Communication
(Letter, Phone, E-Mail)

## Slide 13: Comms Framework - Simple IoT Layers Model
Transports
Transports
Applications & Services
Comms Protocols
Profiles, Data & Resource Models
Data & Control Points
Comms Protocols
Profiles, Data & Resource Models
What to talk about and how to describe it
(which words in what order – grammar & spelling)
Language
(French, Chinese, English)
Method of Communication
(Letter, Phone, E-Mail)

## Slide 14: Example – Current Consumer Radio-Based Standards
Applications & Services
Data & Control Points
Comms Protocols
Transports
Profiles, Data & Resource Models
Wi-Fi
ZigBee
Thread
Z-Wave
IP
802.15.4
802.15.4
IP
Bluetooth® Low Energy
?
?
BLE
IP
?
IP
= 6LoWPAN
Extensible

## Slide 15: Example – Comms Frameworks (Consumer)
Wi-Fi
BLE
OCF Comms Framework
(Single Resource & Data Model)
IP
IP
Thread
IP
802.15.4
Bluetooth® Low Energy
Applications & Services
Data & Control Points
Z-Wave
ZigBee
802.15.4

## Slide 16: Example – Translation Layers (Consumer)
Wi-Fi
ZigBee
Z-Wave
802.15.4
Bluetooth® Low Energy
Extensible
BLE
OCF Comms Framework
(Single Resource & Data Model)
IP
IP
Thread
IP
802.15.4
Bluetooth® Low Energy
Applications & Services
Data & Control Points
Translation Layers
Z-Wave
ZigBee
802.15.4

## Slide 17: OCF Goals

## Slide 18: OCF Goals
Make it easy for developers to deal with the complexity of IoT comms
  Provide a common data model that developers can use to interface with all IoT devices and data
Deliver as much interoperability as possible in the short term
Provide a path towards future consolidation
Supports the needs of multiple vertical markets (since many use cases span multiple vertical markets)
Establish an architectural foundation that can achieve the necessary scalability

## Slide 19: OCF Goals – Implications
Easy for developers
Developers want (free) code
Open Source
Project
Interoperabilty
Current Fragmentation
Translation Layers
Future Consolidation
Multiple Vertical Markets
Specifications & Certification
Scalability
Learning from Experience
Cloud Native Architecture

## Slide 20: OCF & IoTivity Structure

## Slide 21: OCF & IoTivity Structure
Board of Directors
Standards Work Group
Open Source Work Group
Planning / Marketing / Etc…
Specifications
Certification
IoTivity Steering Group
Projects
Functions
Sponsored (funded) by OCF
Develops reference implementation of the OCF specification
Coordination
Innovative coordination – Specs & Open Source ready simultaneously

## Slide 22: Best of Both
Necessary for some vertical markets
Simplest path to international standardisation
Allows liaisons with organisations that operate under NDA
Proven process to gain broad agreement on direction of new technology
Fastest way to enable developers
Can contain more than just the specification (optional features, development tools, etc…)
Proven process to deliver innovation
Standards
Open Source

## Slide 23: OCF & IoTivity Governance
OCF is a non-profit entity governed by its own bylaws
  Board of Directors has fiduciary responsibility (financial, legal, etc…)
  Sets up Working Groups to accomplish OCF goals
IoTivity.org is a project hosted by the Linux Foundation
  Independent governance and infrastructure, sponsored (funded) by OCF
  Charter to provide reference implementation of OCF standard (but not limited to only a reference implementation)

## Slide 24: OCF Board of Directors
Each Diamond member appoints one Director to the Board
  Diamond members also appoint 1 Alternate
2/3rd board majority of current Diamond member appointed Directors required to accept new Diamond Members
Every 2 years, starting 2 years after founding (July 2016)…
  Diamond and Platinum Members vote to elect 2 additional (Platinum) Directors for 2-year term from list of candidates nominated by Platinum Members
Board of Directors may set up Working Groups
  Work group rules or flexibility concerning membership, participation, voting, leadership and the ability to set up Task Groups is determined by the BoD at time of formation

## Slide 25: Current Board of Directors
Primary
Jong-Deok Choi
President
Secondary
Daniel Park
Primary
Imad Sousou
Vice-President
Secondary
Scott Lofgren
Non-Voting
Mike Richmond
Executive Director
Primary
John Oberon
Treasurer
Secondary
Ram Jagadeesan
Primary
Greg Petroff
Secondary
Abhi Kunté
Secretary
Primary
Charles Cheevers
Secondary
Nav Kannan
Primary
Ralph Brown
Secondary
Mike Glenn

## Slide 26: OCF Organisational Structure
Open Source Work Group
Standards Work Group
Board of Directors
Marketing Communications Work Group
Compliance & Conformance
Core
Security
Smart Home
Technology Planning Work Group
Membership Work Group
Industrial
New Items
PR
Branding
Liaisons
Discovery & Connectivity
Primitive Services
Project Planning & Requirements
Security
Health
Events
Ecosystem
Use Cases
oneM2M
UPnP Work Group
AV
IoT Data Modelling Tool
UPnP Certification
Certification Work Group
Remote Access
Digital Media

## Slide 27: First Major Consolidation in IoT Standards

## Slide 28: OCF & UPnP
1st January 2016 – OCF completed “asset transfer” from UPnP
  OCF acquired substantially all assets from UPnP Forum
  Technically not a merger since UPnP legal entity survives
UPnP IoT efforts became part of OCF
  Increased technical depth (membership, participation), market reach (millions of products supporting UPnP today)
Many UPnP members joined OCF
  There was already substantial overlap of membership and efforts
OCF’s UPnP task group will maintain legacy UPnP specs, continue certification program

## Slide 29: Membership (& How to Join)

## Slide 30: Sample of Current Members (Website for Latest)
Gold
Diamond
Platinum

## Slide 31: Sample of Current Members
Gold (continued)

## Slide 32: Sample of Current Members
Non-profit
Liaisons

## Slide 33: How to Join
IoTivity.org
No need to join – just participate:
Download, Use & Submit Code
OCF members can: influence spec development; certify products; benefit from OCF patent license & marketing activities
openinterconnect.org/join
Download:
Membership Application Form
Bylaws
IPR Policy
Articles of Incorporation
IoTivity.org
openinterconnect.org/join

## Slide 34: IPR Policy

## Slide 35: Royalty Free* Licenses
Apache v2.0
Incoming: Companies license their patent claims covering their code
Outgoing: All users (unless they sue another user for patent infringement via IoTivity code)
Both IPR policies bind corporate affiliates
RAND-Z
(By default – RAND under some circumstances*)
Incoming: All members license their claims to IP essential to implementing the specification
Outgoing: Compliant portion of certified products

## Slide 36: Code Related Patent License – Apache v2.0
+
+
+
+
License
License
License
License
CODE
CODE
CODE
CODE
Developer or User
Patent license covers company’s code contributions

## Slide 37: Code Related Patent License – Apache v2.0
Developer or User
Outbound license is terminated if company sues another code user for patent infringement by the open source code
Developer or User
Suit for infringement of patent

## Slide 38: Spec-Related Patent License – RAND-Z
Member
Product
SPEC
Certification
Program
Compliant Portion
License
Patent license covers everything in specification

## Slide 39: What Patent Claims are Licensed?
Usually defined as “necessarily infringed”, “necessary claims”, or similar
  Specific patents claims are not defined, but…
  If A sues B for infringing specific patent claims, which are necessary to the specification or implementation, then those claims are covered
License only covers the “compliant portion” (RAND-Z) or a contributor’s “contributions” (i.e. code in Apache 2.0)
  The bit that implements the standard / open source project
  Infringe in 2 places, only one of which is part of the standard / open source? You can still be sued based on the other infringement.
OCF license is limited by defined scope

## Slide 40: OCF IPR Scope

## Slide 41: Reasonable And Non-Discriminatory Licensing
RAND (similar to FRAND)
  “Reasonable” royalties are permitted
  You are entitled to a license under reasonable & non-discriminatory terms
  “Reasonable” is often ill defined in other organisation’s IPR policies; OCF defines it according to well recognised fairness principles
RAND-Z (Similar to RAND-RF)
  Zero Royalty (Royalty Free)

## Slide 42: OCF RAND Exemption Process
During 60 day IPR review period of new specifications, OCF members may file a RAND Exemption for specific patents covering a narrowly defined area of technology
  Up to 4 exemptions permitted in any 60 month period independent of number of specs published during that period
Upon receiving an Exemption request the Board may choose to approve spec…
  Member may charge reasonable royalties (under fairness principles) for IP exempt from RAND-Z default license, but…
  If charged royalties, other members may similarly charge the exempting member fair, reasonable royalties for the other members’ IP that would otherwise be covered by RAND-Z license
…Or Board may choose to re-work specification to avoid the identified patents
Delivers long-term predictability while not excluding all licensing
No rising royalties as tech becomes increasingly essential

## Slide 43: OCF Development Process
Raise Objections &
Highlight Out-of-Scope
Adoption
Board Approval
& IPR Review
Certification
Test Dev.
Market Requirements
Technical
Specification
1 – 2 Years
File RAND
Exemption
(Rare)

## Slide 44: Technical Architecture

## Slide 45: Table of Contents
Internet of Things Standard Consideration
Introduction of Open Interconnect Consortium
  Overview
  Core Framework
  Smart Home Profile
  Security
  Remote Access

## Slide 46: Technical Principles for an Internet of Things Ecosystem

## Slide 47: Scope of IoT
service #2 domain
service #1 domain
Local Control
Remote Control
Server to Server
Industrial
Smart Home
Healthcare
Security
Device management
Group management
Protocol Bridge/GW
Messaging
Streaming
Discovery
ID & Addressing
CRUDN
Common Resource Model
…
Wi-Fi
BT/BLE
Thread
…
Vertical
Profiles
Baseline Functionality
Connectivity
Controller
Controller
Cloud Servers
Cloud Servers
Things
Controller App
Cloud Interface
Remote Access
Controller
WebAPI

## Slide 48: Definition of various Things
By defining resources of things and its properties
By defining functions/operations of things
  e.g., Light bulb
BinarySwitch
Dimming
Brightness
- true(on), false(off)
- dimmingSetting (int)
- step (int)
- range [0-100]
- brightness (int)
Resources
- properties
SetSwitch
SetDimmingLevel
SetBrightness
- Power(in)
- brightness (in)
- step(in), range(in)
Functions
- Input & Output Parameters
- (no Verbs) + Objects
*Fixed set of verbs (CRUDN) from transport layer will be used
- Resource model in RESTful Architecture
(e.g., W3C, CSEP, etc.)
- (Verbs + Objects)
- RPC model

## Slide 49: Support of Constrained Things
Less overhead/ Less Traffic
  Minimize CPU Load, Memory impacts, Traffic and Bandwidth
  Compact header
  Binary protocol
  Compressed encoding of payload
  Low Complexity
  Simple Resource Model
    > Short URI (Late Binding w/ resource type defined)
    > Broad and Shallow Hierarchy
*RAM <10KB, Flash <100KB (RFC 7228)

## Slide 50: Support of Multiple Verticals
Legacy vertical services usually designed as silos
 No common way to communicate among them
A common platform provides a foundation for vertical services to collaborate and interwork by providing common services and data models
Insulin level low!
Need Help!
Home Health Domain
Smart Home Domain
Health
Home
Industrial
Common Platform
Health
Home
Industrial
…
…
Discovery
Addressing
Messaging
Security
…
Health
Home
Industrial

## Slide 51: Interoperability
Full interoperability from the connectivity layer up to the service layer is the only way to truly guarantee a satisfactory UX
Interoperability at the Connectivity and/or Platform layer only provides partial interoperability which can ultimately lead to fragmentation
Vertical Services
Platform
Connectivity
Vertical Services
Platform
Connectivity
① Connectivity Level
Interoperability
③ Service Level
Interoperability
Vertical Services
Platform
Connectivity
Vertical Services
Platform
Connectivity
② Platform Level
Interoperability
Vertical Services
Platform
Connectivity
Vertical Services
Platform
Connectivity

## Slide 52: Interoperability & Certification
Prerequisites:
Dependency Certification
(e.g. Connectivity)
Conformance Test
Interoperability Test
Certificate Issue
& Logo Licensing
PASS
PASS
Device under Test
Conformance test - Each device proves conformance to specifications
Interoperability test - Each device proves interoperability with other devices
Certification Scope
CERTIFIED
Mandatory
(in spec, cert & committed in Open Source Project)
Optional Open Source
Features
Tested Optional Open Source
Features
Tested Optional Spec
Features
Optional Spec
Features
Specification
Open Source

## Slide 53: OIC Specification Overview
Core Framework Specification

## Slide 54: Specification Structure
Infrastructure
Core Framework
Security
Remote Access
Certification Test Plans and Test Cases
Resource Model
Resource Specification (Domain agnostic)
Per Vertical Domain
Device Specification
Domain Specific Resource Specification

## Slide 55: Core Framework Specification
Overview

## Slide 56: Objectives
Core Framework Specification Scope
  Specifies the technical specification(s) comprising of the core architectural framework, messaging, interfaces and protocols based on approved use-case scenarios
  Enables the development of vertical profiles (e.g. Smart Home) on top of the core
Architect a core framework that is scalable from resource constrained devices to resource rich devices
Evaluate technical specification(s) for maximum testability and interoperability
Ensure alignment with OIC open source releases

## Slide 57: OIC Roles
OIC Client
  i) Initiate an transaction (send a request) & ii) access an OIC Server to get a service
OIC Server
  i) host OIC Resource & ii) send a response & provide service
57

## Slide 58: OIC Architecture
OIC adopted RESTful Architecture
Current OIC Architecture defines 2 logical roles that devices can take
    - OIC Server : A logical entity that exposes hosted resources
    - OIC Client : A logical entity that accesses resources on an OIC Server
OIC Client
OIC Server
Model 1
R

## Slide 59: Organization of an OIC Device
OIC Device concept
Physical Device e.g. light bulb
OIC Device 2
OIC Device 1
/oic/p
/oic/res
/oic/res
/oic/d
/oic/d
/oic/prs
/oic/mnt
Resource URI: /oic/p
rt: oic.wk.p
if: oic.if.r
n: homePlatform
policy: bm:11
pi: at1908
mnmn: Samsung
Mandatory
Optional

## Slide 60: Device example: light device (oic.d.light)
Example overview
  Smart light device with i) binary switch & ii) brightness resource
Device type: Light device (oic.d.light) [Defined by the domain]
Associated resources
  Core resources: ① oic/res, ② oic/d
  Device specific resources: ③ Binary switch (oic.r.switch.binary),
  Other optional resources can be exposed, in this example ④ Brightness resource (oic.r.light.brightness)
Device Title | Device Type | Associated Resource Type | M/O
Light | oic.d.light | oic/res (oic.wk.core) | M
 |  | oic/d (oic.d.light) | M
 |  | Binary switch (oic.r.switch.binary) | M
 |  | Brightness (oic.r.light.brightness) | O
Example: Smart light device with 4 resources
oic/res
oic/d
Binary switch
Brightness

## Slide 61: Core Framework Specification
Key Features

## Slide 62: OIC Spec Features – Core Framework Spec
Discovery: Common method for device discovery (IETF CoRE)
Messaging: Constrained device support as default (IETF CoAP) as well as protocol translation via intermediaries
Common Resource Model: Real world entities defined as data models (resources)\
CRUDN: Simple Request/Response mechanism with Create, Retrieve, Update, Delete and Notify commands
Device Management: Network connection settings and remote monitoring/reset/reboot functions
ID & Addressing: OIC IDs and addressing for OIC entities (Devices, Clients, Servers, Resources)
Security: Basic security for network, access control based on resources, key management etc
Transport
Networking
L2 Connectivity
Vertical Profiles
Industrial Internet
Smart Home
…
OIC Core Framework
Security
Device management
Group management
Protocol Bridge/GW
Messaging
Streaming
Discovery
ID & Addressing
CRUDN
Common Resource Model
①
②
③
④
⑤
⑥
⑦

## Slide 63: OIC Core Framework Basic Operation
Discovery - Discover access policies, device info and resources on the devices
Operation
- Get device information by retrieving resources
- Control devices by changing resources
- Observe change on the properties of resources
Basic common services
- Device Monitoring
- Maintenance (e.g., reboot, factory reset, statistics collection, etc.)
Connectivity
Networking
Security
Transport
Discovery
Operation
Goal

## Slide 64: Protocol Stack
UDP
TCP
IPv6
Resource Model
DTLS
TLS
L2 Connectivity (Wi-Fi)
Encoding (CBOR)
CoAP
Encoding | JSON or XML/EXI can be negotiated
IP Version | v6 (v4 supported for legacy devices)
Application
Alternatives
Project B OIC Stack

## Slide 65: End point Discovery (CoAP Discovery)
OIC devices make use of CoAP Discovery (defined by IETF RFC 7252)
  Resource Discovery (Possible to discovery resource being hosted by device directly)
  Low processing overhead on each node
  High traffic efficiency (in terms of amount of data sent/received for discovery)

## Slide 66: Encoding Schemes – JSON, XML/EXI, CBOR
OIC resource is represented as sequence of bits by encoding schemes when to transfer it over the network
OIC supports several encoding schemes and it will be negotiated and accepted by OIC Server when OIC Client requests
OIC has mandated CBOR as the default encoding scheme
 | JSON | XML/EXI | CBOR
Description | - Lightweight, text-based, language-independent data interchange format | - Binary compression standard for XML | - Concise binary object representation based on JSON data model
Standard | IETF RFC 7159 | W3C Efficient XML Interchange Format 1.0 | IETF RFC 7049
Content Type | /application/json | /application/exi | /application/cbor
OIC M/O | Optional | Optional | Mandatory
* JSON: JavaScript Object Notation, EXI: Efficient XML Interchange, CBOR: Concise Binary Object Representation

## Slide 67: Collection Resources
A container is used to model complex structures
An OIC Resource that contains one or more references (specified as OIC Links) to other OIC Resources is an OIC Collection
An OIC Link embraces and extends typed “web links” as specified in RFC 5988

## Slide 68: Resource Directory
Offloads handling of discovery (response to multicast messages) to devices that are capable of doing so
Key enabler for sleepy end nodes, enhances battery life.
OIC Device A
OIC Device B
OIC Device C
/oic/res
/oic/res
OIC Device D
/oic/res
Multicast Group
Multicast Discovery
Request by Device C
Unicast
Response with resources for Devices A, B and D
Publish
(to /oic res)
Device B acts as Resource Directory for Device A and Device D; Device A and D do not respond to multicast query
Publish
(to /oic res)

## Slide 69: Scenes/Rules/Scripts (1 of 3)
Overview
  Mechanisms for automating certain operations
  Rules, Scripts and Scenes can be grouped and reused
Scenes
  A static entity that stores a set of defined resource property values for a collection of resources.
  Provide a mechanism to store a setting over multiple OIC Resources that may be hosted by multiple separate OIC Servers.
  Once set up, can be used by multiple OIC Clients to recall a setup

## Slide 70: Scenes/Rules/Scripts (2 of 3)
Rules
  A logical “if then” statement
  Consists of a rule condition and a Rule Member (a script)
  The rule condition is an evaluation criterion which can include evaluation of the value of a sensor on an OIC Server
  When the evaluation criterion is evaluated true then the Rule Members are set to a specific determined value
  A rule condition is evaluated when one of the observed resources in the rule condition changes

## Slide 71: Scenes/Rules/Scripts (3 of 3)
Scripts
  A programmatic element that can be used to incorporate conditionals, delays, loops and other programmatic devices, including reading and writing scenes
  Scripts can consist of a set of steps that are executed either upon meeting the conditions of a rule or as part of another script, in order to automate tasks
  Scripts can also be used to set a scene to a specific value
  A Script is realized as the set of Rule Members that are executed when a rule condition holds true
Summary
  Scenes are bundled user settings
  Scripts are automated background tasks
  Rules are conditional statements that execute scripts when the condition is true

## Slide 72: Block Transfer with CoAP Messaging
Basic CoAP messages work well for the small payloads we expect from light-weight, constrained IoT devices
It is envisioned whereby an application will need to transfer larger payloads
CoAP block wise transfer as defined in IETF draft-ietf-core-block-17 shall be used by all OIC Servers that receive a retrieve request for a content payload that would exceed the size of a CoAP datagram

## Slide 73: Messaging Protocol Negotiation
Supported messaging protocols are conveyed in the property (mpro) on the /oic/res (resource discovery)
Omitting this property defaults to the messaging protocol as specified in the vertical specification (e.g., CoAP for Smart Home)
After discovery, an OIC Client can use any of the supported messaging protocols supported by the OIC Server

## Slide 74: CoAP Serialization over TCP
Provides the ability for CoAP to run over TCP in environments where TCP is already available and where UDP may be blocked.
If TCP is used then reliability is provided by TCP rather than the inherent reliability mechanisms within CoAP (confirmable messages).
Use the new protocol negotiation feature to convey support during resource discovery (/oic/res)

## Slide 75: Smart Home Device and Resource Specification
Way of Working

## Slide 76: Defining OIC Components (on top of CORE)
OIC Servers
  Defined by device identifier: standardized name of the device
  List of mandatory OIC resources per device
  Note that OIC Clients are implicitly specified as “opposite” side of an OIC Server.
    Currently OIC does not impose interaction sequences.
    All Resources are allowed to talk to/from any OIC Client at any point in time
OIC Resource
  Defined by resource identifier: standardized name of the resource
  List of mandatory properties per resource
  List of allowed actions (read/readwrite/..) per resource

## Slide 77: Vendor extensions
Vendor is allowed to:
  Create own defined (none OIC standardized) resources
  Create own defined (none OIC standardized) device types
  Extend existing devices with additional (not mandated) resources
    With standardized resource types
    With vendor defined resource types

## Slide 78: Tooling
SHTG defines all resource schemas using JSON, all resource APIs using RAML
SHTG developed Python based tool chain that auto-generates specification text based on the RAML and JSON that is defined per resource.
Capabilities provided by the tooling include:
  Auto validation of the RAML against RAML syntax rules
  Auto validation of the JSON schemas against JSON Draft-04 rules
  Auto validation of all example JSON against the applicable JSON schemas
High confidence level in the validity of the resource definitions
Ability to simulate all resources

## Slide 79: Specifications
Specifications are split in 2 documents:
  Device specification
  Resource specification
The Device specification uses the resources defined in the resource specification

## Slide 80: Device Specification
Contains profiles of
  Core specification
  security specification
Contains list of smart home devices
Each Smart home device definition contains:
  unique identifier (rt)
  a list of mandatory resources

## Slide 81: Smart Home Device and Resource Specification
Key Features

## Slide 82: Resource Specification
List of reusable resources that are used in an Smart Home Device
  Contains generic list of error codes
  Uses core definitions
Each Smart home resource definition contains:
  unique identifier (rt)
  Indication if the resource is an sensor or actuator
  List supported methods
  List per method the JSON schema for input and output
  Resources are specified in RESTful API Modelling Language (RAML)

## Slide 83: Smart Home Use Cases
Selected key enabling use cases to scope activity
Use Case | Priority
Indoor Environment Control | 1
Lighting control | 
Energy Saving Washer/Dryer | 
Energy Management | 
Remote Access for Device Control | 
Smart watch notify and control | 6
Smart Video Environment | 3
Smart Home Office | 
Smart Garage | 
Device Grouping and Control | 
Multi player gaming | 7
Smart watch gaming on TV | 
Fire safety monitor and Notify | 4
Keyless Entry | 2
Home Security | 
Health Monitor and Notify | 5
1
Control proximal OIC Devices
On board new Devices
Control remotely with an OIC Client
2
3
Cloud
Gateway
1
2
3
Smart Phone
OIC
OIC
OIC
OIC
OIC

## Slide 84: Indoor Environment Control
LAN Network (Home)
Home GW
A/C
Smart device
WAN Network (Cloud)
Smart device
Temperature
Windows
Humidity
84

## Slide 85: Lighting Control
LAN Network (Home)
Home GW
Lighting
Smartphone
WAN Network (Cloud)
Smartphone
Lighting
Lighting
85

## Slide 86: Energy-saving washer/dryer
LAN Network (Home)
Home GW
Smart device
WAN Network (Cloud)
Smart device
Washer
Dryer
86

## Slide 87: Energy Management
87

## Slide 88: Remote Access Device Control
88

## Slide 89: Keyless Entry
LAN Network (Home)
Home GW
Door locks
Smartphone
WAN Network (Cloud)
Smartphone
Door lock
89

## Slide 90: Home Security
90

## Slide 91: Health Monitor & Notify
LAN Network (Home)
Home GW
Smartphone
WAN Network (Cloud)
91

## Slide 92: Smart Home Device Type
Device Type | Minimum Resource Set
Air Conditioner | Binary Switch, Temperature
Air Purifier | Binary Switch
Blind | Open Level
Dishwasher | Binary Switch, Mode
Door | Open Level
Clothes Dryer | Binary Switch, Mode
Clothes Washer | Binary Switch, Mode
Fan | Binary Switch
Garage Door | Door
Light | Binary Switch
Oven | Binary Switch, Temperature (2)
Printer | Binary Switch, Operational State
Device Type | Minimum Resource Set
Refrigerator | Binary Switch, Refrigeration, Temperature (2)
Robot Cleaner | Binary Switch, Mode
Smart Plug | Binary Switch
Switch | Binary Switch
Thermostat | Temperature (2)
Camera | Media
Generic Sensor | Sensor
Receiver | Binary Switch, Audio, Media Source List (2)
Scanner | Binary Switch, Operational State, Automatic Document Feeder
Security Panel | Mode
Television | Binary Switch, Audio, Media Source List
Water Valve | Open Level
Exposure of an OIC Device Type is Mandatory.
If an OIC Server hosts an OIC known device then it shall follow all normative requirements in the Device Specification applicable to that Device.
92

## Slide 93: Defined Resource Types (1/2)
Resource Types | Use Case
Air Flow | Indoor Environment Control
Air Flow Control | 
Battery | Device Control
Binary switch | Device Control
Brightness | Lighting Control
Colour Chroma | 
Colour RGB | 
Dimming | 
Door | Indoor Environment Control
Energy Consumption | Energy Management
Energy Usage | 
Humidity | Indoor Environment Control
Icemaker | Device Control
Resource Types | Use Case
Lock | Keyless Entry
Lock Code | 
Mode | Device Control
Open Level | 
Operational State | 
Ramp Time | Lighting Control
Refrigeration | Device Control
Temperature | Indoor Environment Control
Time Period | Device Control
93

## Slide 94: Defined Resource Types (2/2)
Resource Type | Use Case
Audio | TV, Home Entertainment
Auto Focus | IP Camera
Auto White Balance | IP Camera
Automatic Document Feeder | Scanner Support
Button | Device Control
Colour Saturation | IP Camera
DRLC | Smart Energy
Energy Overload | Smart Energy
Media | IP Camera
Media Source List | TV, Home Entertainment
Movement (Linear) | Robot Cleaner
Night Mode | IP Camera
PTZ | IP Camera
Signal Strength | Proximity
Resource Types are Conditionally Mandatory. If an OIC Server hosts an OIC known resource then it shall follow all normative requirements in the Resource Specification applicable to that Resource.
Sensor Resource Type | Use Case
Acceleration | Extended Sensor Set (for a Generic Sensor Device)
Activity Count | 
Atmospheric Pressure | 
Carbon Dioxide | 
Carbon Monoxide | 
Contact | 
Glass Break | 
Heart Rate Zone | 
Illuminance | 
Magnetic Field Direction | 
Presence | 
Radiation (UV) | 
Sleep | 
Smoke | 
Three Axis | 
Touch | 
Water | 
Sensor Support Resources
94

## Slide 95: OIC Bridge - Background & technical need
There are many different IoT standards
There are many different vendor solutions
Hence it would be good for OIC if OIC could use these devices and create a (vendor defined) bridge to these non-OIC devices.
Goal:
  To represent non OIC devices by means of a bridge as an OIC server on the network.
Conceptual:
  Bridge establishes an OIC standardized north bridge so that all OIC clients can use the bridged devices.
  The south bridge will be vendor/implementation specific: it uses the protocol defined by the bridged device.
    For example: it needs to realize Philips Hue APIs if a Hue light is bridged
95
Notes: Non oic communication: any medium: USB/BT/IP/RS232

## Slide 96: OIC Bridge - Definition
An OIC smart home bridging device is a device that represents one or more other non-OIC devices as OIC Smart Home Devices on the network.
The represented devices themselves are out of the scope of OIC. The bridging (that is, how the bridge communicates with the non-OIC devices) is implementation and vendor specific.
The only difference between a ‘regular’ OIC Device and a bridged device is that the latter is encapsulated in an OIC Smart Home Bridge Device.
An OIC Smart Home Bridge Device shall be indicated on the network with an “rt” of “oic.d.bridge”. When such a device is discovered the exposed resources on the OIC Smart Home Bridge Device describe the devices that are being bridged.
OIC device (client)
OIC bridge device
OIC light device
OIC fan device
Entity
Entity
Non OIC
communication
OIC
communication
96
Notes: Non oic communication: any medium: USB/BT/IP/RS232

## Slide 97: Bridge Device example: bridge (oic.d.bridge)
oic/res
oic/d (oic.d.light)
Binary switch
baseURI: 100.0.0.1:5683/0
OIC light device
oic/res
oic/d (oic.d.fan)
Binary switch
baseURI: 100.0.0.1:5683/1
OIC fan device
oic/res
oic/d
baseURI: 100.0.0.1:5683
OIC bridge device
97

## Slide 98: Bridging relationship with oic/res
/oic/res
[
{"di": "bridge_device_id",
"links": [
{ "href": "/oic/d",
"rt": "oic.d.bridge",
"if": "oic.if.r",
"rel": "hosts"}]},
{"di": "light_device_id",
"links": [
{ "href": "0/oic/d",
"rt": "oic.d.light",
"if": "oic.if.r",
"rel": “contains external"},
{ "href": "1/myLightSwitch",
"rt": "oic.r.switch.binary",
"if": "oic.if.a",
"rel": “contains external"}]},
{"di": "fan_device_id",
"links": [
{ "href": "1/oic/d",
"rt": "oic.d.fan",
"if": "oic.if.r",
"rel": “contains external"},
{ "href": "1/myFanSwitch",
"rt": "oic.r.switch.binary",
"if": "oic.if.a",
"rel": “contains external"}]}
]
/oic/d
{
"n": "myRoomBridgeDevice",
"rt": “oic.d.bridge",
"if": "oic.if.r",
“di": “bridge_device_id“,
"icv": "oic.1.5“,
}
/oic/d
{
"n": "myRoomFanDevice",
"rt": “oic.d.light",
"if": "oic.if.r",
“di": “fan_device_id“,
"icv": "oic.1.5"
}
/oic/d
{
"n": "myRoomLightDevice",
"rt": “oic.d.light",
"if": "oic.if.r",
“di": “light_device_id“,
"icv": "oic.1.5"
}
98

## Slide 99: Security Specification

## Slide 100: OIC Security Summary
OIC key management supports end-to-end device protection
Resource layer ACLs allow intended interactions while preventing unintended interactions
Secure device ownership helps prevent attacks when devices are added to the network
100

## Slide 101: To Cross a Boundary We Must Define the Endpoint
An OIC device is the endpoint
...more specifically it is the OIC resource layer
OIC resources define how device capabilities are exposed to other OIC devices
Resources are accessed securely through a secure channel such as DTLS
  End-to-end message encryption, integrity and replay protection
OIC does not define endpoint hardening techniques
  Resource layer hardening is implied
OIC Device
101

## Slide 102: Secure Resource Manager (SRM)
OIC Device
SRM Duties
  Manage secure endpoint resources (Creds, ACLs, Device ID, Config status)
  Enforce resource access and endpoint protection
Secure Resource Manager (SRM) Layer
Persistent Storage Interface (PSI)
Policy Engine (PE)
Resource Manager (RM)
Secure Virtual Resource database
Connectivity Abstraction (CA) layer
Resource Introspection (RI) layer
OIC Application
102
  Device ownership
  Security provisioning
  SVRD storage protection

## Slide 103: Ownership Transfer and Bootstrapping
Devices typically ship from a manufacturer in an “un-owned” state
The user does some magic to affect taking ownership of the device, using an Onboarding Tool (OBT)
  Take over responsibility of the device and relieve manufacturer of any liability due any actions the device may take under user’s ownership
Ownership transfer creates a relationship between an OIC device and an OBT.
  The relationship is defined through establishment of an Ownership Credential and a set of ownership-complete states
Device Gets on the Network
OBT Discovers the Device
Device is Un-owned
Ownership Transfer
Bootstrapping / Provisioning

## Slide 104: Ownership Transfer and Bootstrapping
Security Spec Defines Several Ownership Transfer Methods (OTM):
  Just-Works, DECAP, Random-PIN, Manufacturer Certificates
  Also allows Vendor Specific Method
All OTMs are optional for an OIC device to implement, but it is mandatory to support at least one among Just-Works, DECAP, Random-PIN or Manufacturer Certificates.
  (We will need to be able to test all for certification ultimately)
  Might change in the future spec
OTMs differ in:
  How a device establishes trust
  How the physical owner’s “intent” is proved
  What cipher suites are used
OTMs should bring the device to a well defined state

## Slide 105: Secured vs. Un-secured
OIC Servers support a secured and un-secured interface.
Generally speaking, the un-secured interface is for discovery only. All other services should be visible on the secured interface only.
  The un-secured interface has no message protection and no access control enforcement
  Publicly visible unique IDs (device, platform, etc.) may present a privacy problem
Discoverable resources are resources that can be delivered as part of a discovery request (secured interface or not)
  At the time of creating, a resource is defined as “discoverable” or not.

## Slide 106: Message Integrity and Confidentiality
DTLS only for now.
The devices communicating need to have useable credentials to talk to each other. If they are missing, the devices could contact the CMS to get them.
All secured communication is encrypted and signed.

## Slide 107: Access Control
Resources on the secured interface (that should be almost everything) are only accessible if there is a proper entry in the Access Control List
  No ACL, No Service
An ACL says “X can do Y on resource Z”
  X can be a deviceID, a role, or a group (in the future)
  Y can be any combination of CRUDN
If no ACL is present, and the device has an AMS configured, it can ask the AMS what authorization X has on Z.

## Slide 108: Access Control : example
/oic/sec/acl
Subject: device/group or role
Resource(s): one or more URN
Permission: bitmap of CRUDN
Period(s): validity periods
Recurrence(s): recurrence rule(s)
Rowner: the service that owns this acl
{
"Subject": ”switch1",
"Resource": "/light",
"Permission": "00000100", <update>
"Period": " ",
"Recurrence": " ",
"Rowner": "oic.sec.ams"
}

## Slide 109: Resource Access Example
OIC Server Device3
Access is blocked if no ACL match is found
Device1 request to get /oic/d is accepted due to ACL Read permission
Device2 request to update /oic/light/1 is denied due to time-of-day policy
An intermediary (Device4) may also enforce ACLs
/oic/d
Model
Mfg Date
OIC Client
GET /oic/d
Device1
OIC Client
Properties:
acl1
acl0
Device1
/oic/d
Read
/oic/light/1
On-Off
DimLevel
Properties:
OIC Stack
/oic/light/0
On-Off
DimLevel
Properties:
Device2
PUT /oic/light/1
Device2
/oic/light/1
Read, Write
11 – 5p
Daily
[{“/oic/d”, “Model”, “T”, “Mfg Date”, “1/1/2015”}]
[{“/oic/light/1”, “On-Off”, “Off”, “DimLevel”, “80”}]
RSP 4.01
x

## Slide 110: Credential Management
OIC devices can support the use of both symmetrical and asymmetrical credentials for establishing secure communication
  Symmetric Key is mandatory
  Local PKI mechanism is supported (Keys are issued in home domain and used only within that domain.)
Missing credentials could be procured from a CMS
Credentials may have an expiration period
  Expired credentials can be refreshed

## Slide 111: Credential Management : example
/oic/sec/cred
CredID: Local short ID
SubjectID: device or group
RoleID(s): roles this credential allows a subject to assert
CredType: sym/asym/cert/…
PublicData, PrivateData, OptionalData
Credential Refresh Method:
Rowner: service that can modify this resource
Period: Expiration period of credential
{
”CredID": ”1”,
"SubjectID": ”device1”,
”RoleID”: ” ”,
”CredType": "1”, <symmetric pair-wise>
”PublicData”: “”,
“PrivateData”: “ABCDEFGHIJKLMNP”,
"Period": ”P1W ",
"Recurrence": " ",
"Rowner": "oic.sec.ams"
}

## Slide 112: OIC Specification Overview
Remote Access

## Slide 113: Remote Access (“RA”) in OIC (implementation plan)
Remote Access endpoint Devices:
  Remote Access Endpoints (“RAE”):
    OIC Servers also capable of XMPP, optionally capable of ICE-client
  Remote Access Proxies (“RA-Proxy”):
    Superset of RAE – Capable of ‘representing’ “RA-constrained devices”
      “RA-Constrained”: Devices incapable of natively supporting RA tech
Cloud Components:
  XMPP Server(s)
113

## Slide 114: The OIC RA Model
XMPP Server 1
XMPP Server 2
A
B
C
D
E
F
G
H
J
?
…
RA-Constrained OIC Device
“RAE”
“RA-Proxy”
Non-OIC (RA-Constrained) device
K
L
M
N
P
Q
R
S
CoAP
XMPP-native
Realm I
Realm II

## Slide 115: Remote Access
Server Components:
  Device Management Server: Device/Capability Registration and Authorization
  Signaling Server: Delivering candidate address to recipient, discovery, presence, low BW data, SDP control
Client Components: RA Endpoint (RAE) & RA-Proxy
  XMPP Client
Remote
Client
Things (RAE)
Discovery,
control
Media data
XMPP Servers
Platform
XMPP
IP
BLE
BT
DM Client
Routing
CA Layer
RI Layer
Resource Model
ACL/Cred
SRM
Application
115

## Slide 116: RA as defined in Spec 1.0
Format for bare-JIDs (owner) and full-JIDs for RAEs
  Includes JID-Resource overloading for:
    OIC Spec version
    Device-type
    UUID
Mapping from Core/Smart-Home Resources to full-JID format
  Allows for Presence, Remote Discovery, XMPP-Roster-based access
Communication of CRUDN messages between the OIC clients and OIC servers that are in the same roster
116

## Slide 117: RA-Roadmap – Post Spec 1.0 priorities
Defining RA-Proxy functionality
  Leverage XMPP PubSub (XEP-0060)
  Extending full-JID overloading model & XMPP Presence
    Adding RA-Proxy Device-type – avoid gratuitous remote device queries
“App notes” for temporary remote access via XMPP Multi-User Chat (MUC – XEP-0045),
  Family members, neighbors, etc.
Adding Jingle (XEP-0166) for media signaling
117