## Slide 1
January 30, 2019
Cam Williams
Schneider Electric
Introduction to Dotdot

## Slide 2: Evolution of
The Zigbee Cluster Library (2005) and Zigbee Application Architecture (2012) documents have evolved organically from a loose set of rules into Dotdot. The result is a very extensible data model, and set of object classes that support a variety of devices engaging in many applications and types of interactions. The model is not overly prescriptive, nor has it ever been considered complete. The Zigbee Alliance enjoys a large & diverse membership that continually add and incrementally refine the model.

## Slide 3: Dotdot Elements
Node, Device, Endpoint, Cluster, Attribute, Command, Data Type
    All have numeric identifiers and managed name space
    All are revision controlled (later slide).
  Node – An addressable instance of a Dotdot application on a single network
  Endpoint – An addressable instance of a virtual device (e.g. 3 light switches on 1 node)
  Device – Specification for an endpoint conforms to a well-known set of functions and features (e.g. Dimmer, Thermostat, etc.), by defining objects on that endpoint.
  Cluster - Object class specification (or object instance on an endpoint)
    For example: The On/Off Cluster spec contains all the functionality related to turning a device on & off and storing its on/off state
  Attribute – Cluster data of a fixed Data Type
    Cluster Revision is the only Mandatory global Attribute
  Global Commands – Read, Write, Report, Discover, etc.
  Cluster Specific Commands – On, Off, Toggle, Move to Level, Step Up, etc.
© Zigbee Alliance. All rights reserved.

## Slide 4: Dotdot Revisioning
Any revision of spec text is always vetted for backward/forward compatibility
    Any change increments revision number (because we can't predict the future).
Dotdot – Basic Cluster has Attribute for Dotdot (ZCL) Revision
    Global Commands & Attributes - spec text rarely changes or needs interpretation updates
    Name Space – change in identifier ranges
    Data Types – New types but no new identifiers
    Tracks with annual release of ZCL with any normative change to Foundation chapter
Device – Device Revision is always read with the Device Identifier
    Any change to M/O/D conformance in device spec
Cluster – Global Attribute: Cluster Revision
    Any non-editorial change to cluster spec text including M/O/D changes
    New or updated Attributes and Commands
    This is the revision that changes most as clusters are refined by domain experts
© Zigbee Alliance. All rights reserved.

## Slide 5: Dotdot Clusters
Minimal independent functional element
Client/Server – Client instance controls, and Server instance has data (loosely defined)
Simple clusters – On/Off, Level Control, sensors, etc.
Complex clusters – Thermostat, Door Lock, etc.
More complex control & behavior is not always RESTful
Utility Clusters – Basic, Identify, Groups, Scene, Power Config, etc.
Binding – connects an instance of a cluster to one of more instances of a corresponding cluster
    Type 1 transaction – client commands server: e.g. Switch to Light(s)
    Type 2 transaction – server reports it's state: e.g. sensor server configured to send reports to one or more aggregators
  Simple devices – mandatory to support configurable persistent bindings
  Dynamic devices – not mandatory for gateways and mobile devices
© Zigbee Alliance. All rights reserved.

## Slide 6: Dotdot Utility Clusters
Configuration, commissioning, provisioning, reset, diagnostics, etc, etc.
Many utility functions are supported by clusters on an endpoint
Other more global utilities, such as endpoint discovery & binding, are supported by the Zigbee Device Object on endpoint 0.
Groups cluster to allow a groupcast message and a group binding
Identify cluster for discovery includes user involvement
Basic cluster has node-wide or product-wide state
OTA Upgrade cluster is for over-the-air upgrade and supports many use cases with constraints on time, persistent memory, and synchronization of upgrades.
Power Configuration cluster to represent battery measurement on a device
Stack specific diagnostic and performance clusters

## Slide 7: Dotdot Evolution
Cluster Inheritance Derivation is supported and backward/forward compatible:
    Support both base and derived cluster identifier on and endpoint for one instance
    Legacy products only know original base cluster and not new features
    New products can use new features of derived cluster
    Level Control -> Pulse Width Modulation added Frequency
  Cluster Inheritance Reverse Derivation (instant ancestor)
    Create base cluster with common properties for existing (now derived) cluster.
    Legacy still use original specific cluster
    New products can discover common cluster for common features and behaviors
    Legacy RH cluster and new Soil Moisture created Water Content base cluster.
  Base Cluster never instantiated (pure virtual)
    Concentration Measurement cluster allows unlimited derived clusters to measure 0.0 to 1.0 concentration of a substance in a substrate, but by itself it has no use (as of today)
  Optimizes development and testing
    Code and test scripts can be reused
    Spec text is already certified

## Slide 8: Dotdot Cluster Applications
These are chapters in the Zigbee Cluster Library
Foundation
General
Measuring and Sensing
Lighting
HVAC
Closures
Security and Safety
Protocol Interfaces
Smart Energy
Over the Air Updating
Telecommunication
Commissioning
Retail
Appliances
Most common Application Domains
Residential Lighting
Residential Safety
Residential HVAC
Residential Smart Energy
1 Dimmable Light
2 Energy Service Int
3 Color Scene Control
4 Control Bridge
5 In-Premise Display
6 Metering Device
7 Extend Color Light
8 IAS Zone
9 Color Dim Light
10 Combined Interface
11 Color Temp Light
12 Non-Color Control
13 On/Off Light
14 Color Controller
15 Load Control
16 Smart Plug
17 On/Off Plug In Unit
18 On/Off Sensor
19 Remote Comms
Most Common Devices

## Slide 9: Dotdot Development and Testing
Test Harness for Dotdot/Zigbee
Test Harness for Dotdot/Thread & Dotdot/IP
Test Harness for Dotdot/??? framework
XML representation of Clusters, Devices, & PICs for each
PICs generate Test Scripts in Python or Java Script
Tools built around machine readable database of elements & instances
Dotdot Commissioning App for iOS and Android
All Source Code for above is owned today by Zigbee members
Next step – generate code, scripts, specs, emulators, etc.

## Slide 10: What is in Dotdot/IP
IPV6, UDP
CoAP (RFC 7252)
Core Link Format (RFC 6690)
CoAP Resources
Dotdot/IP uses several IETF documents to map Zigbee into the world of IP and a RESTful interface.
    Constrained RESTful Environments (CoRE) Link Format (RFC 6690)
    Constrained Application Protocol (CoAP) (RFC 7252).
    Concise Binary Object Representation (CBOR) (RFC 7049)
ZDO information is available through queries using the CoRE Link Format
ZDO commands are available through CoAP methods GET, PUT, POST and DELETE
ZCL General Commands and Cluster commands are accessible through CoAP methods GET, PUT, POST and DELETE
ZCL General and Cluster response commands are returned in CoAP responses
ZCL payloads are encoded in CBOR which makes them small and scalable
Dotdot over IP

## Slide 11: How does Zigbee map to Dotdot/IP?
Zigbee Network Layer
Zigbee Application Support Layer (APS)
Zigbee Device Object (ZDO)
Zigbee Cluster Library (ZCL)
Bindings, Device Discovery
Attributes and
Commands
IPV6, UDP
CoAP (RFC 7252)
Core Link Format (RFC 6690)
CoAP Resources
Zigbee PRO
Dotdot over IP

## Slide 12: Dotdot/Zigbee vs Dotdot/IP Transactions
In Dotdot/Zigbee each transaction consists of two commands, an originating command and a corresponding response command.
Dotdot/IP follows a RESTful design in which each transaction consists of an originating CoAP Method (GET, PUT, POST, DELETE) and a corresponding CoAP response such as 2.05 Content or in an an error case 4.05 method not allowed.
  Dotdot/Zigbee Command IDs are sometimes included in the originating URI but are excluded from the CoAP response.

## Slide 13: ZDO Commands & CoRE Link Format
Discovery of a device’s exposed functionality which in Zigbee is accessible through ZDO discovery commands are available through CoAP GET to .well-known/core
    Example: Multicast query used to discover Zigbee endpoints implementing the client side of the on/off cluster (ClusterID 0x0006):
    GET COAP://[FF03::FD]/.well-known/core?rt=urn:zcl:c:6.c
    Returns a CoAP response code 2.05 (content) with the information about which endpoint implements this cluster
    2.05 Content (Content-Format: application/link-format (40)) <coap://[2002:8290:4eed::8290:4eed]/zcl/e/1/c6>;rt=urn:zcl:c:6.c;ze=urn:z:cl:d.103.1

## Slide 14: ZDO Commands and CoAP
Zigbee Device Object commands such as those involved in creating and managing bindings are available through CoAP methods such as GET, PUT, POST and DELETE to /b
  Example: To retrieve the binding located at index 0 the device would send:
    GET coap://[2002:8290:4eed::8290:4eed]/zcl/e/1/s6/b/0

## Slide 15: General Commands and CoAP
ZCL General Commands map to the CoAP RESTful interface using methods GET, PUT, POST and DELETE.
    ReadAttributes = GET to /a/<aid>
    WriteAttributes = PUT, POST to /a/<aid>
    DiscoverAttributes = GET to /a
    ConfigureReporting = PUT, POST, DELETE to /r/<rid>
    ReadReportingConfiguration = GET to /r/<rid>
    ReportAttributes = POST to /n
    DiscoverCommandsReceived = GET to /c
For Example:
    ReadAttribute on the OnOff attribute on the On/Off cluster (0x0006) on Endpoint 1 becomes:
      GET coap://[2002:8290:4eed::8290:4eed]/zcl/e/1/s6/a/0
    ReadAttributesResponse on the OnOff attribute on the On/Off cluster (0x0006) on endpoint 1 becomes:
      CoAP Response 2.05 Content with a CBOR map {0:0} indicating that the OnOff attribute is currently in the Off state.

## Slide 16: Cluster Commands and CoAP
Cluster Commands map to the CoAP RESTful interface using method POST to /c/<cid>
Cluster Command responses map to the CoAP response of a given CoAP POST.
For example: On Command sent to endpoint 1 becomes:
    POST coap://[2002:8290:4eed::8290:4eed]/zcl/e/1/s6/c/1
    CoAP response 2.05 Changed with a payload {0:0} indicating a Default Response with status SUCCESS

## Slide 17: Dotdot/IP Resource Table
Resource | Methods | URI
Resource discovery | GET | /zcl
Endpoints | GET | /e
Attributes | GET, PUT, POST | /a
Commands | GET, POST | /c
Bindings | GET, PUT, POST, DELETE | /b
Report Configuration | GET, PUT, POST, DELETE | /r
Report Notification | POST | /n
Group Notification | POST | /g
EZ-Mode Commissioning | GET, POST | /m

## Slide 18: Application Layer Security
Unique ID: All devices have a device certificate from the manufacturer to provide identity and a unique ID. Each device will either be provided at manufacture or self generate a raw public private key pair.
Operational Certificates: All devices must support handling of operational certificates if the network supports provisioning and usage of such certificates.
DTLS: All devices must support application level DTLS sessions for either device to device or device to cloud interactions. The DTLS session can be based on pre-shared key, raw public key or certificates.
Application Layer Security: A device SHALL restrict access based on application level security. For example, a status may be accessible to all devices while a command may only be accepted with application level security included. The specification will detail what is required for each device and how the security session is initiated. Note this does not apply to group communications.
Service Discovery: Service discovery on network does not require application level security.
Network Layer Security: When network level security is available, it SHALL be used.