## Slide 1: Ideas for an ETSI white paper with MEC and OneM2M
Presented by: Dario Sabella, Enrico Scarrone
For: ETSI ISG MEC
15/11/2022
Document number WORKSHOP(22)000001r1

## Slide 2: Agenda
Overview of ETSI MEC architecture
Overview of OneM2M architecture
OneM2M deployment in MEC environments
Proposal for a joint ETSI white paper
Conclusions
2

## Slide 3: Overview of ETSI MEC architecture
Ref. ETSI GS MEC 003 v.3.1.1

## Slide 4: MEC architecture: definitions
The MEC platform is the collection of essential functionality required to run MEC applications on a particular Virtualisation infrastructure and enable them to provide and consume MEC services. The MEC platform can also provide services.
A MEC application is instantiated and run as a virtualised software application, within for instance a Virtual Machine (VM) or OS containers provided as part of the application package as a software image(s), on top of the Virtualisation infrastructure of the MEC system. It can also potentially interact with the MEC platform to consume and provide MEC services.
4
A MEC service is a service provided and consumed either by the MEC platform or a MEC application. When provided by an application, it can be registered in the list of services to the MEC platform over the Mp1 reference point .
A MEC application can subscribe to a service for which it is authorized over the Mp1 reference point

## Slide 5: MEC scenarios: constrained device @far edge
Draft ETSI GR MEC 036 V3.0.7 (2022-04)
5
The computing layer is composed of different computing tiers, namely, the central cloud, the edge cloud (e.g. Telco Edge) connected to network edge and far edge capabilities associated with the constrained devices (e.g. UEs or CPEs).
NOTE: applications and functions may be hosted anywhere in the computing stratum (cloud, edge or far edge devices).
Far edge capabilities may be embedded in the constrained terminal devices or dynamically provisioned. Constrained devices may be battery-powered, mobile, volatile, with limited compute and connectivity as compared to the traditional edge clouds. The constrained devices may collaborate and exchange information among themselves.

## Slide 6: Overview of oneM2M architecture

## Slide 7: oneM2M simplified Architecture
Underlying Network
Underlying Network
CSE
AE
NSE
CSE
AE
NSE
CSE
AE
NSE
NSE
Application Service Node
(Edge device/GW)
Middle Node
(Fog node/GW)
Infrastructure Node
(Cloud / company servers))
Application Layer
Service Layer
Network Layer
Mca
Mcn
Mca
Mca
Mcn
Mcn
Mcn
Mcc
Mcc
Reference Point One or more interfaces - Mca, Mcn, Mcc and Mcc’ (between 2 service providers)
Common Services Entity Provides the set of "service functions" that are common to the IoT environments
Application Entity Provides application logic for the end-to-end IoT solutions
Network Services Entity Provides services to the CSEs besides the pure data transport
Node Logical equivalent of a physical (or possibly virtualized, especially on the server side) device
CSE
Mcc’
Inf. Node
(Other cloud/ companies servers)

## Slide 8: OneM2M deployment in MEC environments
(for consideration and discussion)

## Slide 9: Possible scenario: connected devices at the “far edge”
CSE is like a “service producing MEC App”, connected to consumers AE
AE can be seen by MEC system as a MEC App
Note: according to GS MEC 011, all applications and functions can be also LCM managed by MEC or other systems
9
CSE
AE
Application Service Node
(Edge device/GW)
CSE
AE
Middle Node
(Fog node/GW)
CSE
AE
Infrastructure Node
(Cloud / company servers)
CSE
Inf. Node
(Other cloud/ companies servers)
e.g. constrained device
e.g. @telco edge
e.g. @central cloud

## Slide 10: Proposal for a joint ETSI white paper
(for consideration and discussion)

## Slide 11: Possible joint ETSI white paper
Some initial consideration are being made, on synergy between MEC and oneM2M.
  A presentation from oneM2M (Enrico) at a MEC call.
  A joint discussion at the ETSI IoT Week, and a couple of MEC sessions (chaired by Dario).
Few stakeholders from both groups want to explore first of all how MEC and OneM2M can integrated effectively, and a tool for that would be a common ETSI paper.
  This ETSI white paper should not be wide-scope (e.g. including Digital Twins, for example), but rather a very focused paper, on the architectural integration
  The goal indeed is to honestly clarify to the reader what is available in the standards, how they are compatible, and how to deploy OneM2M in a MEC environment, and finally if there are any gaps.
We don’t need many authors, but at least few experts from each group at least. Everybody interested in joining the paper can contact Dario(MEC)+Enrico&JaeSeung Song(oneM2M).
  Once we have gathered some interest, and possibly reached a minimum number of authors, we may start drafting the paper together, and also Dario can offer asking ETSI the approval, in case we decide to go for that.
11

## Slide 12: Discussion
In principle, MEC and oneM2M can be deployed together in an edge node
It would be good to have common use cases to discuss in the paper (e.g., VRU?, ...)
Clarifications:
  MEC architecture (MEC 003) is not showing cardinality of entities.
  Each CSE need to relate to a DB (they are influencing oneM2M performance)
When MEC and oneM2M can interwork, then there are benefits in terms of performance (e.g. availability of functions locally at the edge)
In principle a same application (AE, seen as a MEC App) can consume services from both CSE and also MEC platform.
  However, there could be in principle some need to share information on capabilities.
In the paper, we may also discuss/capture scenarios where MEC is already deployed and one wants to add a oneM2M system.
Next steps:
  Share information on this White Paper discussion at our respective meetings (29/11 – 2/12).
  Open invitation to other authors and decision by the first Mid of December.
  Then Dario can volunteer to write a WP proposal toward ETSI for approval of the paper initiative.
12

## Slide 13: Thank you for your attention
Follow us on: