## Slide 1: Development Status & Preview of Release 4 features
Roland Hechwartner, TP Chair, Deutsche Telekom
Shane He, RDM Chair, Nokia
Dale Seed, SDS Chair, Convida Wireless
Andrew Han, TDE Chair, Hansung University
oneM2M Webinar
June 17th, 2020

## Slide 2: Content
The oneM2M Partnership Project - the standard for an IoT eco-system
  Roland Hechwartner of Deutsche Telekom, Chair of the oneM2M Technical Plenary
oneM2M enables data interoperability
  Shane He of Nokia, Chair of the Requirements and Domain Models working group
oneM2M testing, certification and developers outreach program
  Andrew Min-gyu Han of Hansung University, Chair of the Testing and Developers Ecosystem working group
oneM2M Release 4 - a preview of new features
  Dale Seed of Convida Wireless, Chair of the System Design and Security working group

## Slide 3: oneM2M Introduction
Roland Hechwartner, oneM2M TP Chair
Deutsche Telekom

## Slide 4: oneM2M Partnership Project
founded1 July, 24th 2012
TP#1: Sep 24th-29th 2012
[1] Partnership Agreement V 2.0 (Approved March 2013)
Release 2 transposition
ITU-T SG20 Y.4500.x
Partner transpositions
De jure Standard
focus on interoperability
“collaborate on standard - compete in implementation”
www.oneM2M.org All documents and specifications are publically available
=> Reuse e.g.
Join forces => reduce fragmentation
HGI
Almost 200 member organizations in oneM2M
Steering Committee
Technical Plenary
Requirements and Domain Models
Testing and Developers Ecosystem
System Design and Security

## Slide 5: oneM2M Standard – Testing – Certification Program
Certification Program
Industry
Public Services
Enterprise
Healthcare
Energy
Transportation
Other
Residential
REQUIREMENTS TS-0002
TECHNICAL SPECS
TECHNICAL REPORTS
TECHNICAL SPECS
TECHNICAL REPORTS
TECHNICAL SPECS
TECHNICAL REPORTS
Interoperability Test Events
Transposed to Partner Specifications Regional Standards

## Slide 6: oneM2M Key-events Timeline
Industry Day 5
2014
2013
2017
2016
2015
2020
2019
2018
2012
Industry Day 4
Industry Day 3
Industry Day 2
Industry Day 1
oneM2M
established
Release 1
Release 2
Release 2A
Release 3
Release 4 planned
oneM2M Hack-a-Thon Event
Interop 1
Interop 2
Interop 3
Interop 4
Interop 5
Interop 6
oneM2M
Certification
launch
15+ products certified
GCF oneM2M
Certification
launch
Interop 7 planned

## Slide 7: oneM2M is an End-to-End IoT Technology
Service Layer
Service Layer
Communication Network(s)
Service Layer
App
App
App
App
Non-oneM2M
App
Flexible Deployment Options
  IoT Cloud / Enterprise
  IoT Gateway
  IoT Edge Device
  IoT User Devices

## Slide 8: oneM2M’s modular service functions fit into a coherent framework
Service Layer
Service Layer
Communication Network(s)
Service Layer
App
App
App
App
Non-oneM2M
App
Service Layer

## Slide 9: oneM2M enables vertical domains & data interoperability
Shane HE, oneM2M RDM Working Group Chair
Nokia Bell Labs

## Slide 10: oneM2M Breaks Down the Silos
Smart
Emergency
Services
Smart
Transportation
Smart
Infrastructure
Vertical
Information Flow
Vertical
Information Flow
Vertical
Information Flow
Smart
Emergency
Services
Smart
Transportation
Smart
Infrastructure
Service Layer
…
…
…
Horizontal
Information Flow

## Slide 11: Release 4 - More Vertical Domain Support
Industry
Smart city
Enterprise
Public warning
Disaster Alert
Vehicular
Railway
REQUIREMENTS TS-0002
TECHNICAL SPECS
TECHNICAL REPORTS
TECHNICAL SPECS
TECHNICAL REPORTS
TECHNICAL SPECS
TECHNICAL REPORTS
Industry
Smart city
Vehicular
Enhancement on common service functions
Enhancement on common information models
Interworking with non-oneM2M systems
INTERWORKING TOWARDS DOMAIN-SPECIFIC TECHNOLOGIES

## Slide 12: Domain models enable data interoperability
Industry domain models
Railway domain models
  Use cases and requirements to find gap between the railway domain and oneM2M
  Discovering information model and mapping to adapting oneM2M
Module Instance Name | Module Class Name | Multiplicity
binarySwitch | binarySwitch | 1
clock | clock | 1
touchScreen | touchScreen | 0..1
emergencyButton | pushButton | 0..1
audioVolume | audioVolume | 0..1
ticketReader | prePaidCardReader | 1
crossingSensor | traceSensor | 1
connectivity | connectivity | 1
gateState | runState | 1
directionPanel | directionPanel | 0..1
crossingIndicatorColour | colour | 1
crossingIndicatorColourSaturation | colourSaturation | 1
crossingIndicatorColourBrightness | brightness | 1
crossingBarrier | crossingBarrier | 1
Example: device model of deviceSmartGate
OPC-UA Information model
oneM2M Information model

## Slide 13: Emerging technologies for Smart cities
Smart Lift
  Focus on predictive maintenance (operating technician/building owners/users and administrators)
  Services for emergency situation support, remote operation, city services, etc.
  Develop smart lift data models in the semantic supported by oneM2M
Ontology on Smart cities
  Standardize ontologies for Smart City services through integrating SmartM2M SAREF work to oneM2M as the baseline
  Develop a framework to maintain developed ontologies and get input from various domain actors using a oneM2M SmartCity portal service
Adaptability
Clarity
Completeness
Conciseness

## Slide 14: Public warning services enablement
IPAWS in US
CBS in Korea
MoWaS in Germany
CAP in Italy
J-ALERT in Japan
Source: TR-0046 Study on Public Warning Service Enabler
oneM2M architecture enables Public Warning Service
Public Safety
Disaster Alert
Public Health

## Slide 15: SDT 4.0: make it easy for IoT developers
Provides an abstraction layer for connected devices
Together with other organizations, such as OCF and OMA, oneM2M Rel 3 defines 84 ModuleClasses and 50 Devices with various functionalities
In Rel 4 (ongoing) SDT is restructured to fit more the verticals (Home, City, Industry, Health, Automotive,…)
URL to GitLab: https://git.onem2m.org/MAS/SDT (master)

## Slide 16: SDT based Information Models
SDT based Information Model and Mapping for Vertical Industries (TS-0023)
Name | Type | R/W | Optional | Unit | Documentation
powerGenerationData | xs:float | R | true | W | Amount of instaneous generation data.
roundingEnergyGeneration | xs:integer | R | true |  | This energy consumption data is calculated by multiplying significantDigits with multiplyingFactors, and rounding down the result.
significantDigits | xs:integer | R | true |  | The number of effective digits for data.
multiplyingFactors | xs:floatr | R | true |  | The unit for data multiplying factors, for example 1 kWh, 0,1 kWh, 0,01 kWh etc.
generationSource | xs:string | RW | false |  | The type of generating source.
Common Domain
115 ModuleClass 17 DeviceModel
Home Domain
32 DeviceModel
City Domain
Vehicular Domain
Health Domain
Railway Domain
Name | Type | R/W | Optional | Unit | Documentation
flowInterval | xs:integer | RW | false | s | The measurement interval of water comsumption.
reverseFlowIntervral | xs:integer | RW | false | s | The measurement interval of reverse water comsumption.
waterTemperatureInterval | xs:integer | RW | true | s | The measurement interval of water temperature.
waterPressInteveral | xs:integer | RW | true | s | The measurement interval of reverse water pressure.
intensiveSampleInterval | xs:integer | RW | true | s | The time interval of intensive data sampling.
intensiveReportInterval | xs:integer | RW | true | s | The time interval of intensive data report.
intensiveReportStartTime | m2m:timestamp | RW | true |  | The start time of data intensive report.
Module Instance Name | Module Class Name | Multiplicity | Description
openLevel | openLevel | 0..1 | See clause 5.3.1.56.
doorlock | lock | 0..1 | See clause 5.3.1.52.
doorStatus | doorStatus | 0..1 | See clause 5.3.1.29.
Module Instance Name | Module Class Name | Multiplicity | Description
binarySwitch | binarySwitch | 1 | See clause 5.3.1.12.
runState | runState | 0..1 | See clause 0.
dishWasherJobMode | dishWasherJobMode | 0..1 | See clause 5.3.1.29.
ModuleClass
DeviceModel

## Slide 17: oneM2M Testing, Certification and Developers Outreach Program
Andrew Min-gyu Han
(andyhan@hansung.ac.kr)
TDE Chair, Hansung University

## Slide 18: oneM2M Specification
<oneM2M TS-0004 Figure 5.4.1-1>
Various Specs covering a various specific area.
TS 0001
Functional Architecture
TS 0004
Service Layer Core Protocol
TS 0008
CoAP Protocol Binding
TS 0009
HTTP Protocol Binding
TS 0010
MQTT Protocol Binding

## Slide 19: Collaboration for developing oneM2M Test Spec
Developing
oneM2M Testing Spec
Implement
TTCN-3 code base
Test cases
Validation
(Spec, test cases, test system)
Defining
oneM2M Product Profiles
oneM2M TDE WG
ETSI CTI STF531
And
oneM2M TF-001
Initial Korea Market
requirements

## Slide 20: Testing Scope
Interoperability Testing
  Verification of end-to-end functionality in accordance with oneM2M binding protocols (HTTP, CoAP and MQTT) and serializations (XML and JSON).
    Interoperability test specification for oneM2M certification based on TS-0013(Interoperability Testing)
  Total Test Cases : 288
Conformance Testing
  Based on oneM2M conformance testing specifications
    TS 0017 Implementation Conformance Statements
    TS 0018 Test Suite Structure and Test Purpose
    TS 0019 Abstract Test Suite and Implementation eXtra Information for Test
    TS 0025 Product Profiles
  Total Test Cases : 328

## Slide 21: TS-0018 Test Purposes
General Capability(GEN)
Registration(REG)
Data Management and Repository(DMR)
Subscription and Notification(SUB)
Security(SEC)
Group Management(GMG)
Discovery(DIS)
Release 1
Release 2
Release 3
Release 4
Communication Management and Delivery Handling(CMDH)
FlexContainer
Ontology based Interworking(OBI)
Home Appliance Information Model and Mapping(HAIM)
Location(LOS)
Device Management(DMG)
Resource Announcement(ANNC)
3GPP Interworking
General Capability(GEN)
Registration(REG)
Data Management and Repository(DMR)
Subscription and Notification(SUB)
Communication Management and Delivery Handling(CMDH)
Ontology based Interworking(OBI)
Home Appliance Information Model and Mapping(HAIM)
Group Management(GMG)
Discovery(DIS)
Location(LOS)
Device Management(DMG)
Security(SEC)
Resource Announcement(ANNC)
3GPP Interworking
FlexContainer
General Capability(GEN)
Registration(REG)
Data Management and Repository(DMR)
Subscription and Notification(SUB)
Group Management(GMG)
Discovery(DIS)
Communication Management and Delivery Handling(CMDH)
Security(SEC)
FlexContainer
General Capability(GEN)
Registration(REG)
Data Management and Repository(DMR)
Subscription and Notification(SUB)
Security(SEC)
Group Management(GMG)
Discovery(DIS)
Release 4 features
Smart Device Template based Information Model and Mapping for Vertical Support (SDT)

## Slide 22: TS-0018 Test Groups (Rel-3)
Functional Entity Groups: AE, CSE
Common Services Functions Subgroups: Registration, Data Management and Repository, Subscription and Notification, Group Management, Discovery, Location, Device Management, Communication Management and Delivery Handling, Security
oneM2M Resource Primitives Specific Operations: Resource announcement, timeSeries, location, 3GPP interworking, Semantic, HAIM, Dynamic Authorization, FlexContainer

## Slide 23: oneM2M Certification Goal
oneM2M Certification is intended to create an ecosystem of certified products that ensures interoperability among oneM2M certified products
oneM2M Certification is LOGO program, NOT an compulsory program.
  Representation that oneM2M products and services meet oneM2M Specification and Test requirements that ensure interoperability.

## Slide 24: oneM2M Certification Organization
SC
TP
TST
Certi.
Ad-Hoc
oneM2M
oneM2M
Certification Body (CB)
Authorized Test Lab(ATL)
1st oneM2M Certification Body!
TTA (Korea, 2017.2)
DEKRA J.J (Japan, 2018.2)

## Slide 25: Product Type
oneM2M certification product type consists of End Product and Component
  End Product is a product that claims to have implemented at least one of oneM2M node types.
  Component is an implementation of one or more of embedded oneM2M node types as software that is used to produce End Product.
End Product or Component must implement at least one of oneM2M node types.
  Node type: ADN, ASN, MN, IN

## Slide 26: Certification Type
New product
  Any product that is certified using oneM2M standard specification for the first time
Product change
Rebranding
  Previously certified product that acquired a new name, term, symbol, design, or combination of two or more external change
Product Change Type | Description | Testing Scope | New Certification issue
Major | Change impacts all oneM2M functionality and is regarded as a new product | Full Re-testing | O
Partial | Change impacts a portion of oneM2M functionality | Additional testing of new functionality and/or changed functionality | O
Minor | Change does not impact oneM2M functionality (e.g., add another model name) | No testing required | X

## Slide 27: Certification Process
5 steps to oneM2M GCF Certification
  Join GCF
  Develop a test plan
  Execute your test plan
  Review the test results
  Receive your GCF certification

## Slide 28: oneM2M Certification Websites
www.onem2mcert.com

## Slide 29: oneM2M Certification Websites
onem2m.globalcertificationforum.org

## Slide 30: oneM2M Interop & Hackathon 2020
Date & Place: Oct. 2020 (Physical(Seoul, Korea), e-Meeting or Hybrid)
Interop Features:
  R2 + R3 new scope
Tentative Interop new scope
  3GPP Interworking
  HAIM(SDT based Information Model)
  DM
  Initial Provisioning
  Authentication Security
  Semantics
Hackathon event
  Hackathon is held with Interop, schedule and place is also sync with Interop

## Slide 31: oneM2M Release 4 Preview of new features
Dale Seed, oneM2M SDS Working Group Chair
Convida Wireless

## Slide 32: oneM2M Feature Summary by Release
Release 1
Registration
Discovery
Security
Group Management
Data Mgmt. & Repository
Subscription & Notification
Device Management
Communication Mgmt
Service Charging
Network Service Exposure
App & Service Mgmt
HTTP/CoAP/MQTT Bindings
Release 3
Semantic Querying/Mashup
3GPP SCEF Interworking
    Non-IP Data Delivery
    UE reachability Monitoring
    Device triggering
    Etc.
  Transaction Management
  Service Layer routing
  Common oneM2M Interworking Framework
    OCF
    OPC-UA
    OSGi
  oneM2M Conformance Tests and Profiles
  Security Enhancements
    Distributed Authorization
    etc.
  Ontology Based Interworking
Release 2
Time Series Data
Flexible Resources that can be customized by app developers (flex container)
Semantics Description & Discovery
Security Enhancements
    Dynamic Authorization
    Content Security
    E2E Security
WebSocket Binding
Ontology for Home Area Information Model
oneM2M App-ID Registry
oneM2M Interworking
    LWM2M
    Alljoyn
    3GPP Triggering
Release 4 (planned)
  SDT 4.0 and the Information Models for Multiple Domains
  oneM2M Conformance Tests
  Geo Query
  Process Management
  Message Primitive Profiles
  Semantic Reasoning
  Time Management
  Enhanced 3GPP Interworking
    Session QoS
    Congestion Monitoring
  Fog/Edge Computing
    Software Campaigning
    Resource Synchronization
  Service Subscriber Management
  Security Enhancements
  Group Anycast/Somecast
  Modbus Interworking
  Discovery Based Operations
  Semantic Ontology Mapping
2015
2016
2018
2020

## Slide 33: Quick Overview of oneM2M Entities
temp
AE-2
AE: Application Entity
AE-1
temp
AE-3
temp
AE-4
AE-2
CSEBase
AE-3
AE-4
AE-3
CSE
CSE: Common Services Entity
CSE resource tree for storing metadata/data of applications and devices

## Slide 34: Geo Query
Rel-4 Feature
NEW
temp
AE-2
CSE
AE: Application Entity
CSE: Common Services Entity
Geo Query Request
geoQuery = Point, [40.71, -74.0], …
AE-1
AE sends a geo query request to discover temperature sensor in New York City
temp
AE-3
temp
AE-4
Location: New York
[40.71, -74.0]
AE-2
location: [40.71, -74.0]
CSEBase
Location: LA
[34.05, -118.24]
Location: Chicago
[41.85, -87.65]
AE-3
location: [34.05, -118.24]
AE-4
location: [41.85, -87.65]
Response (AE-2)
CSE looks up locations of AEs and finds AE-2 matches Geo Query criteria

## Slide 35: Process Management Services
Rel-4 Feature
NEW
CSE
AE: Application Entity
CSE: Common Services Entity
processManagement
1. Create <processManagement>,
<state>, <action> resources
CSEBase
AE-1
state-1
state-2
action-1
…
…
5. While performing the process, CSE transitions to individual process states based on transition criteria and performs actions defined for each state.
3. CSE monitors start/stop conditions to determine if/when to perform the process
An AE can offload to a CSE a process that the CSE performs on the AE’s behalf.
2. A process consists of a set of states and actions much like a state machine
5. While performing the process, CSE transitions to individual process states based on transition criteria and performs actions defined for each state.
4. While performing the process, CSE transitions to individual process states based on transition criteria and performs actions defined for each state if/when specified conditions have been met.
AE-2
5. Unlock Door

## Slide 36: Message Primitive Profiles
Rel-4 Feature
NEW
temp
AE-1
CSE
AE: Application Entity
CSE: Common Services Entity
primitiveProfile
resourceTypes = contentInstance
operations = CREATE
additions =
labels=temperature,
creator=AE-1, contentInfo=application/xml:1 …
AE-1
CSEBase
1) Request to create contentInstance resource
[content = 32]
CSE
AE-2
2) CSE uses Message Primitive Profile to add additional useful metadata to message
A Message Primitive Profile is used by a CSE to add, modify and delete attributes of messages flowing to/from constrained IoT devices. This helps minimize size of messages without sacrificing useful info needed by apps interacting with these devices
3) Request to Retrieve contentInstance
4) Rich set of information needed by AE-2 included in response
4) Response
[labels = temperature, creator = AE-1,
contentInfo = application/xml:1, content=32]
Only bare minimal amount of info needed in request (i.e. just the sensor reading)
container
contentInstance
labels = temperature
creator = AE-1
contentInfo = application/xml:1 …
content=32

## Slide 37: Time Management
Rel-4 Feature
NEW
temp
AE-1
CSE
AE: Application Entity
CSE: Common Services Entity
timeSeries
AE-1
CSEBase
1) Request to create timeSeriesInstance resource
[Originating Timestamp = 20201003T112432,
Data Generation Time = 20201003T112405
content = 32, …]
timeSeriesInstance1
dataGenerationTime = 20201003T113140,
content = 32
CSE
AE-2
.
.
.
2) Based on AE-1’s Originating Timestamp value, CSE detects time synchronization offset of +7mins 35secs
3) CSE compensates for time offset by adjusting Data Generation Time by 7mins 35secs
4) Request to Retrieve timeSeriesInstance resource
[Originating Timestamp = 20201003T161349]
5) Based on AE-2’s Originating Timestamp value, CSE detects time synchronization offset of +4mins 15secs and adjusts Data Generation Time to compensate for offset when responding to AE-2
6) Response
[Data Generation Time = 20201003T113555
content = 32, …]
CSE compensates for time offset by adjusting Data Generation Time by 11mins 50secs

## Slide 38: Software Campaigning
CSE
AE: Application Entity
CSE: Common Services Entity
AE-1
CSEBase
softwareCampaign
version = 1.2.5
name = MN-CSE
targets = Node-2, Node-3, Node-4
softwareOperation = INSTALL
URL = http://images/MN-CSE
softwareTriggerCriteria = subjectResource123
CSE-1
AE-1
2) When software campaign trigger criteria are met, CSE-1 performs operations to manage CSE SW on targeted Fog/Edge nodes
CSE-2
CSE-3
CSE-4
3a) Install CSE software
AE-1 offloads software management to CSE-1 using software campaigning to orchestrate CSEs deployed on Fog/Edge nodes
4) Response
[Aggregated software campaign results]
Node-2
Node-3
Node-4
1) Software Campaign Request
[targets, trigger criteria, operation, version, URL, …]
3b) Install CSE software
3c) Install CSE software
Rel-4 Feature
NEW

## Slide 39: Semantic Reasoning
Rel-4 Feature
NEW
Located in Area-A
Located in Area-B
AE-2
CSEBase
AE-3
semanticDescriptor2
“AE-2” “is-a” “Temperature Sensor”
“AE-2” “isLocatedIn” “Area-A”
semanticDescriptor1
Semantic Resource Discovery Request
temp
AE-2
CSE
AE: Application Entity
CSE: Common Services Entity
AE-1
AE sends a semantic based resource discovery request
SELECT ?sensor
WHERE {
?sensor “is-a” “Temperature Sensor”
?sensor “isOwnedBy” “Organization-A”
}
temp
AE-3
semanticRuleRepository
reasoningRules
If X “isLocatedIn” “Area-A”  X “isOwnedBy” “Organization-A”
Response (AE-2)
CSE applies semantic reasoning rules to perform semantic discovery and determine that
“AE-2” “is-a” “Temperature Sensor”
that “isOwnedBy” “Organization-A”

## Slide 40: Modbus Interworking
Rel-4 Feature
NEW
temp
CSE
AE: Application Entity
CSE: Common Services Entity
IPE: Interworking Proxy Entity
IPE-AE
Retrieve deviceThermometer1 Request
CSEBase
AE-1
AE-1 can retrieve the value of a temperature sensor without having to be aware it is a Modbus device
temp
temp
Response
(temperature = 72)
Modbus
Device 1
Modbus
Device 2
Modbus
Device 3
IPE
deviceThermometer1
deviceThermometer2
deviceThermometer3
Modbus devices represented as oneM2M devices

## Slide 41: End-to-End QoS Session
Rel-4 Feature
NEW
temp
AE-2
CSE
AE: Application Entity
CSE: Common Services Entity
AE-1
CSEBase
3) E2E request with QoS from
AE-1 to AE-2 with
e2eQosSession
e2eQosRequirements = QoS level, schedule, etc.
CSE
AE-1
2) CSE configures QoS session parameters between AE-1 and AE-2 in underlying 3GPP network
3GPP Network
Request to establish
E2E QoS Session between
AE-1 and AE-2
4) E2E request from
AE-1 to AE-2 with QoS
AE-1 needs to communicate with AE-2 with a guaranteed level of QoS (e.g. low latency)

## Slide 42: Network Congestion Monitoring
Rel-4 Feature
NEW
CSE
AE: Application Entity
CSE: Common Services Entity
AE-1
CSEBase
4) Notification of high
network congestion in New York
nwMonitoringReq
geographicArea = [40.71, -74.0]
CSE
AE-1
2) CSE subscribes to 3GPP network to receive notifications of high congestion level in a New York area
3GPP Network
AE-1 requests to be notified if network congestion in a New York area becomes high
temp
AE-2
temp
AE-3
temp
AE-4
Location: New York
[40.71, -74.0]
Location: New York
[40.71, -74.0]
Location: New York
[40.71, -74.0]
3) 3GPP network notifies CSE that network congestion in the specified New York area is high
AE-1 scales communication with devices in New York area to help reduce network congestion

## Slide 43: Resource Synchronization
Rel-4 Feature
NEW
AE-2
CSEBase-2
Door
doorLock = False
Announced AE-2
CSEBase-1
Announced Door
doorLock = False
CSE
CSE-1
AE-1
2) Synchronize original resource to announced resource
[doorLock = False]
AE-2
CSE-2
1) Request to unlock door using announced resource
[doorLock = False]
3) Notify when original door resource updated via synchronization
[doorLock = False]
Synchronization
In Rel-4, when announced resource is updated, original resource is updated automatically to keep it synchronized. Synchronization in the opposite direction supported in prior releases.
AE: Application Entity
CSE: Common Services Entity

## Slide 44: Service Subscriber & User Management
Rel-4 Feature
NEW
CSEBase
m2mServiceSubscriptionProfile
CSE
AE: Application Entity
CSE: Common Services Entity
serviceSubscribedAppRule
serviceSubscribedUserProfile
Defines Service Subscription information for an individual Service Subscriber and their authorized Service Users
Defines settings & restrictions for an individual Service User (e.g. how much data a user can store in the CSE)
Defines which AEs can register to a CSE and which Service User are authorized to access services of the CSE using these AEs
New Service Subscriber / User Features:
Service Subscriber & User profiles
Service User based authorization
Service User based charging & accounting

## Slide 45: Security Enhancements
Rel-4 Feature
NEW
CSEBase
CSE
AE: Application Entity
CSE: Common Services Entity
accessControlPolicy
flexContainer
Enhanced to support limit-based access rules (e.g. grant access only 5 times)
Different access control rules can now be defined for different attributes of a resource rather than the entire resource (e.g. attribute 1, attribute N).
New Security Features:
Attribute level access control policies
Context aware access control policies
Permission-based discovery
accessControlPolicyIDs
attribute 1
attribute N
Enhanced to support access control rules that are contingent on the state of other resources

## Slide 46: Group Anycast / Somecast
Rel-4 Feature
NEW
temp
AE-2
CSE
AE: Application Entity
CSE: Common Services Entity
Group-1
memberIDs = AE-2,
AE-3,
AE-4,
AE-5
Group-1 Anycast/Somecast Retrieve Request
(Group Somecast Target Number = 1)
CSEBase
AE-1
Retrieve Request
AE sends a request to retrieve the value of any temperature sensor within a group
CSE selects1 group members based on algorithm
(e.g. round robin)
temp
AE-3
temp
AE-4
temp
AE-5
Anycast/Somecast Response
( AE-5 temp)

## Slide 47: Discovery-based Operations
Rel-4 Feature
NEW
AE-2
labels = temperature
appName = tempSensor
CSEBase
Discovery-based UPDATE Request
[Filter Criteria: [filterUsage = discoveryBasedOperation, labels=temperature]
Content: appName = tempSensor]
temp
AE-2
CSE
AE: Application Entity
CSE: Common Services Entity
AE-1
AE can send a single request to both discover AEs with labels set to “temperature” and then to update the “appName” attribute to “tempSensor”
temp
AE-3
Response
[Aggregated Update Results for AE-2 and AE-3]
CSE performs discovery and then update operations
AE-3
labels = temperature
appName = tempSensor

## Slide 48
Thank you!

## Slide 49: Q&A
The oneM2M Partnership Project - the standard for an IoT eco-system
  Roland Hechwartner of Deutsche Telekom, Chair of the oneM2M Technical Plenary
oneM2M enables data interoperability
  Shane He of Nokia, Chair of the Requirements and Domain Models working group
oneM2M testing, certification and developers outreach program
  Andrew Min-gyu Han of Hansung University, Chair of the Testing and Developers Ecosystem working group
oneM2M Release 4 - a preview of new features
  Dale Seed of Convida Wireless, Chair of the System Design and Security working group

## Slide 50: Backup

## Slide 51: oneM2M Adoption is Global
oneM2M Product Offerings
oneM2M Trial Deployment
oneM2M Commercial Deployment
oneM2M Open Source Project
oneM2M adoption is
expanding
Use of oneM2M recommended (Smart Cities)
New LA with ICA*
*ICA .. IoT Connectivity Alliance
Notes: Korea
  Ministry of the Interior (MOIS) issued IoT deployment guidelines stating that it is necessary to adopt a standards-based open architecture for smart cities. Use of oneM2M is recommended.
India
  TSDSI has submitted transposed specifications to India’s Department of Telecommunications (DoT)/ Telecommunication Engineering Centre (TEC) for adoption consideration
  TEC has formed a Consultative Committee of experts to lead the oneM2M adoption process and formulate recommendations for use of oneM2M in the M2M/IoT ecosystem and smart cities in India
China
  oneM2M liaison agreement with ICA (IoT Connectivity Alliance) and the Chinese market including Alibaba
  China Communications Standards Association (CCSA) has transposed the oneM2M specifications, now submitted to Govt.
Japan
  Gov’t is being lobbied to mandate use of oneM2M by association of Radio Industries and Business (ARIB), Telecoms Technical Committee (TTC), NTT, KDDI…..
USA
  Liaison work with OCF which stands to bring in the local-area and consumer devices market

## Slide 52: oneM2M Implementation Ecosystem
IotDM
OS-IoT
  Industry-driven Open source implementations
  Regular Interop Events (6 Held from 2015-2018)
  Examples of Commercial implementations, Prototypes, Trials
  Certification Test Houses and Test Tool Vendors
A vibrant and healthy oneM2M ecosystem continues to build
oneM2M.org lists
65
Deployments List of deployments
Based on slides by: Dale Seed, oneM2M Overview 2019

## Slide 53: Takeaways
oneM2M
is a global open standard, not controlled by a single private company
specifies a common set of horizontal IoT services
  architecture, common services functions, information model
enables data interoperability
  Information model, semantics, ontology based interoperability
interworks with existing IoT technologies
has interoperability testing and a certification program
  standardized APIs simplify the life for IoT stakeholders
  minimize development, deployment & maintenance costs
is a mature and a commercially deployed technology
Work progressing on
oneM2M release 4
Expected: Q4 2020

## Slide 54: Publicly Accessible Links
Smart Device Template SDT 3.0 is available under Apache 2 License: https://git.onem2m.org/MAS/SDT
TS-0023 : SDT based Information Model and Mapping for Vertical Industries The latest published version of TS-0023 is available: http://www.onem2m.org/technical/published-drafts
Tools A utility for converting SDT to other formats is the SDTTool: https://github.com/Homegateway/SDTTool
Twitter @oneM2M
Stackoverflow https://stackoverflow.com/questions/tagged/onem2m
Web Site http://www.oneM2M.org
Developer Guides http://www.onem2m.org/developer-guides
Technical Questions http://www.onem2m.org/technical/technical-questions
Published Specifications http://www.onem2m.org/technical/published-documents
Webinars http://www.onem2m.org/technical/webinars
YouTube Channel https://www.youtube.com/c/onem2morg
Events http://www.onem2m.org/news-events/events
Certified Products http://www.onem2mcert.com/sub/sub04_01.php