## Slide 1: System implementation on Edge X with oneM2M
oneM2M SDS#43
SeungMyeong Jeong
KETI

## Slide 2: Harmony of Edge and Cloud
CSE
EdgeX provides Edge G/W, while oneM2M provides Cloud
EdgeX is open source implementation based on MSA
  Microservices talks each other using REST
EdgeX – device services (layer) supports heterogeneous protocols/devices
Collected data can be used in the edge (e.g. analysis by supporting services
Also can be exported to the cloud

## Slide 3: Edge gateway architecture
G/W architecture based on EdgeX
  IPEs on northbound and southbound
  Edge applications rules (e.g. Drools rule engine)
  Machine learning modules

## Slide 4: Implementations (1/2)
Edge G/W based on Edge X is served as AE
  manages devices and collect/process data
  communicates with CSE with the export services
  uses MQTT binding as MQTT can be used as well for communications for Edge X micro services

## Slide 5: Implementations (2/2)
Device management done by Edge G/W (possibly with ML) is exposed to oneM2M cloud
Devices list and/or hierarchy gets instantiated as oneM2M resources
  Edge G/W maintains local DB and synchronize this to the oneM2M platform
  Data measurements also gets populated in oneM2M platform

## Slide 6: PoC Service
Wildfire alerting service
  Disposable IoT sensors deployed in wide area
  Sensors get registered to the Edge G/W
  Edge G/W manages sensor registration as well as sensor readings
  Collected data is processed (e.g. statistics, inference) and posted to the oneM2M platform with raw data
  Task orchestration can also be performed via Edge G/W