## Slide 1: CMDH Complexity
Bob Flynn, bob.Flynn@exactagss.com
SDS-2021-0054-CMDH_Complexity

## Slide 2: Current CMDH Resources

## Slide 3: DB Calls based on Current CMDH Resources
New request or response message for CMDH validation
Partially Retrieve “nodeLink” attribute from target resource where resource id = To URI of the request/From URI of the response (DB Call 1)
Retrieve the CMDH Policy resource (DB Call 3)
Partially Retrieve “activeCMDHPolicy” attribute from selected node resource (DB Call 2)
Retrieve cmdhLimits resource where requestOrigin = From URI of the request and highest order (DB Call 6) and apply the limits to CMDH Parameters
Retrieve cmdhEcDefParamValues resource where applicableEventCategory = selected ec value (DB Call 5) and fill the default values for CMDH Parameters
Partially Retrieve “defEcValue” attribute from cmdhDefEcValue resource where requestOrigin = From URI of the request and highest order (DB Call 4)

## Slide 4: DB Calls based on Current CMDH Resources
Partial Retrieve “mgmtLink” attribute from cmdhNetworkAccessRules resource resource where applicableEventCategory = selected ec value (DB Call 7)
Conditionally retrieve cmdhNwAccessRule resource by applying condition “mgmtLink” attribute = scheduleId of selected schedule (DB Call 8)
End
Check all available schedule resources in the schedule registry under node based on the rqet and rset parameters of request/response. Fetch the scheduleId of matching schedule.
Retrieve cmdhBuffer resource where applicableEventCategory = selected ec value (DB Call 9)

## Slide 5: DB Calls based on Current CMDH Resources
9 Accesses to the database just to figure out parameters of a request when CMDH is supported. This is before we handle the request.
Generally speaking, this is for “retargeted” requests.

## Slide 6: Optimized CMDH Resources
Node
cmdhPolicy
cmdhEcLimits
cmdhNwAccessRule
1… n
1… n
0… 1
schedule
0… n
CSEBASE
cmdhPolicy
cmdhEcLimits
cmdhNwAccessRule
1… n
1… n
0… 1
schedule
0… n
At IN-CSE
At MN-CSE

## Slide 7: Optimized CMDH Resources at ASN-CSE
remoteCSE (IN)
cmdhPolicy
cmdhEcLimits
cmdhNwAccessRule
1… n
1
0… 1
Note: IN-CSE cannot be represented by a node resource at ASN-CSE. Hence for the demo call flow, cmdhPolicy resource and child resources can be created under the remoteCSE representing IN-CSE on ASN-CSE. Also, IN-CSE will be available always, therefore schedule resource is not required at ASN-CSE

## Slide 8: Optimized CMDH Resources
Changes required to existing cmdhPolicy resource
Add a new custom attribute “maxBufferSize” to the resource to represent the bufferSize for the target entity associated with the parent node.
Attributes | Multiplicity | RW/RO/WO | Description
maxBufferSize | 1 | RW | Maximum amount of memory that can be used for buffering requests for the associated target entity

## Slide 9: Optimized CMDH Resources
Changes required to existing cmdhNwAccessRule resource
The set of CMDH policies associated with a node shall contain at most one [cmdhNwAccessRule] resource with distinct targetNetwork.
Add a new custom attribute “allowedScheduleLink” which represents the schedule resource id of the schedule resource associated with the target entity.
There should be at least one cmdhNwAccessRule to apply for when entity is the source and when entity is the target.
Attributes | Multiplicity | RW/RO/WO | Description
allowedScheduleLink | 1 | RW | Resource Id of the schedule resource associated with the target entity
maxWaitingTime | 1 | RW | Maximum amount of time for which request needs to wait before forwarding if the schedule is available. If minReqVolume is not satisfied within this time period, the request will be forwarded at the end of the waiting time
minWaitingTime | 1 | RW | Minimum amount of time for which requests needs to wait before forwarding even if minReqVolume is satisfied. The requests will be forwarded at the end of the waiting time.
poa | 1 | RW | The pointOfAccess of the target on this particular targetNetwork.
sendingPriority | 1 | RW | The priority of network access rule resource. The resource with allowedSchedule and highest priority will be selected.
applicableEntity | 1 | RW | It determines whether to apply these rules on uplink or downlink data. Values can be “Source” or “Destination”.

## Slide 10: [cmdhEcLimits] Resource
It is used to define a value for the Event Category parameter if not set and limits for other cmdh related parameters based on the requester.
It also contains storage priority for the request/response based on the requester.
Attributes | Multiplicity | RW/RO/WO | Description
defEcValue | 1 | RW | The value to use for Event Category parameter.
requestOrigin | 1 | RW | The requestOrigin attribute is a list of zero or more local AE-IDs or the strings 'localAE' or 'thisCSE’. The set of CMDH policies associated with a particular node shall contain at most one [cmdhEcLimits] resource that contains 'localAE’, ‘thisCSE’ or local AE-IDs in the requestOrigin attribute.
minReqSize | 1 | RW | Minimum amount of data from this requestor that needs to be aggregated before forwarding.
limitsEventCategory | 0..1 | RW | Allowed values for the Event Category parameter) in a request or response.
limitsRequestExpTime | 0..1 | RW | Range of allowed values for the Request Expiration Timestamp parameter in a request

## Slide 11: [cmdhEcLimits] Resource Contd..
Attributes | Multiplicity | RW/RO/WO | Description
limitsResultExpTime | 0..1 | RW | Range of allowed values for the Result Expiration Timestamp parameter in a request or response
limitsOpExecTime | 0..1 | RW | Range of allowed values for the Operation Execution Time parameter in a request
limitsRespPersistence | 0..1 | RW | Range of allowed values for the Result Persistence parameter in a request
limitsDelAggregation | 0..1 | RW | List of allowed values for the Delivery Aggregation parameter in a request
storagePriority | 0..1 | RW | Storage priority for data that is stored for buffering request or response messages matching with the requestOrigin attribute.
latestDefault | 0..1 | RW | Default value for latest i.e. latest request for particular to, from and operation should be buffered. This should be only present if defEcValue is bestEffort.
allowedLatest | 0..1(L) | RW | Allowed values for the latest. This should be only present if defEcValue is bestEffort.
Note: If any of the optional parameters are not set in the selected [cmdhEcLimits] resource,
then values of those parameters of [cmdhEcLimits] resource with requestOrigin as “localAE” or “thisCSE” should be applied.
For example, [cmdhEcLimits] resource with requestOrigin as “localAE” or “thisCSE” should have all the optional attributes set.

## Slide 12: CMDH Parameters
Below is the list of CMDH-related Request parameters :
Event Category ('ec’)
Request Expiration Timestamp ('rqet')
Result Expiration Timestamp ('rset')
Operation Execution Time ('oet')
Result Persistence ('rp')
Originating Timestamp ('ot')
Delivery Aggregation ('da’)
Latest (‘lat’) - New CMDH Parameter which determines if the request/response is latest i.e. always send the latest request/response for particular originator and target.

## Slide 13: CMDH Processing
New request or response message for CMDH validation
Determine the associated [cmdhPolicy] child resource of the node resource
Fetch the maxBufferSize attribute from selected [cmdhPolicy] resource
Determine “ec” parameter value from [cmdhEcLimits] resource based on the request originator
Apply network access rules based on targetNetwork
Determine if message is to be buffered and complies with the buffer limits.
CMDH Message Validation Successful
End
Determine and apply limits to CMDH Related Parameters retrieved from [cmdhEcLimits] resource

## Slide 14: DB Call for CMDH Processing at IN-CSE
New request or response message for CMDH validation
Partially Retrieve “nodeLink” attribute from target resource where resource id = To URI of the request/From URI of the response (DB Call 1)
Store retrieved values in the registry. Fill key as target uri and value as cmdhPolicyId, maxBufferSize and nodeId in the registry
Partially Retrieve “maxBufferSize” attribute from cmdhPolicy resource under the selected node resource(DB Call 2)
Conditionally retrieve cmdhEcLimits and cmdhNwAccessRule resource by applying condition pi = cmdhPolicyId and (cnd=cmdhEcLimits and requestOrigin IN (originator, localAE, thisCSE) or (cnd = cmdhNwAccessRule and allowedScheduleLink = scheduleId)(DB Call 3)
End
Check all available schedule resources in the schedule registry under node based on the rqet and rset parameters of request/response. Fetch the scheduleId of matching schedule.

## Slide 15: DB Call for CMDH Processing at ASN-CSE for PTN
Conditionally retrieve cmdhEcLimits and cmdhNwAccessRule resource by applying condition pi = cmdhPolicyId and (cnd=cmdhEcLimits and requestOrigin IN (originator, localAE, thisCSE) or (cnd = cmdhNwAccessRule)(DB Call 2)
End
Store retrieved values in the registry. Fill key as target uri and value as cmdhPolicyId and maxBufferSize in the registry
Partially Retrieve “maxBufferSize” attribute from cmdhPolicy resource under the target resource where resource id = To URI of the request/From URI of the response (DB Call 1)
New request or response message for CMDH validation
Note : When the request/response is targeted to IN-CSE, ASN-CSE will perform above steps for CMDH Validation. As IN-CSE will not be represented as node resource and will not have schedule, hence those steps are not required.