## Slide 1: CMDH Buffering
Bob Flynn, bob.Flynn@exactagss.com
SDS-2022-0002-CMDH_Buffering

## Slide 2: Background
CMDH capabilities are needed to comply with GSMA TS.34 requirements for efficient communications
SDS-2021-0054-CMDH_complexity demonstrated some issues the exist in current specifications
  We agreed to address the CMDH complexity and other issues in the context of WI-0096 and via changes proposed in TR-0063
This contribution will highlight more issues with the current CMDH specification

## Slide 3: CMDH specifications
TS-0001, Clause 8.1.2 Request
  Event Category
  Delivery Aggregation
TS-0001, Clause 9.6.11 Resource Type <delivery>
  Provides a RESTful API to CMDH storage
TS-0001, Clause D.12 Resource cmdhPolicy
  Default settings when not provided in the request primitive
  Limits when provided in the request primitive
  Network usage policy; e.g. when to use cellular VS wifi VS lorawan
  Buffering based on Event Category
TS-0004, Clause H CMDH Processing

## Slide 4: Basic Concept essential to CMDH
When a primitive is received at CSE determine if the message can be retargeted to the “next” CSE.
  If YES send via the appropriate interface
  If NO store the message
If messages are stored, when and how are they transmitted
As of today, most primitives do not use any of the request parameters associated with CMDH.
  We need to specify defaults that make sense when these primitives target a CSE that is constrained by a communication schedule
    CSE can be source or destination

## Slide 5: Issue 1: Primitive Request
Event Category
  immediate -> Do not store request. Do not use CMDH
  bestEffort -> Use CMDH. Store the request if necessary
  Latest
    CRUD -> normal CMDH with max buffer size of 1
    NOTIFY -> keep only 1 notification for a specific notificationURI from a given subscription
Slightly different semantics in these parameters
  Immediate -> should this be used to “override” a schedule?
    Force CIoT based device to communicate immediately
    Force IN-CSE to “trigger” a device to “wake-up”
    Should this require special authorizations?
      Without special authorization we essentially lose this capability in certain conditions
  Latest -> should this functionality be exposed on the request or as a policy
    Already covered for notifications in the <subscription> resource
    Should this be a policy associated to a specific resource?

## Slide 6: Issue 2: delivery aggregation
Used to specify whether messages should be delivered in bulk or 1 at a time to destination CSE
  Does not seem appropriate for a “Request Parameter”
  Seems more appropriate as a CMDH policy
    Delivery using a Cellular network should use delivery aggregation (TS.34 recommendation), i.e. to be PTN compliant aggregated delivery SHALL be supported.
    Delivery to constrained devices MAY be better to send messages 1 at a time

## Slide 7: Issue 3: <delivery> resource
There seems to be an implied relationship to <request>, but no real relationship is defined.
  I propose that a relationship should exist and be fully defined.
According to clause 10.2.5.7, specifying deliveryAggregation = ON triggers use of <delivery> resource.
  I propose that this should not be determined by the AE. This should be CMDH/CSE logic.
According to clause 10.2.5.7, CSE1 will create a local <delivery> and then a remote <delivery> on CSE2. CSE2 will create remote <delivery> on CSE3 (target of multi-hop request)
  I propose that this be simplified. Too much responsibility for a potentially constrained ASN-CSE

## Slide 8: Buffering Concepts
TS-0001, clause D.12.8 cmdhBuffer
  Summary:
    A maxBufferSize is specified for each applicableEventCategory
      Immediate, bestEffort, latest, default [ each type can only appear 1 time ]
    A configurable storagePriority is defined (not clearly) for management of the buffer size
    Some CMDH parameters are embedded into <subscription> attributes (storagePriority, latest)
      These parameters could be applied more generically to other primitives where the originator is a CSE, such as announcements, fanout, etc.
TS-0004, Clause H CMDH Processing
  Message Validation:
    Parameter pre-processing: discussed in SDS-2021-0054-CMDH_complexity
    Buffering: This contribution
  Message forwarding: This contribution

## Slide 9: Buffering Concepts
Summary:
  A [cmdhPolicy] is a parent “container” (no functional attributes). It contains (related to buffering)
    1 or more cmdhNetworkAccessRules
    1 or more cmdhBuffer
  Usage as defined
    Specify the active policy to use
      This will define available cmdhNetworkAccessRules and cmdhBuffer
    Some entity will change the active policy where some of the linked cmdhNetworkAccessRules and cmdhBuffer [or defaults/limits] may be different

## Slide 10: Buffering Concepts
NWAR1
Buffer1
Policy1
NWAR1
Buffer1
NWAR2
Buffer2
Policy2
When the buffers change it creates confusion.
For example: Buffer1 is default. Buffer 2 is BestEffort.
When the active policy is changed from 1 to 2 should we delete messages?
This seems to be a fairly undesirable behavior.
Purpose of changing the active policy is to manage communication over the Network versus storage on the device.

## Slide 11: Buffering Concepts
Proposed Usage
  Propose to eliminate Buffer based on EventCategory
    Immediate does not get stored
    Latest can be managed within a common buffer, no need for a separate buffer
    Simplifies concepts and logic
  Single buffer for each destination CSE
    cmdhNetworkAccess policy will determine how messages are sent
      Bulk size
      Retry rate
      Etc.
NWAR1
Buffer1
CSE1-Node
NWAR2
Buffer2
CSE2-Node

## Slide 12: Buffering Concepts
NWAR1
IN-Node
NWAR2
ASN-CSE-Node
NWAR3
MN-CSE-Node
Optional or NA for always available connection
Size based on memory available on device
Size not necessarily constrained
Different policies based
on conditions. E.g.
use NWAR1 if networkCondition >8
use NWAR2 if Ec = immediate
Buffer1
Buffer2
Buffer3

## Slide 13: Proposal: Align functionality of similar features
CMDH - <delivery> - <request> - <pollingChannel>
  All involve management of requests that MAY be delivered asynchronously
    CMDH -> communication channel is not available
    <delivery> -> used if the originator uses deliveryAggregation for CMDH
    <request> -> used for non-blocking requests
    <pollingChannel> - used for non-request reachable <AE>/<CSE>
Basic Concept: Since <pollingChannel> and <request> have been implemented and tested we should align to these as much as possible.
  Any message that is not forwarded by a CSE is stored in a <request>
  <delivery> is the parent of all <request> resources
    There is a <delivery> for each registree <AE> and <CSE> (next hop only) (this relates to cmdhBuffer)
  Limit access to <delivery> similar to <pollingChannel>
  When entity does long polling, responses come from <delivery>/<request>
  When CMDH channel is available messages are sent from <delivery>/<request>
  CMDH policies govern the size/number of <request> resources stored
    like we do for container sizes

## Slide 14: Next Step
If this concept is agreeable to the working group, then I’ll start working on contributions.
One more significant topics to discuss in separate contributions
  Process for selecting appropriate communication channel to use
  Contribution is pending

## Slide 15: Buffering Concepts
Issues:
  cmdhBuffer: what granularity do we want to support?
    Single buffer for each destination CSE -> This is a good fit for GSMA TS.34
    Buffer based on Originator -> not described in current specifications
      Prevent a single Originator from using highest priority and causing other originator messages to be removed.
    Buffer based on EventCategory -> Propose to eliminate this concept
  TS-0004 links buffer size limits to the cmdhNwAccessRule(s)
    Buffer size should be linked to the device only (host CSE)
    cmdhNwAccessRule(s) should focus on
      When to use a particular NwAccess
      How much data to send on that channel.
      For example:
        cmdhNwAccessRule for ASN-CSE to IN-CSE:
          wifi -> schedule always available for all messages. (need to define available. i.e. if response is not received then message should be listed as not sent)
            Buffer 10 requests / max hold time of 5 minutes for regular messages
            Buffer 1 request / no hold time for immediate messages
          3GPP ->
            schedule always available for immediate messages max hold time of 10 minutes.
            schedule available for priority 1-3 messages max hold time of 2 hours
            schedule available at 11:00 send all messages