## Slide 1
Discussion on announcement issues
Andreas Kraft – Deutsche Telekom
Miguel Angel Reina Ortega - ETSI
1

## Slide 2
Introduction
During the implementation and validation of the changes made to the announcement procedure in both TS-0001 and TS-0004, several issues have been identified
Issue#1 - acpi attribute in the announced resource
Issue#2 – Instance resource to be announced when its parent is not announced
Issue#3 – Behaviour for unsuccessful announcement
Issue#4 - Checking of existing CSEBaseAnnc
Issue#5 - Description of announceTo and announcedAttribute
For discussion - Hierarchical addressing for announced resources

## Slide 3
Issue#1
acpi attribute in the announced resource
acpi is defined as MA: “if not present in the original resource, it shall be set to the same value as the parent resource or set using the local policy of the original resource”
If local policy is to use the creator (so no associated ACP), what value should be used in apci of the announced resource?
option 1) Original resource hosting CSE should create an ACP for that originator (and the original resource Hosting CSE) and set the acpi to that ACP
option 2) To allow non presence of acpi for announced resources, so only creator have access to them (only original resource Hosting CSE)
option 3) To use creator/custodian attribute of the announced resource for setting access to the originator
In case the original resource has an acpi value and this is used in the announced resource acpi, how does the original resource Hosting CSE get access to the announced resource for further updates, de-announcement, etc..?
  Option 1) original resource Hosting CSE should always have access to the announced resources that it creates independently of the acpi of the announced resource, for instance, by looking at the link attribute

## Slide 4
Issue#2
Instance resource to be announced when its parent is not announced
Specs say that “the Hosting CSE shall send an unsuccessful response with the Response Status Code indicating an "OPERATION_NOT_ALLOWED" error in response to the received Request”
Correction: the received request should not be rejected. Instead, the announceTo attribute should be updated by the instance resource Hosting CSE and either remove the CSE-ID or keep it (issue#3) as if the announcement was unsuccessful

## Slide 5
Issue#3
Behaviour for unsuccessful announcement
Specs does not clearly indicate what to do when an unsuccessful announcement occurs. “Step 3) Replace the CSE-ID or URI in the content of the announceTo attribute contained in the original request’s resource representation with the URI of the successfully-announced resource from the Response received in step 2”
Correction: To add “Remove the CSE-ID or URI in the content of the announceTo attribute contained in the original request’s resource representation for unsuccessfully announced resource.”
Alternative: Leave the CSE-ID or URI for further retry by the Hosting CSE

## Slide 6
Issue#4
Checking of existing CSEBaseAnnc
Specs does not indicate how to detect existing CSEBaseAnnc resource for a given CSE
Correction: Include a checking for the creation of the CSEBaseAnnc so that if there exists any CSEBaseAnnc with the same value in the link attribute (which means representing the same CSE), the CSEBaseAnnc creation is rejected with responseStatusCode indicating “CONFLICT”. Originator CSE can then know that its CSEBaseAnnc already exists.
Small issue/procedure: Originator CSE needs to retrieve its own CSEBaseAnnc by using discovery filtering by resource type and link attribute to retrieve the URI of the CSEBaseAnnc resource

## Slide 7
Issue#5
Description of announceTo and announcedAttribute
Specs specifies in table 6.3.6-1:
Correction:
Note: Depending on resolution of Issue#3 the description may change with regards to empty list value
announceTo | list of xs:anyURI | Absence of this attribute means that this is not an announced resource
announcedAttribute | list of xs:NCName | Absence of this attribute means that this is not an announced resource
announceTo | list of xs:anyURI | Absence of this attribute means that either this is not an announceable resource or this is not been announced yet. Empty list means that an unsuccessful announcement or de-announcement occurred
announcedAttribute | list of xs:NCName | Absence of this attribute means that either this is not an announceable resource or no OA attribute has been announced yet. Empty list means that an unsuccessful attribute announcement or attribute de-announcement occurred

## Slide 8
For discussion
Hierarchical addressing for announced resources
Default announced resources structure cannot be used for hierarchical addressing as resource name of announced resources is not used
How to be able to use structured announced resource tree?
Proposal: To add an attribute to announced resources originalResourceName to transfer the original resource name to its announced resource. If this originalResourceName attribute exists, then it should be taken as the resource name of the announced resource so that hierarchical addressing can be used.
Potential issue: conflicts due to non announced parent resource (name conflicts)

## Slide 9
Thank you