## Slide 1: Discussion paper for enhancing Public Warning Service in oneM2M
Sherzod Elamanov (SyncTechno), TaeHyun Kim (SyncTechno)
SDS 59., May 2023

## Slide 2: Background

## Slide 3: Introduction (1/2)
The Public Warning Service (PWS) allows public authorities to send warning alerts to individuals and things in the event of a disaster (e.g. earthquake, tsunami).
This discussion paper describes the requirements and enhancements needed in oneM2M to enable PWS.
Warning issuing authority
IN-CSE
CAP*
Warning gateway AE
MN-CSE
ASN-CSE
ASN-CSE
AE
AE
AE
AE
Mca
Mcc
Mca
Mca
Mcc
Mcc
Mca
Mca
* CAP: Common Alerting Protocol
How to deliver warning messages and activate things
How to disseminate warning efficiently
How to represent warning information

## Slide 4: Introduction (2/2)
PWS Features | Release-4 | Release-5 (Objectives of WI-0113) | Target WG
How to represent warning information | SDT based information model (devicePWSCenter) | Interoperability with standard warning message data formats such as CAP. | RDM
How to disseminate warning efficiently | Possible architecture | Prioritized handling of warning messages over other messages in the oneM2M Service Layer. Efficient delivery of warning messages to the large number of IoT devices. | SDS
How to deliver warning message and activate things | SDT based information model (devicePWSEquipment) | Configuration of the behaviour of IoT devices when they receive a warning message. | SDS
WI-0113
TS-0001 & TS-0004
TS-0037 & TS-0023
WI-0070
TR-0046
TS-0037 & TS-0023
Overall features to enable Public Warning Service through oneM2M

## Slide 5: Public Warning Service in Rel-4
WI-0070 Public Warning Service Enabler was the first iteration of enabling PWS in oneM2M in Release 4.
All WI-0070 work was done in the RDM WG.
Output of WI-0070:
  Use cases and requirements related to PWS (TR-0046)
  SDT based PWS information model which compatible with Common Alerting Protocol (CAP) (TS-0037, TS-0023)
  Potential architecture for PWS[informative] (TS-0037)
Limitation
  Only focused on “How to represent warning information”

## Slide 6: STD based information model for PWS (TS-0037)
devicePWSCenter
devicePWSEquipment
disseminator
settings
emergencyHandler
ModuleClass
Device module
1
1
1
DataPoints
Actions
disseminator <DataPoints>
cancel <Action>
emergencyHandler <DataPoints>
Settings
<DataPoints>
For CSEs which forward warning message
For AEs which have the PWS capabilities
Derived from a CAP (Common Alerting Protocol) message

## Slide 7: WI-0113 Enhanced Public Warning Service Enabler

## Slide 8: WI-113 Objectives
WI-113 Enhanced Public Warning Service Enabler has the following objectives:
  Interoperability with standard warning message data formats such as CAP.
  Prioritized handling of warning messages over other messages in the oneM2M Service Layer.
  Efficient delivery of warning messages to the large number of IoT devices.
  Configuration of the behaviour of IoT devices when they receive a warning message.

## Slide 9: Objective #1:
Issues
  Rel-4 work does not fully support CAP’s capability
    Overly simplified representation of geographic information.
    Does not support variable number of system specific parameters
  flexContainer update
    omitted property values being preserved as garbage values when implemented with flexContainer.
Interoperability with standard warning message data formats such as CAP
  Revise SDT Information Model (TS-0023, TS-0037 @RDM WG)
  Propose a way to update all custom attributes when a <flexContainer> is updated (TS-0001, TS-0004)

## Slide 10: Issue on flexContainer update
A <flexContainer>
rn
lbl
…
ca_led_red: on
ca_led_yellow: on
ca_led_green: on
A <flexContainer>
rn
lbl
…
ca_led_red: on
ca_led_yellow: off
ca_led_green: on
UPDATE flexContainer { ca_led_yellow: off}
<Basic usage of flexContainer>
<Issue on PWS specialization for warning>
A <flexContainer>
rn
lbl
…
eventCode: Earthquake
magnitude: 5
A <flexContainer>
rn
lbl
…
eventCode: Blizzard
windSpeed: 10
magnitude: 5
UPDATE flexContainer {
eventCode: Blizzard
windSpeed: 10
}
XML CAP Message
Custom attributes which is derived from CAP are linked
Must update all or nothing in same time update operation

## Slide 11: Objective #2:
Issues
  Public warning service is a mission-critical service with high time constraints. Therefore, it should be prioritized and delivered ahead of other primitives.
    eventCategory property of RequestPrimitive only handle CMDH buffer management.
Prioritized handling of warning messages over other messages in the oneM2M Service Layer.
  Will proposed prioritization mechanism of RequestPrimitives (TS-0001, TS-0004)
  How to indicate mission-critical primitive
  How to handle based on priority of primitives

## Slide 12: Objective #3:
Issues
  Public Warning Messages need to be delivered to a large number of devices within a short time. Therefore, Therefore, using multicast/broadcast communication can be effective in achieving this goal.
    <gourp>, <localMulticastGroup>, <subscription> could be used to deliver warning message
  Efficient delivery of warning messages to the large number of IoT devices.
  Will proposed small CRs to optimize use of <group>, <localMulticastGroup> and <subscription> resources (TS-0001, TS-0004)

## Slide 13: Objective #4:
Issues
  Devices may have different types and levels of events to which it can respond. Therefore, oneM2M system provide way to configure device policy.
  Configuration of the behaviour of IoT devices when they receive a warning message.
  Will proposed new mgmtObj specialization to configure PWS related device policies (TS-0001, TS-0004)