## Slide 1: 3GPP Interworking via NEF N33 API
Sherzod Elamanov (SyncTechno), TaeHyun Kim (SyncTechno)
SDS 61.5, 17 October 2023

## Slide 2: Background
oneM2M has specified 3GPP interworking in Rel-3 and Rel-4 in TS-0026 for utilizing Cellular IoT features exposed by the 3GPP network.
The scope was the interworking with the SCEF Northbound API via T8 interface.
The interworking was based on SCEF T8 API Rel-13, Rel-14, and Rel-15 (TS 29.122).
Since 3GPP Rel-15, 3GPP has been standardizing NEF N33 API (TS 29.522) as a Northbound interface of the 5G System. The latest completed version of TS 29.522 is Rel-17.
Most of the functionality defined for SCEF are also exposed by NEF (but with different API). New features exclusive to NEF are also developed by 3GPP.
NEF
N33
AF
NEF Northbound API reference model

## Slide 3: 3GPP Interworking via NEF N33 API
oneM2M needs to support the interworking with 3GPP network via NEF N33 API to support the recent advances of 3GPP in Rel-15, Rel-16, and Rel-17 for the NEF Northbound API introduced in the 5G System.
As a first step, the interworking via NEF N33 API needs to cover the existing interworking functionality that was defined for SCEF T8 API in TS-0026 (e.g. NIDD, monitoring events, etc.).
Most of the existing oneM2M Service Layer functionality related to 3GPP interworking will remain the same.
New features exclusive to NEF API may be added as well.

## Slide 4: Potential interworking reference model with NEF
UE (ADN/ASN/MN)
AF
(IN/MN-CSE)
5G Core network
N33
(Mcn)
UPF
AMF
SMF
PCF
UDM
NEF
5G
(R)AN
N6
(Mcc/Mca)
Uu
N2
N1
N3
UE User Equipment
RAN Radio Access Network
AMF Access Mobility Function
SMF Session Management Function
PCF Policy Control Function
UDM Unified Data Manager
NEF Network Exposure Function
UPF User Plane Function
AF Application Function
5G System

## Slide 5: Proposal for a new Work Item
A new Work Item is needed to specify the interworking with 3GPP network via NEF N33 API.
Scope of the Work Item:
  Introduce NEF, NEF API and its role in 3GPP interworking architecture of oneM2M including:
    NEF functionality within 3GPP network.
    Cellular IoT features and services of NEF.
    NEF N33 API (e.g. protocol, serialization, etc.)
    Functional mapping between 3GPP network and oneM2M.
  Connectivity establishment between oneM2M nodes via 3GPP Network (5G System)
  Map the interworking solutions defined in clause 7 of TS-0026 that were defined with respect to SCEF API into NEF API considering the advanced of NEF compared to SCEF.
Target TS: TS-0026 (3GPP Interworking). CRs to TS-0001, TS-0002, TS-0004 may be needed for alignment purposes.
New features of NEF API may be added depending on the work progress and Rel-5 timeline.