## Slide 1: Default Announcement of Optional Announced Attributes
Proposed oneM2M Change Requests for TS-0001 and TS-0004
Source: Bob Flynn bob.Flynn@exactagss.com
Andreas Kraft andreas.kraft@jk-conpro.de
Meeting Date: 2025-11-10

## Slide 2: Current Implementation
Only attributes explicitly listed in announcedAttribute are announced.
If announcedAttribute is not specified, no OA attributes are announced by default.
Developers must manually maintain announcedAttribute lists for each resource type.
Custom flexContainer attributes are not announced unless explicitly added.
This behavior increases configuration complexity and risk of inconsistent propagation.

## Slide 3: Desired Change
If announcedAttribute is absent or empty → all OA attributes (including custom flexContainer attributes) are announced.
If announcedAttribute is present and non-empty → only the listed OA attributes are announced.
Mandatory (MA) attributes remain always announced.
Synchronization direction remains governed by announceSyncType.
Simplifies configuration and ensures consistent announcement across CSEs.

## Slide 4: Backward Compatibility
Existing systems that list attributes in announcedAttribute retain identical behavior.
Deployments that omit announcedAttribute now gain full OA announcement automatically.
No schema or API version changes required.
Access Control and synchronization (announceSyncType) remain unchanged.

## Slide 5: Benefits of Proposed Change
Simplifies implementation and reduces configuration errors.
Ensures consistent data propagation between CSEs.
Improves interoperability across vendors.
Reduces developer effort in maintaining announcedAttribute lists.
Maintains full backward compatibility.

## Slide 6: Specification Impact
TS-0001 Functional Architecture:
  10.2.13.1 – Clarify default and selective announcement behavior.
  10.2.13.7 – Redefine attribute selection as whitelist logic.
  10.2.13.9 – Specify Hosting CSE applies whitelist rule.
  10.2.13.10 – Clarify dynamic effects of announcedAttribute changes.
TS-0004 Service Layer Core Protocol:
  7.4.26 – Modify OA attribute note in Table 7.4.26-1.
  7.4.26.2 – Add procedure linking to TS-0001 whitelist rule.

## Slide 7: Summary of Change
Introduces default behavior for announcement of all Optional Announced (OA) attributes when announcedAttribute is absent or empty.
If announcedAttribute contains entries, only those attributes that are specified are announced.
Maintains backward compatibility with existing selective announcement implementations.
Affects TS-0001 (10.2.13.1, 10.2.13.7, 10.2.13.9, 10.2.13.10) and TS-0004 (7.4.26, 7.4.26.2).
No changes to Access Control Policy or synchronization rules.

## Slide 8: Conclusion
The proposed change improves usability and interoperability of resource announcements.
By defaulting to announce all OA attributes when unspecified, oneM2M ensures consistent behavior across CSEs, reduces implementation burden, and aligns with developer expectations.

## Slide 9: Thank You!