## Slide 1
Discussion: Discoverability of Announced Resources
Andreas Kraft, Bob Flynn – Exacta
1

## Slide 2
Presentation Evolution
R01
Changed suggestion to make resourceName “Mandatory Announced” to “Optional Announced” to keep backward compatibility.
Added “bad solution” to check the original resource’s announceTo attribute for the address of the announced resource.

## Slide 3
Problem
When announcing resources nothing is specified about naming the announced resources and the <CSEBaseAnnc>.
The resourceName attribute is marked as “Not Announced”
Default CREATE behaviour: If no resourceName is provided when creating a resource, then a CSE assigns a random and unique identifier (in the scope of its parent resource). This is the situation for announced resources today.
Effects
The resourceName of the announced <CSEBase> resource is unknown, except to the CSE that announced the resources.
The resourceName of every announced child resource under the announced <CSEBase> is unknown to the originator.
This makes the discoverability and use of the announced resources very difficult.

## Slide 4
Discoverability - Complex „Solutions“
The originator AE that announced the resource forwards somehow the value of the announcedTo attribute to every other consuming AE that needs to access the announced resources. How are the “other” AEs known, and is this communicated?
The originator AE and the consuming AE(s) agree on a label that is announced together with the resources. The consuming AE(s) discover the resources by the labels on the announcement target CSE. This is an unspecified extra “contract” (e.g. the label’s name) and leads to constant polling.
The consuming AE(s) retrieve the announceTo attribute of the original resource in order to . This probably needs to be done before every access to the announced target to make sure it still exists. This creates extra load, and makes announcement rather useless.

## Slide 5
Example – Situation Now
cse-mn
  myAE
    myFlexContainer
  …
cse-in
  1234abcd – <CSEBaseAnnc>
    5678efgh – <AEAnnc>
      9012ijkl – [SpecializationAnnc]
    …
  …
Note This example shows the announcement under the <CSEBaseAnnc> resource. But resources may be announced anywhere in the resource tree. resourceNames are used in the shown resource trees.

## Slide 6
Possible Solution
Provide the same resourceName as the original resource.
  If the announced resources are stored in the same hierarchy there should be no naming conflicts
  If an announced resource is stored outside the original hierarchy, there may be naming conflicts. In this case the resource cannot be announced and the conflict must be resolved differently (similar to any other naming conflict)
  The consuming AE only needs to know the resource structure and path.
  resourceName needs to become “Optional Announced”. The AE can then add the resourceName to the announcedAttributes attribute. Not announcing the resourceName keeps the original behaviour, ie. the announcement target CSE assigns a unique identifier.
  The <CSEBaseAnnc> needs to be announced with a resourceName according to the procedure described on slide 8.

## Slide 7
Example – Easier to Use
cse-mn
  myAE
    myFlexContainer
  …
cse-in
  cse-mn – <CSEBaseAnnc>
    myAE – <AEAnnc>
      myFlexContainer – [SpecializationAnnc]
    …
  …
Note This example shows the announcement under the <CSEBaseAnnc> resource. But resources may be announced anywhere in the resource tree. resourceNames are used in the shown resource trees.

## Slide 8
SP Compatibility – Problem
The name of the <CSEBaseAnnc> might cause another problem:
  Must be unique under the CSE’s resource tree root. Could be a conflict with existing resources with the same name.
    A managed deployment could prevent this, but takes extra efforts.

## Slide 9
SP Compatibility – Proposal
Using only the resourceName of the <CSEBaseAnnc> is not enough when announcing resources across multiple Service Providers.
  Using only the CSE-ID for the resourceName is not enough. It might already be taken for a <remoteCSE> resource name (remote CSE registration).
  Choosing a resourceName for the <remoteCSE> resource is also not defined. oneM2M doesn't define a naming scheme for <remoteCSE> resources. A CSE implementation might choose its own scheme, e.g. "<sp-id>_<cse-id>". This might lead to a conflict. And since we are dealing with resourceNames the suggestion is to use the resource name. However, CSE’s resourceName isn’t guaranteed to be unique, either.
  Add the SP-Provider-ID to the resourceName.
  A scheme needs to be specified to ensure interoperability. E.g. “{SP-ID stem}_{CSE resourceName}”
  Who is responsible to assign the resourceName for the <CSEBaseAnnc>? The announcing or the announcement target CSE?

## Slide 10
Example – Absolute Scope
cse-mn
  myAE
    myFlexContainer
  …
cse-in
  sp.example.com_cse-mn – <CSEBaseAnnc>
    myAE – <AEAnnc>
      myFlexContainer – [SpecializationAnnc]
    …
  sp.example.com_id-mn - <remoteCSE>
  …
Note This example shows the announcement under the <CSEBaseAnnc> resource. But resources may be announced anywhere in the resource tree. resourceNames are used in the shown resource trees.

## Slide 11
Thank you